## Slide 1: Module post-assembly reception QC
D. Warner
11/15/22

## Slide 2: Module receipt and Initial Inspection
Modules received from CSU. Filter plates installed(?)
Initial receipt inspection to confirm safe transit
  Confirm complete QC record in place (checklist)
  Visual inspection of module with check-list (WLS plates, screws tight, etc.)
  Check of module fit into mechanical model (ensure fit into APS rails)
  Final module scan in warm scanner
    DAPHNE readout
    Check against CSU exit scan

## Slide 3: Module installation, checkout
Install module into APA scanning APA/Module position information
Confirm continuity to connector at APA exit
Confirm cable continuity during Upper-Lower APA connection

## Slide 4: APA cold box test/installation checkout
Confirm connections before cold box test
Confirm operation in cold box
  DCR measurement each PD channel
  LED test (Diffusers)?
Confirm connections at flange following APA installation/cabling ni cryostat

## Slide 5: Warm monitoring in cryostat
Periodic warm checkout with LED/Monitoring system in cryostat
  Darken cryostat and operate PDs warm to validate continued performance

## Slide 6: Procedures required:
Module visual/reception inspection (check points, screw torque…) with traveler (Store in DB)
Initial installation continuity checkout with traveler (Store in DB)
Cold box test procedure with traveler (Store in DB)
Post-cryostat installation checkout with traveler (Store in DB)
Post-installation warm dark operation in cryostat (monitoring) with traveler (Store in DB)