## Slide 1
Impressions from the High Order Mode Workshop,
Daresbury, 25-27 June 2012
V. Yakovlev
PX meeting, July 13, 2012

## Slide 2
The first HOM
Workshop
Cornell, 2010
(M.Liepe)

## Slide 3
The second HOM
Workshop
Daresbury, 2012
(R. Jones)

## Slide 4
Topics:
  HOM BPM diagnostics and measurement methods
  HOM couplers and influence of FP couplers
  Novel HOM suppression in TEM and other cavity shapes
  Special considerations in third harmonic, deflecting and crab cavities
  RF absorbing materials
  Antenna HOM absorbers
  Beam-pipe HOM absorbers
  Waveguide HOM absorbers
  HOM simulation tools and models
Working Groups:
HOM Damping Requirements on a Project Basis (J. Sekutowicz,
V.P. Yakovlev and N.A. Solyak )
B . HOM-based Diagnostics (N. Baboi, C. Welsch and R.M. Jones)
RF Simulations and Beam Dynamics (M. Liepe, O. Napoly
and S. Molloy)
D. HOM Damping Couplers and Loads (J. Delayen and G. Burt)
E. Low-level RF, Controls and System Integration (T. Power)

## Slide 5
Attendees:
• Rob Ainsworth Royal Holloway, University of London
• Rob Appleby, Uniman/CI
• Nicoleta Baboi, DESY
• David Brett, University of Manchester/Cockcroft
• Rachael Buckley, STFC/ASTeC
• Stephen Buckley, STFC/ASTeC
• Graeme Burt, Lancaster University
• John Byrd, LBNL
• Lee Carver, University of Manchester
• Swapan Chattopadhyay, Cockcroft Institute
• Yahia Chergui, engineering, electricity and electronics
• John Corlett, LBNL
• Kathrin Cottel, DESY
• Tomasz Cybulski, Cockcroft Institute
• Jean Delayen, Old Dominion University
• Daniel Doherty, Lancaster University
• Nathan Eddy, Fermilab
• Thomas Flisgen, University of Rostock
• Tomasz Galek, Universität Rostock
• Philippe Goudket, ASTeC/STFC
• Pengda Gu, Diamond Light Source
• Harald Hahn, BNL
• Ben Hall, Lancaster University
• Lee Hammons, Brookhaven National Laboratory
• Roger Jones, University of Manchester/Cockcroft Inst.
• Alexander Kalinin, ASTeC Daresbury Laboratory STFC
• Philipp Kolb, TRIUMF
• Taro Konomi, Institute for Molecular Science
• Frank Krawczyk, Los Alamos National Laboratory
• Vladimir Kudrin, ITE, Darmstadt
• Matthias Liepe, Cornell University
• Chris Lingwood, Lancaster University
• Cong Liu, TEMF TU Darmstadt
• Peter McIntosh, STFC
• Fan-bo Meng, Institute of High Energy Physics
• Boris Militsyn, STFC ASTeC
• Stephen Molloy, ESS
• Alireza Nassiri, ANL
• Inna Nesmiyan, University of Manchester/CI
• Axel Neumann, Helmholtz Zentrum Berlin
• Ruediger Onken, DESY
• Shivaji Pande, Diamond Light Source Ltd
• Shrikant Pattalwar, ASTeC
• Tom Powers, Jefferson Lab
• Massimiliano Putignano, University of Liverpool
• Bernard Riemann, Dortmund University
• Jacek Sekutowicz, DESY
• Ian Shinton
• Jonathan Smith, Tech-X UK Ltd
• Susan Smith, STFC
• Nicholas Valles, Cornell University
• Ursula van Rienen, Rostock University
• Ken Watanabe, KEK
• Carsten Welsch, Cockcroft
• Alan Wheelhouse, ASTeC/STFC
• Guoxing Xia, University of Manchester
• Vyacheslav Yakovlev, Fermilab
• Pei Zhang, The University of Manchester/ DESY

## Slide 6
http://www.cockcroft.ac.uk/events/HOMSC12/programme.html

## Slide 8
A. Neumann | HZB | Cavity and HOM design for the BERLinPro ERL project
Ken Wanatabe | KEK | Development of the HOM coupler and the rf feedthrough for cERL injector at KEK
Ali Nassiri | ANL | Status of SiC-Based High-Power Waveguide Dampers R&D for the Short –Pulse X-Ray Project at the Advanced Photon Source
Philippe Kolb | Triumf | HOM considerations for the TRIUMF eLINAC
Lee Hammons | BNL | Development of SRF gun and HOM consideration at BNL
Nicoleta Baboi | DESY | HOM Damping Requirements at the European XFEL
Matthias Liepe | Cornell | HOM damping in the Cornell ERL SRF injector module: HOM measurements and high current beam operation
Rob Ainsworth | RHUL | HOM damping requirements and accelerating structure design for ESS
Working group A: 8 presentations.

## Slide 9: Introduction: TESLA and 3rd Harmonic Cavities
Common features
  9 cells/cavity
  8 cavities / module
  2 HOM couplers in adjacent pipes
TESLA cavities
  1.3 GHz
3rd harmonic cavity
  3.9 GHz
  Purpose: flatten RF field
  Scaled down from 1.3 GHz cavity, but pipes larger for better damping
  Built at Fermilab
  Nicoleta Baboi, DESY

## Slide 10: HOM Damping in 1.3 GHz Cavities
trapped &
quasi trapped modes:
~ resonant effects
f /GHz
100
101
102
103
f0
propagating modes
~ single bunch effects
HOM couplers
HOM absorbers
J. Sekutowicz
    J. Sekutowicz’s talk
    J. Sekutowicz et al., IPAC10, Kyoto, p. 4092
    N. Mildner et al., SRF 2005, Cornell, p. 593

## Slide 11: HOM Damping in 1.3 GHz Cavities: Multi-bunch Beam Dynamics (w/o 3.9 GHz Cavities)
Beam
  Frequency: 5 MHz
  Train length: 800 ms
  Charge: 1 nC / bunch
  Energy: 20 GeV
  (not latest nominal parameters)
Cavities
  Considered dipole modes in bands 1, 2, strongest in 3rd band
    worse Qs than measured in TTF cavities (typically 105)
  Misalignment: 0.5 mm rms
  Detuning: 0.1 % rms
  Inject beam on-axis
  100 linacs were simulated
(average over 100 linacs)
    N. Baboi, LINAC 2004, Lübeck, p. 357
st. dev.
ave.

## Slide 12: HOM Damping in 1.3 GHz Cavities: HOM Damping Requirements in the 1.3 GHz Cavities
    From HOM Workshop, Cornell, 2010 (J. Sekutowicz)
Average HOM Power / Cavity:
  0.5 W
Worst case HOM peak power per cavity in case of resonant mode excitation:
  2 kW
90% of HOM power:
  < 100 GHz
Required HOM damping for strongest modes
  Monopole modes: Q < 105
  Dipole modes: Q < 105

## Slide 13: Summary
Modes in the 1.3 GHz cavities
  High R/Q modes are damped to Q ≈ 105 or better
  Beam dynamics (w/o 3.9 GHz cavities) show small multi-bunch emittance growth
HOMs in 3.9 GHz cavities
  Even better damped than in 1.3 GHz cavities
  No multi-bunch problems observed (yet) at FLASH
  Every second cavity is rotated → compensate coupler kicks

## Slide 14
Same order Modes and Higher order modes for ESS linac – Rob Ainsworth

## Slide 17
WGs B&E

## Slide 18
WG D: HOM Couplers and Loads
Taro Konomi (KEK)
M. Liepe, N. Valles, Cornell

## Slide 20
  The 27000 high quality bunches/s will generate high average brilliance photon beam at
  very short wavelength:
  1.6·1025 photons/0.1%bw/s/mm2/mrad2 @ 1 Å.
Two addition features could make the XFEL photon beam even more attractive.
  The first is an increased, to several µ-seconds, intra pulse distance between bunches,
  which will allow for less technically demanding detectors.
  The second is a few kHz photon burst repetition rate, which will allow to use less expensive optical lasers (few kHz rep.-rate) for pump-and-probe experiments.
With the present nominal beam these features will lead to substantially reduced number of bunches/s and significantly lower average brilliance.
  Introduction and Motivation: b. European XFEL

## Slide 21
HOMSC-2013 at Fermilab!