## Slide 1: LAr TPC R&D in the U.S.
Bruce Baller - Fermilab
October 6, 2012
NNN12

## Slide 2: Outline
R&D approach
Materials testing
Computational Fluid Dynamics modeling
Electronics test stand – cryogenic electronics
ArgoNeuT
Light collection
Liquid Argon Purity Demonstrator (LAPD)
LAr Time Projection Chamber (TPC) in a test beam
LAr R&D Coalition
Summary
Slide “contributions” from many people
S. Mufson, S. Pordes, B. Rebel, E. Voirin

## Slide 3: R&D Approach
Learn as much from previous work
  Single phase TPC based on pioneering work on ICARUS
Develop U.S. experience and facilities
  Cryostats design, filters, HV feedthroughs, cryogenic electronics
Explore technical areas in detail
  Materials testing, CFD simulations, light detection
Develop operational detector experience
  ArgoNeuT, MicroBooNE
Demonstrate good LAr purity in a non-evacuated commercial cryostat
  Liquid Argon Purity Demonstrator (LAPD), LBNE 35 ton membrane cryostat
Understand the response of particles in a test beam
  Liquid Argon in A Test beam (LArIAT)
Develop simulation and reconstruction tools
  LArSoft
LAr Roadmap

## Slide 4: LAr Test Systems at Fermilab
Argon Source
Materials Test System
Electronics Test System

## Slide 5: Material Test System Results
Sample data on different materials (bad, good,OK in liquid)
`A system to test the effects of materials on the electron drift lifetime in liquid argon and observations on the effect of water’ R. Andrews et al., Nucl.Instrum.Meth.A608:251-258,2009.
Main Findings
All tested materials have good lifetime (~6 ms) when in the liquid argon
Primary contaminant is water vapor outgassing from “warm” components
Teflon is preferred over polyolefin in “warm” areas of the cryostat (ullage)
Application to LArTPCs
Reduce/eliminate the cable plant in the ullage  in-liquid electronics + MUX

## Slide 6: Argon Liquid Flow Modeling
Erik Voirin (FNAL)
0.03K DT
10 min real time movie MicroBooNE detector
Time evolution of impurities and positive ions
Anode plane
Cathode plane
Field cage
Field cage

## Slide 7: Argon Gas Flow Modeling
Warm cables in chimneys are main source of impurities by 3 – 5 orders of magnitude
Buoyancy driven fluid motion and turbulent mixing makes gas purging ineffective
Several solutions…
Gas purge
Erik Voirin (FNAL)
Insulation
Ullage
Chimney
Cables

## Slide 8: Electronics Test System
FNAL
Argon,TPC
HV Feedthrough
Warm electronics readout (Michigan State University)
Cryogenic CMOS electronics (MSU)
Equivalent Noise Charge (electrons)
Temperature (K)
ENC drops by ~2X
CMOS Ideal for operation in LAr
Low power, low noise
Brookhaven National Lab

## Slide 9
Warm electronics S/N = 15
wire
wire
wire
Raw Data
Raw Data
Cryogenic electronics S/N > 30
Collection
Collection
Induction
Induction
Induction
Induction

## Slide 10: BNL CMOS ASIC Development
Front End Amplifier
ENC (electrons)
Channel
300K
77K
MicroBooNE 128 channel mother board
Clock-less Low Power Current Mode ADC
One ADC stage
Fabricated in ASIC for SNS, see De Geronimo, et al., IEEE Trans NSS, 54 (2007) 541.
Measured linearity
  DNL < 1.5 LSB for majority of codes
  INL ~1% of Range
Equivalent input noise measurement
  1.27 LSB
  Effective resolution: 11.6 bits
The ADC has been tested with an FPGA, both immersed in LN2

## Slide 11: ArgoNeuT
Bern (CH), FNAL, INFN/Gran Sasso, L’Aquila, KSU, MSU, Syracuse, Texas, Yale
1m x 50 cm x 50 cm;
2 views +/- 300 to vertical;
480 channels total;
External (warm) electronics
Ran in NuMI beam
neutrino (1 month)
anti-neutrino (4 months) in 2009
C. Anderson et al., The ArgoNeuT detector in the NuMI low-energy beam line at Fermilab, [arXiv:1205.6747]  JINST

## Slide 12: ArgoNeuT Data in NuMI Beam
400
360
320
280
240
200
160
120
80
40
400
360
320
280
240
200
160
120
80
40
time (ms)
time (ms)
65 cm
65 cm
100 cm
1
1
2
3
4
2
3
4
Channel No.
Collection Plane
Induction Plane
~10,000 n interactions
Event with 4 photon conversions (2 p0)

## Slide 13: ArgoNeut Physics
C. Anderson et al., Analysis of a Large Sample of Neutrino-Induced Muons with the ArgoNeuT Detector, [arXiv:1205.6702], accepted by JINST
C. Anderson et al., “First Measurements of Inclusive Muon Neutrino Charged Current Differential Cross Sections on Argon”, Phys.Rev.Lett. 108 (2012) 161802, [arXiv:1111.0103]
Anti nm CC-inclusive differential cross-sections: in progress
nm CC-QE total and differential cross-sections: in progress
Final State Interactions in nm and anti- nm CC-QE events: in progress
Neutral strange particle production: in progress

## Slide 14: Light Collection
Provides sub-mm position accuracy in drift direction
Cosmic ray rejection for a surface detector
Supernova and proton decay trigger for underground detector
Reject cosmic ray spallation background
Neutrino time-of-flight
SiPM
128 nm g
425 nm g
TPB/Bis-MSB doped coating
Acrylic light guide
wire planes
wire planes
Energy deposition in LAr
LBNE system based on concept developed at MIT
Bugel et al. Nucl.Inst.Meth. A 640, 69 (2011)

## Slide 15
IU
MIT
1/4 of light t = 6 ns
3/4 of light t = 1.6 ms
15
Light guide spray booth and LAr testing at Indiana
R&D areas
Improve light yield
Attenuation length
Wavelength shifters
Large SiPMs
Production scale

## Slide 16: Liquid Argon Purity Demonstrator (LAPD)
Demonstrate that required drift electron lifetime can be achieved in a commercial vessel without evacuation – 1) gas purge, 2) gas recirculation + filtration, 3) liquid recirculation + filter

## Slide 17: LAPD Results
Concentrations of O2, N2 & H20 during
purge,
gas recirculation through filters, and
liquid recirculation.
Note: constant level of H20 (in vapor)* and the removal of N2 (which affects light production at 1 ppm level)
*H20 in liquid below measurable levels
c)
Tank 1/3 full

## Slide 18: LAPD Phase 2 - Long Drift TPC
Cylindrical TPC with 2m drift
Cold CMOS electronics
Challenge purification with a TPC in the volume – 2 m drift, 100 kV
Fully characterize filter sizing and material performance
Study the effect of varying the recirculation rate on the drift lifetime
Perform studies of how quickly lifetimes can be recovered from (intentional) poisoning of the Argon

## Slide 19: LBNE 35 Ton Membrane Cryostat Prototype
Demonstrate that required drift electron lifetime can be achieved in a commercial membrane cryostat using techniques developed in LAPD
Primary SS membrane installation in September
Concrete structure complete in May

## Slide 20: LArIAT
LArIAT  LAr in a Test Beam (MCenter at Fermilab)
Phase 1: Modified ArgoNeuT detector
  Study charge response from single particles dE/dx  dQ/dx
  Study low energy EM showers, e to po/g separation
Phase 2: a mid-scale TPC (~2m x ~2m x ~5m)
  Study EM/hadronic shower containment
  Medium scale test bed for LAr TPC development, e.g. light collection, detector design, electronics testing

## Slide 21: LAr R&D Coalition – “An alliance for combined action”
MTS
LBNE
LAPD
Micro
BooNE
Argo
NeuT
ETS
TPC Read-
out
Dark
Side
Distill-
ation
Column
Purity and Detector Materials, Filters, Controls
Physics Capability
Purity and Detector Materials, Non-evacuable Cryostat, Insulation, Filters
Front-end Electronics
Low Radioactivity Argon
Cold
Elec.
SCENE
Light
Detection
Light Detection
LArTPC in Test Beam
R&D
Projects
Dark Matter R&D

## Slide 22: Summary
Liquid argon is ideal for low rate TPCs
  mm-scale resolution in large volumes in a benign environment – hermetic cryostat, uniform low temperature  chemical reactions, mechanical creep  long term operation
Results from materials testing, LAPD and CFD modeling point the way to achieving excellent liquid argon purity  long drift TPC’s
  These ideas will be tested in the next 1 – 2 years in LAPD Phase 2, LBNE 35 ton prototype and MicroBooNE
CMOS is a natural solution for in-liquid electronics
  Low power, minimum noise, in-vessel zero suppression & multiplexing
Low-profile light collection conceptual design exists for LBNE
  R&D focused on improving light yield  lower cost
Fermilab is launching a new LAr test beam initiative
  Characterize response of various particles in argon
  Test bed for evaluating new detector concepts