## Slide 1: ILC as a Higgs Factory
Nick Walker (DESY)
for the Global Design Effort
Accelerators for a Higgs Factory: Linear vs. Circular (HF2012)
Fermilab, 14.11.12
Higgs & Co
Powered by
250 GeV
…you gotta have Mass!

## Slide 2: Known () Physics
~125 GeV ‘that new boson’
  125+91=216 GeV cm  250 GeV
173 GeV Top quark
  2x173=346 GeV cm  350-400 GeV
Higgs self coupling (t-coupling) ???
  ≥ 500 CM (up to 650 ??)
TeV and beyond….?
Staging / Upgrading

## Slide 3: ILC in a Nutshell
Damping Rings
Polarised electron source
Polarised positron source
Ring to Main Linac (RTML)
(inc. bunch compressors)
e- Main Linac
Beam Delivery System (BDS) & physics detectors
e+ Main Linac
Beam dump
not too scale

## Slide 4: The ILC
200-500 GeV Ecm e+e- collider L ~2×1034 cm-2s-1
  upgrade: ~1 TeV
SCRF Technology
  1.3GHz SCRF with 31.5 MV/m
  17,000 cavities
  1,700 cryomodules
  2×11 km linacs
Developed as a truly global collaboration
  Global Design Effort – GDE
  ~130 institutes
  http://www.linearcollider.org

## Slide 5: SCRF Linac Technology
1.3 GHz Nb 9-cellCavities | 16,024
Cryomodules | 1,855
SC quadrupole pkg | 673
10 MW MB Klystrons & modulators | 436 / 471 *
Approximately 20 years of R&D worldwide
 Mature technology, overall design and cost
* site dependent

## Slide 6: Global SCRF Technology
KEK, Japan
SLAC
JLAB
Cornell
DESY
LAL
Saclay
INFN Milan
IHEP, China
◉
TRIUMF, Canada
FNAL, ANL
GDE
STFC
BARC, RRCAT India
◉
◉
◉
◉
◉
◉
◉
◉
◉
◉
◉

## Slide 7: Luminosity Scaling Law
RF→beam power efficiency
Beamstrahlung (physics)
Vertical emittance

## Slide 8: The Luminosity Issue
High Beam Power
Small IP vertical beam size
High current (nb N)
High efficiency (PRF Pbeam)
Small emittance ey
strong focusing (small b*y , s*y ~ nm)

## Slide 9: ILC Published Parameters
Collision rate | Hz | 5 | 
Number of bunches |  | 1312 | 2625
Bunch population | ×1010 | 2 | 
Bunch separation | ns | 554 | 366
Pulse current | mA | 5.8 | 8.8
Beam pulse length | ms | 730 | 960
RMS bunch length | mm | 0.3 | 
Horizontal emittance | mm | 10 | 
Vertical emittance | nm | 35 | 
Electron polarisation | % | 80 | 
Positron polarisation | % | 30 | 
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/item.jsp?edmsid=D00000000925325
Centre-of-mass independent:
Luminosity Upgrade

## Slide 10: ILC Published Parameters
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/item.jsp?edmsid=D00000000925325
Centre-of-mass dependent:
Centre-of-mass energy | GeV | 200 | 230 | 250 | 350 | 500
Electron RMS energy spread | % | 0.21 | 0.19 | 0.19 | 0.16 | 0.12
Positron RMS energy spread | % | 0.19 | 0.16 | 0.15 | 0.10 | 0.07
IP horizontal beta function | mm | 16 | 16 | 12 | 15 | 11
IP vertical beta function | mm | 0.48 | 0.48 | 0.48 | 0.48 | 0.48
IP RMS horizontal beam size | nm | 904 | 843 | 700 | 662 | 474
IP RMS veritcal beam size | nm | 9.3 | 8.6 | 8.3 | 7.0 | 5.9
Vertical disruption parameter |  | 20.4 | 20.4 | 23.5 | 21.1 | 24.6
Enhancement factor |  | 1.83 | 1.83 | 1.91 | 1.84 | 1.95
Geometric luminosity | ×1034 cm-2s-1 | 0.25 | 0.29 | 0.36 | 0.45 | 0.75
Luminosity | ×1034 cm-2s-1 | 0.50 | 0.59 | 0.75 | 0.93 | 1.8
% luminosity in top 1% DE/E |  | 92% | 90% | 84% | 79% | 63%
Average energy loss |  | 1% | 1% | 1% | 2% | 4%
Pairs / BX | ×103 | 41 | 50 | 70 | 89 | 139
Total pair energy / BX | TeV | 24 | 34 | 51 | 108 | 344
Notes: General observations:
Factor of 2 in L from enhancement – relatively large disruption parameter -> tight tolerances on collisions to IP (feedback)

## Slide 11: ILC Published Parameters
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/item.jsp?edmsid=D00000000925325
Centre-of-mass dependent:
Centre-of-mass energy | GeV | 200 | 230 | 250 | 350 | 500
Electron RMS energy spread | % | 0.21 | 0.19 | 0.19 | 0.16 | 0.12
Positron RMS energy spread | % | 0.19 | 0.16 | 0.15 | 0.10 | 0.07
IP horizontal beta function | mm | 16 | 16 | 12 | 15 | 11
IP vertical beta function | mm | 0.48 | 0.48 | 0.48 | 0.48 | 0.48
IP RMS horizontal beam size | nm | 904 | 843 | 700 | 662 | 474
IP RMS veritcal beam size | nm | 9.3 | 8.6 | 8.3 | 7.0 | 5.9
Vertical disruption parameter |  | 20.4 | 20.4 | 23.5 | 21.1 | 24.6
Enhancement factor |  | 1.83 | 1.83 | 1.91 | 1.84 | 1.95
Geometric luminosity | ×1034 cm-2s-1 | 0.25 | 0.29 | 0.36 | 0.45 | 0.75
Luminosity Upgrade | ×1034 cm-2s-1 | 1.00 | 1.18 | 1.50 | 1.86 | 3.6
% luminosity in top 1% DE/E |  | 92% | 90% | 84% | 79% | 63%
Average energy loss |  | 1% | 1% | 1% | 2% | 4%
Pairs / BX | ×103 | 41 | 50 | 70 | 89 | 139
Total pair energy / BX | TeV | 24 | 34 | 51 | 108 | 344

## Slide 12: ILC Published Parameters
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/item.jsp?edmsid=D00000000925325
Centre-of-mass dependent:
Centre-of-mass energy | GeV | 200 | 230 | 250 | 350 | 500
Electron RMS energy spread | % | 0.21 | 0.19 | 0.19 | 0.16 | 0.12
Positron RMS energy spread | % | 0.19 | 0.16 | 0.15 | 0.10 | 0.07
IP horizontal beta function | mm | 16 | 16 | 12 | 15 | 11
IP vertical beta function | mm | 0.48 | 0.48 | 0.48 | 0.48 | 0.48
IP RMS horizontal beam size | nm | 904 | 843 | 700 | 662 | 474
IP RMS veritcal beam size | nm | 9.3 | 8.6 | 8.3 | 7.0 | 5.9
Vertical disruption parameter |  | 20.4 | 20.4 | 23.5 | 21.1 | 24.6
Enhancement factor |  | 1.83 | 1.83 | 1.91 | 1.84 | 1.95
Geometric luminosity | ×1034 cm-2s-1 | 0.25 | 0.29 | 0.36 | 0.45 | 0.75
Luminosity | ×1034 cm-2s-1 | 0.50 | 0.59 | 0.75 | 0.93 | 1.8
% luminosity in top 1% DE/E |  | 92% | 90% | 84% | 79% | 63%
Average energy loss |  | 1% | 1% | 1% | 2% | 4%
Pairs / BX | ×103 | 41 | 50 | 70 | 89 | 139
Total pair energy / BX | TeV | 24 | 34 | 51 | 108 | 344

## Slide 13: Higgs Factory
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/item.jsp?edmsid=D00000000925325
Centre-of-mass dependent:
Centre-of-mass energy | GeV | 200 | 230 | 250 | 350 | 500
Electron RMS energy spread | % | 0.21 | 0.19 | 0.19 | 0.16 | 0.12
Positron RMS energy spread | % | 0.19 | 0.16 | 0.15 | 0.10 | 0.07
IP horizontal beta function | mm | 16 | 16 | 12 | 15 | 11
IP vertical beta function | mm | 0.48 | 0.48 | 0.48 | 0.48 | 0.48
IP RMS horizontal beam size | nm | 904 | 843 | 700 | 662 | 474
IP RMS veritcal beam size | nm | 9.3 | 8.6 | 8.3 | 7.0 | 5.9
Vertical disruption parameter |  | 20.4 | 20.4 | 23.5 | 21.1 | 24.6
Enhancement factor |  | 1.83 | 1.83 | 1.91 | 1.84 | 1.95
Geometric luminosity | ×1034 cm-2s-1 | 0.25 | 0.29 | 0.36 | 0.45 | 0.75
Luminosity | ×1034 cm-2s-1 | 0.50 | 0.59 | 0.75 | 0.93 | 1.8
% luminosity in top 1% DE/E |  | 92% | 90% | 84% | 79% | 63%
Average energy loss |  | 1% | 1% | 1% | 2% | 4%
Pairs / BX | ×103 | 41 | 50 | 70 | 89 | 139
Total pair energy / BX | TeV | 24 | 34 | 51 | 108 | 344

## Slide 14: Positron Production
Polarised positron source
e- Main Linac
not too scale

## Slide 15: ILC Polarised-Positron Production
e- linac
Uses primary electron beam to generate ~30 MeV photons in a SC helical undulator
Photons converted into e+e- pairs in “thin” titanium target
Positron production yield dependent on e- beam energy (and therefore Ecm)
e- to IP

## Slide 16: Beam Delivery System
e- BDS
e+ source
electron Beam Delivery System

## Slide 17: Positron Yield
yield margin
Ebeam = 125 GeV
147m helical undulator (TDR baseline)
design point
Wei Gai (ANL) et al

## Slide 18: Positron Yield for a LHF
yield margin
Ebeam = 125 GeV
Recover yield by going to
~250 m of undulator
Wei Gai (ANL) et al
Notes: Power density on target (WG says OK but should check).

## Slide 19: 10-Hz Mode
For TDR, we are required to have solutions down to Z-pole (~45 GeV beam)
ILC TDR assumes 10-Hz mode where
  e- linac is pulsed at 10 Hz
  first pulse @ 150 GeV to make positrons
  second pulse @ Ecm/2 to make luminosity
Issues
  DR damping time halved (extra cost and MW)
  Beam dynamics in Main Linac (looks OK)
  Additional beam lines and pulsed magnet systems
  Additional AC power for elec linac 10-Hz mode
    But for 500 GeV design, additional power already available
    Not insignificant cost increase for a dedicated LHF

## Slide 20: Conventional Source
T. Omori et al, Nucl. Instrum. Meth. A 672 (2012) 52-56

## Slide 21
Higgs & Co
Powered by
250 GeV
…you gotta have Mass!

## Slide 22: TDR 500 GeV Baseline
2.2 km
1.3 km
10.8 km
1.1 km
BDS
Main Linac
e+ src
bunch comp.
15.4 km
(site length ~31 km)
IP
central region
Main Linac
<Gcavity> = 31.5 MV/m
Geff ≈ 22.7 MV/m
(fill fact. = 0.72)
Cost: 100%
PAC: 161 MW

## Slide 23: 250 GeV Only
1.1 km
1.3 km
5.1 km
1.1 km
BDS
Main Linac
e+ src
bunch comp.
8.6 km
(site length ~16 km)
IP
central region
Half the linac
Shorter BDS ½
RTML LRL ½
10Hz mode e- linac

## Slide 24: 250 GeV staged (scenario 1)
5.1 km
1.1 km
Main Linac
bunch comp.
Half the linac
Full-length BDS tunnel & vacuum (TeV)
½ BDS magnets (instrumentation, CF etc)
½ RTML LTL
Extended tunnel/CFS already 500 GeV stage
10Hz mode e- linac
2.2 km
1.3 km
BDS
e+ src
IP
central region
15.4 km

## Slide 25: 250 GeV staged (scenario 2)
5.1 km
1.1 km
Main Linac
bunch comp.
2.2 km
1.3 km
BDS
e+ src
IP
central region
15.4 km
125 GeV transport
Half the linac
Full-length BDS tunnel & vacuum (TeV)
½ BDS magnets (instrumentation, CF etc)
1 RTML LTL
5km 125 GeV transport line
Extended tunnel/CFS already 500 GeV stage
10Hz mode e- linac
quasi-adiabatic energy upgrade?

## Slide 26: 250 GeV CM (as first stage)
Half linacs solution
G = 31.5 MV/m
Relative to TDR 500 GeV baseline (1312 bunches)
Two stage compressor (5-15 GeV)

## Slide 27: 250 GeV CM (as first stage)
Half linacs solution
G = 31.5 MV/m
Relative to TDR 500 GeV baseline (1312 bunches)
Two stage compressor (5-15 GeV)
POSITRON linac straightforward
~50% ML linac cost (cryomodules, klystrons, cryo etc.)
~50% ML AC power

## Slide 28: 250 GeV CM (as first stage)
Half linacs solution
G = 31.5 MV/m
Relative to TDR 500 GeV baseline (1312 bunches)
Two stage compressor (5-15 GeV)
POSITRON linac straightforward
~50% ML linac cost (cryomodules, klystrons, cryo etc.)
~50% ML AC power
ELECTRON linac needs 10Hz mode for e+ production
DE = 135 GeV instead of 110 GeV (+25 GeV)
~57% ML linac cost (cryomodules, klystrons etc)
10Hz needs (1/2 linac × 10Hz/5Hz):
100% ML AC power (1/2 linac × 10Hz/5Hz)
80% cryo cost (50% static + 100% dynamic)

## Slide 29: 250 GeV CM (as first stage)
Half linacs solution
G = 31.5 MV/m
Relative to TDR 500 GeV baseline (1312 bunches)
Two stage compressor (5-15 GeV)
POSITRON linac straightforward
~50% ML linac cost (cryomodules, klystrons, cryo etc.)
~50% ML AC power
ELECTRON linac needs 10Hz mode for e+ production
DE = 135 GeV instead of 110 GeV (+25 GeV)
~57% ML linac cost (cryomodules, klystrons etc)
10Hz needs (1/2 linac × 10Hz/5Hz):
100% ML AC power (1/2 linac × 10Hz/5Hz)
80% cryo cost (50% static + 100% dynamic)
Total Main Linac infrastructure
Linac components: 50%
Cryogenics: 65%
RF AC power 75%

## Slide 30: Summary
Warning!
Approximate Scaling Only!
Highly likely to change

## Slide 31: Schedule for 500 GeV Machine

## Slide 32: MDI (Detector Hall)
2 Detectors in push-pull configuration
Detector construction:
9 years (can be shorter?)
Notes: Should add mountain 3D graphic

## Slide 33: Central Region
e- BDS
e- BDS muon shield
e+ main beam dump
detector
RTML return line
e+ source
Damping Rings
Central region, detector hall (and detector) are
schedule drivers
Possible reduction for 250 GeV machine is 12-18 months (out of 10 years)

## Slide 34: Summary
ILC (500 GeV) machine already “contains” a light Higgs factory
  Luminosity: 7.5×1033 cm-2 s-1
  (Possible to upgrade by factor 2)
Standalone machine for LHF
  reduced cost to ~65% of 500 GeV machine
    PAC ~ 100 MW
  reduces schedule by 12-18 months (perhaps a little more)
Only really makes sense as part of a first-stage machine
  scope of complete project still ~500 GeV
  TeV upgrade remains optional