## Slide 1
FD2 BDE Cabling and Penetrations

## Slide 2
CRP cable routing
Four patch panels on each full CRP with two on each half CRP.
Patch panels are located toward the TCO.
Each patch panel connects to 6 CE boxes.
2.5m short cables routed from the CE boxes to the patch panels.
Cables are secured on the CRP composite frame with cable ties.
25m long cables will connect the patch panels to the penetration on the cryostat roof.

## Slide 3
25m long cable bundles are installed before CRP installation.
Long cable bundles are supported in ladder cable trays and positioned along the cryostat walls.
Cable routing from patch panels to penetration

## Slide 4
Offsets between cable trays, penetrations and patch panels
Penetrations
Cable trays
Bottom CRPs

## Slide 5
Row #10
Row #9
Row #8
Row #7
Row #6
Row #5
Row #4
Row #3
Row #2
Row #1
Modeling of cable bundles from penetrations to patch panels on the central north CRPs

## Slide 6
TCO
Row #20
Row #19
Row #18
Row #17
Row #16
Row #15
Row #14
Row #13
Row #12
Row #11
Modeling of cable bundles from penetrations to patch panels on the central north CRPs

## Slide 7
Row #7
Row #6
Row #5
24.5m
24.4m
24.3m
P1
P2
P3
P4
Chart: Minimum Required Cable Length from Penetrations to Central Bottom CRPs
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Length to Patch Panel 1 | 23241 | 23364 | 23381 | 23279 | 23729 | 23609 | 23499 | 23282 | 23261 | 23283 | 23470 | 23370 | 23499 | 23487 | 23544 | 23767 | 23663 | 23575 | 23505 | 23826
Length to Patch Panel 2 | 23741 | 23883 | 23887 | 23797 | 24276 | 24153 | 24040 | 23806 | 23775 | 23783 | 23990 | 23899 | 24013 | 23989 | 24035 | 24312 | 24206 | 24113 | 24035 | 24367
Length to Patch Panel 3 | 23440 | 23290 | 23233 | 23374 | 23956 | 23863 | 23735 | 23472 | 23384 | 23329 | 23239 | 23375 | 23694 | 23653 | 23694 | 23609 | 23491 | 23387 | 23273 | 23617
Length to Patch Panel 4 | 23949 | 23816 | 23747 | 23898 | 24484 | 24380 | 24250 | 24004 | 23904 | 23838 | 23765 | 23907 | 24230 | 24174 | 24239 | 24155 | 24034 | 23926 | 23813 | 24165
Modeling of cable bundles from penetrations to patch panels on the central north CRPs
The longest minimum required cable length is 24.5m at Row #5.

## Slide 8
Support plate
Support rods
Cable clamp/lock plates
BDE/PDS penetrations
Each penetration provides two side flanges for BDE and top flange for PDS.
BDE/PDS cables are strain relieved at the cable clamp/lock plates at the bottom of the penetration.
CSSP
Cryostat crossing tube

## Slide 9
BDE/PDS penetrations – Alternative design
Another design idea is to mount the cable clamp/lock plates to the bottom of the cryostat crossing tube. Therefore, the strain relief design can be simplified with the support plate and rods eliminated.
A proposal of directly welding the CSSP to the cryostat crossing tube is being discussed. No flange on the cryostat crossing tube will be available for the support plate to mounted.

## Slide 10
Backup slides

## Slide 13
Gap between floor and low ridge of membrane is 64mm
F40
Gap between floor and high ridge of membrane is 42 mm.
42.4mm
Wood floor
Bottom CRP
Membrane

## Slide 14
Cable bundles pre-routed underneath the floor.

## Slide 15
CRP composite frame
CRP patch panel
87mm gap between CRP and membrane

## Slide 16
Cable length from cable tray to penetration = 1.2m
Cable length inside penetration = 3m

## Slide 17
CSSP
Cryostat crossing tube
Support plate
Support rods
Cable clamp/lock plates
VD Chimney Cable Strain Relief

## Slide 18
Row #7
Row #6
Row #5
21.6m
21.5m