## Slide 1: ICARUS Commissioning and Operations
C. Montanari
FNAL – INFN Pavia
SBN Oversight Board Meeting – March 10, 2023

## Slide 2: Detector status
  The ICARUS detector is running in excellent and stable conditions since the end of last year.
  The free electrons lifetime has stabilized to about 8 ms in the WEST module (liquid filters regenerated) and about 4 ms in the EAST module.
  Neutrino data are being collected with high efficiency.
  Some activities have been completed before Christmas:
    PMTs gain calibration;
    Replacement of some readout boards for horizontal wires with modified boards with an additional filter for coherent noise mitigation;
    Recovery of part of the bottom CRT (DAQ integration is still in progress).
  Other calibration activities take place routinely during beam off periods.
  A power glitch occurred on March 8, around midnight, causing the stop of DAQ servers, of some electronics (PMTs) and of the LAr pumps: the standard run conditions were recovered in the afternoon of March 9.

## Slide 3: Free electrons lifetime trend in the WEST module
Chart: 
  The free electron lifetime in the WEST module has reached a value of about 8 ms and remains stable since the beginning of 2023.
  Periodic venting is still required though the venting rate has been halved wrt the first months of purity recovery.
  A simple recirculation model, based on the measured values of recirculation speed and impurities input (with venting) correctly interprets the data.
Free Electrons Lifetime (ms)
Elapsed time (hours)
Nov 6, 2022
Mar 12, 2023
● - Data
● - Calculated from simple recirculation model
Jan 1, 2023
No venting

## Slide 4: Free electrons lifetime trend in the EAST module
Free Electrons Lifetime (ms)
Elapsed time (hours)
Nov 6, 2022
Mar 12, 2023
Chart: 
  The free electron lifetime in the EAST module has flattened at a value slightly above 4 ms and remains stable since the beginning of 2023.
  Periodic venting is still required though the venting rate has been halved wrt the first months of purity recovery.
  A simple recirculation model, in order to approximate the data, very low recirculation speed and low impurities input  filters require regeneration.
Jan 1, 2023
No venting
● - Data
● - Calculated from simple recirculation model

## Slide 5: Run2 accumulated statistics
Jan 1, 2023
Mar 1, 2023
Feb 1, 2023
Data Collection Efficiency:
BNB: e = 0.96
NuMI: e = 0.98

## Slide 6: PMT Gain Calibration
A new PMT calibration campaign was carried in view of the start of RUN2 (fall 2022) data taking.
The PMT gain was set to an average value of G=4.5x106 with an equalization of 1.8%. This gain value allowed a minimal intervention of the PMT voltages (within ±25V).
The gain measurement/equalization was based on a semi-automatic procedure using single photoelectrons signals from background. For few PMTs a manual adjustment was required.
PMTs requiring a manual adjustment

## Slide 7: PMTs Timing Calibration
A PMT time resolution of ~1 ns is crucial to exploit particle TOF and the bunched structure of BNB spill.
The transit time of each PMT is obtained by flashing it with a laser and measuring the delay w.r.t. the reference laser start time.
This time reconstruction is checked with ~vertical cosmic muons, by performing a linear fit of time vs. y (drift) coordinate. The residual of each PMT w.r.t. the fit is then computed.
early
early
late
late
Up
Up
Down
Down
East
West
Z coord. (cm)
Base m sample:
<>=0.13 ns
s=0.9 ns
Average residuals from m procedure (ns):
Validation
sample:
<>=0.07 ns
s=0.37 ns
# of PMTs/0.1 ns
These residuals are then used for a finer correction (s ≈ 1ns) of each PMT’s transit time
Iterating the procedure on another independent cosmic muon sample, the resolution improves to ~0.4 ns

## Slide 8: Further reducing the TPC wire noise
After the successful campaign performed in 2020-21 to reduce the anomalous electronic noise in the TPC, a further study was done to mitigate the coherent noise in the A2795 TPC readout boards.
Coherent noise
Intrinsic noise
Total noise- 9 boards -576 chs
Without/
With filter
50 % of Induction-1 boards affected by larger noise due to 9 m wire length, were equipped:
~ 0.9 ADC # coherent noise reduction, leaving virtually unaffected the intrinsic one
A 5th order Chebyshev low-pass filter was designed for +7 V frontend supply of the A2795 TPC readout boards to reduce the 32-channels coherent noise propagating into the boards through +7 V line.

## Slide 9: CRT Calibration and Timing
Gain fit from the quantized photoelectron peaks
CRT hit time relative to the neutrino gate start time
Photoelectron conversion
Progress in 2022 includes: accurate timing measurements, calibration and validation of CRT hit reconstruction with data.
Each CRT channel was calibrated in terms of corresponding gain and pedestal.
The CRT hit timing was measured relative to the neutrino beam spill start time.

## Slide 10: Conclusions
  The ICARUS detector is running in excellent and very stable conditions since the end of 2022.
  Data are being collected with high efficiency both of BNB and NuMI, the latter recently brought back into operation after the replacement of the horn.
  All residual calibration and optimization activities on the detector have been successfully completed before Christmas.
  No other activities that would interfere with neutrino data taking are planned before the end of the present neutrino run.