## Slide 1: MQXFA12 Bladder Failure - Missing Key NCR
G. Vallone, D. Cheng, P. Ferracin, L. Garcia Fajardo
January 19, 2023
Structure WG: MQFA12 Bladder Failure – Missing Key NCR

## Slide 2: Introduction
Bladder failed during MQXFA12 disassembly
    Right lower slot had no key in LE, and partially missing key in the RE (0.03” stack)
    We want to verify the impact of this configuration on the coil stresses
Q1
Q2

## Slide 3: Model Description
3D full ‘extruded’ model
Model is not full length – we simulate only the two shells across the central discontinuity
Simulation in 3 steps:
  Nominal loading condition (80 MPa on the pole)
  Before bladder operation/key removal
  Bladder operation at 28 MPa (right bladders)
  Stuck with fully missing key in the bottom right slot
    Conservative

## Slide 4: Interference Values
Key size variation as ‘offset’ in the FE solution
Initial offset is a function of the actual coil pack size (shimming, coil size, etc.), not considered in FE model
 | Inches | mm | mm FE
Nominal | 0.04 | 1.016 | 0.5
Top | 0.04 | 1.016 | 0.5
Left | 0.04 | 1.016 | 0.5
Bottom | 0.04 | 1.016 | 0.5
Right Top | 0.04 | 1.016 | 0.5
Right Bot | 0.04 | 1.016 | 0.5
PreFailure |  |  | 
 | Inches | mm | mm FE
Nominal | 0.04 | 1.016 | 0.5
Top | 0.03 | 0.762 | 0.246
Left | 0.035 | 0.889 | 0.373
Bottom | 0.03 | 0.762 | 0.246
Right Top | 0.03 | 0.762 | 0.246
Right Bot | 0.03 | 0.762 | 0.246
Failure |  |  | 
 | Inches | mm | mm FE
Nominal | 0.04 | 1.016 | 0.5
Top | 0.03 | 0.762 | 0.246
Left | 0.035 | 0.889 | 0.373
Bottom | 0.03 | 0.762 | 0.246
Right Top | 0.03 | 0.762 | 0.246
Right Bot Front | 0.03 | 0.762 | 0.246
Right Bot Back | 0 | 0 | 0

## Slide 5: Deformation History
Step 1 - Nominal

## Slide 6: Deformation History
Step 2 – Before bladder operation

## Slide 7: Deformation History
Step 3 – Bladder operation

## Slide 8: Deformation History
Step 4 – After bladder failure

## Slide 9: Pole and Shell Stresses
Virtual and real gauge locations
z-
Missing key
z+
Q1
Q2
FBG
L = 700 mm
Missing key region
L = 2741 mm
Strain Gauges
L = 3989 mm
LE
RE
FBG
L = 1900 mm
FBG
L = 3800 mm
Q4
Q3

## Slide 10: Shell Stresses
Small variations (<2 MPa)
Might be not visible in the strain gauge signals, even if it is a delta

## Slide 11: Pole Stresses
No effect on the pole stress for the Z+ side
Stress variation (Q1,2,3,4), between step 2 and 4:
  +21.2, 0.6, +7.3, -2.1 MPa
Q1 variation should be visible on the measurements
Q3 also could be visible
Stress increase (compression) negligible

## Slide 12: Pole Stresses - Measured
Strain measurements:
  Step 1: Nominal
  Step 2: Partially unloaded, before bladder failure
  Step 3: Bladder operation
  Step 4: Key, after bladder failure
  No large (20 MPa) effect visible

## Slide 13: Comparison
FBG on 700 mm and 1900 mm locations should see some effect due to the missing key
Some effect at FBG 700, but much smaller than the model
  Probably the model is very conservative
FBG
L = 700 mm
Missing key region
L = 2741 mm
Strain Gauges
L = 3989 mm
LE
RE
FBG
L = 1900 mm
FBG
L = 3800 mm
 | Delta Stress, MPa | 
 | Q1 | Q2
Model | 21.2 | 0.6
FBG 700 | 3.33 | -2.03
FBG 1900 | 1.18 | -5.46
FBG 3800 | 1.37 | -2.83

## Slide 14: Coil Azimuthal Stress
Increase in coil stress on Q4 coil
From 47 to 51 MPa
Significatively below the ‘nominal’ stress peak (72 MPa)

## Slide 15: Coil Longitudinal Strain
Long. strain is negligible in the two initial steps
  This is not a ‘true’ condition, as the ends are missing
Significant increase after key removal, up to 147 um/m in tension
  Far from ‘dangerous’ territory

## Slide 16: Conclusion
A FE model of the unloading operation with bladder failure was created
  Conservative assumptions were used in order to catch the ‘worst case’ coil stress
Measurements show significantly smaller effect on the coil stress
FE model does not show a dangerous stress/strain increase on the coils

## Slide 17: Back-up
FEA raw results

## Slide 18: Back-up
FEA results