## Slide 1: AIDA TASD and MIND Detectors
E. Noah - 21.09.2012
On behalf of AIDA WP8.5.2 co-workers

## Slide 2: Outline
The AIDA project
Planned neutrino facilities
AIDA TASD and MIND detectors
MIND Magnetisation
Plastic scintillators
SiPM characterisation
Electronics – EASIROC
UNIGE MICE EMR experience

## Slide 3: The AIDA project
Advanced European Infrastructures for Detectors at Accelerators:
  Part EU-funded 4-yr project under FP7 Research Infrastructures programme.
  Timeline: 02/2011 – 01/2015
Aim:
  Upgrade, improve and integrate key European research infrastructures.
  Develop advanced detector technologies for future particle accelerators.

## Slide 4: Accelerator-based neutrinos
Two recent proposals (in Europe):
  One short-baseline experiment at CERN-SPS (SPSC-P-347: 15th March 2012): neutrino beam to search for sterile neutrinos with the ICARUS T600 Lar TPC @ 1600m + T150 @ 300m from proton target.
  One long-baseline experiment at CERN-SPS (SPSC-EOI-007-LBNO: 28th June 2012): Investigate all flavour oscillations (nm to nm, nm to nt, nm to ne) with neutrinos and antineutrinos, explicitely testing the existence of CP-violation and conclusively determining mass hierarchy for any value of dCP.
Both instrumented with liquid argon detectors and magnetised iron detectors.

## Slide 5: CN2PY
Mine closure 2018

## Slide 6: LBNO Detectors
MIND detector =
Neutrino Factory baseline detector
as of the NF-IDR
(Interim Design Report)
100kton Magnetized Iron detector
(1.5 T toroidal field)
Scintillator read out with
Wave Length Shifting fibers and SiPMTs
20kton Glacier detector
Liquid Argon TPC
with 2-phase readout (LEM)

## Slide 7: LBNO Far Detectors: Top View
v
v
30m
10m
Liquid Argon Fiducial
40m
20m
neutrino beam

## Slide 8
1m
(SC) coil
Tracking volume:
10 bar Ar gas TPC
B
MIND
2m
4m
THE CN2PY NEAR DETECTOR SKETCH
TASD volume
MIND
MIND

## Slide 9: Excerpt from LBNO SPSC-EOI-007
Based on the expertise present at CERN and in European and in international research groups, and building upon the results of several years of EU-funded design studies, we are confident that the technology for the beam and detectors is sufficiently mature to allow for an early start to realizing the facility. We are calling on CERN to promptly support and engage in the prototyping of the near and far detector components, to investigate options for campaigns of detector performance characterization and calibration with test beams in the North Area, and engage in a collaborative effort with the LBNO Collaboration that should lead to a full engineering design of the CN2PY beam and to an LBNO Proposal by the end of 2014.

## Slide 10: AIDA TASD and MIND
Totally Active Scintillating Detector
  Stopping properties of pions and muons up to 200 MeV/c (MICE EMR)
  Electron and muon charge separation inside a magnetic field, in particular electron charge ID in electron neutrino interaction for the platinum channel at a NF: 0.5 – 5 GeV/c (AIDA – MORPURGO).
Magnetised Iron Neutrino Detector
  Muon charge identification, for wrong sign muon signature of a neutrino oscillation event: golden channel at a NF: requires correct sign background rejection of 1 in 104: test beam 0.8 to 5 GeV/c (AIDA – baby-MIND).
  Hadronic shower reconstruction for identification of charged current neutrino interactions and rejection of neutral current n.i.: test beam protons/pions 0.5 to 9 GeV/c (AIDA – baby-MIND).

## Slide 11: General layout: TASD
TASD
(1 module shown)
MORPURGO magnet

## Slide 12: TASD Parameters
Parameter | Symbol | Unit | Nominal Value | Range Min | Range Max
Detector global dimensions |  |  |  |  | 
Detector width | wdet | m | 1.0 | 0.9 | 1.1
Detector height | hdet | m | 1.0 | 0.9 | 1.1
Detector depth | ddet | m | 0.75 | - | -
Detector depth with gaps | dgap | m | 197.5 | - | -
Plastic scintillator |  |  |  |  | 
Number of planes per module (xy or uv) | - | - | 2 | 1 | 2
Number of modules | nmodule | - | 50 |  | 
Gap between planes within module |  | cm | 0 | 0 | 0.05
Module envelope thickness | tenv | cm | 0.05 | 0 | 0.05
Scintillator bar length | lsci | cm | 90.0 | 80.0 | 100.0
Scintillator bar width | wsci | cm | 1.0 | 1.0 | 3.0
Scintillator bar height | hsci | cm | 0.7 | 0.6 | 1.0
Bars per module | nbars_mod | - | 180 |  | 
Total number of bars | nbars_tot | - | 9000 |  | 

## Slide 13: Morpurgo magnet B-field
X-Y slice

## Slide 14: General Layout: Baby-MIND
MIND area 1
MIND area 2

## Slide 15: Baby-MIND Dimensions

## Slide 16: Baby-MIND Steel Selection
R. Bayes
3.0 cm steel
1.5 cm scintillator
3.0 cm steel
3.5 cm scintillator
2.0 cm steel
1.5 cm scintillator
2.0 cm steel
3.5 cm scintillator
Muon reconstruction efficiencies are good for all scenarios considered here, slightly better for 3.0 cm steel, 1.5 cm scintillator.
Charge I.D. efficiencies are identical for all scenarios.
Cost...
  ARMCO: 5.4 CHF/kg.
  AISI1010
  AISI1006 (MINOS)

## Slide 17: MIND Proto Simulations
MIND Prototype
1 m × 1 m × 2 m
3 cm Fe
2 cm scintillator
7 cm dia. copper STL (for scattering)
Toroidal B-field 100 kA
10 μ+ events :
Generated at random on X-Y plane at Z=L/2
1 million events per simulation
μ+
π+
μ+
π+
Particle | Detector - MIND | Reconstruction efficiency | Charge identification efficiency
μ+ | Prototype | 80% (1GeV) 75% (10GeV) | 99% (1GeV) 91% (10GeV)
μ+ | Far | 81% (Flat 1 to 25GeV) | 99.5% (1GeV) 98% (25GeV)
μ− | Prototype | 60% (1GeV) to 64% (10GeV) | 92% (1GeV) to 83% (10GeV)
π+ | Prototype | 13% (1GeV) to 45% (10GeV) | 80% (1GeV) to 60% (10GeV)
π− | Prototype | 11% (1GeV) to 42% (10GeV) | 75% (1GeV) to 55% (10GeV)
R. Bayes

## Slide 18: Baby-MIND Magnetisation
Magnetic field requirements:
  field nominal value: 1.5 T ± 20%.
  knowledge of field in volume of interest to precision of 1e-4.
  Bx component < 1% of By within steel, along projection of plas. sci.
  field uniformity within steel along projection of plastic scintillator vol.: 10%.
  field value outside MIND volume: maximum = 100 Gauss.
Power supply parameters:
  if possible should match existing power supplies at CERN that could be borrowed for this application,
  if above point not possible, then optimise for cost (purchase and operation).
Ongoing evaluation by CERN TE-MSC-MNC:
  Study A: First optimisation of basic parameters
  Study B: One coil vs. Two coils
  Study C: Normal conducting vs superconducting.

## Slide 19: One coil – no slots
¼ of detector
M. Dumas, J. Bauche

## Slide 20: Two coils - with slot
¼ of detector
Bx < 1% By But:
Double steel height: × 2 cost!
Not representative of big MIND
M. Dumas, J. Bauche

## Slide 21: Measuring B-field
Slit in steel, few mm...
fill with non-magnetic material (e.g. SS316L).
Insert probe to measure field at various points along slit.
Small distortion of field lines.
Use measurements to cross-check and validate simulated field across whole detector.
~23000 At with slot c.f. 4000 At without slot.
M. Dumas, J. Bauche

## Slide 22: Plastic scintillators
Prototyping at INR RAS:
Extruded scintillator slabs produced at Uniplast company, Vladimir, Russia
  polysterene based, 1.5% of paraterphenyl (PTP) and 0.01% of POPOP
Plastics initially used for T2K SMRD detector counters production
Counter surface is etched with a chemical agent (Uniplast) to create a 30-100 μm layer that works as diffusive reflector
Counters of three different sizes:
  895 × 7 × 10 mm3
  895 × 7 × 20 mm3
  895 × 7 × 30 mm3
2 mm deep grooves to embed fibers:
  three different types of fiber
  Fiber diameter: 1.0 mm, 1.2 mm, 1.5 mm
  Groove width: 1.1 mm, 1.3 mm, 1.7 mm
A. Izmaylov, A. Khotjantzev, Y. Kudenko, O. Mineev

## Slide 23: Cosmic telescope tests
Light collection:
Kuraray WLS fiber (200 ppm, S-type, 1.0 mm dia)
Toshiba TSF451-50M silicone grease used to embed fiber
Photosensors (two-sided readout): 667-pixel avalanche photo-diodes Hamamatsu MPPC (~55k MPPCs used in T2K ND)
HV from Hamamatsu, gain of 7.5 × 105 for 25°C
Note!: no correction for cross-talk + after-pulses (~15% in total)
Cosmic telescope:
  two trigger counters
  upper one: 7 × 7 cm2 (L.Y. checks) and 2 × 2 cm2 (timing)
  lower one: 10 x 24 cm2
  measurements at counter center: L.Y. per cosmic MIPs

## Slide 24: Light yield with no chemical reflector
Counter width | MPPC 1 L.Y. [pe] | MPPC 2 L.Y. [pe] | ΣL.Y. [pe]
No chemical reflector/ No Tyvek |  |  | 
10 mm | 15.7 | 15.8 | 31.5
20 mm | 15.5 | 13.6 | 29.1
30 mm | 12.8 | 11.5 | 24.3
No chemical reflector/ Tyvek reflector 100-120 mm |  |  | 
20 mm | 41.8 | 34.8 | 76.6
Light attenuation length in bars ~8 cm.
T2K SMRD experience: L.Y. > 12 p.e. (sum of both ends) allows to achieve 99% detection efficiency.
Highest L.Y. for smallest width.
Tyvek effect
× 2.5

## Slide 25: Light yield with chemical reflector
Counter width | MPPC 1 L.Y. [pe] | MPPC 2 L.Y. [pe] | ΣL.Y. [pe]
Chemical reflector/ Optical grease |  |  | 
10 mm | 46.0 | 36.8 | 82.8
20 mm | 39.7 | 35.7 | 75.4
30 mm | 31.2 | 26.6 | 57.8
Chemical reflector/ no optical grease |  |  | 
20 mm | 25.7 | 22.1 | 47.8
Chemical reflector/optical grease/Tyvek reflector |  |  | 
20 mm | 49.3 | 44.0 | 93.3
× 2.5 effect of chemical reflector compared with no chemical reflector.
60% effect of optical grease (same expected with optical glue).
20% effect of additional Tyvek reflector.

## Slide 26: Timing characteristics
Timing dominated by fiber decay constant: tfiber ~ 12 ns.
0.5 p.e. TDC threshold to suppress timewalk effects.
Two-sided readout  (t1-t2)/2 combination to estimate timing.

## Slide 27: SiPM Characterisation
Have a basic modelling approach to:
  Compare experimental measurements with semi-empirical processes – fitting of raw data...
  Extract parameters from experimental measurements for digitisation
Steps:
  Response of SiPM to single photon
  Estimate number of photoelectrons produced
  Combine single photon response with multi-photon input
  SiPM output and path to digitisation

## Slide 28: Energy deposition in scintillator
m
10 GeV/C
0.1 GeV/C
e
p
p
Chart: Energy deposited in a 1cm deep plastic scint: Beam perpendicular to slab.
| 10.0 | 2.0 | 1.0 | 0.5 | 0.2 | 0.1 | 0.05
Muon+ | 1.9329 | 1.915 | 1.8961 | 1.9055 | 2.1799 | 3.3632 | 13.5629
Electron | 1.9379 | 1.9368 | 1.9394 | 1.937
Proton | 2.2985 | 2.4577 | 3.2337 | 6.7439 | 9.3834
Pion+ | 2.2464 | 2.2695 | 2.2669 | 3.037 | 4.7685 | 15.1845

## Slide 29: L.Y. estimates
Parameter | Unit | AIDA [Perpendicular] | AIDA [MAX]
Energy deposition |  |  | 
Track length | [cm] | 0.70 | 1.00
Peak Edep/cm | [MeV/cm] | 8.82 | 8.82
Peak Edep | [MeV] | 6.17 | 8.82
Edep/MIP/cm | [MeV/MIP/cm] | 2.00 | 2.00
Edep/MIP | [MeV/MIP] | 1.40 | 2.00
Photon conversion |  |  | 
Photon yield | [ph/MeV] | 1.25E+04 | 1.25E+04
Photon yield per bar | [ph] | 7.72E+04 | 1.10E+05
Photon efficiency | % | 5.00E-03 | 5.00E-03
Photons on SiPM | [ph] | 3.86E+02 | 5.51E+02
MRS APD case (PDE = 35%) |  |  | 
Light yield | [p.e./MeV] | 21.4 | 21.4
Total light yield | [p.e./bar] | 132.1236 | 188.748

## Slide 30: Processes leading to SiPM output
Plastic scintillator
WLS fibre
SiPM
Charged particle
Energy deposition
Photon generation in p.s.
Hit probability p.s. to WLS
Blue/green conversion in WLS
Transmission in WLS
Photo-electron conversion
SiPM output

## Slide 31: Number of photons incident on SiPM
Initial photon yield ~ 1.25e4/MeV
Probability that blue photon from p.s. hits WLS
Probability that green photon propagates in
WLS by total internal reflection
Integral of SiPM
quantum efficiency
~ 20% (check)

## Slide 32: SiPM Single photon response
Assume for time being that SiPM circuit is similar to PMT circuit (later derive more appropriate approximation) i.e.:
  Single high-pass filter t1=C1R1
  Series of low-pass filters t2=C2R2

## Slide 33: Time distribution
Three main contributions:
  Decay times in scintillator and WLS
  Propagation delay
  Internal SiPM transit time
Decay time distribution:
  Random variable that is the sum of independent random times
  Characteristic decay times: tp and tf

## Slide 34: SiPM Output
Sum over all photoelectrons of SiPM response to single photoelectron.

## Slide 35: TASD and baby-MIND Electronics
Secondary/Tertiary beam from SPS:
  Slow extraction: < 100000 particles/(10s spill) every 60s
Electronics: 1000-10000 samples/s
Dynamic range: estimate 500 p.e. (100 p.e./MIP)
Number of channels: ~10000 ch.
Allowable noise level: 0.5 p.e.
Timing res.: TBD
Cost: 15 CHF/channel
Options:
  DRS4/5 (PSI, NA61 development)
  MAROC/EASIROC (MICE EMR)
  TRIP-t (T2K ND280)
DRS4

## Slide 36: DRS4
Fabricated in 0.25 mm 1P5M MMC process (UMC), 5 x 5 mm2, radiation hard
8+1 ch. each 1024 bins, 4 ch. 2048, …, 1 ch. 8192
Passive differential inputs/outputs
Sampling speed 700 MHz … 5 GHz
On-chip PLL stabilization
Readout speed 30 MHz, multiplexed or in parallel
SiPM
Ampli
DRS
ADC
FPGA
S. Bravar

## Slide 37: MICE EMR Electronics
MAROC/EASIROC
Option

## Slide 38: Omega Micro Chips - LAL

## Slide 39: EASIROC Description
Number of channels: 32
Analogue core :
  Internal input 8-bit DAC (0-4.5V) for individual SiPM gain adjustment
  Individually addressable calibration injection capacitance
  Energy measurement : 14-bit dynamic range
    2 tuneable gains followed by 2 adjustable shapers
    Analogue memory (Track & Hold cell) for low gain and high gain
    Common 10-bit DAC for threshold adjustment
    Variable shaping time: from 25 ns to 175 ns
    from 160 fC 320 pC (ie. 1 pe 2000 pe @ SiPM gain = 106)
    pe/noise ratio : ~10 @ SiPM gain 106
  Trigger output
    pe/noise ratio on trigger channel : ~ 25
    Fast shaper : ~15ns
    Trigger on 50 fC (ie. 1/3 pe @ SiPM gain = 106)

## Slide 40: EASIROC Schematic

## Slide 41: EASIROC Evaluation Board
Enables tests of most of the functionality of the EASIROC.
Full access to slow control 456 bits.
Pins on I/O allow for easy monitoring.
External ADCs for analogue signal tests.

## Slide 42: Trigger Output
Val Evt signal effect
Trigger output using latch
Trigger output in direct discriminator mode
Latch
Direct

## Slide 43: Preamp Feedback Tests
Chart: HG Preamp Fdbck Capa Test
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0 | 1100.0 | 1200.0 | 1300.0 | 1400.0 | 1500.0
 | 3146 | 3146 | 3139 | 3137 | 3141 | 3142 | 3136 | 3148 | 3167 | 3170 | 3181 | 3186 | 3190 | 3178 | 2872 | 1917
Chart: LG Preamp Fdbck Capa Test
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0 | 1100.0 | 1200.0 | 1300.0 | 1400.0 | 1500.0
 | 3379 | 3232 | 2389 | 1914 | 1644 | 1476 | 1364 | 1283 | 1225 | 1182 | 1148 | 1121 | 1102 | 1083 | 1050 | 992

## Slide 44: Shaper Tests
Chart: Shaper Test : 50 ns t.c.
| 0.0 | 2.5 | 12.5 | 25.0 | 37.5 | 45.0 | 50.0 | 55.0 | 60.0 | 70.0 | 80.0 | 87.5 | 100.0 | 110.0 | 125.0 | 150.0
LG Output | 809 | 874 | 1210 | 1458 | 1586 | 1625 | 1632 | 1637 | 1630 | 1580 | 1486 | 1406 | 1283 | 1194 | 1050 | 860
HG Output | 1557 | 1629 | 2107 | 2543 | 2746 | 2767 | 2907 | 2891 | 2832 | 2640 | 2412 | 2222 | 1908 | 1659 | 1357 | 840
Chart: Shaper Test: 100 ns t.c.
| 0.0 | 2.5 | 12.5 | 37.5 | 50.0 | 60.0 | 70.0 | 75.0 | 80.0 | 82.5 | 87.5 | 95.0 | 100.0 | 110.0 | 125.0 | 150.0 | 175.0 | 187.5 | 200.0 | 212.5 | 225.0
LG Output | 759 | 775 | 883 | 1130 | 1222 | 1280 | 1311 | 1315 | 1315 | 1315 | 1315 | 1317 | 1314 | 1304 | 1254 | 1175 | 1081 | 1044 | 996 | 952 | 914
HG Output | 1298 | 1341 | 1639 | 2230 | 2425 | 2535 | 2568 | 2551 | 2517 | 2515 | 2499 | 2431 | 2368 | 2251 | 2068 | 1688 | 1376 | 1208 | 1057 | 933 | 813
Chart: Shaper Test: 175 ns t.c.
| 0.0 | 2.5 | 12.5 | 37.5 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0 | 110.0 | 120.0 | 130.0 | 140.0 | 150.0 | 175.0 | 200.0 | 225.0 | 250.0 | 275.0 | 300.0 | 325.0 | 350.0
LG Output | 788 | 790 | 835 | 953 | 1011 | 1056 | 1084 | 1102 | 1121 | 1141 | 1152 | 1152 | 1153 | 1154 | 1149 | 1126 | 1094 | 1058 | 1017 | 980 | 943 | 910 | 879
HG Output | 1122 | 1147 | 1311 | 1691 | 1854 | 1954 | 2018 | 2061 | 2082 | 2094 | 2092 | 2073 | 2052 | 2020 | 1975 | 1860 | 1707 | 1549 | 1391 | 1248 | 1108 | 985 | 876
T&H is OR32 with programmable delay through FPGA

## Slide 45: Shaper Tests
Chart: LG Shaper Test
| 0.0 | 2.5 | 12.5 | 25.0 | 37.5 | 45.0 | 50.0 | 55.0 | 60.0 | 70.0 | 80.0 | 87.5 | 100.0 | 110.0 | 125.0 | 150.0
50 ns t.c. | 809 | 874 | 1210 | 1458 | 1586 | 1625 | 1632 | 1637 | 1630 | 1580 | 1486 | 1406 | 1283 | 1194 | 1050 | 860
100 ns t.c. | 759 | 775 | 883 | 1130 | 1222 | 1280 | 1311 | 1315 | 1315 | 1315 | 1315 | 1317 | 1314 | 1304 | 1254 | 1175 | 1081 | 1044 | 996 | 952 | 914
175 ns t.c. | 788 | 790 | 835 | 953 | 1011 | 1056 | 1084 | 1102 | 1121 | 1141 | 1152 | 1152 | 1153 | 1154 | 1149 | 1126 | 1094 | 1058 | 1017 | 980 | 943 | 910 | 879
Chart: HG Shaper Test
| 0.0 | 2.5 | 12.5 | 25.0 | 37.5 | 45.0 | 50.0 | 55.0 | 60.0 | 70.0 | 80.0 | 87.5 | 100.0 | 110.0 | 125.0 | 150.0
50 ns t.c. | 1557 | 1629 | 2107 | 2543 | 2746 | 2767 | 2907 | 2891 | 2832 | 2640 | 2412 | 2222 | 1908 | 1659 | 1357 | 840
100 ns t.c. | 1298 | 1341 | 1639 | 2230 | 2425 | 2535 | 2568 | 2551 | 2517 | 2515 | 2499 | 2431 | 2368 | 2251 | 2068 | 1688 | 1376 | 1208 | 1057 | 933 | 813
175 ns t.c. | 1122 | 1147 | 1311 | 1691 | 1854 | 1954 | 2018 | 2061 | 2082 | 2094 | 2092 | 2073 | 2052 | 2020 | 1975 | 1860 | 1707 | 1549 | 1391 | 1248 | 1108 | 985 | 876
125ns
80ns
50ns
12.5ns
50 ns time constant

## Slide 46: Discriminator DAC Scan
Chart: EASIROC Discriminator DAC Scan
| 1023.0 | 950.0 | 920.0 | 900.0 | 800.0 | 511.0 | 255.0 | 127.0 | 120.0 | 110.0 | 109.0 | 108.0 | 107.0 | 106.0 | 105.0 | 100.0 | 63.0 | 0.0
LG Output | 886 | 891 | 232 | 282 | 1629 | 1633 | 1635 | 1636 | 1638 | 1641 | 1647 | 1668 | 1710 | 1762 | 1797 | 1795 | 0 | 0
HG Output | 911 | 914 | 1068 | 1130 | 2971 | 2968 | 2947 | 2922 | 2922 | 2945 | 3001 | 3112 | 3221 | 3286 | 3304 | 3209 | 0 | 0

## Slide 47: Muon Ionisation Cooling Experiment (MICE)

## Slide 48: MICE EMR

## Slide 49: EMR construction/commissioning
R. Asfandiyarov

## Slide 50: Outlook
Work ongoing to “freeze” a number of parameters for production:
  Magnetisation of MIND (steel Oct. 2012)
  Scintillator slabs (Dec. 2012)
  SiPMs (April 2013)
  Electronics (Aug. 2013)
Simulations:
  Baby-MIND Geant4: similar methodology to MIND/SuperBIND.
  TASD Geant4: similar environment to MICE EMR.
  MIND and TASD Fluka: planned for comparison...

## Slide 51: Summary: what we are here for...
Discuss collaboration on:
Construction of TASD and MIND-type detectors:
  Magnetisation of the MIND (STL?, in-situ measurement of B-field, cost of steel, mechanics).
  SiPM procurement/integration (novel approaches e.g. digital SiPM, connector design, cost/ch).
  Electronics (options, cost/ch).
Simulation:
  Simulation framework.
  Methodology (e.g. hadronic shower reconstruction in B-field).
Use of AIDA detectors as test beds for nuSTORM detector activities (in the spirit of the MINOS CalDet experiments...).

## Slide 52
Back-up slides

## Slide 53: General Layout: Baby MIND

## Slide 54: Baby-MIND parameters I/II

## Slide 55: Baby-MIND parameters II/II

## Slide 56: Basic parameters for magnetisation
Coil and P.S. parameters | Units | AIDA baby-MIND | INO Full | INO Prototype
Coil dimension 1 | cm | 2.6 | 20 | 2.6
Coil dimension 2 | cm | 10 | 100 | 10
Coil height | m |  | 15 | 
Total single turn length | m | 8 | 46 | 4.7 x 2
Total coil length | m | 800 | 92000 | 940
Density of copper | kg/m3 | 8940 | 8940 | 8940
Coil volume | m3 | 0.021 | 9.2 | 0.024
Coil weight | kg | 185.952 | 82248 | 218
Amp-turns | Amp-turns |  | 40000 | 4000x2
Number of turns |  | 20 x 5 | 20 x 100 x 2 | 5 x 20 x 2
Conductor size | cm | 0.5 x 0.5 | 1 x 1 | 0.5 x 0.5
Current 10 A | Amps | 40 | 10 | 40
Resistance | Ohm | 0.5376 | 15.6 | 0.64
Voltage | Volts | 21.504 | 156 | 25.6
Power dissipation | kW | 0.86016 | 3.1 | 1.02
Coil inductance | Henry |  | 1710 | 10
Rise in temperature of coil | oC |  | 4 | 
Rise in temperature of iron surface | oC |  | 2 | 
Stored magnetic energy | MJ |  | 5.3 | 0.01
Characteristic magnetisation time | s |  | 110 | 16

## Slide 57: Baby-MIND scintillator modules

## Slide 58: Example outputs
ws=2cm
hs=3cm
df=0.15cm
Edep=6MeV
PH=13%
PTrans=3.7%
Yield=1.25e4/MeV
2 MeV/MIP
nclad=1.6
ncore=1.49
ts=1ns
tf=6.5ns
PQ=20%
Ws=1cm
Hs=0.6cm
df=0.10cm
Edep=1.2MeV
PH=43%
PTrans=3.7%