## Slide 1: μ Storage Ring for ν beam
David Neuffer
Fermilab f
September 2012

## Slide 2: Outline
Scenario Overview
Stochastic injection
Storage ring options
  Superconducting
  Normal
Current Studies

## Slide 3: Neutrinos from μ Storage Ring
Intense Proton beam on π production target
Collect forward π’s; transport into ring
  Li lens or horn
π decay in injection Straight Section produces μ’s
  50% of 5GeV π decay in 200m SS
μ’s accepted by ring; circulate for ~100 turns
  Decay : produces neutrino beams
  C =~500m
200m straight section
50m arc
π

## Slide 4: Parameter Choices
Need ~GeV neutrino beams
  searching for L/E = 1km/GeV νe, oscillations
Need to cleanly separate μ+ from μ-
  magnetized detector – MIND
    iron/scintillator detector
  needs >~2 GeV neutrinos for clean separation
Need ~3.8 GeV μ storage ring
  Requires ~5 GeV π’s
  requires ~50+ GeV Main Injector Proton source
C. Tunnell

## Slide 5: Li lens or magnetic Horn or?
~ NuMI Horn
  rmin=1.35cm; rmax=15cm
  I0200kA
  B = 3T0.2T
    nonlinear optics
~ Li Lens (pbar)
  r0=1cm; Lactive =15cm
  I0500kA
  B = 10T
    for 20cm focal length,3GeV,
    want ~167kA (3.33T)
    ~50 mrad acceptance
  can get 100 mrad with r0=2cm

## Slide 6: π  μ Injection
Separate Transport for π 
  kick into storage ring after decay
    Requires fast kicker, can only use part of MI/spill
Injection of π into straight section, accept μ in ring acceptance.
  “stochastic injection”
    stochastic was popular in 1980
    stochastic cooling, stochastic extraction, …
  no kickers; phase space of injected π and circulating μ are separated
  Circumvents Liouville’s Theorem
Could also inject into target inside ring
  π’s within acceptance decay
  μ’s within acceptance stored
    circulating beam passes through target
    collection of beam off target more limited
p
π
p
π→μ+ν
p
μ
π→μ+ν
π→μ+ν
π
π→μ+ν

## Slide 7: Overview of stochastic injection
π’s are in injection orbit (~5 GeV/c)
  separated by chicane
μ’s are in ring circulating orbit
  lower energy - ~3.8 GeV/c
~30cm separation between orbits
5 GeV/c π
~3.8 GeV/c μ
Injection Line accepts 5 GeV/c ± 10%
Storage Ring accepts 3.8 GeV/c ± 10%
π

## Slide 8: Transport into Ring
Horn has greater acceptance than Li lens
  more established technology (nuMI)
    large aperture Li lens requires R&D
Sequence of quads from Li lens into Ring (A. Liu)
  good acceptance of transport
  ~0.1 π / p into ring ~5±0.5 GeV
    ~0.01 /p stored in ring
Q1 Q2 Q3 Q4 Q5 Q6 B1 Q7 Q8 B2 Q9 Q10 B3

## Slide 9: Lattices for storage rings
FODO Lattices
  Superconducting
    B  4T
    A. Bogacz
  Normal conducting
    B<2T
  Goal: ±10% momentum acceptance, 0.002m “emittance” acceptance
FFAG Lattices
  A. Sato, Y.Mori
straight section
arc
π

## Slide 10: Arc Optics- High Field
24.8792
0
10
0
1.5
-1.5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
4  900-FODO cells
2  ‘half -empty ’ cells
25 meter 1800 Arc based on 900-FODO lattice
2  ‘half -empty ’ cells
p = 3.8 GeV/c
Aperture radius: r = 15 cm
12  Dipoles: field: 3.9 Tesla length: 85 cm
15  Quads: gradient : 25 Tesla/m (3.8 Tesla at the pole) length: 50 cm

## Slide 11: Decay Ring - 3.8 GeV m
175.959
0
60
0
1.5
-1.5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
25 m Arc
150 m ‘Low-beta’ Straight (half)
p = 3.8 GeV/c
150 m ‘High-beta’ Straight (half)
 2
mirror point
25m Arc
150 meter Straight
25 m Arc
150 meter Decay Straight
350 meter Racetrack Ring
Muons recirculated at central momentum: p = 3.8 GeV/c
injection scheme

## Slide 12: Magnet Cost Estimate
Vladimir Kashikhin
Strauss & Green Costing Model

## Slide 13: Dynamic Aperture – tracking
6/30/08
NuFact08, Valencia
35
-35
Y [cm]
10
-10
Y`[mrad]
30
-30
X [cm]
10
-10
X`[mrad]
Dy = 30 cm
Dy’ = 7 mrad
Dp/p= 10 %
Phase –space after turn 68
Acceptance (geometric) p = 3.8 GeV/c
A = Dx Dx’ = Dy Dy’ = 2.1 mm rad
Acceptance (normalized) bg  36
AN = A bg = 78 mm rad
Dx = 26 cm
Dx’ = 8 mrad
 Dx
 Dy
 Dx’
 Dy’
 Dp/p
100
-100
S [cm]
200
-200
dP/P * 1000,
25000 muons tracked
70% muons left (no muon decay accounted for)

## Slide 14: Alternate FODO lattice
200m straight section
50m arc
π
μ storage ring optics
π injection line
Lower field
  not superconducting
Match into ring

## Slide 15: Alternate Low-field Storage ring
Inject ~5GeV π into Straight section to produce μ’s from decay
  50% of 5GeV π decay in 200m SS (60% in 250m)
  Lower field  longer arc
  B<2T
  longer quads to keep gradient lower
Straight section for π μ capture and μ decay ν production
  decay channel must keep π beam confined to capture μ’s from decay
Neutrino opening angle ~1/γ ~0.03
  beam transport angles ~0.005
    θrms = ~ (εrms/β*)½
    ΔεT= ~ (β*Θdecay2)/2
      Θdecay ~ 30/5000
200m straight section
50m arc
π

## Slide 16: Lattice Parameters Low-Field
Parameter | Symbol | Value | Unit
Cell length | L | 6 | m
Max β | βmax | 10 | m
Dispersion | ηmax, | 1.2 | m
Quad | B’, L | 12T/m | 0.5m
Dipole | B | 1.2T | 2.0m
β range in straight | βss | 20/30 | m
Arc quads would have r<0.15m
  εacc= 0.152/10=0.002m
  εacc,N= ~0.08m
    εacc,N,rms= ~0.015m
  δp/p = ±10%
  θrms = ~0.005 (at β= 30m)
  Angle from π-decay
    30 MeV/5000 -~0.006
Low-Field (<2T) magnets

## Slide 17: Lattice development
Momentum spread of ±10% crosses resonances
  beam loss at resonance momenta
  sextupole reduces loss from resonances
    increases nonlinear orbit distortion
  optimization
    vary tunes,
    sextupoles to reduce chromaticity
-12%
-12%
+12%
+12%
without sextupoles
with sextupoles
Optim tracking
without sextupoles
with sextupoles

## Slide 18: Variations
Ring Design
  Use FFAG-style lattice
  must add injection
    dispersion bump + septum
could have better acceptance
  FODO probably not best …
Inject
  In Space between cells-
    increase space
  Insert septum/separator magnet
p
μ

## Slide 19: Summary
Presented a nuSTORM Storage ring overview
“stochastic” Injection of muons into storage ring
Questions?

## Slide 20: Comparison of facilities
IDS neutrino factory
Low-luminosity Neutrino Factory
nuSTORM