## Slide 1
Robert Zwaska
24 April 2023
EPICS Collaboration Meeting
Welcome to Fermilab and the Fermilab Accelerator Complex

## Slide 2: Outline
Fermilab Science Overview
Accelerator Complex
The push for power:
  NuMI Neutrino Beam & Experiments (400 kW)
  ANU Upgrade (700 kW)
  PIP Upgrade (700+ kW)
  Megawatt Upgrade (1 MW)
The new machines
  LBNF/DUNE (1.2 – 2.4 MW)
  PIP-II (1.2 MW + 1.6 MW)
  Accelerator Complex Enhancement (ACE) (Multiple, Multi-MW “spigots”)
    Main Injector Cycle Acceleration
    Booster Replacement

## Slide 3
Fermilab at a Glance
America's particle physics and accelerator laboratory
Operates the largest US particle accelerator complex
~1,900 staff and ~$600M/year budget
6,800 acres of federal land
Facilities used by 4,000 scientists from >50 countries
As Fermilab moves into its second 50 years, its vision remains to solve the mysteries of matter, energy, space, and time for the benefit of all.

## Slide 4: The Fermilab research community
More than 4,000 scientists in 55 countries use Fermilab and its particle accelerators, detectors and computers for their research
More than 2,200 scientists from 175 U.S. universities and labs in 41 states
Fermilab is attracting and training the next generation of a diverse HEP scientific workforce: 114 postdocs, 273 graduate students, 52 undergraduate interns
Fermilab scientists also work at CERN, Sanford Underground Research Facility (SURF), SNOLAB, Cerro Tololo Inter-American Observatory, South Pole Telescope, NOvA Ash River Laboratory, Matter-wave Atomic Gradiometer Interferometric Sensor

## Slide 5
  Fermilab is following the P5 strategy
  The flagship projects LBNF/DUNE/PIP-II, HL-LHC anchor the program but take many years to realize
  Fermilab simultaneously pursues a broad research effort in HEP
  The goal is a continuous stream of exciting results that attract/build/retain a diverse user community and scientific workforce
  Fermilab projects drive funding growth for HEP

## Slide 6: Fermilab Accelerator Complex

## Slide 7: The Fermilab Linac
Linear (copper) Accelerator
Accelerates H- ions
  750 keV  400 MeV
    Thousands to millions of volts
Beam bunched at 200 MHz
  ~ 1.5 Billion ions / bunch
RF of 200 & 800 MHz
  Distance between drift tubes changes with beam velocity
Pulse length of ~ 80 ms
  Many particles for short periods of time – more efficient operation

## Slide 8
H- ions are stripped and multi-turn injected onto the Booster
Protons are accelerated from 400 MeV to 8 GeV in 33 msec
Fast cycling synchrotron
  Fast magnet ramping
  Frequency of 15 Hz
Single turn extraction
Many pulsed devices requiring upgrade
Booster | 
Circumference (m) | 474
Harmonic Number | 84
Kinetic Energy (GeV) | 0.4 - 8
Momentum (GeV/c) | 0.954 - 8.9
Revolution period (msec) | t(inj) 2.77 – t(ext) 1.57
Frequency (MHz) | 37.9 - 52.8
Batch size | 4.5 E12
Focussing period | FDooDFo (24 total)
Booster
Combined Function Magnets
No failures after initial phase…
but 8 spares have been refurbished as part of PIP…
Booster Overview

## Slide 9: Main Injector & Recycler
Main Injector: 120 GeV Fast-cycling synchrotron
360 main dipole magnets
200 main quadrupole magnets
108 sextupoles, 66 octupoles, corrector dipoles/ quads, specialty injection and extraction magnets
Twenty 53-MHz RF cavities to accelerate beam
170 DC and 360 ramped magnet supplies with total of 140 MVA, 40 specialty pulsed magnet supplies
Recycler: 8 GeV Storage Ring
Originally built for antiproton storage, repurposed for proton stacking
Combined function, permanent magnets
RF cavities for stacking proton beams

## Slide 10: The NuMI Facility: “Neutrinos (ν –> Nu) at the Main Injector”
Intense muon-neutrino beam directed towards Minnesota
Main Injector supplies 50–70e12 120GeV protons every 1.2 seconds
  Designed for 400 kW, operated up to 900 kW
  Multiple upgrade projects to 1 MW
Each pulse produces about 2x1014 ν 
  ~ 20,000,000 Pulses per year
  Direct beam 3o down
Commissioned in 2005, expect to run to ~ 2027
Near Detectors
Far Detectors: 5400 tons & 14000 tons
5
Neutrino beam
“Long-baseline”

## Slide 11: Multiple Experiments Simultaneously in the NuMI Beam
Long-baseline oscillation experiments
Neutrino scattering experiments

## Slide 12: Neutrino oscillations: Big picture questions
What is the origin of neutrino mixing? Is there an underlying flavor symmetry, and how is it broken?
What is the origin of the neutrino masses? Why are the neutrinos so light?
Is leptogenesis a viable explanation of the baryon asymmetry of the Universe?
How must the Standard Model be modified for neutrinos? Is the νSM complete? Are there additional neutrinos?

## Slide 13: Why a Beam of Neutrinos? – Controlled Laboratory Experiment
Natural sources of neutrinos exist – but they are weak and not necessarily well understood
  Solar and atmospheric neutrinos were only understood once oscillations were established and well measured
    Moving from observation to experiment
  Supernovae (for neutrinos) are rare events, though very interesting
Artificial beams are controlled and intense ➩ Precision!
  Decide when, where, and how the beam is generated
  Detectors are placed strategically
  Beams can be controlled with precision – vital as measurements approach 1%
Most all our neutrinos come from pion decays
  Convert the kinetic energy of the accelerator beam into new massive particles (pions), which decay to neutrinos
  A “simple” decay (at first)
    Pion mass ~ 140 MeV/c2, Muon mass ~ 105 MeV/c2

## Slide 14: Neutrino Beam in a Nutshell (NuMI)
400 kW design average power
700 kW upgrade for NOvA
1 MW upgrade just complete
s ~ 1-1.5 mm
2 interaction length, C target
Produces p+, K+ mesons
Pulsed focusing horns @ 200 kA
Toroidal magnetic field
Parabolic inner conductor profile
Focuses meson momentum band
2 m diameter
Roughly decay length for 10 GeV p+
He-filled
Absorbs ~ 40 % of beam power
Allows high-energy muons to penetrate
Measure hadron & muon fluxes
Arrays measure distributions

## Slide 15: NOvA Accelerator & NuMI Upgrades (ANU): the 700 kW Upgrade
Previous Stacking operation (~ 380 kW in 2011):
  H- linac at ~35 mA
  H- stripping into Booster 10-11 turns: 4.3e12 protond
  11 pulses (at 15 Hz) into Main Injector with RF slip stacking
  Ramp to 120 GeV at 204 GeV/s and extract to NuMI target

## Slide 16: Increasing Beam Power to 700 kW
The installation of a direct injection line from the Booster to the Recycler to eliminate Main Injector loading time was the key component of the “ANU” improvement campaign for NOnA (400 kW->700 kW) available by 2015
“slip-stacking” cleverly gets around limits on Booster batch size
15 Hz Booster sets fundamental clock (“tick”)
Employ Recycler ring to load 12 slip-stacked Booster batches while the Main Injector was ramping

## Slide 17
The Proton Improvement Plan should enable Linac/Booster operation capable of
  Delivering 2.3E17 protons/hour (at 15 Hz) x2 previous
  while
  Maintaining Linac/Booster availability > 85%, and
  Maintaining residual activation at acceptable levels
and also ensuring a useful operating life of the linac through 2023, and Booster through 2030 or later
The scope of the Proton Improvement Plan included
  Upgrading (or replacing) components to increase the Booster repetition rate
  Replacing components that have (or will have) poor reliability
  Replacing components that are (or will soon become) obsolete
  Studying beam dynamics to diagnose performance limitations
  Implementing operational changes to reduce beam loss
Proton Improvement Plan (2011-2018) for Linac And Booster

## Slide 18: Booster loss and Linac laser notch
Doubling the beam repetition rate requires cutting the losses per Booster cycle in half
Addressing each of the three main areas of Booster beam loss:
  Injection
  Notching the beam to create a gap for extraction kickers to fire
  Transition, related to RF during acceleration
Phased improvements to notch creation
  New cogging system which allowed notching at 400 MeV instead of 700 MeV  lower energy losses into an absorber
Final phase was a laser notcher in Linac MEBT
  Laser Neutralization of H- with zero space
  Unique laser with micro, meso, and macro timescales, and vertical spatial profile
Optical cavity
(attached end of RFQ)
Laser profile
Successful test of Linac notch Dec 2014

## Slide 19: Booster PIP - Refurbishment of 40 year old cavities
Cavity Removal
Cool-down
Remove Tuners
Rebuild - Cones & Tuners
Rebuild Stems/Flanges
Re-Assemble
Testing
(Weeks)
Cavity Removal - Stripping
Tuners Rebuild
Rebuild and Test

## Slide 20: Booster 15 Hz – A significant achievement for PIP/FNAL
TLG with 13 (fixed target event) beam events & 2 pre-pulses, $17 (Booster event) then replaced the pre-pulses for full 15 Hz beam operation – record intensity >2.1E17/hr !
$19 (NoVA event) or $1D Boone Event) cycles at reduced intensity allowed for 15 Hz beam and some overhead
PIPs success led to the possibility to increase Main Injector beam to close to 1 MW with modest upgrades in other parts of the accelerator chain

## Slide 21: NuMI Megawatt Accelerator Improvement Project (AIP): 2018-2021
Originally designed for 400 kW beam power, then upgraded to 700 kW with NOvA/ANU
Megawatt AIP (Accelerator Improvement Project)
  Upgrade of target, horns, and supporting systems to be capable of accepting 1 MW beam power through 2025
  Completed in 2021 after 3 annual accelerator shutdowns to replace components
  Record 893 kW beam power achieved in April 2022
 | NuMI Design | NOvA | 1 MW upgrade
Proton beam energy | 120 GeV |  | 
Beam power (kW) | 400 | 700 | 1 MW
Energy Spectrum | Low Energy | Medium Energy | 
Cycle time (s) | 1.87 | 1.33 | 1.2
Protons per spill | 4.0 x 1013 | 4.9 x 1013 | 6.5 x 1013
Spot Size (mm) | 1.0 | 1.3 | 1.5
Beam pulse width | 10 microsec |  | 
Notes: 700 kW in 2012

## Slide 22: NuMI AIP – 1 MW Target Upgrade
Core redesigned for increased beam spot size from original 1.3 mm to 1.5 mm
  Graphite fins width increased from 7.4 mm to 9 mm
  Winged fins added upstream in case of beam mis-steering
Cooling loop added on downstream Beryllium window
Former Be window design temperature immediately after beam spill
1 MW Be window design with cooling loop temperature immediately after beam spill
700 kW design | 913
1 MW design | 890
700 kW design | 
1 MW design | 

## Slide 23: NuMI AIP – 1 MW Horn Upgrade
Design changes to increase cooling to keep stripline < 100
  Re-design of air diverter at base of stripline for improved air flow
  T-Block air cooling
Stripline modified for 1 MW
  Changed material from Al 6101-T61 to 6013-T651 in key sections
  Higher yield strength and increased fatigue life
T-block air diverter
Horn stripline air diverter
NuMI 1 MW horn stripline

## Slide 24: NuMI Target Systems Accelerator Improvement Plan (AIP): Target Station Upgraded for 1-MW Beam Operation
Objective reached: capable of accepting 6.5E13 protons/spill at 120 GeV, 1.2 sec cycle time
Project scope: improve and replace Target Hall components / support systems
Tasks completed in 2019 – 2022
1-MW Horn-1 Installation
Upgrade for 1 MW | Reliability / Lifetime Extension
MARS / FEA simulations for all beamline components 1 MW target 1 MW horn 1 Stripline air diverter T-block & HVAC ductwork Target & Horn 1 RAW system Target chase cooling and air handling system | Horn 1 module drive mechanism changeout Absorber intermediate cooling system HX MI-65 condensate rerouting Target chase supplemental shielding Hadron monitor and gas system Target module drive mechanism MINOS surface dry cooler
NuMI Team

## Slide 25: DUNE Deep Underground Neutrino Experiment
  Origin of matter. Investigate leptonic CP violation. Are neutrinos the reason the universe is made of matter?
  Neutron star and black hole formation. Ability to observe neutrinos from supernovae events and perhaps watch formation of black holes in real time.
  Unification of forces. Investigate nucleon decay, advance unified theory of energy and matter.
The LBNF/DUNE project will be the first internationally conceived, constructed, and operated mega-science project hosted by the Department of Energy in the United States” – DOE

## Slide 26: Exquisite Measurement Possibilities with Long Baseline and Broad Beam
DUNE is designed to resolve degeneracies by measuring flavor transitions as a function of energy over more than a full oscillation period
DUNE will determine the mass ordering and measure δCP, regardless of the true values
Expect the unexpected: DUNE is robust against systematic effects and for resolving deviations from νSM

## Slide 27: The LBNF Beam
Facility designed for initial beam power of 1.2 MW, upgradeable to 2.4 MW

## Slide 28: Section View of Target Complex – Target Hall
Beam
Primary Beam Enclosure
Target Hall
Work Cell
Decay Pipe
Primary Beam Window
He Gas
Cooling
Panels
Horn A with Target
Horn B
Horn C
Baffle
N2 Gas
Hatch Covers
Decay Pipe Upstream Window
Steel Shielding

## Slide 29: Proton Improvement Plan II (PIP-II)
Increase Main Injector beam power to 1.2 MW.
  Replace the existing 400 MeV linac with a new 800 MeV superconducting linac => increase in Booster intensity.
    Provide a platform to increase LBNF power to 2.4 MW
  Provide path for a 100 kW Mu2e-II
  Provide capability for 1.6 MW at 800 MeV, CW beam
  Platform for high duty-factor / power operations to multiple experiments

## Slide 30
30
30
PIP-II Linac & Upgrades (1.2 MW power on target)
E. Pozdeyev, SpaceCharge19
Project started in 2016 (CD0)
First beam in Booster: 2028 (plan)
MI 1.2 MW beam on target: 2031 (projection)
Notes: 30
30
30
30
30
30

## Slide 31: PIP-II Project construction begins!
Magnets provided by
PIP-II received DOE CD-3 approval for start of construction/execution on April 18
  Linac complex RFP issued
Front end of PIP-II linac constructed and successfully tested with beam
PIP-II cryoplant building 98% complete
HB650 prototype cryomodule in assembly – first of its kind
PIP-II is the first particle accelerator built in the U.S. with significant international contributions

## Slide 32: LBNF/DUNE/PIP-II in-kind contributions $1.1B with growth potential
LBNF/DUNE-US
  $262M in-kind contributions to LBNF (does not include private @ $70M or State of SD @ $93M to support SURF)
  $310M in contributions to DUNE detectors
  $84M in CERN contributions to protoDUNE efforts (does not include French contributions to protoDUNE R&D)
Additionally, LBNF powered by PIP-II, which has secured $310M in international contributions
In-kind contributions supported by 10 Government-to-Government agreements and 17 I-CRADAS
All in-kind contributions are expressed in DOE TPC units
Numbers do not include other IKCs received in support of Fermilab’s short-baseline neutrino program

## Slide 33: Replacing the Booster
2014 P5 Recommendation: Provide 2.4 MW to DUNE
  Now ~ 0.9 MW max
  With PIP-II can reach ~ 1.2 MW
  Main bottleneck is the Booster synchrotron
  Intensity can be improved but not enough to reach 2.4 MW
Many studies, going back almost 25 years.
  Luciano Ristori presentation to PAC June 2021
  White Papers for Snowmass describe design options and potential for rich low energy science program
  Recent PIU and ACE studies

## Slide 34: Accelerator Complex Evolution (ACE) plan
Increase protons on target to DUNE Phase I detector by
  Shortening the Main Injector cycle time to increase beam power
  Upgrading target systems for up to 2.4 MW
  Improving reliability of the Complex
Establish a project to build a Booster replacement to
  Provide a robust and reliable platform for the future of the Accelerator Complex
  Ensure high intensity for DUNE Phase II CP-Violation measurement
  Enable the capability of the complex to serve precision experiments and searches for new physics with beams from 1-120 GeV
  Create the capacity to adapt to new discoveries
  Supply the high-intensity proton source necessary for future multi-TeV accelerator research

## Slide 35: Shortening the Main Injector cycle time
Advantages over increasing the per-pulse intensity – reduces likelihood of space charge effects and instabilities, and reduces impact of limited aperture
To shorten the MI cycle from 1.2-1.4s to 0.65s, the ramp needs to be ~twice as fast
Requires more voltage and electrical power
  Power supplies, transformers, feeders, service building size, additional tunnel penetrations, additional cooling
RF accelerating system
  Replace cavities with newer design (more volts per cavity) or add cavities of current design
Regulation, control & instrumentation
  New low-level RF, new power supply regulation/control system
Beam dynamics, losses and shielding
  Upgrade MI collimators, upgrade abort line, add shielding

## Slide 36: ACE Booster replacement options and possible add-ons
Booster replacement scenarios are developed informed by studies from the past and input to Snowmass/P5
  Cost-effective and fastest path to increased power to 2.4MW for LBNF.
  Capture options for additional medium and small-scale experiments.
  Enable long-term vision.

## Slide 37: Summary
Fermilab has successfully delivered several modest projects to significantly increase beam power:
  NOvA/ANU -> 700kW
  PIP -> 700+ kW and better throughput / reliability
  NuMI Megawatt AIP -> 1 MW capability
Major Projects are underway
  LBNF 1.2 – 2.4 MW capability
  PIP-II -> 1.2 MW + 1.6 MW
Planning for a successor project to PIP-II: ACE: Accelerator Complex Evolution
  Fixed purpose is providing 2+ MW to LBNF/DUNE as rapidly as possible
  Alternatives of Linac Extension + RCS or 8 GeV Linac for long-term program
  Many potential experimental users of 1, 2, 8, 120 GeV megawatt-class beams

## Slide 38
Robert Zwaska
24 April 2023
EPICS Collaboration Meeting
Welcome to Fermilab and the Fermilab Accelerator Complex

## Slide 39: Fermilab Experiments’ Run Schedule

## Slide 40: Neutrino oscillations: current status
Current precision:
θ13 ~ 2.7% (reactor νe disappearance)
|Δm2 | ~ 3% (reactor ν
32 e
disappearance and accelerator νμ
disappearance), mass ordering unknown
sin2θ23 ~ 0.5 ± 0.1 (atmospheric and accelerator νμ disappearance + νe appearance)
δCP unknown
Measure neutrino oscillations precisely, including νμ→νe that is sensitive to CP violation
Test the three-flavor paradigm → overconstrain the system
●
●
●
●
●

## Slide 41: Critical Issue: Space Charge Limit
Injected intensity is limited by the space charge tune-shift, which can drive harmonic instabilities.
Thus, the maximum injected charge grows rapidly with increasing energy
total protons
normalized emittance
“Bunch factor” = Ipeak/Iave
(Reduce with higher RF harmonics)
= 3 for 95% Gaussian emittance
1 for 100% uniform (painted) emittance
doesn’t include improvement of going to uniform distribution with painting

## Slide 42: Defining Characteristics of Long Baseline Neutrinpo Beams
Proton Beams: synchrotron based, ~ 1 MW
  High Stored Energy: ~ 1 MJ
  Small Beam Spot: 1 – few mm
  High Proton Energy: 30-120 GeV
  Single-turn extraction, long cycle time: 1 – few seconds
Pion Focusing: Pulsed horns
  Horns more efficient than quads
  High currents: few hundred kA
Large Decay volume
  Meters in cross-section
  100s of meters in length
Beam radiation dispersed over extended area
  Tritium, activation, corrosion, cooling

## Slide 43: NuMI AIP – 1 MW Horn Upgrade
Upgraded Horn 1 installed during 2020 summer shutdown
Horn 2 also replaced due to water leak
  12 year/100 million pulses lifetime
Accompanying Horn 1 module rebuilt and replaced
  Drive mechanisms for horn positioning no longer functional
PH2-02 removed after 12 years of service
1 MW PH1-05 being installed
Horn 1 module mechanisms replaced
Horn 1 and module test fitment