## Slide 1: EPICS IOC On SoC FPGA based LLRF Controllers
Shriraj Kunjir Radio Frequency Controls Engineer

## Slide 2: Outline
LLRF Controller
LLRF Controller SoC FPGA
EPICS IOC Implementation
Test
Advantages
Challenges
Summary

## Slide 3: LLRF Controller
Designed and developed for
  Future FRIB 644 MHz upgrade cavity
  MSU ultra-fast electron microscopy UEM 1 GHz cavity
Currently installed and operational at MSU UEM lab.
Specs -
  1x Xilinx FPGA board (1)
  1x RF front-end board (2)
  1x 500 GB solid-state drive (3)
  1x 1U Power supply (4)
1
2
3
4

## Slide 4: LLRF Controller SoC
Specs -
  Arm Cortex A53 Quad-core processor
    ARM v8 architecture
    Total CPU frequency 1.2 GHz
    4 GB RAM
    Debian 11 Bullseye
  Arm Cortex R5 dual-core real-time processing unit
  IO peripherals
    PCIe
    Gigabit Ethernet
    USB 3.0
    SATA
    SD
  FPGA
    600k LUTs
    2520 DSP slices
    24x 16.3 Gb/s Transceivers
    328 I/O pins

## Slide 5: EPICS IOC Implementation
In the current implementation, LLRF controllers communicate with IOC servers over UDP.
Added latency due to network traffic.
UDP connection is unreliable and lossy.
Asyn port driver that uses EPICS timers as its main communication mechanism.
In the new implementation, there’s no need for UDP since the IOC server runs on the LLRF controller.
Minimum latency since IOC server has access to FPGA registers via Linux userspace.
Asyn driver adapted from softGlue driver available inside synApps.

## Slide 6: FPGA – IOC interface (old)
FPGA
IOC
UDP
Array

## Slide 7: FPGA – IOC interface (new)
Linux (IOC)
FPGA
SoC
Device address space

## Slide 8: Test
LLRF controller on test network.
Work in progress to add more PVs, OPI pages, archiver support and features.
25 CS-Studio screens connected to IOC.
CPU load - ~ 0.02%
Memory utilization - ~ 0.03%
350 PVs connected.

## Slide 9: Advantages
Useful in lab environments where it is difficult to have a standalone IOC server.
Targeted maintenance.
  Reduce risk of affecting other devices and IOCs.
Distributed computing.
  Split hardware computing resources.
Direct Memory Access (DMA) support for fast data capture and plotting.
  Gives hardware-level access to data and allows for interrupts to the IOC from the FPGA.
Reduction in network traffic.
  Eliminating unreliable UDP connection frees up network resources.
Reliable TCP connection.
Reliable fault tolerant fallback scenarios for boot mechanism.
  Supports multiple fallback boot image files in case of primary boot image corruption.
Sufficient local storage for log files and data in case of remote archiver failure.

## Slide 10: Challenges
Increase in total number of IOC servers under management.
Maintenance of spares.
  Keep up-to-date with latest packages/versions.
Central configuration management system (Puppet) not supported for Debian on Arm 64-bit architecture yet.
  Hopefully that changes in the future.
  Develop alternate mechanism in the meanwhile.
Define network/system architecture with all stakeholders (controls group, business IT, system administrator).
Determine Arm 64-bit architecture support for all Debian packages currently installed on IOC virtual machines.

## Slide 11: Summary
Proof of concept has been demonstrated.
Future work involves addressing challenges and taking advantage of interrupt and DMA support.
More discussions need to be done to determine maintenance of the LLRF controllers running IOCs.