## Slide 1: Status and Outlook of the LHC
L. Bottura
CERN TE-MSC
US-LUO Meeting 2012
October 18-20, 2012, Fermilab

## Slide 2: Outline
Where do we come from
The present production at the LHC
The foreseeable LHC future
Beyond the LHC
A final message
An insider view
And a special eye for technology

## Slide 3: Outline
Where do we come from
The present production at the LHC
The foreseeable LHC future
Beyond the LHC
A final message

## Slide 4: September 10th, 2008…
IR7
IR3
IR6
First turn !

## Slide 5: …September 19th, 2008…
Initiated by an unprotected quench of defective joint
Arcing in an interconnection
Magnet displacement
Over-pressure
NOTE: this is an intentional defect built for testing purposes

## Slide 6: …November 30th, 2009…
LHC surpasses a proton beam energy of 1 TeV

## Slide 7: March 30th, 2010
3.5 TeV operation

## Slide 8: Outline
Where do we come from
The present production at the LHC
The foreseeable LHC future
Beyond the LHC
A final message

## Slide 9: LHC operation “today”

## Slide 10: LHC luminosity production
Peak luminosity 7.7 1033 1/cm2 s
LHC operation has reached good routine to deliver approximately 20 fb-1 by the end of 2012

## Slide 11: Results from ATLAS on H-Day
Candidate for a 4-e-decay of the Higgs boson
Exclusion limits for the existence of a new particle in the range of 100 to 600 GeV
Fabiola Giannotti, ATLAS, Status of the SM Higgs Boson Search, July 4th, 2012

## Slide 12: Results from CMS on H-Day
J. Incandela, CMS, Status of the SM Higgs Boson Search, July 4th, 2012

## Slide 13: Results from CMS on H-Day
J. Incandela, CMS, Status of the SM Higgs Boson Search, July 4th, 2012

## Slide 14: To be fair, results from Tevatron
Candidate events for Higgs boson decays at CDF
Exclusion limits for the existence of a new particle in the range of 100 to 200 GeV
Homer Wolfe, CDF, The Search For The Brout­Englert­Higgs Boson, March 7th, 2012

## Slide 15: The “Higgs” is there !?!

## Slide 16: Cuddle your Higgs

## Slide 17: No Higgs in Catholic church ?

## Slide 18: A Higgs event in CMS ?
No, a pack of spaghetti !

## Slide 19: Do not forget heavy ions physics
p-Pb run coming up
Fascinating physics !

## Slide 20: Not always plain sailing…
2e14
7e33
Mixed bag
CRYO
BSRT
Injectors
Luminosity logs from weeks 34 and 35 (20th to 29th August 2012)
Beam intensity from weeks 34 and 35 (20th to 29th August 2012)

## Slide 21: What did we learn?
LHC is magnetically very reproducible on a month to month time scale
High precision of the powering system
  (8 independent sectors !)
High availability of the cryogenics and hardware system
Head on beam-beam limit higher than foreseen
Aperture better than foreseen
Not a single magnet quenched due to beam , with 150 MJ per beam and more than 3 GJ stored in the magnets
June 2012, best so far
dQ=0.007
Tune feedback during squeeze

## Slide 22: Concerns of intensity and energy
Single event upsets (SEU) that depend on beam intensity and luminosity (Radiation to Electronics)
Localized short losses, commonly referred to as UFOs (Unidentified Falling Objects : dust ?)
Beam induced heating of injection kickers, collimators, beam screens, beam instrumentation, RF fingers, …
Electron cloud and dynamic pressure rise at very high bunch intensities

## Slide 23: Outline
Where do we come from
The present production at the LHC
The foreseeable LHC future
Beyond the LHC
A final message

## Slide 24: The predictable future: LHC time-line
~2021/22
2017 or 18
2013/14
2009
Start of LHC
Run 1: 7 TeV centre of mass energy, luminosity ramping up to few 1033 cm-2 s-1, few fb-1 delivered
2030
End of the LHC Era ? a Big Party !
Phase-II: High-luminosity LHC. New focussing magnets and CRAB cavities for very high luminosity with luminosity levelling
Injector and LHC Phase-I upgrades to go to ultimate luminosity
LHC shut-down to prepare machine for design energy and luminosity
Run 4: Collect data until > 3000 fb-1
Run 3: Ramp up luminosity to 2.2 x design, reaching ~100 fb-1 / year accumulate few hundred fb-1
Run 2: Ramp up luminosity to design (1034 cm-2 s-1), ~50 to 100 fb-1
By courtesy of R. Heuer CERN DG

## Slide 25: LS1 scope and schedule
10-15 % of interconnections to be opened and to be re-welded
100% (10’000) to be consolidated
  Repair defective interconnects
  Consolidate all interconnects with new design
  Finish off pressure release valves (DN200)
  Exchange magnets with non-conformities
  Repair He leaks (sectors 3-4 and 4-5)
  Maintenance of all the systems after 3 years operation
  Bring all necessary equipment up to the level needed for 7TeV/beam
Schedule is now consolidated, the countdown runs !

## Slide 26: 13 kA splice consolidation
Consolidated dipole magnets bus splice
Consolidated electrical insulation
Final validation test on a laboratory interconnect:
- 13 KA quench
- 20 kCycles
- Thermal cycles

## Slide 27: The diode stacks
August 2011 – anomalous resistance observed in diode circuits during provoked quenches (20…40 mW)
September 2011 – diode task-force activities launched
Q4-2011, Q1-2012 – extensive testing of dipole diode stacks
February 2012 – report at Chamonix 2012 that the behaviour observed in the LHC can be reproduced in most cases in the laboratory and is not critical: the dipole diode stack and interconnects appear sound for operation at 7 TeV.
Q2-2012 – extensive testing of quadrupole diode stacks
Q3-2012 – bus-bus interconnects in quadrupole diode stacks found under-designed
October 2012 – recommend consolidation in the whole LHC
RDiode-HS
RHS-bus
Rbus-bus

## Slide 28: Proposed consolidation
R BB Diode/Plate
R BB SSS/Plate
Room temperature test
  RBBdiode-plate ≈ 0.4 mW
  RBBSSS-plate ≤ 0.1 mW

## Slide 29: LS1 schedule (october 2012)
Courtesy of Katy Foraz, CERN
It is highly unlikely that the LHC will see beam in 2014 (politically corrected statement)

## Slide 30: Radiation to Electronics (R2E)
Operation in 2011 has identified most critical equipment
Mitigation measures integrated “on-the-fly” if and when possible
2011/201212 Xmas Break (and Technical Stops):
  Relocation of most critical elements
  Additional shielding of most critical areas
Aim for operation in 2012 is to dodge radiation issues (no limit to the performance)
LS1 (2013-2014): relocate & shield all critical areas
Beyond LS1: major action required for power converters and other electronics in the tunnel
x50

## Slide 31: From LS1 to LS2
Push the dipole field to the maximum practical value (6.5…6.8 TeV ?) that avoids extensive training and re-training (typically less than 100 quenches)
Accumulate physics at the new c.o.m. energy, 25 ns bunch spacing (efficient ?), without further changes (nominal operating parameters of the LHC)
Run flat-out for (say) 3 years at “nominal” luminosity, which we expect to largely exceed the 1034 cm-2 s-1 (by ≈ 30 % ?)

## Slide 32: LS2 (2018): Injector Upgrades
Connect Linac4 to PS Booster,
New PS Booster injection channel
Upgrade PS Booster 1.4  2.0 GeV
New Power Supplies, RF system etc.
Upgrade transfer lines & instrumentation
Upgrades the PS
Injection region for 2.0 GeV Injection
New/Upgraded RF systems
Upgrades to Feedbacks/Instrumentation
Upgrades to the SPS
Electron Cloud mitigation – strong feedback system, or coating of the vacuum system
Impedance reduction, improved feedbacks
Large-scale modification to the main RF system

## Slide 33: DS Upgrade: collimators & 11 T
11 T Nb3Sn
LS2 2017-2018: IR2 (ions)
LS3 2021-2022: IR1, IR5 (HL-LHC), P3, P7 ?
MB.B8R/L
MB.B11R/L
5.5 m Nb3Sn
5.5 m Nb3Sn
3 m Collim.
5.5 m Nb3Sn
5.5 m Nb3Sn
3 m Collim
11 m Nb3Sn
3 m Collim
LS2: 12 coldmass + 2 spares = 14 CM
LS3: 8 coldmass + 2 spares = 10 CM
Total 24 CM
LS2: 24 coldmass + 4 spares = 28 CM
LS3: 16 coldmass + 4 spares = 20 CM
Total 48 CM
∫BdL = 119.2 Tm @ Inom = 11.85 kA
in series with MB with 20 % margin

## Slide 34: 11 T DS models
Single aperture demonstrator (MBHSP1) tested at FNAL
CERN model manufacturing started
Design of twin aperture in progress
MBHSP1 at FNAL
First 11 T copper coil winding completed at CERN
Twin aperture

## Slide 35: From LS2 to LS3
Increase beam intensity from injectors
Run flat-out for (say) 3 years at “ultimate” luminosity, as dictated by (so far unknown) limits of beam intensity, stability, optics, and vacuum
Expect (typically) a factor 2 increase in peak luminosity, under increased heat and radiation loads
  Radiation induced faults (e.g. SEU)
  Beam losses (e.g. UFO’s)
  Ageing of equipment (e.g. magnet insulation)

## Slide 36: LHC luminosity expectations
Lumi plot from M. Lamont (CERN)
220 fb-1 by 2020
LHC target is 3000 fb-1
Upgrade needed by the 2020’s:
HL-LHC
delivered
planned

## Slide 37: High-Luminosity LHC: Goal
Implement a hardware configuration and a set of beam parameters that will allow to reach a peak luminosity of 5×1034 cm-2s-1 with levelling, and integrated luminosity of 250-300 fb-1 per year (10 times the present LHC)

## Slide 38: Scope of HL-LHC
Cryoplant for IR’s
Cryoplant for RF cavities
Crab cavities
collimation
IR quadrupoles
SC links
≈ 1 BCHF

## Slide 39: Nb3Sn knocks at the door
By courtesy of J. Parrell (OST)

## Slide 40: LARP HQ (120 mm- 13 T)
Nb3Sn has the potential to give a 50 % benefit in gradient (for the same aperture), or larger aperture (for the same gradient), at much increased temperature margin (factor 2 to 3)

## Slide 41: SC links
Repositioning the converters in the cavern
Removal of the converters from the cavern
HTS tapes
Round wires
By courtesy of A.Ballarino, CERN

## Slide 42: Role of crab cavities
RF crab cavities deflect head and tail in opposite directions so that the collision is effectively head-on and the luminosity is maximized
The same principle can be used for luminosity leveling using the crab cavities at variable angle
With crab cavity
Without crab cavity

## Slide 43: Outline
Where do we come from
The present production at the LHC
The foreseeable LHC future
Beyond the LHC
A final message

## Slide 44: Is there a physics beyond the LHC ?
Will the LHC serve the Decepticons to revive Megatron …
Or zap the conscience of Jed de Landa back to Maya time …
Or reveal that the Universe is a sentient being …
Or cause everybody to black-out and see a vision of the future ?
Amazing how much rubbish you can find on the web !!!

## Slide 45: HE-LHC Scope
“[…] a 33 TeV centre-of-mass energy proton–proton accelerator in the LHC tunnel […] and the need for new injectors, possibly with 1 TeV energy”. (The High-Energy Large Hadron Collider, CERN–2011–003, also EuCARD–Conf–2011–001)
Technicolor, Supersymmetry, Extra dimensions: “[…] the need to explore the high energy frontier will remain. We will always be able to make that case, today and tomorrow”. (Elements of a Physics Case for a High-Energy LHC, J.D. Wells, pp. 1-5, CERN–2011–003, 2011)
“A project on the scale and innovation level of the HE-LHC has a long preparation lead time”. (CERN Accelerator Strategy, S. Myers, pp. 6, CERN–2011–003, 2011)

## Slide 46: HE-LHC – (33 TeV cms)
2-GeV Booster
Linac4
SPS+,
1.3 TeV, 2030?
HE-LHC
2030?
By courtesy of R. Heuer

## Slide 47: HE-LHC magnet challenges
27 km of very high field, accelerator grade magnets
  40 mm bore, 20 T dipoles
  40 mm bore, 500 T/m arc quadrupoles
  50 mm bore, 400 T/m IR quadrupoles
7 km of pulsed accelerator magnets with low loss
  100 mm bore, 5 T dipoles
5.6 km of transfer lines, from a SPS+ to HE-LHC
Field swing and field quality
Mechanics, protection, powering and stray field in the constrained LHC tunnel space
Increased heat loads (e.g. a factor 20 on qSynchrotron)
Cost and material availability
Dismantle the LHC to make space for the new ring

## Slide 48: Technical superconductors
Chart: Applied Field (T)
| 0 | 5 | 15 | 20 | 25 | 30
YBCO: Parallel to tape plane, 4.2 K | 4144.6766 | 3507.9375 | 3148.3332 | 2909.0554 | 2090.4933 | 1888.9952
YBCO: Perpendicular to tape plane, 4.2 K | 4144.6766 | 1445.8386 | 975.0997 | 767.7508 | 655.6687 | 571.6114 | 526.7777 | 481.944 | 442.7183 | 428.1462 | 403.4904 | 386.6773 | 364.2626 | 341.8457 | 328.3952 | 319.4289 | 318.3073
2212: Round wire, 4.2 K | 1265.6716 | 1257.7114 | 1257.7114 | 1225.8706 | 1181.0945 | 1126.3682 | 1040.796 | 973.1343 | 929.3532 | 835.8209 | 780.0995 | 704.4776 | 623.8806 | 577.7114 | 529.3532 | 513.4328 | 509.4527 | 489.5522 | 469.6517 | 453.7313 | 435.8209 | 416.9154 | 398.01 | 380.0995 | 364.1791 | 347.2637 | 330.3483 | 315.4229 | 298.5075 | 282.5871 | 265.4726
Nb3Sn: High Energy Physics, 4.2 K | 1754.8557 | 1454.9349 | 1190.9814 | 1072.6374 | 957.7741 | 855.0933 | 757.6336 | 268.0143 | 190.8587 | 118.9241 | 65.5533 | 28.3097
Nb-Ti (LHC) 1.9 K | 1430 | 1195.7692 | 950.7692 | 703.4615 | 475.7692
Nb-Ti
Nb3Sn
HTS

## Slide 49: A really high field dipole
Engineering extrapolation is difficult, but does not seem impossible
May require a genetic mutation in the art of SC magnet design an construction
By courtesy of E. Todesco
Bcoil
Nb-Ti
Nb3Sn
HTS
x 2
x 3

## Slide 50: The big leap: a new tunnel !
Whichever the optimal solution,
a vigorous high field magnet R&D should start today
John Osborne (CERN), Caroline Waaijer (CERN)
The optimal dipole field could be lower (e.g. 16 T) than projected for a HE-LHC in the LHC tunnel (20 T)
Higher collision energy possible !

## Slide 51: Timeline
It seems awfully early to talk about the next machine, and yet we are already late if we wish to have continuity !

## Slide 52: Outline
Where do we come from
The present production at the LHC
The foreseeable LHC future
Beyond the LHC
A final message

## Slide 53: Drawing the line, today
The production of physics material at the LHC proceeds very well, and the physics case for a HL-LHC is strong
The ensuing demands for technology R&D are many, intellectually interesting, technically challenging, and urgent
  Just on magnets (my toy) we are looking at new materials (Nb3Sn, HTS), need a technology proof by 2015, production by 2020
  This will open a new portfolio of applications (laboratory, energy, medical)
HEP, and the LHC as its latest creation, is an ideal herald of innovation and advancement whose stewardship has an unbeatable record

## Slide 54: Have no fear in the future of HEP…
… and thank you for your attention !

## Slide 55: LHC twin-aperture dipole magnets
R. Perin
C. Wyss
L. Rossi
Concept perfected (design), demonstrated (models and prototypes) and realized on a large industrial scale

## Slide 56: The LHC superconducting magnet zoo
By courtesy of S. Russenschuck (CERN)

## Slide 57: Short Straight Sections
1994 – CEA short straight sections (SSS) prototypes reach CERN and are assembled in String-I
14 February 1996 – CNRS-CEA-CERN collaboration protocol signed for the procurement of 392 main quadrupoles and assembly in the LHC-SSS
2006 – production completed

## Slide 58: High luminosity insertion
LHC point 5

## Slide 59: Consolidation work in 2009

## Slide 60: 13 kA splice consolidation
Welds cutting with orbital cutting machine in place
Sleeve sliding
Bus bars machining
Shunts positioning and soldering
Kapton foil insulation along 250mm
Injection envelopes in place
Lower insulation cover insertion
Upper insulation cover insertion
Insulation covers Fixation
Resin injection into the envelopes
Spider insulation in place

## Slide 61: Target parameters for HL-LHC run
Efficiency is defined as the ratio between the annual luminosity target of 250 fb-1 over the potential luminosity that can be reached with an ideal cycle run time with no stop for 150 days: trun= tlev+tdec+tturn. The turnaround time after a beam dump is taken as 5 hours, tdecay is 3 h while tlev depends on the total beam current
baseline
SC Magnets
SC RF Cavities
SC Links
By courtesy of L. Rossi

## Slide 62: The critical zone: magnet changes, cryogenics +…
ATLAS
1. New Magnets in the IRs and interface to detectors; relocation of Power Supplies via use of SC links
2. Deep change also matching section:
Magnets, collimators and SC RF Crab Cavities
3. For collimation we need to change also this part, a new 11 T dipole
CMS
300 m x 4 +…  1.5 km long accelerator
In high radiation environment: 10…100 MGy

## Slide 63: The forms of Nb3Sn
0.7 mm, 108/127 stack RRP from Oxford OST
1 mm, 192 tubes PIT from Bruker EAS
Recent 23.4 T (1 GHz) NMR Magnet for spectroscopy built from Nb3Sn (and Nb-Ti).
15-20 tons/year produced for NMR and HF solenoids, and experimental MRI
ITER: 500 tons in 2010-2015, comparable to LHC!
HEP Nb3Sn:
  High Jc(1 T, 4.2K) = 3000 A/mm2
  Large filaments (50 µm)
  Cost is 5 to 10 times Nb-Ti
Notes: This is not a big problem for HL-LHC, requiring 20 tonnes of superconductors, however it is major
problem for HE-LHC ,requiring in total 3000 tonnes of superconductor, most than half in Nb3Sn.
To gauge these figures in the context, LHC has used 1200 tonnes of Nb-Ti, while ITER requires about 500
tonnes of Nb3Sn.

## Slide 64: 11 T DS models

## Slide 65: US-LARP: IR quadrupoles
SQ
SM
TQS
LR
LQS-4m
HQ
TQC

## Slide 66: SMC tests at CERN
By courtesy of J. Perez and M. Bajko
12.6 T

## Slide 67: SC Link tests
20 m flexible cryostat for prototype tests at CERN
Installation of a SC link cable in the 5 m flexible cryostat used for tests at Southampton university

## Slide 68: A sample from crab cavities R&D
Y. Yakovlev et al.
Compact cavities, small footprint
400 Mhz, 5 MV/cavity
Timing at fs level !

## Slide 69: A first shot for the HE-LHC
Notes: 20 T 33 Tev cm
16 T 26.5 TeV cm

## Slide 70: New materials – Bi-2212
DOE program 2009-11 in USA let to a factor 2 gain. We need another 50% and more uniformity, eliminating porosity and leakage
Round wire, isotropous and suitable for cabling!
HEP only users (good < 20K and for compact cable)
Big issue: very low strain resistance, brittle
Production ~ 0,
Cost ~ 5 times Nb3Sn (Ag stabilized)
By courtesy of L. Rossi

## Slide 71: New materials – YBCO
Tape of 0.1-0.2 mm x 4-10 mm : difficult for compact (>85%) cables
Current is EXCELLENT but anisotropy is an issue;
More than 90% of world effort on HTS are on YBCO! Synergy with the community
Cost : today is 10 times Nb3Sn, target is same price: components not expensive, process difficult to be industrialize at low cost
FP7 Eucard is developing EU YBCO
By courtesy of L. Rossi