## Slide 1: Lepton Colliders at the Energy Frontier
Mark Palmer and Tor Raubenheimer
Snowmass CPM
October 10-12, 2012

## Slide 2: Lepton Energy Frontier Collider Options
e+/e- storage ring
e+/e- linear collider with E < 1 TeV
e+/e- linear collider with E > 1 TeV
m+/m- collider
Also g-g option

## Slide 3: Electron-Positron Storage Rings
LEP2 nearly got to the Higgs
    Rings are relatively robust technology
Higher energy and luminosity designs have been suggested
    LEP3: 1e34 cm-2s-1 at 240 GeV in the LEP tunnel
    TLEP: 1e34 cm-2s-1 at 240 GeV in an 80 km new tunnel  upgrade to 80 TeV p-p collider (Blondel, et al, arXiv:1208.0504.)
Hard to get to much higher energies than 120 GeV
    Limited by SR power as:
Significant challenges
    Requires large energy bandwidth and difficult collective effects
    Installation with LHC would be difficult
    Optimization ongoing
B. Richter, Nucl. Instr. Meth. 136 (1976) 47-60

## Slide 4: Electron-Positron Storage Rings (cont.)
 | LEP2 | LEP3 | LEP3** | TLEP**
Beam Energy [GeV] | 104.5 | 120 | 120 | 175
Circumference [km] | 26.7 | 26.7 | 26.7 | 82.4
Beam current [mA] | 4 | 7.2 | 7.2 | 6.4
Number of bunches | 4 | 4 | 50 | 466
Bunch population [1010] | 57.5 | 100 | 8.0 | 2.36
Horizontal emittance [nm] | 48 | 25 | 4.3 | 1.03
Vertical emittance [nm] | 0.25 | 0.1 | 0.02 | 0.005
bx* [mm] | 1500 | 200 | 50 | 50
by* [mm] | 50 | 1 | 1 | 1
Hourglass factor | 0.98 | 0.67 | 0.76 | 0.80
SR power [MW] | 11 | 50 | 50 | 50
Bunch length [mm] | 16 | 2.3 | 1.5 | 1.3
Momentum acceptance [%] | 1.25 | 4.2 | 3.0 | 3.0
Beam-beam parameter / IP | 0.07 | 0.09 | 0.07 | 0.06
Luminosity [1034 cm-2s-1] | 0.0125 | 1.01 | 1.01 | 1.16

## Slide 5: Possible 80 km TLEP option (future upgrade to ~80 TeV p-p collider)

## Slide 6: Linear Colliders with E < 1 TeV
Lots of options
    ILC design is the most robust
    CLIC design also possible
    g-g collider options may be a lower cost approach
    Advanced accelerator concepts may be possible in far future
If ultimate goal is multi-TeV lepton collisions, probably should think about pursuing options with upgrade possibilities
    Cost of demonstrating technology can be challenging

## Slide 7: ILC Parameters
Centre-of-mass energy | Ecm | GeV | 250 | 350 | 500 |  | 1000
Beam energy | Ebeam | GeV | 125 | 175 | 250 |  | 500
Estimated AC power | PAC | MW | 128 | 142 | 162 |  | 300
Collision rate | frep | Hz | 5 | 5 | 5 |  | 4
Electron linac rate | flinac | Hz | 10 | 5 | 5 |  | 4
Number of bunches | nb |  | 1312 | 1312 | 1312 |  | 2450
Bunch separation | Dtb | ns | 554 | 554 | 554 |  | 366
Pulse current | Ibeam | mA | 5.8 | 5.8 | 5.79 |  | 7.6
RMS bunch length | σz | mm | 0.3 | 0.3 | 0.3 |  | 0.250
Electron polarisation | P- | % | 80 | 80 | 80 |  | 80
Positron polarisation | P+ | % | 30 | 30 | 30 |  | 20
Luminosity (inc. waist shift) | L | ×1034 cm-2s-1 | 0.75 | 1.0 | 1.8 |  | 3.6
Fraction of luminosity in top 1% | L0.01/L |  | 87.1% | 77.4% | 58.3% |  | 59.2%

## Slide 8: Superconducting Rf Cavities
ILC based on high gradient superconducting rf cavities
  Potential for still higher gradients from geometry or new materials
New Acceleration Techniques
Page 8
ILC cavities reaching 35 MV/m routinely
~75% of magnetic field limit
R&D towards new materials and geometries for higher gradients
  Materials with higher Hc and lower Rs: MgB2, NbN, Nb3Sn, …
  Multi-layer materials to reduce fields in bulk material
Yield of ILC 1.3 GHz cavities
From Grigory Eremeev SFR’09
50 MV/m  75 MV/m
Yield ’10 ~ ’12:
> 90% @ 25 MV/m
~ 80% @ 28 MV/m
~ 70% @ 35 MV/m

## Slide 9
CLIC layout at 500 GeV

## Slide 10: Potential Staged CLIC Parameters

## Slide 11: Gamma-Gamma Linear Collider Options
A Higgs factory might provide an entry for a ‘low-cost’ g-g linear collider and technology demonstration
    e-- e- cms energy of only ~160 GeV (g-g cms is roughly 80%)
    Eliminates large portion of ILC infrastructure (e+ source, damping rings, bunch compressors, …) and should save significant $
    Many options:
      SLC configuration with single 85 GeV linac
      Sapphire: 22 GeV recirculating linac in SLC-configuration
      Expandable dual 85 GeV e- linacs in classic LC configuration
R ~ 1 km
85 GeV SCRF linac
Pol. Rf gun
~3 km
Sapphire

## Slide 12: Linear Colliders with E > 1 TeV
ILC is ~ 50 km at 1 TeV
    Possible to consider higher gradient SCRF materials or PWFA boost
CLIC design is aimed at upgradable design  1.5 or 4 TeV
    Geographic gradient of 4x higher than ILC
Advanced acceleration options (plasma, dielectric)
    Plasma acceleration has made great progress however still huge challenges in beam quality and stability
    Extremely low charge dielectric-laser accelerators may provide only reasonable parameters in multi-TeV regime
    None of AARD options are close to being ready
Some plasma and dielectric options act as transformers taking high power beams  high energy beams
    Possible to develop upgrade options for ILC-like technology?

## Slide 13: Concept of Beam-Driven Plasma Linac
Concept for a 1 TeV plasma wakefield-based linear collider
  Use conventional Linear Collider concepts for main beam and drive beam generation and focusing and PWFA for acceleration
    Makes good use of PWFA R&D and 30 years of conventional rf R&D
  Concept illustrates focus of PWFA R&D program
    High efficiency
    Emittance pres.
    Positrons
  Allows study of cost-scales for further optimization of R&D

## Slide 14: Possible Linear Collider Parameters
Case | 0.5 TeV ILC | 3 TeV CLIC | 10 TeV Dielectric Beam Acc. | 10 TeV Plasma Accelerator | 10 TeV Dielectric Laser Acc.
Energy per beam (TeV) | 0.25 | 1.5 | 5 | 5 | 5
Luminosity (1034 cm−2s−1) | 2 | 6.4 | 49 | 71.4 | 105
Electrons per bunch (×109) | 20 | 3.7 | 4 | 4 | 0.002
Rep. rate (Hz) / number / train | 5 / 1312 | 50 / 312 | 50 / 416 | 17,000 / 1 | 25,000,000 / 1
Horizontal emittance gεx (nm-rad) | 10,000 | 660 | 1000 | 200 | 0.1
Vertical emittance gεy (nm-rad) | 30 | 20 | 10 | 200 | 0.1
b* x/y (mm) | 11 / 0.2 | 4 / 0.1 | 10 / 0.1 | 0.2 | 0.4
Horizontal beam size at IP σ*x (nm) | 474 | 49 | 32 | 2 | 0.06
Vertical beam size at IP σ*y (nm) | 3.8 | 1.0 | 0.3 | 2 | 0.06
Luminosity enhancement factor | 1.6 | 1.9 | 1.9 | 1.35 | 6.05
Bunch length σz (μm) | 300 | 50 | 20 | 1 | 335
Beamstrahlung parameter ϒ | 0.07 | 6.7 | 56 | 8980 | 0.4
Beamstrahlung photons per electron nγ | 1.7 | 1.5 | 1.4 | 3.67 | 0.5
Beamstrahlung energy loss δE (%) | 4.3 | 33 | 37 | 48 | 4.3
Accelerating gradient (GV/m) | 0.031 | 0.1 | 0.5 | 10 | 0.5
Average beam power (MW) | 5.3 | 13.9 | 55 | 54 | 38
Wall plug power (MW) | 200 | 568 | ~1200 | ~1200 | ~550
One linac length (km) | 15.5 | 23.5 | 10 | 1.0 | 10.5
ILC and CLIC parameters from design reports; 10 TeV DBA scaled from Wei Gai communication; 10 TeV DLA and Plasma Accelerator from 2010 ICUIL/ICFA Workshop

## Slide 15: Muon Collider
Compact facility accelerating muons with recirculating linacs and rings
Major Challenges
Muon generation
Cooling of muons
Cost-efficient acceleration
Collider ring and backgrounds from decays
Being studied as part of MAP & proposed Lepton
Collider Physics Framework
For 3 TeV

## Slide 16: Muon Collider Parameters
Depends on cooling scenario:
1031a~1032 cm-2sec-1
PWall < 300 MW
s-channel: factor
of ~4×104 in rate

## Slide 17: Steps Toward a Muon Collider
Project-X is being designed to deliver 4 MW of 8 GeV
Muon test facility would demonstrate capture and 1st cooling
NEUTRINO FACTORY
MUON COLLIDER
Share same complex
n Factory Goal: O(1021) m/year
within the accelerator
acceptance
NEUTRINO FACTORY

## Slide 18: Summary
Many options for next-generation lepton colliders
Storage rings can access Higgs but limited in energy reach
ILC-technology is essentially ready for construction
    Important to understand upgrade options
CLIC/NCRF technology might provide an alternate approach with different upgrade possibilities and technology risks
Advanced accelerator concepts not ready but may provide path to future upgrades for LC concepts
Muon collider synergistic with US Intensity Frontier program and may provide path to future Energy Frontier