## Slide 1: Welcome & Introduction
Michael Allitt
STS Accelerator Systems Manager
25D50 Pulsed Dipole Preliminary Design Review
March 6, 2023

## Slide 2: Outline
Second Target Station (STS) Project
Relevant STS Accelerator Systems scope
RTST design overview
Review objectives

## Slide 3: Second Target Station Project
 = 5 Å
SNS-STS
ESS (5 MW)
ESS (2 MW)
J-PARC
SNS-FTS (2 MW)
CSNS
SNS-FTS
ISIS TS2
ISIS TS1
HFIR
ILL
FRM-II
NIST
SONATE (est.)
PSI
ORPHEE
LUJAN
short-pulse
long-pulse
steady-state
USA
Asia
Europe
Planned
Existing
Optimized for cold neutrons
World-leading peak brightness
Provide new science capabilities for measurements across broader ranges of time and length scales, real-time, and smaller samples

## Slide 4: SNS Accelerator Systems – Future State
Second Target Station
700kW average power
15 pulses/sec
Rotating tungsten target
Optimized for cold neutrons
First Target Station
2 MW average power
45 pulses/sec
Liquid Hg target
Optimized for thermal neutrons
Linac
H- ions
1 msec macro-pulses @ 60Hz
1 GeV max energy(today)
1.4 MW max power (today)
1.3 GeV max energy (post-PPU)
2.8 MW max power (post-PPU)
Accumulator ring
Strip electrons from H- ions to create protons
Stack mini-pulses to shorten pulse and increase intensity
Length of extracted pulse < 1 µs
Extraction @ 60 Hz
……..
16.67 ms
1 ms
700 ns
300 ns
Mini-pulse structure
Macro-pulse train

## Slide 5: Relevant STS Accelerator Systems (AS) Scope
Ring To Second Target (RTST) beamline to transport protons from an extraction point in existing Ring to Target Beam Transport (RTBT) line to the Second Target
RTST requirements:
Beam loss < 1 W/m
Meet Target Systems requirements for proton distribution
No impact on first target beam

## Slide 6: RTST Design Approach
RTBT Activation Levels
RTBT beamline has good reliability and tunnel has low activation (beam loss well below 1 W/m), so re-use the design
  Similar FODO lattice
  Large (21cm) aperture
Where possible, use existing magnet & diagnostic designs, base vacuum and cooling designs on existing systems
  Maintain compatibility with existing systems
  Incorporate lessons learned where applicable

## Slide 7: RTST design based on RTBT
Extraction region
RTBT
From ring
To First Target Station
Second Target Station
STS Magnet Type | Quantity
Pulsed Dipole 25D50 | 4
Large Quadrupole 40Q70 | 1
Dipole 17D120 | 15
Quadrupole 21Q40 | 56
Dipole Corrector 27CD30 | 24
RTST length 231.9m
RTST

## Slide 8: Extraction region
Beam Deflection
PD01
QH08
PD02
PD03
PD04
QV09
PD01
PD02
PD03
QV09
QH08
PD4
QH10
QV11
RTST
RTBT
RTBT
One design of pulsed dipole used for all 4 positions

## Slide 9: Extraction Magnet Acquisition Strategy
FNAL are designing 25D50 pulsed dipole & 40Q70 large aperture quadrupole
FNAL have also generated a magnetic design for 21Q40N narrow quadrupole
Designs are on schedule; Final Design completion for 25D50 and 40Q70 expected March 2024
25D50 proof-of-principle unit expected to be available in 2025
Remaining 3 x 25D50 units will be ordered after CD-3A approved (expected September 2024)
40Q70 proof-of-principle unit expected to be available 2026
STS will outsource completion of the 21Q40N design to a commercial vendor, including fabrication & test of a proof-of-principle unit
25D50 pulsed dipole
40Q70 quadrupole

## Slide 10: Review Objectives
Evaluate preliminary design:
  Does it meet the requirements?
  What is the risk (if any) of proceeding with detailed engineering design?
  Any opportunities for improvement / cost reduction?
Presentations & approved meeting minutes will form the preliminary design report

## Slide 11: Questions?