## Slide 1: Results From Particle Tracking Studies
Andrei Shishlo
Accelerator Physicist, AS Group
25D50 Pulsed Dipole Preliminary Design Review
March 6th, 2022

## Slide 2: Outline
RTST Beam Line
Extraction Region RTBT-to-RTST
3D Fields in PyORBIT Code
Tracking Results
Conclusions

## Slide 3: RTST Beam Line
RTST beam line includes mostly the same magnets as the existing RTBT line to FTS
RTBT-to-RTST extraction magnet system is a part that is most different from existing RTBT line
RTBT-to-RTST Extraction Region

## Slide 4: Roles of Pulsed Dipoles in RTBT-to-RTST Beam Extraction
PD4
PD3
QV09
QH10
1.473 m
Pulsed dipoles have the major role in the beam extraction to RTST

## Slide 5: Injection Scheme: 3D Tracking Region
RTBT:QV07
RTBT:QH08
RTBT:QV09
RTBT:QH10
Kicker#1
Kicker#2
Kicker#3
Kicker#4
3D Direct Tracking Region
Initial particle tracking were performed by using idealized quad and pulsed dipoles in PyORBIT code
To test the beam optics with realistic magnetic field distribution we need 3D tracking.
The start point of tracking is the beginning of QV07, and the last point is the end of QH10 magnet in RTBT line
The real magnetic fields of dipole kickers are overlapping with quads, so we cannot use any conventional particle tracking codes
Beam to 1st Target
Beam to 2nd Target

## Slide 6: Magnetic Field along Center Trajectory
Hard edge (ideal) models for quads and dipole kickers
FNAL 3D map field for dipole kickers
Quads and kickers fields are overlapping
FNAL 3D map fields for dipole kickers and RTBT:QV09

## Slide 7: Tracking Results for Trajectory of Beam Center
Difference in traditional and RK4 tracking was .3 mm on top of 534 mm deviation
FNAL 3D map fields for dipole kickers and a big aperture quad (RTBT:QV09)

## Slide 8: RMS Sizes in RTBT Extraction Region
We have difference in the vertical beam sizes – about 1.1 mm on top of 7.5 mm RMS
Reason for that could be a bigger vertical size inside RTBT:QV09 (vertically focusing quad)
The effect on downstream tracking should be estimated

## Slide 9: RTST Tracking the Bunch after 3D Extraction Tracking
RMS Sizes:
Good agreement
About 1 mm diff. for Vertical RMS size on ST
Horizontal Dispersion:
Not so good agreement
As a result, we see losses: 3*10-4
This could be improved by slight retuning of RTST optics
Horizontal
Horizontal
Vertical
Vertical

## Slide 10: RTST Tracking the Bunch after 3D Extraction Tracking 2021.03.28 Quad Power Supplies Redistributed
Horizontal
Horizontal
Vertical
Vertical
The quads at the 1st arc were provided with separate power supplies
The horizontal dispersion was tuned to less than 4 mm
2,000,000 macro-particles no beam loss

## Slide 11: 3D Fields Comparisons – Separate and Combined (for Q+3Kickers)
Kickers’ field should be increased by
RTBT_Mag:HKick08:1 -> +2.5%
RTBT_Mag:HKick08:2 -> +2.0%
The final trajectory is 22 mm to the right (on top of 534 mm), and angle is103 mrad instead of 108.3 mrad.

## Slide 12: RTBT to RTST Sizes
Sizes are as before.
It is possible to correct all angles in distribution and use particles as injected to RTST.

## Slide 13: RMS Beam Sizes in RTBT 1-2
Vertical
Horizontal
Usage of 3D map introduces some deviations in the vertical beam sizes after RTBT:QV09
We can use several quads after QV09 to restore the design sizes in RTBT
Theory says that it could be done with only 4 quads, but we have limitations on a maximal quad fields, so we used 6 quads.

## Slide 14: RTBT Quad Fields Change and Final Sizes after Fitting
RTBT_Mag:QH10 fields (initial,fitted) G[T/m] = ( +5.8755 , +5.8740) change [%] = +0.03
RTBT_Mag:QV11 fields (initial,fitted) G[T/m] = ( -5.6131 , -5.4325) change [%] = +3.22
RTBT_Mag:QH12 fields (initial,fitted) G[T/m] = ( +4.2686 , +4.3039) change [%] = -0.83
RTBT_Mag:QV13 fields (initial,fitted) G[T/m] = ( -3.7275 , -3.8297) change [%] = -2.74
RTBT_Mag:QH14 fields (initial,fitted) G[T/m] = ( +2.8732 , +2.9125) change [%] = -1.37
RTBT_Mag:QV15 fields (initial,fitted) G[T/m] = ( -2.7618 , -2.7675) change [%] = -0.21
After small tweaking of fields for 6 quads we restored beam sizes in the rest of RTBT.
No beam loss was seen for 2,000,000 macro-particles tracking.

## Slide 15: Conclusions
Particles tracking with FNAL 3D maps for Dipole Kickers and the big aperture quad (RTBT:QV09) did not created any surprises
With minimal correction to field integrals for the dipole kickers we reproduced the extraction trajectories and RMS beam sizes
Using realistic 3D magnetic fields with magnet interaction effects can give small losses caused by increased dispersion which is correctable with RTST quads
Changes in RTBT optics to the First Target Station are minimal and correctable
Now PyORBIT has a Particle Tracking Module for 3D Fields

## Slide 16: Backup

## Slide 17: Software Class Structure for Magnetic Field Sources
BaseFieldSource Class
(E,B) = F(r,t)
FieldSourceContainer Class
Container for set of BaseFiledSorces
DipoleFieldSource Class
B = const
QuadFieldSource Class
Bx = G*y
By = G*x
3D FieldSource Class
3D Map of B(x,y,z)
Shifted FieldSource Class
Has coordinate transformation
4x4 matrix
Container
System
Field Source
#1
Field Source
#1
Field Source
#2
Field Source
#3
Each field source has its own internal coordinate system
PyORBIT Code

## Slide 18: Tracker: Runge-Kutta 4th Order Differential Equation Solver
Tracker solves Lorentz equation of motion for a relativistic particle using the field source container
User must specify
  a desired accuracy and initial number of integration steps
  The entrance and exit planes as equation
Slow. About 100 times slower than our usual matrix like Hamiltonian tracker
Lorentz Equation

## Slide 19: FNAL Design: Pulsed Dipole + Large Aperture Quad

## Slide 20: Used Field Sources – Dipole Kicker
Ideal quads and 3D Map from FNAL for large aperture quad
Ideal dipole and 3D map dipole with a field map from FNAL
FNAL Dipole Map was defined only for y > 0 and z >0 region of space. The symmetric considerations were used for other regions
z > 0
z < 0
x > 0
y > 0
x < 0
y > 0
x < 0
y < 0
x > 0
y < 0
x > 0
y > 0
x < 0
y > 0
x < 0
y < 0
x > 0
y < 0
8 regions – for 6 we used symmetric transformations

## Slide 21: Symmetric Transformation Verifications
Fields in all quadrants demonstrated the correct symmetry (as expected).

## Slide 22: 3D Field Map and Symmetry for Quad
Bx
By
Bz
Z = 0.5 m
Z = 0. m
Z = -0.5 m