## Slide 1
Nino Chelidze
Friday, March 17, 2023
One West
9am Meeting

## Slide 2: Current Status of the Machines
Linac
Linac Tank 5 vacuum spiked again Thursday morning
Linac techs and crew worked on it all day
Vacuum holds ok when the water skid is off
Will leave the water off and wait overnight for the ice dam to form again
Next plan F is to use NTF water skid to run colder water through the system. This will be a slower flow and an isolated system. Linac and MSD personnel gathering material to try this plan (hopefully today)
MTA
Commissioned beam Tuesday and Wednesday – congrats!
Standing by before beam returns to Linac
Booster
Is doing well, standing by and waiting for beam

## Slide 3: Current Status of the Machines
MI/RR
RAW system in MI abort
Thursday evening it was noticed that MI abort LCW lost water. This is the RAW skid in the abort room. Turning the pump off didn’t stop the leak. Ops accessed and valved out the pump that was leaking after rad safety approval
The water stayed stagnant after valving out
System was left in the safe state. No danger of overflowing the containment.
Will be switching to a spare pump tomorrow
  Rad safety and fluids group – meet up after 9am
Groundwater between 403 and 324
A lot of water was found in 403 and upstream. After a walkthrough the pump by 324 was found dead. Verified with FIRUS alarms as well.
Duty mechanic (and then Duty Electrician) were notified
  Re-group – after 9am
Miscellaneous work
Orange hose in 336 has a bubble and needs work
  Go around the ring to see if there are any other leaks? – No need as we do not see any significant water loss anywhere in the system

## Slide 4: Current Status of the Machines
BNB Water Leak
BNB has a water leak supposedly in target pile
Fist they isolated MI water from BNB water
Starting Wednesday, they are trying to isolate individual loops to localize the leak
Accessed on Wednesday, today and will access again on Monday (March 20)
After valve manipulation ops rack back in standing by for beam
Muon/SY
Remnant system resistivity low
Muon managed to bring things back up and ran beam on Wednesday through Thursday morning
Last update from Sue was that it would reach 4 by the mid-late afternoon today (Friday)
Waiting for CUB sample result to regenerate column II which will help
Enclosure C pump changeout – not known to personnel, will wait for another time

## Slide 5: Current Status of the Machines
Other outstanding work (can possibly be done today)
MI-10 PS leaking water. Latest repair estimate is 2 hours.
C4 pumphouse – power down the building to do pump maintenance (affects fire suppression system)
BNB water leak – Accessed MI12 on Monday to close off a few valves – observing the leak rate change
MS2 LCW system off – fluids group need to confirm the leak(s) are repaired
Proton studies March 22 – not clear – experiment changeover
MINOS electrical panel work
F sector vacuum work – should start today