## Slide 1
Katsuya Yonehara
4/11/2023
HEP Roadmap, HPT
Beam Instrumentations

## Slide 2: Object of HEP Radiation Hardened Beam Instrumentation for High Power Target facilities
Proton facility
  Multi-Mega Watt beam operation for future beam facilities
Neutrino facility
  Multi-MW target health sensor and secondary beam monitor
Muon facility
  1-MW target health sensor and secondary beam monitor
  Maintain 4-MW target system and secondary beam monitor for muon collider
Electron facility (slightly off topic)
  Monitor intense and ultra fast electron beam in plasma and dielectric wakefield accelerators and FEL beam facilities

## Slide 3: Existing facility and radiation
Institution | Beam energy | Beam intensity | Beam power | Radiation dose at beam instrumentations
CERN CNGS | 400 GeV | 2.4e13 protons per pulse | 500 kW | 
CERN LHC | 7 TeV | 1.2e11 protons per bunch, 2808 bunches per beam | 362 MJ per beam | 
Fermilab NuMI | 120 GeV | 5.5e13 (6.5e13) per 1.2 sec | 870 kW (1 MW) | 1010 mSv/hr at target 104 mSv/hr at muon monitor
Fermilab LBNF | 60-120 GeV |  | 1.2-2.4 MW | 
J-PARC neutrino | 30 GeV | 3.2e14 protons per 2.48 sec (1.32 sec) | Present 515 kW (700 kW-1.3 MW) | 
ESS | 2 GeV |  | 4 MW | 
J-PARC MLF | 3 GeV | (4.5e8 pulses, 25 Hz) | 730 kW (1 MW) | 30 MGy/6 y
SNS | 1 GeV (1.3 GeV) | 1.5e14 per beam | 1.4 MW (2 MW) | 
FRIB | 200 MeV/nucleon |  | 400 kW | 109 mrem/hr
https://arxiv.org/abs/2203.06024
Blue font: Not operational
Orange font: Nuclear beam facility

## Slide 4: Identified Beam Instrumentations (I)
Item | Reported radiation hardness in the workshop | Possible R&D institutions
Light optics | SNS single-mode fiber sensors: >4108 Gy SNS epoxy (Stycast 2850FT with Catalyst 11): > 108 Gy FRIB viewport: Zinc selenide, no detectable RIA @430 Gy FRIB metal mirror: typically 108 Gy MLF Ni: 1MWh and found corrosion MLF Au: More accumulate than Ni but found no corrosion CERN rad hard fiber: FIGR-10, tested RIA @694 kGy by using 60Co (activity is currently stopped) | Various institutions
ASIC | FNAL CMS ECON-T: demonstrated up to 500 Mrad CERN luminosity monitor FBCM: design goal 250 Mrad & 3.5e15 1 MeV neq. Fluence; tested 10 Mrad | CERN, Fermilab
Camera | CERN camera: SYRA camera tested @10 Mrad (100 kGy) CERN Micro-Cameras & Space Exploration SA: tested @11.7 krad & 36 krad J-PARC neutrino: OTR CID camera operated 1 kGy/year for 750 kW beam power | Various institutions
https://arxiv.org/abs/2203.06024

## Slide 5: Identified Beam Instrumentations (II)
Item | Reported radiation hardness in the workshop | Possible R&D institutions
Strain detector | Described in light optics | ESS, J-PARC, SNS
Acoustic sensor | MLF dynamic mic: tested > 4000 MWh | ESS, J-PARC, SNS
Laser Doppler Vibrometer | MLF tested total 5000 MWh, total dose 5000 Gy | Fermilab, J-PARC
Luminescence beam profile | SNS Cr:Al2O3: 100 MW, ~0.1 DPA | SNS
IR monitor | Described in light optics | Various institutions
Thermocouple sensor | Extremely radiation robust, no specific dose reported | Various institutions
Optical Transition Radiation | Described in light optics | Various institutions
Beam Induced Fluorescence | Described in light optics | J-PARC, Fermilab
Secondary Electron emission Monitor | ESS APTM: design goal 4 kGy/h, lifetime > 2 years ESS GRID: design goal 4 kGy/h, 5 DPA/year | Various institutions
Beam Loss Monitor | CERN BLMASIC: > 100 kGy (10 Mrad) | CERN, Fermilab
Electron Multiplier Tube | J-PARC 100 days at 1.3 MW | J-PARC, Fermilab
Gas-filled RF | FNAL 3 yrs test at MI abort line, no signal degradation found | Fermilab
Current Transformer | No specific report in the workshop | J-PARC, Fermilab
https://arxiv.org/abs/2203.06024

## Slide 6: Timeline for major HEP facility beam upgrade plan
USA
  Fermilab: LBNF (2030-), AMF (2045-)
Europe
  CERN: HL-LHC (2026-2041), Muon collider (2045-)
  ESS (2023-): ESSnuSB
Asia
  J-PARC: Hyper-K (2027-), g-2/EDM, COMET
  CSNS: MELODY
R&D of rad hard beam instrumentations should start asap to follow the future HEP roadmap

## Slide 7: Strategic plan (I)
We need to represent our demand to the global communities of beam detectors and beam instrumentation across various beam facilities and companies in the world
  Collider community
    CERN, Fermilab
  Beam instrumentation community
    All beam facilities
  Nuclear physics community
    SNS, ESS, MLF, FRIB, etc

## Slide 8: Strategic plan (II)
Challenge common issue
  Rad hard light optics and visualization device can be a breakthrough technology for directly monitor the target health
    Nuclear physics and collider communities have developed a rad tolerant glass, fiber, and camera
  Rad hard ASIC will improve S/N and fast signal manipulation
    Collider community has developed a rad tolerant beam loss monitor and luminosity detector
  Find new beam detector technology
    Neutrino community has developed a new type of secondary particle detectors
  Develop existing beam detector technology

## Slide 9: Strategic plan (III)
Object of the project
  What is the object?
    Only for the HPT project (e.g. Neutrino and Muon facilities)?
    Or involve more items (e.g. Collider and Nuclear physics facilities)?
Organization
  Budget?
    Where can we get support?
    When?
    How much?
  Size of the project?
    National facility
    University