## Slide 1: TMS Magnet: Flux Density and Magnetic Force Analysis
Lei Xia
ANL - HEP
Work Performed By: VIC GUARINO, RICK FISCHER, SCOTT POREMBA, JEFF WHITE, GUOSHENG YE, ALEENA RAFIQUE, ZELIMIR DJURCIC, LEI XIA

## Slide 2: TMS introduction
TMS is a magnetized range stack that has 100 layers
  40 thin (15mm) steel layers in the front, 40mm air gap between plates
  60 thick (40mm) steel layers in the back, 40mm air gap between plates
  Each layer consists of three plates: middle + 2 sides
  All layers are inter-connected by spacer bolts and lean on the support tubes at the back end
  Active area is between the top and bottom coils
Front view
Side view

## Slide 3: Conceptual Coil Design
Two ‘belts’ of coils in a ‘Helmholtz’ configuration for each role of plates + scintillators
  Reasonably uniform field between coils (active area)
Field inside as large as possible, field outside as small as possible
  The magnetic field configuration is a dipole inside the coils
  Sextupole outside the coils: Its dipole cancelled out and quadruple partially cancelled

## Slide 4: Overview of analysis I
Finite element method, as implemented by ANSYS R19.2, was used throughout this analysis
  Full feature structural analysis program with modest low frequency electromagnet (EMAG) capabilities
Analysis steps
  An EMAG model was constructed with APDL script: steel plates/stack, coils, air gap, exterior air volume (large enough to approximate open boundary)
  EMAG model was converted to a structure model: allow direct application of the magnetic forces from the EMAG solutions to the structure model
  A linear static structural analysis was then performed to determine plate deflections
  Lastly, a pre-stressed eigenvalue buckling analysis was performed
Solid Geometry for the Magnetic Simulation
Electromagnetic Finite Element Model
Structural Finite Element Model

## Slide 5: Overview of analysis II
Steel plate material: hot rolled AISI 1006 steel (‘MINOS’ steel)
Over 20 design versions were looked at: this report is mostly from the latest configuration
Several design optimizations were performed, based on structural analysis
Saturation Curve
Mechanical Properties

## Slide 6: Electromagnetic Analysis: Total Field B
Summed Magnetic Flux Density in the stack
Front View
Back View

## Slide 7: Electromagnetic Analysis: Total Field B, Row 20
Summed Magnetic Flux Density in Row 20 (middle of thin/15mm plates)
Bsum(T)
Vector field

## Slide 8: Electromagnetic Analysis: Total Field B, Row 70
Summed Magnetic Flux Density in Row 70 (middle of thick/40mm plates)
Bsum(T)
Vector field

## Slide 9: Electromagnetic Analysis: Field Components Bx,y,z(z)
Bx,y,z(z) are plotted for the entire stack (100 layers) at 9 (x, y) locations
  1,2,3: along vertical center line of middle plates
  4,5,6: along vertical center line of side plates
  7,8,9: along vertical quarter line of middle plates
Path locations

## Slide 10: Electromagnetic Analysis: Field Components Bx,y,z(z)
Bx,y,z(z) along path 1,2,3: on vertical center line of middle plates
Bx,y,z(z)

## Slide 11: Electromagnetic Analysis: Field Components Bx,y,z(z)
Bx,y,z(z) along path 4,5,6: on vertical center line of side plates
Bx,y,z(z)

## Slide 12: Electromagnetic Analysis: Field Components Bx,y,z(z)
Bx,y,z(z) along path 7,8,9: on vertical quarter line of middle plates
Bx,y,z(z)

## Slide 13: Second Analysis: ANSYS Maxwell
A second analysis was performed using ANSYS Maxwell, to validate the ANSYS EMAG/APDL analysis
  The two analysis are consistent with each other
  The two shows ~10% Bvertical differences  indicate the level of analysis uncertainty
  Some of the comparisons are shown in the next few slides

## Slide 14: EMAG/APDL vs. Maxwell: Path 6

## Slide 15: EMAG/APDL vs. Maxwell: Path 7

## Slide 16: EMAG/APDL vs. Maxwell: Path 9
Line shape looks very similar, absolute value has a small shift

## Slide 17: EMAG/APDL vs. Maxwell: Bsum, row 20

## Slide 18: Recent Maxwell Analysis: Field Component By(y), Row 20
By(Y) along path 1-1,2,3
Average and S.D. are calculated in the region between the coils
Path 1-1 Path 1-2 Path 1-3
By Row 20
By(y)
x=0.911m x=4.135m

## Slide 19: EMAG/APDL vs. Maxwell: Bsum, row 70

## Slide 20: Recent Maxwell Analysis: Field Component By(y), Row 70
Path 3-1 Path 3-2 Path 3-3
By(Y) along path 3-1,2,3
Average and S.D. are calculated in the region between the coils
By Row 70
By(y)
x=0.911m x=4.135m

## Slide 21: Structural Analysis: magnetic force on steel plates
Magnetic forces are summed on each of the steel plates

## Slide 22: Structural Analysis: optimizing spacer bolt positions for side plates (I)
First look at plate deflection using a 25 plate model with spacer bolt on row 25 fixed in the Z direction
Deflection of ‘original design’ (spacer bolts at ~203mm from edge od coil notch)
  Largest deflection >= 12mm (way too much)

## Slide 23: Structural Analysis: optimizing spacer bolt positions for side plates (II)
Optimization study on spacer bolt position performed
Spacer bolts were moved to 150mm from the coil notch edge: ~1mm deflection

## Slide 24: Structural Analysis: optimizing support tube positions for side plates (I)
Optimization study on support tube positions performed to minimize side plate deflection in the 100-layer stack
‘Original’ positions result in large deflection in the last plate: > 2mm

## Slide 25: Structural Analysis: optimizing support tube positions for side plates (II)
‘New’ positions gives smaller deflection everywhere in the stack: < 1mm

## Slide 26: Structural Analysis: optimizing spacer bolt positions for middle plates (I)
Optimization study on spacer bolt positions for middle plates were performed too
Two spacer bolts were moved to reduce overall deflection in the 100-layer stack

## Slide 27: Structural Analysis: optimizing spacer bolt positions for middle plates (II)
Original locations: max deflection ~1.7mm

## Slide 28: Structural Analysis: optimizing spacer bolt positions for middle plates (III)
Modified locations: max deflection ~0.6mm

## Slide 29: Buckling Analysis: Side Plates (I)
The solutions from the magnetic analysis was used as a pre-stress for the bucking analysis for the side plates, which extracted the first 3 bucking loads
First buckling mode is shown here: load factor = 27.7

## Slide 30: Buckling Analysis: Side Plates (II)
Second buckling mode is shown here: load factor = 30.1

## Slide 31: Buckling Analysis: Side Plates (III)
Third buckling mode is shown here: load factor = 31.3

## Slide 32: Buckling Analysis: Middle Plates (I)
Similar bucking analysis was performed for the middle plates
First buckling mode is shown here: load factor = 44.7

## Slide 33: Buckling Analysis: Middle Plates (II)
Second buckling mode is shown here: load factor = 49.1

## Slide 34: Buckling Analysis: Middle Plates (III)
Second buckling mode is shown here: load factor = 49.6

## Slide 35: Conclusions
Magnetic analysis of the TMS coil/stack design is performed with ANSYS EMAG/APDL, verified with ANSYS Maxwell
The magnetic flux density magnitude at the center of the plates is at least ~0.9 Tesla in EMAG/APDL (~1.0 Tesla in Maxwell), uncertainty is at the level of 10%
The magnetic flux density in the area of the plates between the coils acts in a vertical direction
Out of plane plate deflections are sufficiently small so as not interfere with the fit or function of the scintillator modules
The range stack is structurally stable