## Slide 1: Dopant R&D in LArTPCs
Raisa Tasnim Raofa
Neutrino Division, Fermilab
Advisors: Joseph Zennamo & Fernanda Psihas (Fermilab)
Report No: FERMILAB-SLIDES-23-111-ND

## Slide 2: LArTPC (Liquid Argon Time Projection Chamber)
An incoming charged particle ionizes Ar producing Ar ions & ionization electrons
Trajectory is measured by ionization charge and time is measured through scintillation light
Created by: Fernanda Psihas
Fernanda Psihas
Notes: If we have to calculate only based on charge, ½ the info is lost
So light is an important aspect and need to collect more light info
Sufficient ratio for physics in GeV scale
Unable to do physics in MeV scale
Liquid Argon – noble gas
Add the black diagram Fernanda sent in case animation does not work
Your talk going well is about practicing, but it is also about discipline. Stick to what I practiced.
Wordings:
Allow people time to think
Try to say in few words as possible.
You have TPC filled with liquid argon.

## Slide 3: Event Display in LArTPC
Fig: Simulation of 10 GeV electron neutrino
Event display shows collected ionization charges
Energy reconstruction relies on collected charge
Very small signals for low energy events
Joseph Zennamo
Number of Wires
Time [2 ms]
Color scale: Number of charge collected
Notes: If we have to calculate only based on charge, ½ the info is lost
So light is an important aspect and need to collect more light info
Sufficient ratio for physics in GeV scale
Unable to do physics in MeV scale
Change the
Overall trajectory and topology depends on the charge
Instead use Joseph’s Pure one 10 GeV -> Find any of the smaller dots and say what MeV events will look like.
Event Display
Gets trajectory information -> by collecting number of charges collected on large number of channels (each wire is a channel). More trajectory info -> better energy information. Longer path -> estimate the energy based on the trajectory.
Small energies only falls on a handful of channels. Only depends on the charge not the trajectory.
Event Display:
  Relies on the charge collected

## Slide 4: Charge & Light Collection in LArTPCs
In LArTPC, ratio of charge and light is 50:50
Sum of charge and light is constant
  Charge + Light = Constant
~50% of information lost for low light collection efficiency
Notes: Apart from the charge, we also have light
If we have to calculate only based on charge, ½ the info is lost
So light is an important aspect and need to collect more light info
Sufficient ratio for physics in GeV scale
Unable to do physics in MeV scale

## Slide 5: Light Collection for Energy Measurements
Using light and charge information can yield more accurate energy information
1% energy resolution requires collection of ~15000 photons/MeV
LArTPCs currently collects ~160 photons/MeV
Notes: If we have to calculate only based on charge, ½ the info is lost
So light is an important aspect and need to collect more light info
Sufficient ratio for physics in GeV scale
Talk about the plot
Unable to do physics in MeV scale
No light for small points-> we can do 5% Energy Resolution at 1 MeV.
If we want to measure 1% -> need better light collection efficiency -> requires 15000 photons. But we cannot collect that many.

## Slide 6: Now what?
Photosensitive dopants saves the day!
  Convert light to charge
Notes: If we have to calculate only based on charge, ½ the info is lost
So light is an important aspect and need to collect more light info
Sufficient ratio for physics in GeV scale
Talk about the plot
Unable to do physics in MeV scale

## Slide 7: Past Photosensitive Dopant Test Stand
ICARUS used Tetramethylgermane (TMG)
  30% increase in muon charge signals
Small test stands
  Explored different chemicals
  Found an increase in charge collection for highly scintillating particles
We will use Isobutylene
Expect all dopants to convert more than 50% of the light to charge
Notes: Change the order of the pictures.
Small test stands explored different chemicals and found an increase in charge for highly scintillating particles
These plots are from test stand data
Studies done in 90s
The dopants we will use should give us a 7 time increase in charge
Muon -> closer to gamma, makes less light so makes less charge from doping
Bottom one is for alpha, alphas make more light so makes more charge from doping
We should see about 30% increase from our source
Stable operation for 250 days
Found a more linear detector response for highly ionizing particles

## Slide 8: Photosensitive Dopant Simulations
Converting light to charge
  Lowers 1.1 MeV threshold to 10 keV
  Improves charge only energy resolution
Created by: Fernanda Psihas
Joseph Zennamo
Joseph Zennamo
Dopants
Number of Wires
Time [2 ms]
J. Zennamo
Notes: Do the event display first and then talk about the plots.
Just use the Pure event display(10 GeV) instead of the microBooNE
Could drop the injection one
In Joseph’s simulation’s we can show how qualitative representation of we can see some points showing up.
The graph is quantitively simulation.
The simulations are full detector simulation.
We are interested in 2MeV electron energy region.
Highlight these are simulations

## Slide 9: Dopant R&D @ Fermilab
Fig: LArTPC Ready to be Deployed (From LArPix Documentation)
Stage 1: Run TPC with the pixel readout LArPix V2 in the cryostat Blanche
Stage 2: Introduce radioactive sources to measure LArPix V2 performance at low energy
Stage 3: Add photosensitive dopants to demonstrate charge enhancements in LArTPC
Stage 4: Explore optimal doping strategies for low energy events
Notes: Put the logo of Rutgers and LBNL

## Slide 10: Progress
TPC in the making
Testing Mechanical Design
Completed TPC
Bench test of TPC
Panos Englezos
Rutgers U.
Hannah Lemoine
UMN Duluth
Ready to be deployed!
Raisa T. Raofa &
Fernanda Psihas
TinyTPC
@ PAB
Notes: Put in pictures of people working in this slide and say: TPC is assembled, mechanical design is done, will be deployed in the coming weeks
Put this and the next 2 slides in the backup, have people and their institutions.

## Slide 11: Thank You! Question?
Special thanks to everyone in PAB for all their input and help. 
Notes: -Thank you to people at PAB who have helped in this slide. Thanks to Rutgers, LBNL -> put their logos

## Slide 12: Back Up Slides
Notes: -Thank you to people at PAB who have helped in this slide. Thanks to Rutgers, LBNL -> put their logos

## Slide 13: LArTPC Functionality
some of them will collide with Ar atom
Liquid Argon in cryostats: very cold, dense =
high chance of interaction
Charged particles!
→ knock electrons along the way
→ create trails
→ drift through liquid Ar to detector
→ record the particle tracks
Intense neutrino beam
Liquid Argon
Most of them just pass through :(
Created by: I-see Jaidee

## Slide 14: Steps to Dope LArTPC
Components Tiny LARTPC (Source: LArPix documentation)
Step 1:
Completed Tiny LARTPC (Source: LArPix documentation)
Charge Drift Path
Step 2:
Blanche Cryostat (Source)
Step 3:
TPC in the making
Notes: Just have one slide which has -> TPC is assembled, mechanical design is done, will be deployed in the coming weeks

## Slide 15: R&D in the Lab: Mechanical Design
Diagram of TPC when Deployed in Blanche
Testing Mechanical Design
(Source: LArPix documentation)

## Slide 16: R&D in the Lab: Test Electronics
    Resistors on the
    Field
    Cage Panels
Picoammeter
Voltage
Source
Notes: Main goal : Checking none of the resistance is shorted

## Slide 17: Future Steps
Conducting bench tests of the TPC once it is assembled
Completing Python scripts to collect and analyze data (aka Questioning One’s Existence)
Deploying the TPC in the Cryostat
Completing Safety Protocol
Collecting and analyzing data
Python

## Slide 18: DUNE (Deep Underground Neutrino Experiment)
The detectors are in
  Fermi National Accelerator Laboratory, Batavia, Illinois
  Sanford Underground Research Facility, Lead, South Dakota
Objective
  Accelerator neutrino
  Neutrino oscillations
  Supernova neutrino
  Source:
  Figure:https://www.dunescience.org/
Operational Diagram of DUNE (Source)
One of Four DUNE Far Detector Modules (Source)
Notes: Fermilab has one detector. This one is finalized.
Sanford has multiple detectors and the R&D questions focused in our project is more directly related to these detectors.

## Slide 19: Energy Resolution at Low Energy
  Using both light and charge information can yield a more accurate energy information
  According to NEST, the (%) energy resolution requires collection of at least 6000 photons per MeV
  The best LArTPC collects 160 photons/MeV
Less noise in charge readout
Better Energy Measurement
ProtoDUNE-SP
JINST 15 (2020) P12004
Notes: - This image shows what happens if we can collect sufficient amount of light
But light collection is hard.

## Slide 20: Photosensitive Dopant Concept
Using photosensitive dopants will convert light to charge
Converting light to charge
  Lowers 1.1 MeV threshold to 10 keV
  Improves charge only energy resolution
J. Zennamo

## Slide 21: Photosensitive Dopant Concept
Using photosensitive dopants will convert light to charge
Converting light to charge
  Lowers 1.1 MeV threshold to 10 keV
  Improves charge only energy resolution
Created by: Fernanda Psihas
J. Zennamo
Benefits of MeV Reco In LArTPCs
Phys. Rev. D 102, 092010
Notes: - Do the event display first and then talk about the plots.

## Slide 22: Objective : LArPix V2
Measure the energy of low energy events in LArTPCs
  Background/cosmic data
  Radioactive source
  Photosensitive dopants
  Analyze the data
Completed Tiny LARTPC (Source: LArPix documentation)
Anode or readout plane: the pixel is in the back
Field cages
Components Tiny LARTPC (Source: LArPix documentation)
Fig 5 : Blanche Cryostat (Source)
Charge Drift Path
Notes: Construct a tiny LArTPC prototype
  Focus on R&D
  Lower the threshold
  Improve the precision
TPC is deployed in Balance in PAB
The picture is from the one made in LBNL

## Slide 23: Steps to Build a LArTPC
Completing paperwork
  TSW = Technical Scope of Work
  ORC = Operational Readiness Clearance
Preparing work area
Mechanical Designs
  TPC in the Cryostat
Test Electronic Equipment
Test Assemble the TPC
Soldering

## Slide 24: Mechanical Design (Theory vs Application)
Diagram of TPC when Deployed in Blanche
Blanche Lid (Source)
TPC Top Details
Mechanical Design of Metal Plate
Detailed Design of Metal Plate and the Corresponding Locations on Blanche Lid and TPC

## Slide 25: Mechanical Design (Theory vs Application)
Inside of Blanche Lid
Engineering Design of Blanche Lid (Source)
Proposed Idea to Stabilize TPC
Solution = Use metal strips instead of a metal plate

## Slide 26: Test Assemble
TPC in the making
Goal:
Ensure proper functionality of all elements
Test existing assembly procedure
Diagram of the TPC Assemble Procedure
Notes: Waiting on Anode plane.

## Slide 27: Soldering
Checklist
  Electronic schematics
  Description of procedure
Schematics of the Electronics
Drawings for Soldering
Expected Outcome
(Source)

## Slide 28: Low Energy Signals in LArTPCs
Fig: MicroBooNE Simulation of 2.2 GeV electron neutrino
Signals are very small in low energy events
Not much information to reconstruct the events
Notes: If we have to calculate only based on charge, ½ the info is lost
So light is an important aspect and need to collect more light info
Sufficient ratio for physics in GeV scale
Unable to do physics in MeV scale

## Slide 29: Neutrino Detector Event Display
Energy measurements require charge and light measurements
Light is collected with low efficiency
Fig: MicroBooNE Simulation of 2.2 GeV electron neutrino
Notes: If we have to calculate only based on charge, ½ the info is lost
So light is an important aspect and need to collect more light info
Sufficient ratio for physics in GeV scale
Unable to do physics in MeV scale