## Slide 1: Programmable-trajectory ultrafast flying focus pulses
Manfred Virgil Ambat (he/him)
Advanced Accelerator Concepts Workshop
Naperville, IL
July 21 – 26, 2024

## Slide 2: Programmable, spatiotemporal control of ultrashort laser pulses offers tunability for laser-based applications
Summary
Flying focus pulses feature an intensity peak that can travel at any velocity, independent of the group velocity, over distances much longer than a Rayleigh range
We outline a generalized method for designing optical configurations that produce flying focus pulses with ultrashort duration and arbitrary, longitudinal focal trajectories at velocities close to the speed of light
We propose an axiparabola for extending the focal range and a deformable mirror – spatial light modulator pair to dynamically control the focal trajectory
Simulations demonstrate the flexibility of exotic focal trajectories for laser-based applications

## Slide 3: Collaborators
J. L. Shaw, J. J. Pigeon, K. G. Miller, T. T. Simpson, D. H. Froula, and J. P. Palastro

## Slide 4: Flying focus pulses offer optimization of laser-based applications that require velocity matching or extended interaction1-3
Additional talks about this topic:
  J. P. Palastro (Monday, WG6, 4:20pm)
  D. Ramsey (Tuesday, WG6, 2:30pm)
1 Sainte-Marie et al. Optica 4, 10 (2017)
2 Froula et al. Nat. Photonics 12, 5 (2018)
3 Palastro et al. Phys. Rev. Lett. 124, 13 (2020)
4 Miller et al. Sci. Rep 13, 21306 (2023)
5 Simpson et al. Phys. Rev. Res. 6, 013041 (2024)
Laser wakefield acceleration4
THz Generation5

## Slide 5: Ultrafast flying focus pulses require optics that produce an extended focal range
Spatial control

## Slide 6: Ultrafast flying focus pulses require optics that produce an extended focal range
Spatial control

## Slide 7: By separately controlling the focal times via radial group delay, the focal trajectory can be controlled
Spatial control
Spatial + temporal control

## Slide 8: By separately controlling the focal times via radial group delay, the focal trajectory can be controlled
Spatial control
Spatial + temporal control
Exotic spatiotemporal control
Ambat et al. Opt. Express 31, 19 (2023)

## Slide 9: The axiparabola1 is one optic that produces an extended focal range
1 Smartsev et al. Opt. Lett. 44, 14 (2019)
Spatial control
Nominal focal length, f0 = 50 cm | Optic radius, R = 5 cm | Extended focal range, L = 1 cm

## Slide 10: The axiparabola is one optic that produces an extended focal range
The axiparabola naturally produces an accelerating focal trajectory, thus requiring separate optics to control the focal time of the pulse via radial group delay.
Spatial control
Nominal focal length, f0 = 50 cm | Optic radius, R = 5 cm | Extended focal range, L = 1 cm

## Slide 11: By tailoring the radial group delay, the trajectory of the ultrafast flying focus can be controlled
Temporal control

## Slide 12: By tailoring the radial group delay, the trajectory of the ultrafast flying focus can be controlled
Temporal control

## Slide 13: By tailoring the radial group delay, the trajectory of the ultrafast flying focus can be controlled
Temporal control

## Slide 14: By tailoring the radial group delay, the trajectory of the ultrafast flying focus can be controlled1
1 Ambat et al. Opt. Express 31, 19 (2023)
Temporal control

## Slide 15: The recently proposed1 and demonstrated2 radial echelon provides a reflective approach to structuring the radial group delay
1 Palastro et al. Phys. Rev. Lett. 124, 13 (2020)
2 Pigeon et al. Opt. Express 32, 1 (2024)
RGD optics
1 cm

## Slide 16: The recently proposed1 and demonstrated2 radial echelon provides a reflective approach to structuring the radial group delay
RGD optics
1 Palastro et al. Phys. Rev. Lett. 124, 13 (2020)
2 Pigeon et al. Opt. Express 32, 1 (2024)
1 cm

## Slide 17: To improve upon the static echelon, adaptive optics can be used to tailor the radial group delay
1 ISP Systems
RGD optics
Deformable Mirror1
Glass
CMOS Backplane
Liquid crystals
VLC ≠ 0
VLC = 0
VLC = 0
Reflected wavefront
Incident wavefront
Spatial Light Modulator
Echelon

## Slide 18: To improve upon the static echelon, adaptive optics can be used to tailor the radial group delay1, 2
1 Li and Kawanaka Commun. Phys. 3, 1 (2020)
2 Ambat et al. Opt. Express 31, 19 (2023)
RGD optics
Deformable Mirror
Glass
CMOS Backplane
Liquid crystals
VLC ≠ 0
VLC = 0
VLC = 0
Reflected wavefront
Incident wavefront
Spatial Light Modulator

## Slide 19: To improve upon the static echelon, adaptive optics can be used to tailor the radial group delay1, 2
RGD optics
Deformable Mirror
1 Li and Kawanaka Commun. Phys. 3, 1 (2020)
2 Ambat et al. Opt. Express 31, 19 (2023)

## Slide 20: To improve upon the static echelon, adaptive optics can be used to tailor the radial group delay1, 2
RGD optics
Deformable Mirror
Glass
CMOS Backplane
Liquid crystals
VLC ≠ 0
VLC = 0
VLC = 0
Reflected wavefront
Incident wavefront
Spatial Light Modulator
1 Li and Kawanaka Commun. Phys. 3, 1 (2020)
2 Ambat et al. Opt. Express 31, 19 (2023)

## Slide 21: Programmable-trajectory ultrafast flying focus pulses offer rapid tunability of a wide variety of focal trajectories
An accelerating focus can be used to control the trapping and acceleration of electrons in a laser wakefield accelerator
Ambat et al. Opt. Express 31, 19 (2023)

## Slide 22: Programmable-trajectory ultrafast flying focus pulses offer rapid tunability of a wide variety of focal trajectories
A pulse with an oscillating focal point could provide a novel method for quasi-phase-matching nonlinear optical processes
Ambat et al. Opt. Express 31, 19 (2023)

## Slide 23: Programmable, spatiotemporal control of ultrashort laser pulses offers tunability for laser-based applications
Conclusions
Flying focus pulses feature an intensity peak that can travel at any velocity, independent of the group velocity, over distances much longer than a Rayleigh range
We outline a generalized method for designing optical configurations that produce flying focus pulses with ultrashort duration and arbitrary, longitudinal focal trajectories at velocities close to the speed of light
We propose an axiparabola for extending the focal range and a deformable mirror – spatial light modulator pair to dynamically control the focal trajectory
Simulations demonstrate the flexibility of exotic focal trajectories for laser-based applications

## Slide 24: Additional slides

## Slide 25: Adaptive optics, such as deformable mirrors and spatial light modulators, offer dynamic programmability of the focal trajectory.
Li and Kawanaka, Sci. Rep. 10, 1 (2020)
Ambat et al. Opt. Express 31, 19 (2023)
RGD optics

## Slide 26: Figure 4
This figure shows the electric field of the laser pulse modified by the RGD optics. Insets show the fine structures within a 500 um x 15 fs window. Laser propagates from left to right.

## Slide 27: Derivation of the ultrafast flying focus

## Slide 28: Derivation of the ultrafast flying focus

## Slide 29: Derivation of the ultrafast flying focus

## Slide 30: Derivation of the ultrafast flying focus

## Slide 31: Figure 5
As the SLM pixel size goes to zero, the intensity of the echelon is recovered.
The maximum on-axis intensity of flying focus pulses with vf = c created using (a) an echelon or a DM-SLM pair with an SLM pixel size of (b) p = 200 µm, (c) p = 100 µm, and (d) p = 50 µm.

## Slide 32: An accelerating focus can be used to control the trapping and acceleration of electrons in a laser wakefield accelerator.

## Slide 33: A pulse with an oscillating focal point could provide a novel method for quasi-phase-matching nonlinear optical processes