## Slide 1: Injection of collider-quality e-beams in plasma accelerators
A. Jain1, J. Yan1, J. Palastro2, T. Simpson2,*, J. Pierce3, W. B. Mori3, N. Vafaei-Najafabadi1
1Stony Brook University, 2University of Rochester, 3UCLA
* Currently at Johns Hopkins University

## Slide 2: Synthesis
Plasma accelerators create accelerating gradients that are hundreds of times higher than conventional accelerators
A “plasma photoinjector” for a collider application needs to create
  Low emittance (<100 nm)
  High charge (order of nC)
  Trapezoidal shape for low energy spread in subsequent accelerating plasma stages
By applying the spatiotemporal pulse shaping to two-color ionization injection, such plasma photoinjector can be demonstrated at ATF

## Slide 3: Luminosity
In addition to energy, beam quality is a critical consideration
In colliders, quality is measured by Luminosity
C.B. Schroeder et al 2023 JINST 18 T06001
DOI 10.1088/1748-0221/18/06/T06001
Beam charge High charge
Focusability low emittance and energy spread
& & Q
Beam collision rate High rate
Plasma Collider: kHz
Plasma Collider: pC ,
Plasma Collider:
Emittance, nm
Energy spread, 1%
Notes: Having a high acceleration gradient is not enough, you also need a high quality beam
Luminosity determines number of events (collisions) per second

## Slide 4: A relatively low-power LWIR laser generates a clean, highly nonlinear wakefield
Strength of ponderomotive force scales with , so LWIR drivers () can reach with modest intensities (at ~20 TW power)
can be reached by and LWIR laser without triggering self-injection in LWFA*
Bubble created by LWIR driver can be >100 µm, providing the ability for precise alignment of multiple beams with respect to the bubble
P. Kumar, Physics of Plasmas, 28, 013102 (2021)
,
P=20 TW,
𝜏=0.5 ps,
cm-3
* See A. Jain, Proceedings of AAC 2022
Notes: LWIR drives clean wakefield

## Slide 5: Two-color ionization injection
Yu, PRL 112, 125001 (2014)
Schroeder, European Conference on Lasers and Electro-Optics (2015)
See also Xu, PRSTAB, 17, 061301 (2014)
Schroeder, PRSTAB 17, 101301 (2014)
A second laser can trigger ionization injection in the wakefield driven by the LWIR laser, creating a high-quality beam
Drive laser needs large to form plasma wakefield, but we want low field to avoid prematurely ionizing the gas
Injector laser needs high field to ionize the gas, but low to avoid disturbing the plasma
Low emittance
Excellent phase space
Very intense, small
Less intense, large

## Slide 6
Solution:
Inject a trapezoidal beam and flatten the plasma wakefield through beamloading
M. Tzoufras, Phys. Rev. Lett. 101, 145002 (2008)
Shortcomings:
The charge produced is low (3-30 pC)
Lack of beam loading results in relatively large energy spread (few %)
Key constraint is a very localized injection of high-quality electrons

## Slide 7: Varying the location of ionization is possible through spatiotemporal control of the ionizing laser
By varying the chirp, the region of peak intensity (focus) can be made to travel at any velocity
D. H. Froula, Nature Photon 12, 262–265 (2018)

## Slide 8: Varying the location of ionization is possible through spatiotemporal control of the ionizing laser
Motion of the focus with corresponds to an “ionization wave” in the co-moving coordinate

## Slide 9
Open source
40+ research groups worldwide are using OSIRIS
300+ publications in leading scientific journals
Large developer and user community
Detailed documentation and sample inputs files available
Using OSIRIS 4.0
Visit osiris-code.github.io
OSIRIS framework
Massively Parallel, Fully Relativistic Particle-in-Cell Code
Parallel scalability to 2 M cores
Explicit SSE / AVX / QPX / Xeon Phi / CUDA support
Extended simulation/physics models

## Slide 10
CO2 and flying focus laser intensities are chosen based on Kr8+ Kr9+ ionization rates
FF laser- , ,
CO2 laser- , , s,
Notes: Also below the level of self injection

## Slide 11
Ionization wave in the co-moving coordinate results in an extended region of injection
FF laser- , ,
CO2 laser- , , s,
Plasma: , , L= 4 mm
Plasma density
Injected electrons

## Slide 12: The injected beam is gradually assembled with the motion of the ionization front

## Slide 13: Charge and emittance are consistent with collider requirements
 | 20 GeV Demonstrator Facility* | Two Color FF Injector
Q (pC) | 200 | 220
 | 0.1 | 0.076
 | 100 | 0.17
Bunch length | 8.5 (rms) | 25
 | 20 GeV Demonstrator Facility* | Two Color FF Injector
Q (pC) | 200 | 220
 | 0.1 | 0.076
 | 100 | 0.17
 | 8.5 (rms) | 25
*C.B. Schroeder et al 2023 JINST 18 T06001

## Slide 14
A. Jain, in preparation
Motion of the ionization location and the shape of the function result in injection of a trapezoidal profile
CO2
laser
FF laser
(a)
(b)
(c)
Plasma formed by ionization of Krypton gas
Plasma wake driven by CO2 laser pulse

## Slide 15: Beam generated in this photo injector can be accelerated in subsequent stages at 10 GeV/m and at high efficiency
A. Jain, in preparation
,
Final Emittance:
nm rad
nm rad
Transfer efficiency: 43%

## Slide 16: This method can easily be scaled to higher charge, albeit with higher emittance
A. Jain, in preparation

## Slide 17: Beam loading of the nC beam
,

## Slide 18
BNL’s Accelerator Test Facility (ATF) has unique infrastructure
for developing such photoinjector.
New York
RHIC
NSLS
ATF
Multi-TW discharge-pumped CO2 laser
• 8J, 2 ps (2024)
• 10 J, 0.5 ps (projected 2027)
TW – class Ti:Sapphire Laser
Dr. Rafal
Zgadzaj
Dr. Irina
Petrushina
Synched S-band
linac (50 MeV, 100 fs)

## Slide 19: Full-energy post-compressor
Seed from the present
CPA laser
2 ps
5 TW
500 fs
5 TW
✔️ State of the art
⚙️ 10-mJ seed
⚙️ post-compression
Seed from a CPA laser with 10-mJ seed
500 fs
15 TW
100 fs
25 TW
See M. Polyanskiy, Monday 5:40, on enabling LWIR upgrades

## Slide 20
2014
InTech (2012)
2019 Optica 2, 675 (2015)
OSA Continuum 3, 459 (2020)
2010 Opt. Express 19, 7717 (2011)
2025
Opt. Express 29, 31714 (2021)
Front. Phys. 10, 1390225 (2024)
Gas
Solid state
⚙️
✔️
✔️
⚙️
⚙️
2030+
Photonics 8, 101 (2021)
Opt. Express 29, 31455 (2021)
See M. Polyanskiy, Monday 5:40, on enabling LWIR upgrades
Hybrid L-WIR laser architecture

## Slide 21: Integration of Ti:Saph at ATF
Parameter | Value | Comments
Energy (compressed) | >15 mJ (@1.5 Hz) | Compressed on target. <5% std long-term variation To be increased to 100 mJ @ 12 Hz
Energy (stretched) | >200 mJ | Out of 4-pass amplifier <8% std long-term variaiton
Duration | <70 fs | FWHM
Focused spot size | <4 µm FWHM | With F/1.5 OAP <1µm std pointing stability (~25µrad std)
Polarization | Vertical | Horizontal available upon request
Synchronization | Synchronized to the facility 81.6 MHz master clock | Rough timing (ns) by SRS delay generators. Fine adjustments (~10fs) by phase tuning the oscillator (Coherent Vitara+Synchrolock)
Transport line+ compressor transmission | 60% | 
Peak intensity | >1018 W/cm2 | 
Beam size in transport | <1.5” | Limited by aperture of vacuum line between Nd:YAG and Gun Hutch rooms
Addition of Ti:Saph is represents an important upgrade in the capabilities of ATF

## Slide 22: Summary
A “plasma photoinjector” for a collider application needs to create
  Low emittance ( 100 nm)
  High charge (order of nC)
  Trapezoidal shape for low energy spread in subsequent accelerating plasma stages
By applying the spatiotemporal pulse shaping to two-color ionization injection, such plasma photoinjector can be demonstrated at ATF, BNL

## Slide 23: The End

## Slide 24: Self Injection of CO2 Driven Wakes
 | (TW) |  | /2) | ) | ) | ) | )
 | 23 | 3.80 | 2.6, 145 | 3.67, 173 |  | 5.2, 205 (341 pC) | 6.37, 227 (916 pC)
2 | 11.5 | 3.32 | 1.84, 87 | 2.6,103 |  | 3.7, 123 (40 pC) | 4.5, 135 (330 pC)
3 | 7.7 | 3.14 | 1.5, 64 | 2.1, 75 | 3, 90 |  | 3.67, 100 (48 pC)
4 | 5.7 | 3.05 | 1.3, 51 | 1.82,61 | 2.6, 73 |  | 3.16, 80 (25 pC)
5 | 4.6 | 2.99 | 1.16, 43 | 1.64,52 | 2.32, 61 |  | 2.84, 65 (7pC)
 | 23 | 3.80 | 2.6, 145 | 3.67, 173 |  | 5.2, 205 (341 pC) | 6.37, 227 (916 pC)
2 | 11.5 | 3.32 | 1.84, 87 | 2.6,103 |  | 3.7, 123 (40 pC) | 4.5, 135 (330 pC)
3 | 7.7 | 3.14 | 1.5, 64 | 2.1, 75 | 3, 90 |  | 3.67, 100 (48 pC)
4 | 5.7 | 3.05 | 1.3, 51 | 1.82,61 | 2.6, 73 |  | 3.16, 80 (25 pC)
5 | 4.6 | 2.99 | 1.16, 43 | 1.64,52 | 2.32, 61 |  | 2.84, 65 (7pC)

## Slide 25: Beam energy after injection stage
nm rad
Peak energy=10MeV
FWHM=6 MeV
%

## Slide 26: Beam loading of the nC beam

## Slide 27
a
b
c
d
e
f
g
d
pC
nC

## Slide 28
Slope= 0.22
,

## Slide 29: Beam Loading Physics

## Slide 30: Recent infrastructure upgrade allow the delivery of 2-ps, <5Tw pulses to IP
Seed Laser Table
Final amplifier
Shielding wall
Experimental Hall
CO2 Room
Flexible polarization rotator (FPR)
Compressor
FEL Room
CO2
YAG
Plasma shutter
Nonlinear pulse compressor
Test chamber
YAG
CO2
plasma
See M. Polyanskiy, Monday 5:40, on enabling LWIR upgrades

## Slide 31: Two Compressors Enable Integration of the Ti:Saph at User IPs