## Slide 1
Update on the progress of the E-320 SFQED experiment
A. Knetsch on behalf of the E-320 Collaboration
SLAC National Accelerator Laboratory

## Slide 2: The collaboration
Carleton University, Ottawa, Ontario, Canada | Thomas Koffas
Aarhus University, Aarhus, Denmark | Christian Nielsen, Allan Sørensen, Ulrik Uggerhøj
École Polytechnique, Paris, France | Sébastien Corde, Pablo San Miguel Clave, Mickael Grech, Aimé Matheron, Sebastian Meuren (PI), Caterina Riconda
Technical University (TU) of Darmstadt | Stephan Kuschel, Christian Rödel
MPI für Kernphysik, Heidelberg, Germany | Antonino Di Piazza, Christoph H. Keitel, Matteo Tamburini
HI Jena and University of Jena, Germany | Harsh, Felipe Salgado, Jannes Wulff, Matt Zepf
Universidade de Lisboa, Portugal | Thomas Grismayer, Luis Silva, Marija Vranic
Imperial College London, UK | Stuart Mangles
Queen’s University Belfast, UK | Niall Cavanagh, Elias Gerstmayr, Gianluca Sarri, Matthew Streeter
California Polytechnic State University, CA USA | Robert Holtzapple & students
Lawrence Livermore National Laboratory, CA USA | Félicie Albert
SLAC National Accelerator Laboratory and Stanford PULSE Institute, Menlo Park, CA USA | Robert Ariniello, Phil Bucksbaum, Christine Clarke, Angelo Dragone, Alan Fisher, Frederico Fiuza, Alan Fry, Spencer Gessner, Siegfried Glenzer, Carsten Hast, Mark Hogan, Chris Kenney, Alexander Knetsch (POC), Doug McCormick, Rafi Mir-Ali Hessami, Brendan O’Shea, David Reis, Tania Smorodnikova, Douglas Storey, Glen White, Vitaly Yakimenko
University of California Los Angeles, CA USA | Chan Joshi, Warren Mori, Brian Naranjo, James Rosenzweig, Oliver Williams, Monika Yadav
University of Colorado Boulder, CO USA | Chris Doss, Michael Litos
University of Nebraska - Lincoln, NE USA | Matthias Fuchs, Junzhi Wang
Former members | Zhijiang Chen, Henrik Ekerfelt, Erik Isele

## Slide 3
Non-linear inverse Compton scattering :
Non-linear Breit-Wheeler pair creation :
SFQED processes we are studying
Schwinger critical field
onset of non-perturbative physics
Laser-beam collisions
onset of nonlinear effects

## Slide 4
E-144: previous study of nonlinear Compton scattering at SLAC
~ 50 GeV electrons + ~ 1018 W/cm2 laser intensity: a0 ≲ 0.5, χ ≲ 0.5
E-144: observed onset of nonlinear effects
SLAC E-144 (simulation) Bula et al., PRL 76 (1996) Bamber et al., PRD 60 (1999)

## Slide 5
Accessible parameters at FACET-II
Up to 2 nC bunch charge
~ 10 GeV beam energy
Bunch length (rms) < 100 µm
FACET-II electron beam parameters
Yakimenko et al., PRAB 22, 101301 (2019)
FACET-II laser parameters
~ 300 mJ on target
~ 50 fs pulse length
a0 > 1
  χ ~ 1

## Slide 6: The E-320 interaction point

## Slide 7: Improved laser parameter
Beam diameter | 40 mm
f# | ~ 2
wavelength | 0.8 μm
Spot size (w0) | 1.4 x 1.7 μm
Pulse duration | ~ 48 fs
Energy on target | 0.28-0.38 J
Max a0 | ~ 4.5
Status 2022
Focal scan
Status 2024
Extensive work on wavefront improvements
Intensity and focal quality greatly improved
Major contributions by J. Wang, and R. Ariniello

## Slide 8
Laser focal stability
Sub-um position jitter for laser focus measured
Few-um position jitter for e-beam achievable
E320_06968
E320_05469
Dominated by drift and dispersion
Improved accelerator setup: Jitter only
Stability of experiment
σx = 0.65 um
σy = 0.94 um
Electron beam transverse stability

## Slide 9: Finding spatial overlap: knife-edge scan
Old procedure: YAG position scan
Laser spot:
Fully blocked by YAG (left) vs. full transmission (right)
Electron beam:
Bremsstrahlung and scintillation when intercepted by YAG
Yellow = YAG scintillation
Blue = gamma-ray yield
But… beams are too intense
Peripheral knife-edge scan

## Slide 10: Shot-to-shot timing information via EOS (UC Boulder)
Hunt-Stone et al., NIMPRA 999, 165210 (2021)
EOS installed in the picnic basket
electro-optical sampling (EOS) measures relative time-of-arrival between laser and e-beam
Shot-to-shot non-invasive time-stamping
Dial in collisions with EOS signal

## Slide 11
Time-of-arrival jitter as low as 50 fs measured
Time-of-arrival drift can vary up to ~1 ps
Drift compensation: PID loop between EOS-measured TOA and laser target time reduces variation to < 100 fs
Relative time-of-arrival stabilization

## Slide 12: Electron detection: High charge sensitive screen
Insertable light-tight detector
Charge calib. 4.8 +- 0.3 e-/count
Peak noise level ~ 2 counts
Dark current charge: 306.9 +- 19.9 fC

## Slide 13
Performance example

## Slide 14
Dialing in highest intensity on electron beam
Coarse timing scan to find highest intensity interaction conditions
Low- and high-intensity interaction populations due to geometry
Higher-order scattered electrons have higher sensitivity on peak a0
analysis plots by T. Smorodnikova
n=2 (non-linear)
n=1
n>2 (non-linear)

## Slide 15
Multi-shot averaging
EOS reveals timing-dependence of interaction
Shots grouped by time-of-arrival show show similar results
Possibility for improved SNR by multi-shot averaging

## Slide 16
Evidence of transition to non-perturbative regime
With a0 exceeding unity, a transition to a continuous spectrum is expected
The transition to continuous marks the transition to the non-perturbative regime
Laser energy scans as well as timing scans show great resemblance of simulation prediction
Simulation
Data
Simulation plots by R. Holtzapple, analysis plots by T. Smorodnikova and J Wang

## Slide 17
Outlook for E-320: More data - more detectors !
B. Naranjo et al., IPAC2021 THPAB269, THPAB270 (2021)
Gamma pair spectrometer (UCLA): energies: 0.1-10 GeV
gamma spectrum can be reconstructed
Positron tracking and Cherenkov calorimeter (Jena)
based on: Salgado et al. NJP 24 (2021)
Single electron detection with ePix module provided by the SLAC detector group
(Chris Kenney et al.)
Gamma ray profiler
Weizmann institute
LUXE
Cherenkov tubes detector testing

## Slide 18: Thank you for your attention! Questions ?