## Slide 1: 72 Hour Summary
Patrick Dowdle
MCR Crew Chief
May 1, 2023

## Slide 2: Summary
In general:
  Fought RR LLRF and LRF3 gradient issues all weekend
  Lots of tuning
Friday:
  1 hour downtime to swap RR LLRF components
  Established beam to Muon (Mu2e studies first then g-2) after AP0 HVAC work
Saturday:
  B:MP02 PS fault on #2, EE support switched from supplies 2&4 to 1&3
  I:H310 DC O/I, regulator was replaced
Sunday:
  GMPS trip on water temp/cap pressure high, prepared for access and Booster Group and Rad Safety went in and put a jumper on the pressure switch
  MS2LVL low, MSD filled the system
Today:
  Muon 95 faulty temp sensor, mixing valve needs to be adjusted manually
  MI-20 LCW pump #1 tripped, running fine on 2&3
Currently:
  730 kW to NuMI
  3.19E16/hr to BNB
  1.02E12 POT to Muon
  Beam to MTest