## Slide 1: Accelerator Session Summary
Jeffrey Eldred
ACE Science Workshop
June 15, 2023

## Slide 2
2
High-Level Summary, Programs
2
LBNF: Both ACE RCS and ACE Linac approaches are both technically sound and reasonably costed solutions. Power, reliability, flexibility.
- Both start with a 2 GeV Linac
New Physics: Spigots presented yesterday, Both scenarios extend linac to 2 GeV and increase beam power at 8 GeV, but some variation in the relative beam powers available for each spigot.
Muon Collider: Neither ACE RCS not ACE Linac can be directly used as an 2-3 MW MuC proton driver. Should be re-optimized.
- ACE RCS should be modified to be 100-200e12, 5-10 Hz. This requires
serious consideration of space-charge issues.
- Possibility of 2-8 GeV 10 Hz RCS upgrade to 3-12 GeV 5Hz RCS?
- ACE Linac should be as high current as possible at 10 Hz.
- 5mA x 2ms x 10Hz configuration upgrade to 20mA x 2ms x 10Hz.
- ACE Linac a more natural fit for MuC than ACE RCS.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 2
2
2

## Slide 3
3
High-Level Summary, R&D Needs
3
***** High-Power Targetry R&D
We need to develop 2+ MW DUNE/LBNF target as soon as possible.
All our ambitious muon programs require novel/advanced targets.
*** H- Laser Stripping
H- Foil injection is the most challenging part of both ACE RCS/Linac
- For 8-GeV H- stripping, no direct precedent.
** Muon Collider Target Demonstrator, Cooling Demonstrator
Planning to use 0.8 GeV, 2 GeV Linac beam and/or 8 GeV Booster beam.
** GeV-Scale Accumulator Ring Design
Real opportunity for 0.8 GeV compact AR with short pulses
- Start with 100-300 kW at 0.8 GeV suitable for PIP2-BD
- Updated to 1+ MW at ~2 GeV great for AMF/PIP2-BD
* Metallized Ceramic Beampipe
For 20 Hz RCS configurations, benefit from developing a prototype.
* High-Gradient, High-Q SRF Linac
Continuous improvement in cost/benefit SRF technology.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 3
3
3

## Slide 4
4
Final Slides
Three Questions about
Accelerator Upgrades
4
4
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 5
How will your system/development address the BR goals of DUNE/LBNF, New Physics, MuC?
  DUNE/LBNF: 10Hz RCS may be the lowest cost, lowest risk configuration.
  New Physics: Spigots yesterday, CW up to 2 GeV
  MuC: There’s a viable path, but advantage goes to Linac option.
    RCS gets more interesting with higher energies.
2. What are the biggest technical/performance risks of your system/development?
  H- Foil Injection, Laser stripping R&D. Looks okay, but biggest risk/limit.
  Ceramic/Dielectric Beampipe. Barrier to 20+ Hz ramp rate.
  MuC R&D, proton compression, HTS, muon production, cooling.
3. What are the most sensible first steps to enable progress in your system/ development? What can be done before the next ACE event (Fall’23 workshop)?
  Start prototype RCS ceramic beampipes.
  Develop decision tree/timeline for choosing RCS vs Linac upgrade.
  Resolve MuC R&D plan, role for Fermilab proton complex.
Jeff Eldred – ACE “2-Gev Linac + 8-GeV RCS” Design
5
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 6
How will your system/development address the BR goals of DUNE/LBNF, New Physics, MuC?
  All 3 BRL options deliver 2.4 MW to LBNF/DUNE and have extra beam for other experiments. The linac can be designed with additional spigots at intermediate energies if desired. Option C would have 1.2 MW power at 8 GeV available, which is close to what MuColl R&D would need.
What are the biggest technical/performance risks of your system/development?
  Develop a robust injection scheme?
What are the most sensible first steps to enable progress in your system/ development? What can be done before the next ACE event (Fall’23 workshop)?
  R&D on: high-gradient SRF cryomodule, laser-assisted injection, modeling the complete linac design, simulation and optimization of the injection painting and foil heating.
  Fall’23 is too soon to accomplish anything, but we can initiate some R&D topics and perhaps have preliminary results.
Sergey B – ACE “8-GeV Linac + 8-GeV AR” Design
6
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 7
How will your system/development address the BR goals of DUNE/LBNF, New Physics, MuC?
a) help LBNF/DUNE Phase II and improve reliability of the accelerator complex;
  To achieve Phase II – you have to be successful in phase one! Success requires operating the Booster for the initial power ramp up during the critical commissioning and at least 5 years of running at required power. PAR is capable of helping the Booster deliver the necessary beam by reducing losses in the Booster and significantly reducing the complexity of the Booster operations.
  Taking the Booster Injection out of the Booster has several benefits that can’t be underestimated:
  More space for a robust beam dump – will be a HRA in Booster!
  Single turn injection into a rapid cycling Booster – still uncertain how to do this without PAR
  Simplify the Booster RF locking to PIP-II
  Does not require Booster correctors to flatten orbit – removing risks associated with pushing correctors
  Simple acceleration process in the Booster – no longer need to transition from flat to ramping GMPS
b) enable new physics “spigots” (RPF, etc);
  The only way to achieve a DS or any other beam based new physics program within a decade is PAR!
  Every other plan is 20 years away – unless you leave Fermilab (the nations' HEP lab)
c) layout foundation for the future MuColl R&D and facility
  If an accumulation ring is required for MuColl – this will be a testing ground.
  We have not built an accumulator ring in decades – PARs unique design and potential training is important to helping us ensure success at the next stage.
B. Pellico – PAR “AR for Booster” Design
7
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 8
What are the biggest technical/performance risks of your system/development?
  I see no significant technical risks, but I do see timing challenges – given approval – how quickly can you manufacture required magnet systems – fully tested.
  Placement ands design of service building requires site planning outside the PAR immediate group and may delay deployment of PAR.
  Performance risk – Should be thought of as Flux limit(s) .
    Pulse systems – 60to 80 Hz been shown – how much is 100 Hz going to stress design
    Beam extraction loss,
    Beam Injection Loss
What are the most sensible first steps to enable progress in your system/ development? What can be done before the next ACE event (Fall’23 workshop)?
  The PAR beam dump needs to be designed (Could be done by fall)
  Actual mechanical stands and supports
    It would take two years to complete ME designs and drawings
  Civil work on building, penetrations, and cable runs all to be done
B. Pellico – PAR “AR for Booster” Design
8
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 9
Katsuya Yonehara – Muon Collider R&D
9
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Experiments:
  How does the experiment make use of the ACE beam?
    Muon collider demo facility
  Is the experiment uniquely enabled by The ACE upgrades?
    Yes
  Can this experiments be performed elsewhere?
    ACE BR is needed to demonstrate muon collider system which is the last stage to construct real muon colliders
  What particular accelerator components or capabilities are necessary?
    What proton energies are needed?
    5-15 GeV
    What proton quantities are needed?
    > 1012 protons per bunch
    What time structure is needed? (bunch length, train structure)
    Bunch length something in the ns scale, Repetition rate is not so important for the demo facility
    Can the demonstrator be performed with 800 MeV protons from PIP-II or 8 GeV protons from the Booster with PIP-II?
    Yes for 8 GeV, No for 800 MeV

## Slide 10
Katsuya Yonehara – Muon Collider R&D
10
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
How might an eventual Muon Collider benefit from ACE?
  What particular accelerator components or capabilities are necessary for the experiment?
    What proton energies are needed?
5-15 GeV approximately
What proton quantities are needed?
10^14 approximately
What time structure is needed? (bunch length, train structure
1-3 ns bunches, ideally at 5-10 Hz

## Slide 11
Katsuya Yonehara – Muon Collider R&D
11
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
2. What are the biggest technical/performance risks of your system/development?
  Lower than nominal luminosity due to performance of target/capture and ionization cooling systems
3. What are the most sensible first steps to enable progress in your system/ development? What can be done before the next ACE event (Fall’23 workshop)?
  Initiate design work towards a self consistent set of parameters for the demo and the final facility hosted at Fermilab

## Slide 12
Kevin Lynch – Targetry R&D
12
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
How will your system/development address the BR goals of DUNE/LBNF, New Physics, MuC?
  HPT R&D required for a successful LBNF 2.4MW target and beam windows
  HPT R&D required for other high power “spigots” (Mu2e-II, AMF, BD, etc)
What are the biggest technical/performance risks of your system/development?
  Not getting started early enough! Irradiating materials followed by PIE is time and resource intensitive: significant planning, coordination, cooldown, etc
  Failures/conservative operations limit beam power and physics reach
What are the most sensible first steps to enable progress in your system/ development? What can be done before the next ACE event (Fall’23 workshop)?
  We have already articulated a plan to P5 for ACE target R&D, and outlined a roadmap for GARD. Execution requires a funding profile.