## Slide 1
RF-Mechanical design of the 650 MHz buncher
I. Gonin, T. Khabiboulline, G. Romanov, V Yakovlev

## Slide 2
Why separate feeding of the cavity cells is better than use of a coupled-cell resonator:
No coupling cells and coupling slots, which also improves Rsh by ~20% compared to pi-structure
The separate cells are shorter, that allows further improvement transit time factor and shunt impedance;
No power combiner in the amplifier, which provides 1.5-2 dB loss and additional cost.
One needs not a big coaxial line, but a number of thinner coaxial cables. The cables may have higher loss than a coaxial line, but because of (1-3) the total input power from the grid may be even smaller than for a coupled cell cavity.
No high-power coupler, which is expensive, may be unreliable (big ceramic window) and needs long time for design and tests;
The separate cell cavity needs individual phase control, which is not a problem.
Separate feeding cavity design was completed on 09/13/2021

## Slide 3
Parameter | Value
 | 46
 | 323.4/326.74/329.82
L | 140/145/150
gap | 65/70/75
t | 5
R1 | 2.5
R2 | 2.5
R3 | 21
R4 | 55/57.5/60
Parameter | Value
 | 46
 | 323.4/326.74/329.82
L | 140/145/150
gap | 65/70/75
t | 5
R1 | 2.5
R2 | 2.5
R3 | 21
R4 | 55/57.5/60
All parameters in mm
V = 300 kV
β = 0.841 (800 MeV)
Parameter | L = 140 mm | L = 145 mm | L = 150 mm
, kV | 272.5 | 269.8 | 267.0
R/Q ,Ω | 277.5 | 280.8 | 283.2
Q | 28790 | 29520 | 30220
/L ,MΩ/m | 57.07 | 57.16 | 57.05
Losses, kW | 9.29 | 8.78 | 8.33
, MV/m | 13.9 | 13.25 | 12.7
Parameter | L = 140 mm | L = 145 mm | L = 150 mm
 | 272.5 | 269.8 | 267.0
R/Q ,Ω | 277.5 | 280.8 | 283.2
Q | 28790 | 29520 | 30220
 | 57.07 | 57.16 | 57.05
Losses, kW | 9.29 | 8.78 | 8.33
 | 13.9 | 13.25 | 12.7
L
gap
R4
R3
t
vs. gap length
vs. cavity length
RF design

## Slide 4
RF design
Cell to cell coupling

## Slide 5
RF design, HOM’s up to 2 GHz
162.5 MHz
650.000 | 2.81E+02 | 2.5E+04 | 2.92E+04
1221.607 | 1.88E+01 | 1.89E+06 | 3.73E+04
1431.673 | 4.12E+01 | 1.02E+04 | 2.72E+04
1817.310 | 1.32E+01 | 2.33E+04 | 1.13E+04
1203.069 | 7.93E+00 | 6313 | 4.61E+03
1207.507 | 3.51E+04 | 1.89E+06 | 3.70E+04
1233.400 | 1.71E+03 | 1.12E+05 | 2.56E+04
1236.031 | 3.55E+01 | 1.14E+04 | 3.21E+04
1350.614 | 1.19E+04 | 6.04E+04 | 3.24E+04
1429.210 | 1.11E+05 | 5714 | 4.02E+04
1434.044 | 1.67E+04 | 2.49E+04 | 4.05E+04
1569.860 | 2.01E+03 | 7175 | 4.57E+04
1576.470 | 8.41E-05 | 3.53E+07 | 4.82E+04
1578.802 | 2.88E-02 | 1.29E+04 | 5.28E+04
1677.496 | 6.17E+01 | 3937 | 3.38E+04
1689.249 | 1.02E+00 | 1.37E+04 | 4.43E+04
1755.785 | 3.22E+03 | 5.64E+04 | 2.94E+04
1758.544 | 5.10E+03 | 2.97E+04 | 3.67E+04
1854.736 | 3.00E+04 | 9.86E+04 | 1.24E+03
1916.479 | 1.05E+04 | 4876 | 3.83E+04
1926.444 | 9.52E+03 | 1.07E+04 | 2.35E+04
1931.249 | 4.86E+01 | 4.40E+06 | 4.22E+04
1931.531 | 8.99E+03 | 2.13E+04 | 5.19E+04
1934.704 | 2.37E+04 | 1.18E+06 | 3.85E+04
1936.059 | 3.41E+04 | 7.20E+05 | 3.38E+04
1947.611 | 2.59E+01 | 3449 | 3.22E+04
1966.735 | 3.78E+02 | 9300 | 2.02E+04
Monopole, m = 0
m ≥ 1
F, MHz
R/Q, Ω
Ω/
F, MHz
Port’s BC applied

## Slide 6
RF design, plunger tuner
dF/dL ~ 10.9 kHz/mm
dF/dL ~ 13.3 kHz/mm
dF/dL ~ 17.1 kHz/mm

## Slide 7
Voltage = 300 keV
Log scale of E-fields in the same range
Loop coupler 1
CH structure coupler
Loop coupler 2
RF design, power coupler
gap ~ 3.2 mm
gap ~ 3.2 mm
gap ~ 6.2 mm
gap ~ 1.5 mm

## Slide 8
2 water channels, Ø 9 mm
Voltage = 300 kV, duty cycle 5%
Outer wall 20 mm
ΔT 12.8⁰C
30 mm
RF design, water cooling, vacuum

## Slide 9
Outer wall thickness 20 mm Weight ~ 394 kg
Outer wall thickness 15 mm Weight ~ 337 kg
Outer wall thickness 10 mm Weight ~ 283 kg
Mechanical design, deformation due to gravity + vacuum

## Slide 10
Thickness, mm | Δ F, kHz
10 | -5.9
15 | -5.45
Outer wall thickness 15 mm
Outer wall thickness 10 mm
Von Mises stresses in 7-cells cavity under vacuum are < 2MPa
2 supports lags
Frequency change due to vacuum
Mechanical design, deformation due to gravity + vacuum

## Slide 11
Multipacting simulations
Total design voltage of the multicavity PIP-II 650 MHz re-buncher is Unom = 2.5 MV (without transit time factor).
Chosen number of cavities N = 14, so design voltage per cavity U14 nom = 2500/14 ≈ 179 kV.
Model for eigen mode field simulation,
i.e., there is SW in the coupler.
Planes of symmetry are not used.
Magnetic boundary
Coupler 1 (old)
Coupler 2
Coupler 3
Electric field in the gaps of the coupler
designs at U14 = 300 kV.

## Slide 12
Multipacting simulations, PIC models
Coupler 1 (old)
Coupler 2
Coupler 3
SEY, same for all
models
Initial energy distribution,
same for all models

## Slide 13
Multipacting simulations, PIC models
Coupler 2, U=83 kV
Coupler 2, U=130 kV
The coupler #3 is free of MP in the voltage range
that corresponds to 14 cavities variant.

## Slide 14
RF amplifiers, R&K

## Slide 15
RF amplifiers, TOMPCO

## Slide 16
Summary
RF design completed
  Accelerating cell optimized for maximum
  14 independent accelerating cells combined in 2 cavities
    7 cell in each cavity, length <1.2m each
  200 kHz range tuning plunger proposed
  Cavity MP free up to 300 kV
Power coupler design optimized for minimizing MP
  FPC MP free up to 300 kV
Power amplifier bids received
  300-400 k$ for 14 channel, 5.5 kW each
Next steps:
  Production drawings for cavities
  Cavity procurement
  Purchase FPC and PickUp parts
  LLRF development