## Slide 1
LCLS-II-HE BCC Stands Engineering Peer Review
Colin Narug
6/6/2023

## Slide 2: Introduction
BCC Cryomodule will be supported on two stands updated from the ones used to the support the LCLS-II cryomodules.
Front support fixed design, back support allowed to slide
Required to support cryomodule during seismic operations while additionally resisting pressure loads during operations.

## Slide 3: Design Methodology
Exact methods to evaluate stand design is difficult due to non traditional features.
Outside of scope of BPVC as per VIII-2,U-1(e)(2)
AISC 360 Advanced Analysis Methods are more for beam line elements than solid body, detailed components.
A combination of methods will be employed
  Manual AISC/ASCE/Traditional calculations
  FEA verification to ASME BPVC
    Weld with joint efficiency = 1 due to compressive welds
    FESHM Safety not explicitly required for vacuum vessels
    Div. 1 vessels have a loading factor of 3.5

## Slide 4: Design Methodology cont.
Design of stands is based on the analysis of the cryomodules:
Exact details outside of the scope of this review
Stand Analysis
End Cover/Internal Components
Cryomodule Analysis

## Slide 5: Seismic Parameters

## Slide 6: Pipe Loading
Pipe | Description | Pressure (psi) |  | Apx. Thrust Loads (lbf) | 
 |  | Operating | Design | Operating | Design
A | 2.2 K Supply Line | 3 | 20 | 192.8 | 1285.1
B | Helium Gas Return | 0.031 | 4.1 | 53.3 | 7046.9
C | 4.5 K Supply Line | 3 | 20 | 192.8 | 1285.1
D | 5.5 K Return Line | 2.8 | 20 | 179.9 | 1285.1
E | 35 K Supply Line | 3.7 | 20 | 237.7 | 1285.1
F | 55 K Return Line | 2.7 | 20 | 173.5 | 1285.1
G | 2-Phase He Line | 0.031 | 4.1 | 5.7 | 747.3
H | Cool Down Warm Up Line | 3 | 20 | 94.2 | 627.8
 |  | Net Force (lbf): |  | 1129.8 | 14847.3
A
C
B
E
D
F

## Slide 7: Pipe Flange Loads
D
K
J
H
I
A
B
C
G
A
F
Port | Diameter (mm) | Area (in²) | Force (lbf)
A | 370 | 166.7 | 2449.9
B | N/A | 480.4 | 7062.1
C | 250 | 76.1 | 1118.5
D | 630 | 483.2 | 7102.7
E | 298.5 | 108.4 | 1594.0
F | 220 | 58.9 | 866.1
G | 260 | 82.3 | 1209.7
H | 253.2 | 78.0 | 1147.2
I | 250 | 76.1 | 1118.5
J | 220 | 58.9 | 866.1
K | 220 | 58.9 | 866.1
E

## Slide 8: Cryomodule Load Conditions
P2
P1
Load Case | Conditon Simulated | Loads
1 | Operation | P1 = 14.7 psi
 |  | P2 = 0 psi
 |  | Pipe Thrust
 |  | Acceleration = Gravity
2 | Seismic, Operation | P1 = 14.7 psi
 |  | P2 = 0 psi
 |  | Pipe Thrust
 |  | Acceleration = Gravity + 0.82G horizontal
3 | Transport, Support | P1 = 14.7 psi
 |  | P2 = 14.7 psi
 |  | Acceleration = 3G All Directions
4 | Insulating Vacuum Leak Check | P1 = 14.7 psi
 |  | P2 = 0 psi
 |  | Additional Seal Loads
 |  | Acceleration = Gravity
5 | Transport, Lugs | P1 = 14.7 psi
 |  | P2 = 14.7 psi
 |  | Acceleration = 3G All Directions
6 | Relief | P1 = 14.7 psi
 |  | P2 = 22.05 psi
 |  | Pipe Thrust
 |  | Acceleration = Gravity + 0.82G horizontal
Material | Tensile Strength (ksi) | Yield Strength (ksi) | Allowable Strength (ksi) | Elastic Modulus (psi) | Poisson's Ratio | Density (lbf/in^3)
ASTM A516 Steel, Grade 60 | 60 | 32 | 17.1 | 2.94E+07 | 0.3 | 0.28
ASTM A36 Steel | 58 | 36 | 16.6 |  |  | 
304 Stainless Steel | 75 | 30 | 20 | 2.83E+07 | 0.31 | 0.29
304L/316L Stainless Steel | 70 | 25 | 16.7 |  |  | 

## Slide 9: Cryomodule Loading Conditions

## Slide 10: Input Loading
Using the force reactions from the cryomodule the stand will be modeled at the supports:
Load Case | Loading Condition | Force Reaction (lbf) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Moment Reaction (lbf in) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Fixed Support |  |  |  |  |  |  |  | Sliding Support |  |  |  |  |  |  |  | Fixed Support |  |  |  |  |  |  |  | Sliding Support |  |  |  |  |  |  | 
 |  | Side Support 1 |  |  |  | Side Support 2 |  |  |  | Side Support 1 |  |  |  | Side Support 2 |  |  |  | Side Support 1 |  |  |  | Side Support 2 |  |  |  | Side Support 1 |  |  |  | Side Support 2 |  |  | 
 |  | X | Y | Z | Total | X | Y | Z | Total | X | Y | Z | Total | X | Y | Z | Total | X | Y | Z | Total | X | Y | Z | Total | X | Y | Z | Total | X | Y | Z | Total
1 |  | -1545.7 | -6243.1 | 1501.6 | 6604.566 | 1130.6 | -6651.0 | 951.2 | 6813.14 | -1455.2 | -5931.5 | -49.866 | 6107.601 | 1542.4 | -6271.6 | 56.803 | 6458.73 | -7079.6 | 1283.2 | -4075.3 | 8268.942 | -1924.2 | -1922.7 | 3138.8 | 4153.479 | 4919.7 | -1570.0 | -3156.8 | 6052.581 | 758.8 | 2160.7 | 2972.3 | 3752.185
2 | 1 | -2743.0 | -10018.0 | 1547.4 | 10501.0 | 2284.8 | -10661.0 | 898.9 | 10941.0 | -2373.2 | -9328.4 | -59.3 | 9625.7 | 2471.3 | -9429.4 | 67.8 | 9748.1 | -9643.4 | 2327.0 | -6397.8 | 11804.0 | -4967.4 | -2953.7 | 5346.1 | 7872.8 | 6506.7 | -2116.7 | -4984.3 | 8465.2 | 1473.2 | 2810.2 | 4648.6 | 5628.2
 | 2 | -342.7 | -2473.8 | 1457.7 | 2891.7 | -29.6 | -2648.9 | 999.3 | 2831.3 | -549.3 | -2555.7 | -40.4 | 2614.4 | 624.9 | -3132.3 | 45.5 | 3194.4 | -4591.0 | 292.2 | -1763.0 | 4926.6 | 1045.2 | -927.9 | 946.3 | 1687.9 | 3386.0 | -1052.8 | -1366.8 | 3800.2 | 98.8 | 1534.4 | 1334.8 | 2036.1
 | 3 | -2331.7 | -6855.6 | -5589.6 | 9147.7 | 2169.6 | -8393.3 | -6120.0 | 10612.0 | -897.2 | -5335.3 | 32.9 | 5410.3 | 795.3 | -4528.6 | 99.9 | 4598.9 | -14899.0 | 3695.9 | -4546.2 | 16010.0 | -9554.7 | -4832.1 | 4594.6 | 11651.0 | -691.5 | -945.1 | -2523.9 | 2782.4 | -2337.0 | 1043.0 | 1870.7 | 3169.9
 | 4 | -737.8 | -5615.5 | 8603.1 | 10300.0 | 61.9 | -4889.2 | 8010.3 | 9384.7 | -2010.5 | -6527.9 | -132.9 | 6831.8 | 2292.7 | -8017.5 | 14.0 | 8338.9 | 754.7 | -1171.8 | -3572.0 | 3834.3 | 5574.4 | 940.9 | 1646.7 | 5888.2 | 10566.0 | -2208.0 | -3790.4 | 11440.0 | 3939.2 | 3309.9 | 4080.3 | 6566.7
 | 5 | -2486.4 | -1533.3 | -1780.9 | 3421.2 | -1161.1 | -11003.0 | 4263.9 | 11857.0 | -4887.3 | -6032.9 | 109.2 | 7764.9 | -2772.6 | -6046.7 | -129.7 | 6653.3 | -3091.7 | 3697.2 | -1489.1 | 5044.4 | -8961.0 | 249.3 | 5099.5 | 10313.0 | -2222.6 | -4811.3 | -3975.7 | 6625.3 | 3260.3 | -47.6 | 1736.9 | 3694.4
 | 6 | -577.3 | -10649.0 | 4854.8 | 11717.0 | 3454.5 | -2153.3 | -2441.0 | 4746.5 | 1918.3 | -5706.8 | -201.7 | 6023.9 | 5780.9 | -6280.2 | 236.3 | 8539.1 | -10704.0 | -1256.2 | -6682.6 | 12681.0 | 5391.8 | -4012.2 | 1381.4 | 6861.3 | 11858.0 | 1584.4 | -2547.3 | 12232.0 | -1992.0 | 4224.5 | 4445.8 | 6448.2
3 | 1 | -4306.1 | -13612.0 | 147.3 | 14278.0 | 4159.3 | -14536.0 | -168.2 | 15121.0 | -3303.5 | -12216.0 | -29.9 | 12655.0 | 3253.6 | -11358.0 | 35.4 | 11815.0 | -8654.8 | 3425.1 | -8317.1 | 12482.0 | -11087.0 | -3678.2 | 8068.5 | 14197.0 | 5105.4 | -1847.1 | -6651.2 | 8585.8 | 2294.4 | 2222.4 | 6158.6 | 6937.7
 | 2 | 2833.9 | 10804.0 | -173.7 | 11171.0 | -2689.8 | 11334.0 | 173.1 | 11650.0 | 3722.7 | 12857.0 | 36.8 | 13385.0 | -3732.3 | 12389.0 | -47.7 | 12939.0 | 5492.5 | -2425.9 | 6276.4 | 8685.9 | 6238.8 | 2557.1 | -5976.3 | 9009.9 | -7823.8 | 2147.7 | 7173.8 | 10830.0 | -4403.5 | -2767.3 | -6864.1 | 8611.9
 | 3 | -2758.3 | -2256.2 | -26001.0 | 26244.0 | 3574.2 | -6171.4 | -25804.0 | 26771.0 | 2134.3 | 2348.3 | 299.1 | 3187.4 | -2674.2 | 6320.8 | 163.6 | 6865.1 | -28712.0 | 8763.7 | -1688.8 | 30067.0 | -27665.0 | -10527.0 | 5068.1 | 30031.0 | -20220.0 | 2175.2 | 2332.2 | 20470.0 | -11150.0 | -3970.0 | -3960.2 | 12481.0
 | 4 | 3009.3 | 2411.5 | 26039.0 | 26323.0 | -3846.5 | 6334.5 | 25766.0 | 26810.0 | -2032.6 | -2288.0 | -299.8 | 3075.1 | 2588.0 | -6262.3 | -162.9 | 6777.9 | 28681.0 | -8972.4 | 1955.3 | 30115.0 | 27774.0 | 10616.0 | -5406.0 | 30221.0 | 20188.0 | -2190.9 | -2211.5 | 20427.0 | 11234.0 | 4006.8 | 3837.5 | 12530.0
 | 5 | -4139.4 | 17481.0 | -12546.0 | 21912.0 | -8153.7 | -16858.0 | 12691.0 | 22622.0 | -14512.0 | -2136.9 | 693.6 | 14685.0 | -17371.0 | 1911.8 | -812.4 | 17495.0 | 15282.0 | 9849.6 | 8930.3 | 20256.0 | -26648.0 | 9028.8 | 6157.0 | 28802.0 | -26130.0 | -11210.0 | -3985.4 | 28712.0 | 8162.9 | -7729.2 | -6247.8 | 12861.0
 | 6 | 3794.3 | -17073.0 | 12599.0 | 21555.0 | 8486.4 | 17235.0 | -12770.0 | 23068.0 | 14417.0 | 2217.1 | -696.3 | 14603.0 | 17489.0 | -1824.0 | 815.5 | 17602.0 | -14441.0 | -9402.2 | -8908.3 | 19399.0 | 29003.0 | -9785.9 | -6276.8 | 31247.0 | 24744.0 | 10482.0 | 3900.8 | 27154.0 | -9255.4 | 8328.7 | 6206.3 | 13912.0
4 |  | -2632.1 | -7606.5 | -10924.0 | 13569.0 | 2632.1 | -9044.7 | -10645.0 | 14215.0 | -731.0 | -4383.8 | -3.5 | 4444.3 | 387.8 | -3682.9 | 2.4 | 3703.3 | -16328.0 | 5249.6 | -5094.2 | 17892.0 | -13188.0 | -6006.1 | 5307.9 | 15433.0 | -1841.1 | -596.8 | -2248.6 | 2966.8 | -2998.1 | 452.7 | 1549.6 | 3405.1
6 | 1 | -1685.6 | -4141.0 | -10895.0 | 11776.0 | 2217.2 | -4925.1 | -11063.0 | 12311.0 | 543.8 | -476.4 | 6.0 | 723.0 | -118.3 | 1531.4 | -3.7 | 1535.9 | -10895.0 | 3794.0 | -2409.5 | 11786.0 | -12208.0 | -4832.9 | 3246.4 | 13525.0 | -5015.4 | 843.2 | 235.1 | 5091.2 | -5176.9 | -366.8 | -387.4 | 5204.3
 | 2 | -2825.6 | -7830.2 | -10861.0 | 13684.0 | 3319.7 | -8871.6 | -11104.0 | 14596.0 | -357.2 | -3807.6 | -2.2 | 3824.3 | 765.3 | -1567.1 | 6.0 | 1744.0 | -13448.0 | 4793.2 | -4626.3 | 15008.0 | -15354.0 | -5896.0 | 5403.0 | 17312.0 | -3643.5 | 354.0 | -1564.5 | 3980.9 | -4529.6 | 239.0 | 1277.2 | 4712.3
 | 3 | -529.1 | -446.1 | -10935.0 | 10957.0 | 1098.1 | -967.5 | -11018.0 | 11115.0 | 1433.4 | 2843.3 | 13.9 | 3184.2 | -995.2 | 4623.2 | -13.5 | 4729.1 | -8623.4 | 2908.8 | -184.9 | 9102.7 | -9262.1 | -3862.4 | 1076.8 | 10093.0 | -6368.1 | 1329.2 | 2022.4 | 6812.5 | -5796.4 | -967.2 | -2046.6 | 6222.7
 | 4 | -2410.5 | -4747.2 | -17984.0 | 18755.0 | 3153.4 | -6588.5 | -18135.0 | 19550.0 | 1134.4 | 174.5 | 88.0 | 1151.1 | -844.9 | 3254.0 | 40.9 | 3362.1 | -18589.0 | 6148.9 | -2825.8 | 19783.0 | -19614.0 | -7704.4 | 4581.4 | 21565.0 | -10493.0 | 1428.2 | 879.9 | 10627.0 | -8195.0 | -1446.5 | -1462.1 | 8449.2
 | 5 | -887.3 | -3490.8 | -3798.5 | 5234.6 | 1202.6 | -3214.1 | -4001.5 | 5271.5 | -43.3 | -1125.3 | -76.2 | 1128.7 | 608.7 | -192.1 | -48.1 | 640.1 | -3236.1 | 1464.6 | -1911.7 | 4033.9 | -4823.1 | -2001.8 | 1819.6 | 5529.9 | 484.9 | 249.7 | -407.4 | 680.8 | -2126.4 | 724.7 | 687.6 | 2349.3
 | 6 | -2744.4 | 359.7 | -14061.0 | 14331.0 | -63.3 | -9314.7 | -7862.4 | 12189.0 | -2842.3 | -611.1 | 154.7 | 2911.4 | -4313.8 | 1594.9 | -179.0 | 4602.7 | -7237.6 | 6361.4 | 19.3 | 9635.9 | -19686.0 | -3051.1 | 5065.7 | 20555.0 | -11843.0 | -2315.9 | -481.1 | 12077.0 | -2486.4 | -2343.9 | -1699.0 | 3816.1
 | 7 | -588.2 | -8567.0 | -7739.9 | 11561.0 | 4471.0 | -477.1 | -14257.0 | 14949.0 | 3871.0 | -386.1 | -143.8 | 3892.9 | 4120.4 | 1448.4 | 171.7 | 4370.9 | -14963.0 | 1552.4 | -4781.8 | 15785.0 | -5032.5 | -7004.8 | 1380.2 | 8734.9 | 1829.3 | 3896.0 | 899.9 | 4397.2 | -7880.1 | 1681.5 | 952.5 | 8113.6
1
2

## Slide 11: Maximum Forces/Moments
Converting all of the Forces/Moments to maximum conditions…
Largest Combined Force/Moment:
  26,810.0 lbf of force
  31,247.0 lbf-in of moment
Force (lbf) |  |  | Moment (lbf-in) |  | 
X | Y | Z | X | Y | Z
17,489 | 17,481 | 26,039 | 29,003 | 11,210 | 8,930.3
X
Y
Z

## Slide 12: Initial Assessment
Initial assessments indicated that the assembly would not be able to withstand loading.
Bolts would exceed slip critical conditions
Anchors overloaded without considering effects of friction
Bolt tear-through occurred on FEA models at anchors and at the attachment points of the stand

## Slide 13: Design Changes

## Slide 14: Simulation Setup
Load Step | Load Scaler | Purpose
1 | 0 | Gravity
2 | 1 | Initial Loading
3 | 1.7 | Local Failure
4 | 2.4 | Div. 2 Plastic Collapse
5 | 3.5 | Div. 1 Plastic Collapse

## Slide 15: Load Case 1

## Slide 16: Load Case 2 Plastic Collapse
LC1
LC2
LC3
LC4
LC5
LC6

## Slide 17: Load Case 2 Local Failure
LC1
LC2
LC3
LC4
LC5
LC6

## Slide 18: Load Case 4

## Slide 19: Load Case 6 Plastic Collapse
LC1
LC2
LC3
LC4
LC5
LC6

## Slide 20: Load Case 6 Local Failure
LC1
LC2
LC3
LC4
LC5
LC6

## Slide 21: Load Case 6, Condition 7

## Slide 22: Conclusions
Design of stands have been validated using FEA using ASME BPVC Design by Analysis methods.
Manual Calculations have also been performed to validate the design of the components.
  Details can be seen in backup slides.
Results show that the design will be able to withstand all relevant loading conditions
Stands have been updated to be made wider to account for

## Slide 23
Backup Slides

## Slide 24: First-Order Stand Reactions to Vacuum Loading:
Assume radius of 22.8”
Pressure of 14.7 psi
F = 24,080 lbf
1
Assume center of connection is center of fixed stand
Generated Moment at anchorage center = 784,820 lbf-in
32.5922”
58.7488”
2
Force at other stand will help balance out
Will occur even without anchors
Force = 13,359 lbf for 100% absorption
3

## Slide 25: Stand Component Flexure
Simplified Cross Section:
Hollow Tube
Wall Thickness: 0.5”
Ix: 113.0833 in^4
Iy: 71.0833 in^4
6”
8”
Simplified Cross Section:
2 Rectangular Bars
Ix: 54.1218 in^4
Iy: 0.7217 in^4
1”
8.66”
Simplified Cross Section:
Rectangular Bar
Ix: 43.7965 in^4
Iy: 0.6725 in^4
1”
8.07”
X
Y
Parts made of A36 Steel
Em = 29e6 psi
Ys = 36 ksi
Yt = 58 ksi

## Slide 26: Stand Flexure Calculations
X-Axis Force
Moment Arm (l): 20.3”
Iy: 0.6725 in^4
c = 0.5”
=2,385.2 lbf
Y-Axis Force
Moment Arm (l): 20.3”
Ix: 43.7965 in^4
c = 4.035”
= 19,249 lbf
X-Axis Force
Moment Arm (l): 8.5433”
Iy: 0.7217 in^4
c = 0.5”
/2= 6,082.2 lbf
Y-Axis Force
Moment Arm (l): 8.5433”
Ix: 54.1218 in^4
c = 4.33”
/2= 52,670 lbf
X-Axis Force
Moment Arm (l): 20.25”
Iy: 71.0833 in^4
c = 3”
= 42,123 lbf
Y-Axis Force
Moment Arm (l): 20.25”
Ix: 113.0833 in^4
c = 4”
= 50,259 lbf
lbf
X
Y
Assumptions: Find Max Load Part can hold assuming maximum possible bending moment (x-Axis force) or half the width of the part (y-Axis force) as per AISC 360 Section F7
Combined, all sections should have a combined of 51,004.8 lbf the X axis Direction and 157,363.2 lbf in the y axis direction
Limit of forces is 26,810 lbf, combined stands can reset moments

## Slide 27: Bolt Limits
Three Sets of Bolts hold the stand together
Two in slip critical conditions, one just withstanding vertical loads.
SHCS M24 x 3 Class 8.8
SF-568M
Proof Load: 212 kN - 233 kN
Proof Load: 47.7klbf – 52.4 klbf
HHCS 1”-8
SA-325
Proof Load: 51.5 klbf – 55.8 klbf
M36 x 2 Connection
SF-568M (for M36x4)
Proof Load: 184 kN - 792 kN
Proof Load: 41.4 klbf – 178 klbf

## Slide 28: Bolt Moment Reactions pt. 1
133.35 mm
47.625 mm
41.275 mm
55.88 mm
69.4709 mm
141.5993 mm
F = F’+F’’
  V = Shear Force
  N = # of bolts
  M = Applied Moment
  R = Distance from Center
F = ____
Bolt Shear =
A = bolt area
____
Bearing Area Stress =
318.8792 mm
F = F’+F’’
  V = Shear Force = 26,039 lbf
  N = # of bolts
  M = Applied Moment = 29,003 lbf-in
  R = Distance from Center
F = 9,174.3 lbf
Bolt Shear =
A = bolt area = 0.7012
13,084 psi
Bearing Area Stress =
Bearing Area = 0.945 in²
9,708 psi

## Slide 29: Base Force Reactions
To transfer the forces to the bottom set of bolts:
Moment loading will transfer.
  For the sake of being conservative, it will be assumed to be additive.
    P = 26,039 lbf, x = 12.5543 in
    M_r = 326,900 lbf-in
  Combined Moment Reaction of 355,900 lbf-in
Reaction Force of 26,810 lbf
M
M
M_r
P
F

## Slide 30: Bolt Moment Reactions pt. 2
133.35 mm
47.625 mm
41.275 mm
55.88 mm
69.4709 mm
141.5993 mm
F = F’+F’’
  V = Shear Force = 26,810 lbf
  N = # of bolts
  M = Applied Moment = 355.9 klbf-in
  R = Distance from Center
F = 22,663 lbf
Bolt Shear =
A = bolt area = 0.7854
28,855 psi
Bearing Area Stress =
Bearing Area = 1 in²
22,663 psi
318.8792 mm
F = F’+F’’
  V = Shear Force = 26,039 lbf
  N = # of bolts
  M = Applied Moment = 29,003 lbf-in
  R = Distance from Center
F = 9,174.3 lbf
Bolt Shear =
A = bolt area = 0.7012
13,084 psi
Bearing Area Stress =
Bearing Area = 0.945 in²
9,708 psi

## Slide 31: Slip Critical Conditions
To determine if the connection will hold, slip critical bolt calculations will be performed as per J3-4 and J3-5a using LRFD methods.
Where
= 0.7, , = proof load of fastener, =number of slip plains (1), = 0.3
= factor for fillers (1.0 for SHCS, and 0.85 for HHCS in this configuration)
The Bolts can hold:
SHCS = 11,309 lbf per bolt (45,238 lbf for 4 bolts)
  - 25% pretension from SHCS issues, 8,482 lbf per bolt, 32,550 lbf for 4 bolts.
HHCS = 10,388 lbf per bolt (39,989 lbf for 4 bolts)

## Slide 32: Slip Critical Condition Maintained
The slip critical condition of the side plate is not able to maintain a slip critical condition during the highest load case. If the plate is in contact with the bottom of the plate.
Moment needs to resist ~355.9 klbf-in
  Reaction force of 49,776 lbf needed.
  Cross section area of apx. 7.925 in² at the reaction location
  ~6,281 psi of shear stress.
    Within limits of material
All of these assumptions are if contact can be made
  Otherwise bolts can slip
7.15 in
49,776 lbf
355.9 klbf-in

## Slide 33: Base Reactions
17.2667 in
6.2667 in
11.5496 in
Component is held to ground through 6 anchor bolts.
Maximum Loads:
Shear Anchors
  Resist F_x, F_z, My
Moment Anchors
  Resist F_y, M_x, M_z
Will assume all loads will combine
  Assuming no friction.
Z
X
Y
Force Reaction (lbf) |  |  | Moment Reaction (lbf-in) |  | 
X | Y | Z | X | Y | Z
4,692.1 | 9,469.7 | 6,517.1 | 17,967.1 | 5,452.4 | 5,301.2
Force Reaction (lbf) |  |  |  | Moment Reaction (lbf-in) |  |  | 
X | Y | Z | Total | X | Y | Z | Total
7,991.4 | 20,679 | 36,119 | 37,863 | 38,204 | 116,550 | 152,640 | 183,300

## Slide 34: Anchor Reactions
F = F’+F’’
  Fxz = Shear Force = 36,992 lbf
  N = # of bolts
  My = Applied Moment = 116,550 lbf-in
  R = Distance from Center
F = 23,542 lbf
Bolt Shear =
A = bolt area =
Bearing Area Stress =
Bearing Area =
F = F’+F’’
  Fy = Tension Force = 20,679 lbf
  N = # of bolts
  Mx = Applied Moment = 38,204 lbf-in
  R = Distance from Center = 11.5496 in
  Mz = Applied Moment = 152,640 lbf-in
  R = Distance from Center = 15 in
F = 8,540.7 lbf
Bolt Tension =
A = Anchor Area =
Shear Anchors
Tension Anchors

## Slide 35: Design Changes
Slip critical and Anchor Loading was exceeded in calculations
To ensure that the components will withstand loading, modifications will be made.
Calculations that will be examined are:
  SHCS M24 X3 Class 8.8
    SF-568M
  HHCS 1”-8
    SA-325
  Anchor Bolts
    Will use HILTI HVU2 Anchors
    Anchor_PTG_21 final.pdf (hilti.com)
    6 1” Dia. Shear Anchors => ~7,847.3 lbf per anchor
    8 Tension Anchors with current design => ~4,270.4 lbf per anchor
    Connection significantly overdesigned, but room to reduce number if SLAC team needs to reduce anchorage
      Their design decision.

## Slide 36: HHCS Considerations
6” Radius
4 Bolts
6 Bolts
8 Bolts
8” Radius
10” Radius
12” Radius
Old Configuration
New Configuration

## Slide 37: Bolt Design Design
To increase the slip critical loading of the bolted connections:
SHCS should be switched to M30x3.5
  Will have a proof load of 17,978 lbf per bolt and 71,912 lbf for the set
  FEA switched to M36x4.0 to 26,140 lbf per bolt and 104,560 lbf for the set
HHCS will require more design changes
  Largest bolt load is 20,977.3 lbf for 1 1/2 -6 bolt
  HHCS connection will be designed for
    1 1/4 -7 Bolt
      Slip load of 14,462.2 lbf per bolt
      57,849 lbf for full set

## Slide 38: Anchorage Design
Anchorage design is complex and relates a lot to SLAC design parameters.
If stand is larger, design effort and their requirements should be handled by SLAC.
Updated Design
  6, 1” Dia. Shear Anchors => ~7,847.3 lbf per anchor
    Total of 47,083.8 lbf total
    May need 1-2 more to exceed 54,368.08 lbf as per ASCE 7-16 base shear
      If friction is allowed to be used, this is not an issue.
  8, Tension Anchors with current design => ~4,270.4 lbf per anchor
  Calculations based on old ones, will be lower
  Connection significantly overdesigned, but room to reduce number if SLAC team needs to reduce anchorage