## Slide 1
Muon Spin Rotation Spectroscopy
Utilizing Muons in Solid State Physics
Andreas Suter
Laboratory for Muon Spin Spectroscopy
Paul Scherrer Institute, Switzerland

## Slide 2: µSR Facilities around the World
J-PARC (2009)
from “µSR brochure” by J.E Sonier, Simon-Fraser-Univ., Canada, 2002. http://musr.org/intro/musr/muSRBrochure.pdf
pulsed (50Hz) muon beams
continuous muon beams
pulsed (25Hz) muon beams
continuous muon beams

## Slide 3: µSR Facilities around the World
Cyclotron (1972)
590 MeV Ring Cyclotron

## Slide 4: Proton Accelerator at PSI
Cockcroft Walton 870keV
Injector II Cyclotron 72 MeV
Ring Cyclotron 590 MeV
2.2 mA / 1.3 MW
Pion/Muon
Production Targets
Center for
Proton Therapy
(250MeV SC Cyclotron)
SINQ
Neutron Spalation Source
Ultra Cold Neutrons

## Slide 5: Muon Production – Example: Target E at PSI
Rotating Graphite Target (1 Hz)
Radiation Cooled, Tavg = 1700K
Thickness t=40 mm; h=6 mm;  450 mm
Radiation Losses 30%
590 meV p beam
rotation axis
Pions / Muons
t
h
Target E
solenoids
quadrupoles
T.Prokscha et al NIM-A (2008)
2200 μA ≈ 1.4∙106 p/sec →
≈ 107 – 108 μ+/sec
100% polarized
Surface Muons: ≈ 4 MeV
μE4 beamline at PSI: 4 ∙ 108 μ+/sec

## Slide 6: Beam Power of Accelerators World Wide
from M.Seidel, GFA, PSI

## Slide 7: Parity Violation is at the Heart of μSR
1st step: 100% polarized muon, i.e. P=1 (NMR: P ≈ 10-5)
φ
2nd step:
Positrons preferentially emitted along the direction of muon spin at decay time

## Slide 8: Surface Muons Stopping in Matter
Muon
Production
Surface Muons
Energy: 4.1 MeV
v ≈ 0.27 c
Sample
Ionization of atoms
105 – 106 excess e–
2-3 keV
v ≈ 0.007 c
Muonium formation (μ+e–)
charge cycling
100 eV
v ≈ 0.0013 c
mainly elastic collisions
(dissociation, μ+e– → μ+)
stop typically at an interstitial site
thermalized μ+
Total stopping time in matter < 0.1 ns
Only electrostatic processes → no loss of polarization!
Penetration ≈ 0.1 mm
Low Energy Muons:
much less excess electrons
Penetration ≈ 1 – 200 nm

## Slide 9: Different Energies for Different Studies
LE µSR
Bulk µSR
Decay beam
Surface beam
Cu
Cosmic muons
Bulk µSR:
“Normal” samples (sub-mm)
Bulky samples or samples in containers or pressure cells
LE-µSR:
Depth-selective investigations (1–200 nm)

## Slide 10: Muon Spin Precession – Bloch Equation
Left side: Sz is an eigenstate and hence nothing happens. (spont. emission rate at 10T: 10-12sec)
Right side:
Sz is NOT an eigenstate and hence the state due mix → precession
Ehrenfest Theorem
m
B
θ
Larmor frequency
Bloch Equation
Dissipation due to a heat bath

## Slide 11: Principle Setup for Time Differential μSR
Bµ
Bμ internal or external field
G(t) contains the physics

## Slide 12: μSR Spectra
Frequency  Value of field at muon site Damping  Field distribution
aG(t) ~ Muon Spin Polarization

## Slide 13: μSR Spectra - Fourier
f(Bµ)
<Bµ>
θ angle between magnetic field and muon polarization at t = 0 By choosing θ = 90°, one obtains:
P(0)
Bμ
θ
P(0) sin2θ cos(γ Bμ t=0)
P(0) cos2θ

## Slide 14: μSR: Time Window and Sensitivity
µSR time window: 10-20 µsec  Frequencies down to 50 kHz detectable Fields of few Gauss Distributions of few tens of a Gauss (perfect earth field compensation required!!)
Internal field at the muon site:
contact field
 static moments as low as 0.001 μB can be detected by μSR
m

## Slide 15: μSR: Magnetic Volume Fraction
Inhomogenous
Homogenous
Amplitude = Magnetic Volume Fraction
Frequency = Value of the field at the muon site
Damping = Magnetic field distribution

## Slide 16: μSR Techniques
Zero-Field / Longitudinal Field (ZF / LF), B parallel to the muon spin LF: distinguish between static and dynamic contributions
Transverse Field (TF) B perpendicular to the muon spin → precession
Avoided Level Crossing (ALC) B parallel to the muon spin → spin flip and spin flip-flop transitions
Radio Frequency-µSR (RF-µSR)
time-differential µSR Ni(t) = Ni(0)exp(-t/tµ)[1+aG(t)] + Bkg (ZF, LF, TF, RF-µSR)
time-integral µSR Ni = ∫ Ni(t) dt Forward-Backward asymmetry (F-B)/(F+B)= ∫e-st aG(t) dt, s=1/tµ, Laplace transform of aG(t) (LFQ, ALC, RF-µSR)

## Slide 17: Muon Beam Time Structure
ISIS
324 ns
FWHM
68 ns
20 ms
20 ms
double pulse structure
every 5th pulse missing (goes to TS2)
J-Parc
600 ns
FWHM
65 ns
40 ms
40 ms
double pulse structure
with gaps to fill the 50GeV ring
(26ns)
(26ns)
(26ns)
(26ns)
Triumf
26ns wide pulses every 43ns
PSI
26ns wide pulses every 20ns

## Slide 18: Difference between CW and Pulsed Beams
Pulsed (50Hz) Muon Beams
Continuous Muon Beams
Very good time resolution (down to ~60 ps) → Detection of large magnetic fields
→ Detection of fast relaxing signals
No negligible background (this can be improved by MORE)
Reduction of the muon rate to avoid “pileup”
Very low background → measure slow relaxation
High muon rates possible, but this requires highly segmented detector systems
Limited time resolution (~ 10-20 ns) → Detection of large magnetic fields and/or fast relaxing signals impossible

## Slide 19: What means good timing? The High Field Instrument at PSI
Oxford Instruments 8 / 9.5T
Recondensing System

+
e+
Sample
Scintillators
Muon
counter
Veto
counter
Ø 32mm
APD Spectrometer
A. Stoykov et al. Physics Procedia 30, 7, (2012)
http://lmu.web.psi.ch/facilities/facility.html
Notes: TDC V1290A Caen
CFD950 PSI

## Slide 20: What means good timing? The High Field Instrument at PSI
1
2
3
4
Mu
E/ħ (MHz)
12
34
B (T)
Muonium in synthetic quartz crystal @ 8.0T
→ Time resolution from amplitude ratios

## Slide 21: Typical Research Fields of μSR
Magnetism
Superconductivity
Semiconductor Physics
Chemistry

## Slide 22: Typical Research Fields of μSR
ZF-μSR on YBaCo2O5.49
Magnetism
Superconductivity
Semiconductor Physics
Chemistry
Spin State Ordering in RBaCo2O5.5 / Luetkens et al. PRL101, 017601 (2008)

## Slide 23: Typical Research Fields of μSR
Magnetism
Superconductivity
Semiconductor Physics
Chemistry
Frustrated magnets: Twoards an Ideal Kagomé Lattice ZnxCu4-x(OH)6Cl2
P. Mendels et al. PRL98, 077204 (2007)
x=1
AF
AF
AF
?

## Slide 24: Typical Research Fields of μSR
Magnetism
Superconductivity
Semiconductor Physics
Chemistry
Exotic Superconductivity: Nonunitary Triplet Pairing in the Centrosymmetric Superconductor LaNiGa2 A.D. Hillier et al. PRL109, 097001 (2012).

## Slide 25: Typical Research Fields of μSR
Magnetism
Superconductivity
Semiconductor Physics
Chemistry
Bext
Bext
Magnetic Field Distribution
due to Vortices

## Slide 26: Typical Research Fields of μSR
T>Tc
T<Tc
damping, σ
→ magnetic penetration depth, λ (via theory)
→ Uemura plot: classification of superconductors
μSR studies of the vortex state in type-II superconductors, J.E. Sonier et al., RMP 72, 769 (2000)
Magnetism
Superconductivity
Semiconductor Physics
Chemistry
s-wave
d-wave
Uemura et al. PRL66, 2665 (91)

## Slide 27: Typical Research Fields of μSR
Magnetism
Superconductivity
Semiconductor Physics
Chemistry
C.G. Van de Walle & J. Neugebauer, Nature 423, 626 (2003)
Universal alignment of hydrogen levels in semiconductors, insulators and solutions
E.A. Davis et al., APL82, 592 (2003)

## Slide 28: Typical Research Fields of μSR
Magnetism
Superconductivity
Semiconductor Physics
Chemistry
static
Roduner et al., J. Phys. Chem. A 102, 7591 (1998)
Dynamics of Muoninated C6H6Mu
Pol.
Notes: Delta0: muon-proton spin flip-flop
Delta1: muon spin flip
Delta2: muon-proton spin flip-flip

## Slide 29: Generation of Thermal μ+ at a Pulsed Muon Beam
P. Bakule,Y.Matsuda,Y.Miyake, K. Nagamine, M. Iwasaki,
Y. Ikedo, K. Shimomura, P. Strasser, S. Makimura
Nucl. Instr Meth. B 266, 335 (2008)
Pulsed beam (25Hz) @ RIKEN-RAL:
Intensity: ~15 LE-μ+/sec Polarization: ~50% Beam Spot: 4mm

## Slide 30: Generation of Polarized Epithermal μ+
100 μm Ag
 500 nm
s-Ne, Ar,
s-N2
6 K
„Surface“
Muons
 4 MeV
 100% polarized
T. Prokscha et al., Appl. Surf. Sci. 172, 235 (2001).
T. Prokscha et al., Phys. Rev. A58, 3739 (1998).
E. Morenzoni et al,. J. Appl. Phys. 81, 3340 (1997).
D. Harshmann et al., Phys. Rev. B36, 8850 (1987).
motivated by experiments for positron moderation

## Slide 31: Characteristics of Epithermal μ+
Layer Thickness [nm]
Efficiency [a.u.]
E. Morenzoni, et al. Phys.Rev.Lett. 72, 2793 (1994).
AP(t)
P(0) 1
time [μsec]
Eg
suppression of electronic energy loss for E<Eg (Eg ~ 10-20eV)
large escape depth L~ 50-200nm
moderation efficiency:
no loss of polarization during the moderation

## Slide 32: Low Energy μ+ Beam and Setup for LE- μSR
Spin
Surface μ+ beam ≈ 4MeV
≈ 1.7 ∙ 108 μ+/sec
UHV chambers, 10-10 mbar
All transport elements LN2 cooled
Beamspot at the sample position
T = 2.5 – 320 K
B = 0 – 0.3 T
Polarized Low Energy Muon Beam
Energy: 0.5 - 30 keV
ΔE, Δt: 400 eV, 5 ns
Depth: ≈ 1 – 300 nm
Polarization: ≈ 100 %
Beam Spot: 10-20 mm
≈ 4500 μ+/sec
≈ 1.1 ∙ 104 μ+/sec
accelerate up to
20keV

## Slide 33: Low Energy μ+ Beam and Setup for LE-μSR
Muon Spin
Muon Momentum
Moderator low energy μ+
source
Mirror
energy filter
Trigger
implantation time
Spin-Rotator / Separator
E-Field
B-Field
Sample Cryo

## Slide 34: μE4 Beamline at PSI
At 2 mA proton current:
≈ 4.0 ∙ 108 μ+/s total, Δp/p = 9.5% (FWHM) ≈ 1.7 ∙ 108 μ+/s on LEM moderator
T. Prokscha, E. Morenzoni, K. Deiters, F. Foroughi,
D. George, R. Kobler, A. Suter and V. Vrankovic
Nucl. Instr. Meth. A 595, 317 (2008).

## Slide 35: Meissner State Measurements
B(z)
z
0
Superconductor in the Meissner State
Bext
l

## Slide 36: keV μ+ Stopping Profiles in Matter
YBa2Cu3O7-δ
E. Morenzoni et al., Nucl. Instr. and Methods B 192, 254 (2002 )

## Slide 37: Absolute Determination of the Magnetic Penetration Depth
A. Suter et al., PRB 72, 024506 (2005).

## Slide 38: Example: Anisotropy of the Meissner State in YBa2Cu3O6.95
samples produced by R. Liang, W. Hardy, D. Bonn, Univ. of British Columbia
← effective mass
← superfluid density
Allows to measure the temperature dependence of nS (T), and hence, i.e. the gap symmetry.

## Slide 39: Example: Anisotropy of the Meissner State in YBa2Cu3O6.95
100 K
8 K, 14.1 keV
8 K
at low T for a d-wave SC:
λa = 126(1.2)nm, λb = 105.5(1.0) nm, λa/λb =1.19(1)
R.F. Kiefl et al., PRB 81, 180502(R), (2010).

## Slide 40: Fermilab Nb Cavity Meissner Screening
Clear difference of the Meissner response between cold and hot parts!

## Slide 42: Spatially homogeneous ferromagnetism of (Ga,Mn)As
muon decay asymmetry (10 mT TF top) and zero field (ZF) relaxation rate (bottom) as a function of temperature and doping
Mn-doped GaAs potential ‘spintronics’ material
great interest in fundamental research: evolution from a paramagnetic insulator to ferromagnetic metal
controversy if FM is associated with intrinsic spatial inhomogeneity
Low-energy µSR (in combination with conductivity and DC/AC magnetization) results:
sharp onset of FM order, developing homogeneously in the full volume fraction, in both insulating and metallic films.
smooth evolution of ordered moment size across metal-insulator transition at x ~ 0.03
FM coupling between Mn before full emergence of itinerant hole carriers
S.R. Dunsiger, et al., Nature Materials 9, 299 (2010).

## Slide 43: Dimensionality Control of Electronic Phase Transitions
Motivation
Dimensional tuning of collective electronic phases in order to stabilize new phases.
LaNiO3 is a correlated metallic paramagnet down to the lowest temperatures, whereas RNiO3 are typically showing a metal-insulator transition, accompanied by a magnetic phase transition, e.g. NdNiO3. Hence LaNiO3 is an interesting case.
A.V. Boris et al., Science 332, 937 (2011).
Results
LaNiO3/LaAlO3 N=4 superlattices are similar to LaNiO3 bulk.
LaNiO3/LaAlO3 N=2 superlattices show a metal-insulator transition, and at lower temperature a magnetic phase transition (likely to be antiferromagnetic).
Contrary to bulk, TMI ≠ TN.
Strain is NOT the driving mechanism since both superlattices grown on LaSrAlO4 or SrTiO3 substrates show a similar behaviour.

## Slide 44: Measuring the Spin-Diffusion Length in a Functional Organic Spin Valve
Motivation / Questions
Organic semiconductors are very promising candidates for spintronic devices (cheap, flexible, long spin coherence times).
Is it possible to measure the spin–diffusion length in an operational device, i.e. within buried interfaces?
Results
Measurement of the spin-diffusion length in an operational device is possible.
In principle, the spin-diffusion length can be related to the
magneto-resistance.
A.J. Drew et al., Nature Mater. 8, 109 (2009).

## Slide 45: La2-xSrxCuO4 Heterostructures – Giant Proximity Effect
entire ‘barrier’ layer of thickness d much larger than typical c-axis coherence exhibits Meissner effect for temperatures well above Tc’
Supercurrents flow in c-direction and ab-planes.
Results:
The measured Meissner screening is not expected within conventional proximity effect theory and constrains the theory of HTS and our understanding of the pseudogap phase.
E. Morenzoni, et al., Nat. Commun. 2, 272 (2011).

## Slide 46: Cold Muonium Source
A. Antognini et al., PRL 108, 143401 (2012).
Thermalized Muonium from mesoporous thin SiO2 films.
At T=250K, >2 x more than from SiO2 powder at room temperature
Allows cw laser spectroscopy of 1S-2S interval from which the muon mass can be determined ≈ 1 order of magnitude more precise than previously measured.

## Slide 47: Low Dimensional Magnetism – La2-xSrxCuO4 Superlattices
A. Suter et al., PRL 106, 237003 (2011).
A few-unit-cells thick LaCu2O4 layers synthesized by MBE are antiferromagnetically ordered. Below a thickness of about 5 CuO2 layers the long-range ordered state breaks down, and a magnetic state appears with enhanced quantum fluctuations and a reduced spin stiffness.