## Slide 1: Network Engineering Group Update
Joe Metzger, Network Engineer
ESnet Network Engineering Group
ESCC
January 17 2013

## Slide 2: Outline
Current Network Status
Short-term next steps (6 months)
What comes after that?

## Slide 3: Current Status ESnet5 Transport Network
Shared Optical System
  All common components deployed & commissioned
  Dec 4th Optical System Inventory report has 6495 components!
    341 nodes total, 60+ are add/drop/regen
    80% are common, the rest are dedicated to ESnet or Internet2 (over 500 are XFPs.)
    Sunnyvale has 4 32-slot shelves
    Sacramento is a 7-direction node
  Still refining processes for sharing spectrum, chassis, configuration, management, etc.

## Slide 4
ESnet5 Optical System January 2012
Geography is only representational

## Slide 5
ESnet5 Optical System January 2012
Lit Waves
Notes: The long path from NERSC to Starlight is the 100G Testbed wave.

## Slide 6: ESnet5 Routed Network
Routers
  16 new Alcatel Lucent (ALU) 7750-SR12
    10-slot router with up to 200G per slot
    56 100G interfaces & 200+ 10G interfaces
  35 existing Juniper MX’s
    Used in 10G hubs, commercial exchange points, sites
  12 existing Juniper M7i & M10i
    For terminating links slower than GE
  5 very old Cisco 7206
    For terminating links slower than GE
Services
  Standard routed IP (including full Internet services)
  Point to Point Dynamic Virtual Circuits using OSCARS
  Various overlay networks (Private VPN’s, LHCONE VRF)

## Slide 7
SNLL
PNNL
LANL
SNLA
JLAB
PPPL
MIT/ PSFC
BNL
AMES
LLNL
GA
JGI
LBNL
SLAC
NERSC
ORNL
ANL
FNAL
Salt Lake
INL
GFDL
PU Physics
SEAT
STAR
CHIC
WASH
commercial peering points
R&E network peering locations
NASH
ATLA
HOUS
NEWY
AOFA
BOST
KANS
DENV
ALBQ
LASV
BOIS
SACR
ELPA
SDSC
LOSA
Routed IP 100 Gb/s
Routed IP 4 X 10 Gb/s
3rd party 10Gb/s
Express / metro 100 Gb/s
Express / metro 10G
Express multi path 10G
Lab supplied links
Other links
Tail circuits
Major Office of Science (SC) sites
LBNL
Major non-SC DOE sites
LLNL
CLEV
ESnet optical transport nodes (only some are shown)
MANLAN
ESnet managed 10G router
10
ESnet managed 100G routers
100
Site managed routers
100
10
10
10
10
10
100
10
10
10
1
100
100
100
100
10
10
100
100
10
10
10
10
10
100
100
10
10
100
10
100
SUNN
ESnet PoP/hub locations
LOSA
ESnet optical node locations (only some are shown)
10
100
100
100
100
100
100
EQCH
Geography is only representational
ESnet5 January 2013
1
100
10
SUNN
100
100
100
10
100
CHAT
Notes: 7

## Slide 8
Example: Optical System in Sunnyvale

## Slide 9: Next 6 Months
  100G production connections to:
    ANL, BNL, FNAL, LBNL, LLNL, NERSC & ORNL
  100G production connections to exchange points & R&E peers:
    MANLAN, Starlight, PACWAVE, WIX, Internet2
  40G into Equinix Ashburn & re-arranging our Washington DC ring to provide diverse backbone connections for JLAB & other sites in the area
  Diverse fiber laterals & diverse optical nodes at ANL & FNAL
  Deploying diverse routers at ORNL
  Lots of cleanup & consolidation at the hubs, moving connections from the MX’s to the ALUs
  Normalize 100G Testbed infrastructure
  Swap out our un-supported ‘third party’ 10x10 MSA CFPs in our Ciena interfaces with Ciena supported ones covered by 4-hour on-site maintenance contract

## Slide 10: Disclaimer for rest of this slide deck
  The rest of this slide deck makes all sorts of assumptions
    Some have been carefully thought out
    Some haven’t had much thought at all
    Some we don’t even realize we are making
    Some of them are sure to be violated
  It is intended to spur thought and discussion.
    Not to come up with the right answers today, but to make sure we are not missing any important questions.

## Slide 11: Backbone & Traffic Metrics
Backbone Bisection Bandwidth:
Sum of inbound traffic crossing red line from Sites & Peers, converted to Gb/s
ESnet
Site
Peers
Site
Site
Site
Peers
Peers
Peers
Average Accepted Traffic:
Sum of Links crossing the red line
Notes: 11

## Slide 12
Notes: Discuss slope of lines.

## Slide 13
Projections for next 7 years

## Slide 14
Projections for next 7 years
ESnet4
ESnet5
Next Wave Fall 2013
(Testbed?)
10x100G on all routes by 2017
Optical System full in 2020 at 88x100G assuming no 400G Waves
ANI Prototype

## Slide 15
Cost Inflection Points next 7 years
ESnet4
ESnet5
ANI Prototype
Routed network exceeds ESnet4 complexity 2016
Hit optical system capacity at current spectral efficiency in 2020
Need to start deploying next generation network 2017 or 2018
Add routers & optical chassis incrementally with wave adds from 2015 on
Contract on Shared Optical System expires 10/31/19

## Slide 16: Things to consider
  How much ‘head-room’ is enough
    Need less ‘bisection bandwidth’ if traffic is local vs cross-country
    Need more for unpredictable users
    Need less for predictable steady-state users
      Could automated science work-flow systems be more predictable, and sustain utilization >75%?
  Some changes that could drive growth faster than projected
    Science DMZ adoption reducing impacts of poorly performing firewalls & security infrastructure
    PerfSONAR adoption & deployment allowing people to discover & fix broken infrastructure
    Data mobility tools enhancement & adoption
    Commercial Adoption rate of 100GE will affect the price curve of 100G components driving up lab adoption rates
    Changes in science data access models could affect growth rates in either direction
Notes: ----- Meeting Notes (1/10/13 12:13) -----
REwrite last bullet

## Slide 17: Evolution of ESnet5
  Simplifying Hubs where possible
    Removing ‘extra’ points of failure
  Optical Express circuits
    Some circuits could bypass all routers
  Expanding International reach, capacity & control
  For now, we have collapsed Nx10GE of IP & SDN traffic onto single 100G circuits using QOS for logical separation.
  We anticipate moving back to physical separation of traffic onto different links as additional circuits are added.

## Slide 18: Evolution of Site Interconnections
  Goal: provide the best possible service within the constraints
    Dimensions of ‘best’ that are important:
      Bandwidth
      Reliability
      Predictability
      Risk tolerance
      Debug-ability
      Flexibility
      Cost
    Discussion Question: What are the comparative weights of the different dimensions?

## Slide 19: Diversity Examples
Notes: The site at the top has 5 routers and 4 links which are single-points-of-failure strung in series.
The ex4200 and m7i in the hubs are essentially media converters to step down speeds and generations of technology.
The site at the bottom does not have any single points of hardware failure.

## Slide 20: Which is better?
Notes: The top lab would have ESnet measurement infrastructure connected to the MX on-site, as well as the ability to provide interfaces for misc enclaves such as site-wireless, Operations office, remote lab disaster recovery lan, etc,
What is the impact of eliminating site routers?
What is the impact of limiting or reducing the number of physical connections to different enclaves at a site?
Is 10G backup enough?
Does the ability to do optical protection/mesh restoration of the 100G make a difference?
Where does the Science DMZ go?

## Slide 21: Site Connections beyond 200G
Is the architecture this simple?

## Slide 22: Possible Additions to Network Services Portfolio
  Looking at additional types of overlay networks
    Layer2 VPNs
      Point to Point
      Multipoint
    Layer3 VPN’s
      IPV4 and IPV6
    We haven’t figured out which subset we need to support
    Please let us know if you anticipate future requirements for overlay networks so we can take your needs into consideration
Notes: I need more context on this

## Slide 23: Additional NEG Updates
DNS DOS Rate Limiting
Improving site interactions
Trying to figure out how to move from ad-hoc and event driven interactions to something that is more organized and intentional
NEG Ambassador?

## Slide 24: Questions?
Thanks!
Joe Metzger – metzger@es.net
http://www.es.net/
http://fasterdata.es.net/