## Slide 1: Quantum Computing with 3D Cavity QED
Srivatsan Chakram
Rutgers, The State University of New Jersey
U.S. Quantum Information Summer School 2023
Notes: Hello everyone. Thank you all for coming. It’s an honor to be invited to speak at this session. My name is Srivatsan. I am an assistant professor of physics at Rutgers

## Slide 2: Cavity Quantum Electrodynamics
A. Rauschenbeutel et al., S. Haroche, Science 288, 2024 (2000)
Study of the interactions between light confined in a cavity and atoms
  Coherent coupling between single-photons and a quantum object (atom)
  Atom can be real or artificial (superconducting qubits)
  Light field can be at optical or microwave frequencies
C. J. Hood et al., H. J. Kimble, Science 287, 1447 (2000)
Serge Haroche
2012 Nobel Prize
with David Wineland
Notes: Segway using high-cooperativity
They also have restricted decay channels
  Perfect cavity only has photon loss
  Error correction using higher Fock states

## Slide 3: Quantum Computing with 3D Circuit QED
Srivatsan Chakram
Rutgers, The State University of New Jersey
U.S. Quantum Information Summer School 2023
Notes: Hello everyone. Thank you all for coming. It’s an honor to be invited to speak at this session. My name is Srivatsan. I am an assistant professor of physics at Rutgers

## Slide 4: Outline
Introduction to 3D circuit QED
Extracting the cQED Hamiltonian
  Black box quantization
Quantum control using a transmon
  4-wave mixing
  SNAP gates
  Photon blockade
  Conditional displacements
Multimode operations
Notes: Add pictures. Too many points.

## Slide 5: Our artificial atom - the transmon
Key element – Josephson junction
Phase difference – macroscopic quantum DOF
Junction acts as a nonlinear inductor
Non-linearity of junction used to perform gate operations
ge  ef
Notes: You cannot do quantum information processing with only linear objects. In superconducting systems, the key element that provides a non-linearity is a josephson junction.
provides a non-linearity is a Joesphson junction. The josephson junction is awesome because it provides a dissipationless non linearity. The phase difference across the junction serves as a macroscopic quantum degree of freedom, behaving as a single particle in a cosine potential, realizing a quantum pendulum. A transmon qubit consists of a capacitor shunted by a josephson junction. Effectively the junction for our purposes realizes a nonlinear inductor. To lowest order this realizes an anharmonic oscillator. The lowest two levels form our qubit, and the anharmonicity is typically 10% of the qubit frequency. The transmon is itself a charge qubit, made from adding a capacitor to a cooper pair box.
There are many flavors of qubits out there. The transmon itself is a charge qubit. There are other qubits that use other circuit elements, notably linear inductors, and these have given rise to qubits like the flux qubit and the fluxonium. The fluxonium, has recently come back into prominence. I will mention it briefly again at the end of my talk.

## Slide 6: Microwave cavities come in many flavors
The simplest superconducting circuit is an LC oscillator
Single resonant mode of any box
Many types of “boxes”
3D cavities
Notes: Superconducting cirtcuits, as the name suggests, are electrical circuits made out of superconductors. The simples superconducting circuit is an LC oscillator, with equally spaced energy levels. These LC circuits can be realized in 2 dimensions using lithography, in lumped element form, or as a coplanar waveguide, 2D version of a BNC cable. Or alternately, any single mode of a metallic or superconductingf box is a harmonic oscillator. And there are a variety of superconducting boxes we can make. If you just have a harmonic system, you cant do any quantum information. After if you make a coherent state with only a few photons, its still a classical state.

## Slide 7: Circuit quantum electrodynamics
Coupling a superconducting qubit to a microwave cavity
Cavity-QED with a macroscopic artificial atom
A. Walraff et al., 431, 162–167 (2004)
Atom: Cooper pair box
Cavity: Coplanar waveguide resonator
Notes: Circuit QED is the paradigm of coupling a superconducting qubit to a microwave cavity. This is like cavity QED with a macroscopic artificial atom.
The state of the transmon is readout out by coupling the transmon to a cavity. This is analogous to a cavity QED system where the transmon is like an atom, and the microwave cavity is like an optical cavity, with the atom and the cavity being way off resonance. In this regime that atom is like a bead of glass causing a phase shift and a shift in the cavity resonance frequency, that importantly depends on the atomic state of the atom.
Typically our transmon circuits have a frequency of around 5-10 GHz or so, which corresponds to a few 300 mK in temp.

## Slide 8: Circuit quantum electrodynamics
Qubit
Cavity
Protects the qubit from the environment
Readout qubit by probing cavity
Use qubit for universal cavity control
Coupling a superconducting qubit to a microwave cavity
Cavity-QED with a macroscopic artificial atom
Notes: Circuit QED is the paradigm of coupling a superconducting qubit to a microwave cavity. This is like cavity QED with a macroscopic artificial atom.
The state of the transmon is readout out by coupling the transmon to a cavity. This is analogous to a cavity QED system where the transmon is like an atom, and the microwave cavity is like an optical cavity, with the atom and the cavity being way off resonance. In this regime that atom is like a bead of glass causing a phase shift and a shift in the cavity resonance frequency, that importantly depends on the atomic state of the atom.
Typically our transmon circuits have a frequency of around 5-10 GHz or so, which corresponds to a few 300 mK in temp.

## Slide 9: Circuit quantum electrodynamics
Cavity-QED with a macroscopic atom
Cavity size ~ wavelength
Qubit
Cavity
Magnetic field (a.u.)
Frequency (GHz)
6.75
7.05
g ~ 100 MHz
Notes: The state of the transmon is readout out by coupling the transmon to a cavity. This is analogous to a cavity QED system where the transmon is like an atom, and the microwave cavity is like an optical cavity, with the atom and the cavity being way off resonance. In this regime that atom is like a bead of glass causing a phase shift and a shift in the cavity resonance frequency, that importantly depends on the atomic state of the atom.
Typically our transmon circuits have a frequency of around 5-10 GHz or so, which corresponds to a few 300 mK in temp.

## Slide 10: Circuit quantum electrodynamics
Dispersive approximation
Qubit and cavity are off-resonant
High cooperativity
= 105 - 109
Cavity shift based on qubit state
Qubit shift from cavity photon number
HI
Dispersive shift
Notes: The state of the transmon is readout out by coupling the transmon to a cavity. This is analogous to a cavity QED system where the transmon is like an atom, and the microwave cavity is like an optical cavity, with the atom and the cavity being way off resonance. In this regime that atom is like a bead of glass causing a phase shift and a shift in the cavity resonance frequency, that importantly depends on the atomic state of the atom.
Typically our transmon circuits have a frequency of around 5-10 GHz or so, which corresponds to a few 300 mK in temp.

## Slide 11: Circuit quantum electrodynamics
Dispersive approximation
Qubit and cavity are off-resonant
High cooperativity
= 105 - 109
Qubit shift from cavity photon number
HI
Cooperativity: Dimensionless measure of coherence of a cavity QED system
coupling strength
Cavity decay rate
Qubit decay rate
Dispersive shift
Notes: The state of the transmon is readout out by coupling the transmon to a cavity. This is analogous to a cavity QED system where the transmon is like an atom, and the microwave cavity is like an optical cavity, with the atom and the cavity being way off resonance. In this regime that atom is like a bead of glass causing a phase shift and a shift in the cavity resonance frequency, that importantly depends on the atomic state of the atom.
Typically our transmon circuits have a frequency of around 5-10 GHz or so, which corresponds to a few 300 mK in temp.

## Slide 12: 3D circuit quantum electrodynamics
Reduce dielectric loss by diluting electric field
Demonstrations that junctions can be sufficiently low loss
3D cavity just used for readout
Notes: The state of the transmon is readout out by coupling the transmon to a cavity. This is analogous to a cavity QED system where the transmon is like an atom, and the microwave cavity is like an optical cavity, with the atom and the cavity being way off resonance. In this regime that atom is like a bead of glass causing a phase shift and a shift in the cavity resonance frequency, that importantly depends on the atomic state of the atom.
Typically our transmon circuits have a frequency of around 5-10 GHz or so, which corresponds to a few 300 mK in temp.

## Slide 13: Moore’s law for superconducting qubits
10x improvement in coherence every 3 years
Transmon coherence times ~ 100-500 μs
Fermilab SRF Cavity
Fluxonium (Maryland/UChicago)
New 2d/3d transmons
(Princeton)
Cavities still have the best coherences!
2023
Devoret, Schoelkopf, Science (2013)
Notes: Segway using high-cooperativity
They also have restricted decay channels
  Perfect cavity only has photon loss
  Error correction using higher Fock states

## Slide 14: Seamless cavities
Three sources of loss in 3D cavities:
  Dielectric
  Conduction
  Seam
Traditional 3D cavities suffer from loss at seam between pieces of the cavity
Seamless cavities
  Coax cavities
  Flute cavities
  Lifetimes ~ 1 ms
SRF cavities (seams eliminated by e-beam welding)
  Lifetime ~ 1s
Notes: The coaxal cavity I mentioned is also a seamless cavity

## Slide 15: Microwave cavities as quantum memories
Longest lifetimes in circuit-QED
Can be controlled using a transmon circuit
Coaxial quarter wave cavities
Q ~ 100 million
T1 ~ 1-2 milli seconds
2020
D. Gonella et al., JoAP (2016)
A. Romanenko et al., Phys. Rev. Applied (2020)
M. Reagor et al., PRB (2016)
Fermilab accelerator cavities
Q ~ 20 billion @ 1.3 GHz
T1 ~ seconds
Devoret, Schoelkopf, Science (2013)
Notes: Segway using high-cooperativity
They also have restricted decay channels
  Perfect cavity only has photon loss
  Error correction using higher Fock states

## Slide 16: Bosonic quantum error correction
Quantum error correction requires information to be encoded redundantly
With qubits Minimum of 5 physical qubits to encode one logical qubit
Cavities have restricted decoherence channels only photon loss
Simpler error correcting codes that can encode a logical qubit in one oscillator
S. Rosenblum et al., 9, 652 Nat. Comm. (2018),
L. Hu et al., Nat. Phys. 15, 503–508 (2019)
Binomial code
Same mean photon #
Photon loss
No change in coefficients
Error syndrome = Parity
Notes: Segway using high-cooperativity
They also have restricted decay channels
  Perfect cavity only has photon loss
  Error correction using higher Fock states

## Slide 17: Bosonic quantum error correction
Quantum error correction requires information to be encoded redundantly
With qubits Minimum of 5 physical qubits to encode one logical qubit
Cavities have restricted decoherence channels only photon loss
Simpler error correcting codes that can encode a logical qubit in one oscillator
N. Ofek et al., Nature 536, 441–445 (2016)
Cat code
S. Rosenblum et al., 9, 652 Nat. Comm. (2018),
L. Hu et al., Nat. Phys. 15, 503–508 (2019)
Binomial code
GKP
P. Campagne-Ibarq et al.,
Nature 584, 368–372(2020)
Notes: Segway using high-cooperativity
They also have restricted decay channels
  Perfect cavity only has photon loss
  Error correction using higher Fock states

## Slide 18: Seamless multimode rectangular flute cavity
Straightforward design of a variety of spectra and spatial distributions
Taper the cavity to create equally spaced modes
99.999% purity Al
Transmon coupled at one end
Notes: Show a dot for the E field
Location and cartoon for 3D transmon
Indicate the cavity length stretched out..

## Slide 19: Coupling a 3d cavity to a transmon
Readout
Add a 3D readout cavity and a bridge transmon
Bridge transmon
Storage cavity
How do we calculate the expected system Hamiltonian?
Notes: Fix this slide. Don’t use middle figure

## Slide 20: Outline
Introduction to 3D circuit QED
Extracting the cQED Hamiltonian
  Black box quantization
Quantum control using a transmon
  4-wave mixing
  SNAP gates
  Photon blockade
  Conditional displacements
Multimode operations
Notes: Add pictures. Too many points.

## Slide 21: Black box quantization
Finding the effective Hamiltonian for a system of weakly anharmonic superconducting circuits coupled to an arbitrary EM environment
First treat the junction as a linear object with some inductance/capacitance
Find correct basis by solving the coupled linear problem
Parameters extracted from impedance
Perturbatively add back the non-linear terms while rewriting in the new basis
  m
Black-Box Superconducting Circuit Quantization, S. Nigg et. al., PRL 108, 240502 (2012)
Notes: 2) Here is an outline of the talk. I will start by presenting the kind of quantum computing architecture we have in mind.
I will then present results of a random access quantum information processor module realized in a 2D architecture. The processor consists of a chain of strongly coupled CPW resonators, with the memory bits consisting of photons in the resonator modes. These photonic states are stored and retrieved using a single transmon circuit serving as a central processor. We use the transmon to then perform universal quantum operations between arbitrary modes.
I will then discuss our progress towards realizing a 3D version of the same architecture, controlling the quantum state of the high-Q seamless cavities that Ravi had described in the previous talk, using transmon circuits, and plans for the future.

## Slide 22: Black box quantization
The relevant parameter to be extracted from is the participation of each of the normal modes at the junction
Total impedance found by combining that of the EM environment and the junction in parallel
Forster’s theorem : can be synthesized as a series of LCR oscillators
Notes: 2) Here is an outline of the talk. I will start by presenting the kind of quantum computing architecture we have in mind.
I will then present results of a random access quantum information processor module realized in a 2D architecture. The processor consists of a chain of strongly coupled CPW resonators, with the memory bits consisting of photons in the resonator modes. These photonic states are stored and retrieved using a single transmon circuit serving as a central processor. We use the transmon to then perform universal quantum operations between arbitrary modes.
I will then discuss our progress towards realizing a 3D version of the same architecture, controlling the quantum state of the high-Q seamless cavities that Ravi had described in the previous talk, using transmon circuits, and plans for the future.

## Slide 23: Extracting the admittance of the cavity using HFSS
Use finite element software
  ANSYS HFSS
Compute the admittance as seen by the junction
Assign the junction as a lumped port with high impedance
Sample particularly near the expected locations of the modes and the range of transmon frequencies

## Slide 24: Finding the locations of the modes
Add the admittance of the junction by hand to get to the total admittance
Modes are found from the zeroes of the admittances
Admittance near the modes is used to extract capacitances and inductances
  mc
Readout
Storage
cavity
Transmon

## Slide 25: Diagonalized linear Hamiltonian of circuit + cavity
Hamiltonian of the linearized system in terms of flux/charge or number/phase
Write zero-point phase fluctuations at the junction from each of the modes
Rewriting the junction phase in terms of normal modes
  mc

## Slide 26: Mapping to a multimode Jaynes-Cummings model
Multimode JC Hamiltonian with a single transmon
The normal modes can be found to lowest order by doing a dispersive transformation
extracted using
  mc

## Slide 27: Reintroducing the nonlinearity
Reintroduce the quartic nonlinear term and rewrite in terms of the normal modes
  mc
  Lamb shift
  Cross-Kerr interaction/dispersive shift
Notes: Don’t need to write in terms of E_{CJ}. That’s just to match with the black box paper

## Slide 28: Extracting the dispersive shifts and cross-Kerr interactions
Reintroduce the quartic nonlinear term and rewrite in terms of the normal modes
  mc
  Lamb shift
  Cross-Kerr interaction/dispersive shift
Notes: Don’t need to write in terms of E_{CJ}. That’s just to match with the black box paper

## Slide 29
Hamiltonian parameters for a 3D circuit QED system
Multimode Jaynes-Cummings Hamiltonian

## Slide 30
Multimode circuit QED system
Cavity modes are far detuned from the transmon
Dispersive approximation
Notes: As I pointed out before, the transmon is not just a qubit.

## Slide 31: Putting it all together
T1 = 86 µs
T2* = 65-120 µs
nthq = 0.5 – 1%
nthR = 0.1-0.5%
Readout
Storage cavity
Add a 3D readout cavity and a bridge transmon
Light tight packaging
Notes: Fix this slide. Don’t use middle figure

## Slide 32: Packaging, shielding, and filtering matters!

## Slide 33: Multimode coherences
  For 9 modes
  Q ~ 70-95 million
  T1 ~ 2 ms
  T2 ~ 2 - 3.5 ms
S.Chakram*, A. Oriani*, R.Naik, .., D.Schuster,
Phys. Rev. Letters (2021)
Notes: Average the T2 data
Mention properties of the transmon
Mention the changes that were made to achieve the coherences
Compare with the previous results from 2D
Say something about the fidelity of the SWAP operations

## Slide 34: Outline
Introduction to 3D circuit QED
Extracting the cQED Hamiltonian
  Black box quantization
Quantum control using a transmon
  4-wave mixing
  SNAP gates
  Photon blockade
  Conditional displacements
Multimode operations
Notes: Add pictures. Too many points.

## Slide 35: Schemes for control using a fixed frequency transmon
  Resonant charge sideband interactions
  SNAP Control - number resolved transmon and cavity drives
  Cavity drive and photon blockade
  Conditional displacement gates
Rely on the Josephson nonlinearity
4-wave mixing
Dispersive interaction

## Slide 36
4-wave mixing using the non-linearity of the Josephson junction
f0-g1 charge sideband transition
Cavity control with charge sideband transitions
A. Wallraff et al, Phys. Rev. Lett. (2007)
M. Pechal, Phys. Rev. X (2014)
S. Rosenblum et al, Nat. Comm. (2017)
Drive
Notes: No equation. Too much.

## Slide 37
4-wave mixing using the non-linearity of the Josephson junction
Cavity control with charge sideband transitions
A. Wallraff et al, Phys. Rev. Lett. (2007)
M. Pechal, Phys. Rev. X (2014)
S. Rosenblum et al, Nat. Comm. (2017)
Drive
Notes: No equation. Too much.

## Slide 38
Addressing the cavity modes through sidebands
SWAP
Any single-mode gate operation
T1 = 1.95  0.1 ms
T2 = 2.4  0.3 ms
Notes: Get this data with sidebands for the multimode flute for 1 mode.

## Slide 39: Addressing the cavity modes through sidebands
Readout
Storage cavity
Transmon
f0-g1 SWAP
Drive

## Slide 40: Beam splitter operations between cavity modes!
Cavity modes
b
a
Drive tones
2
1
4-wave mixing with two drive tones
a -b = 1 -2
Drive 1
Drive 2

## Slide 41: Beam splitter operations between cavity modes!

## Slide 42: Schemes for control using a fixed frequency transmon
  Resonant charge sideband interactions
  SNAP Control - number resolved transmon and cavity drives
  Cavity drive and photon blockade
  Conditional displacement gates

## Slide 43: Universal control using the dispersive interaction
Cavity displacements
Selective number dependent
arbitrary phase (SNAP)
Uses the dispersive interaction
Number selective transmon pulses

## Slide 44: Optimal control SNAP pulses
SNAP allows universal control
Can numerically find optimal
control pulses
N. Leung, M. Abdelhafez, J. Koch, and D.Schuster,
Phys. Rev. A 95, 042318 (2017)

## Slide 45: Optimal control SNAP pulses
SNAP allows universal control
Can numerically find optimal
control pulses
  Speed up gates
  Improve fidelities
Error

## Slide 46: Parity measurements and Wigner tomography
Parity measurement
  Ramsey after idling
Partial fourier transform of density matrix
Negativity - non-classicality
Wigner Tomography
  Displace cavity
  Measure Parity
Uses the dispersive interaction
x
p
Notes: Fourier transform of the density matrix.
Make all the wigner functions square. Regenerate them.
Label x and y axis in the graph
1/2chi is pi phase shift.

## Slide 47: Schemes for control using a fixed frequency transmon
  Resonant charge sideband interactions
  SNAP Control - number resolved transmon and cavity drives
  Cavity drive and photon blockade
  Conditional displacement gates
Error

## Slide 48: Quantum dynamics with photon blockade
A pure cavity drive can only generate classical states
Notes: Add ellipsis to indicate more levels

## Slide 49: Quantum dynamics with photon blockade
L. Bretheu,…,B.Huard, Science, 348, 6236 (2015)
Use a number selective transmon pulse
Blockade specific photon numbers
Blockade of
Cavity drive results in a Rabi oscillation
Notes: Remove title on figure
Cite houck photonic qubit paper
Flip colors
Keep the epsilon at the end
Maybe mention its trivial to calibrate

## Slide 50: Quantum dynamics with photon blockade
Use a number selective transmon pulse
Blockade specific photon numbers
Blockade of
Notes: Get a wigner tomography plot for no blockade..
R corresponding to green highlight saying it is sqrt(2)
For upto r = 2 and no population there

## Slide 51: Quantum dynamics with photon blockade
Use a number selective transmon pulse
Blockade specific photon numbers
  Blockade infidelity
Leakage to
Purcell decay of by blockade drive
Same infidelity as SNAP gates
for a lossless cavity
Notes: Get a wigner tomography plot for no blockade..

## Slide 52: Quantum dynamics with photon blockade
Blockade of higher photon numbers
Blockade radius increases as
Blockade of

## Slide 53: Quantum dynamics with photon blockade
Can use blockade multiple photon numbers
Rabi oscillation between and

## Slide 54: Universal qudit control with photon blockade
Can achieve arbitrary qudit control just by driving the cavity
S. G. Schirmer, H. Fu, C. Solomon, Phys. Rev. A, 63, 063410 (2001)
Optimal control
Numerically find pulses
using gradient descent
N. Leung, M. Abdelhafez, J. Koch, and D.Schuster,
Phys. Rev. A 95, 042318 (2017)
Notes: Increase time font size
Y axis of optimal control curve change to kHz

## Slide 55: Universal qudit control with photon blockade
Can achieve arbitrary qudit control just by driving the cavity
]
=
Notes: Increase time font size
Y axis of optimal control curve change to kHz
Indicate green is blockade
And |1> where it

## Slide 56: Universal qudit control with photon blockade
Can achieve arbitrary qudit control just by driving the cavity
]
=
Notes: Increase time font size
Y axis of optimal control curve change to kHz

## Slide 57: Schemes for control using a fixed frequency transmon
  Resonant charge sideband interactions
  SNAP Control - number resolved transmon and cavity drives
  Cavity drive and photon blockade
  Conditional displacement gates
All schemes have similar infidelity in the absence of cavity decay
Gate error

## Slide 58: Conditional displacement gates
GKP
P. Campagne-Ibarq et al., …, M. H. Devoret, Nature 584, 368–372(2020)
A. Eickbusch, S. Elder, ..., R. Schoelkopf, M. Devoret, V31.00005, March meeting (2021)
Use a large displacement to enhance the dispersive interaction
Gate speed
Notes: Add ellipsis to indicate more levels

## Slide 59: Schemes for control using a fixed frequency transmon
  Resonant charge sideband interactions
  SNAP Control - number resolved transmon and cavity drives
  Cavity drive and photon blockade
  Conditional displacement gates
All schemes have similar infidelity in the absence of cavity decay
Gate error
Gate error <

## Slide 60: Outline
Introduction to 3D circuit QED
Extracting the cQED Hamiltonian
  Black box quantization
Quantum control using a transmon
  4-wave mixing
  SNAP gates
  Photon blockade
  Conditional displacements
Multimode operations
Notes: Add pictures. Too many points.

## Slide 61: Multimode interactions through photon blockade
Modes typically have different dispersive shifts
Qubit cannot distinguish between modes with same
Blockade drive generates interactions between modes
Mode 6
Mode 2
Mode 6
Mode 5
Drive mode 6
Blockade drive frequency
Disallows and
Notes: This slide sucks. Show number splitting with and without dressing.

## Slide 62: Multimode interactions through photon blockade
Modes typically have different shifts
Qubit cannot distinguish between modes if shifts are the same
Blockade drive generates interactions between modes
Blockade drive frequency
Mode 6
Mode 5
Disallows and
Drive mode 5
Notes: This slide sucks. Show number splitting with and without dressing.

## Slide 63: Multimode interactions through photon blockade
Modes typically have different shifts
Qubit cannot distinguish between modes if shifts are the same
Blockade drive generates interactions between modes
Drive mode 6 after
adding a photon in mode 5
Mode 6
Mode 5
Entangling gate
Disallows and
Blockade drive frequency
Notes: This slide sucks. Show number splitting with and without dressing.

## Slide 64: Multimode interactions through photon blockade
Entanglement can also be generated if the are different
Blockade by driving the of the transmon
Drive both cavities simultaneously
Mode 2
Mode 3
Blockade drive frequency
Notes: This slide sucks. Show number splitting with and without dressing.
Blockade should be green

## Slide 65: Multimode interactions through photon blockade
Blockade drive used to disallow a hyperplane of states
Realizes a pure N-body interaction
S.Chakram*, K. He*, .., L. Jiang, D. Schuster, arXiv:2010:15292 (2020)
kHz
Notes: 1 and 0 photons, blockading 3 photons.

## Slide 66: Multimode W state preparation
Blockade at mean frequency of all 2-photon peaks
Drive all cavity modes simultaneously
3 mode W state
Notes: This slide sucks. Show number splitting with and without dressing.

## Slide 67: Multimode W state preparation
Blockade at mean frequency of all 2-photon peaks
Drive all cavity modes simultaneously
4 mode W state
Notes: This slide sucks. Show number splitting with and without dressing.

## Slide 68: Multimode W state preparation
Blockade at mean frequency of all 2-photon peaks
Drive all cavity modes simultaneously
5 mode W state
Notes: This slide sucks. Show number splitting with and without dressing.

## Slide 69: Multimode Wigner tomography
2-mode Bell state tomography
Notes: X and y axis label |mn>
Make Re and Im bigger or nex t to colorbar

## Slide 70: Multimode Wigner tomography
2-mode joint Wigner functions

## Slide 71: Multimode Wigner tomography
3-mode W state tomography
Consistent with master equation simulations
(2-mode) =
(3-mode) =
Entanglement Witness
Tripartite entangled
Notes: This slide sucks. Show number splitting with and without dressing.
Add fidelity of the blockade
Mneiton phases
Add outlook after this
Compare 2, 3 and 4
Add Kevin talk
Mention the actual numbers below in the inequalitly
Mention next steps
Quote fiditlies
And statement of the limitation

## Slide 72: Summary
Introduction to 3D circuit QED
Extracting the cQED Hamiltonian
  Black box quantization
Quantum control using a transmon
  4-wave mixing
  SNAP gates
  Photon blockade
  Conditional displacements
Multimode operations
Notes: Add pictures. Too many points.

## Slide 73: Chakram lab @ Rutgers
Positions open for students and postdocs!
Contact: schakram@physics.rutgers.edu

## Slide 74: Thank you!
Questions?

## Slide 75: Energy participation method
Computes the participation of the modes in the junction using eigenmode rather than driven modal simulations.
Again - solve the linear problem and then add the nonlinearity back
extracted from inductive participation factor
GOAL- find
Obtained in black-box from impedances

## Slide 76: Energy participation method
Participation factors obtained from total electric and magnetic energies in each mode
In the case of no junction by Virial theorem
With additional lumped elements
is the total inductive energy of the Josesphson Junctions
Participation factor is therefore
Calculator based on the above @
https://github.com/zlatko-minev/pyEPR