## Slide 1: Quantum computers as quantum sensors
Aaron S. Chou (Fermilab)
USQIS Summer School
August 14, 2023
Topics:
Environmental disturbances impacting quantum computers
Measuring tiny forces using the quantum RAM as a probe
Using prepared quantum RAM states to enhance force sensitivity

## Slide 2: How textbooks describe physics problems:

## Slide 3: In real life, everything is on fire!

## Slide 4: What you see on an oscilloscope:
Voltage
time
Nyquist-Johnson noise is the population of thermal blackbody photons emitted by output resistor and the load resistor and living in your coax cable.

## Slide 5: Thermal noise power spectral density
Bose-Einstein thermal population of blackbody photons on a 1-dim transmission line, + zero point fluctuations:
Energy/mode = kT (½ kT for each quadrature).
Modes of linewidth are defined by the integration time t = 1/(2 required to resolve these modes. This defines the “Hilbert space.”
        Thermal noise power emitted from each mode P = kT
        At T=0, replace kT with quantum noise P = hf .
PSD/kT
# photons/mode:
https://en.wikipedia.org/wiki/Johnson–Nyquist_noise

## Slide 6: Why does your quantum mechanics professor ask you to square the wave function?
To detect a signal, the variance of its waveform must be visible above the variance of the thermal fluctuations within the “detection bandwidth” of the measurement, i.e. = frequency bin size.
Voltage
Vsignal2/R
kT
Measure voltage across load resistor R as a function of time.
Use Fast Fourier Transform (FFT) to convert to the frequency domain representation
Square the wave function to obtain the “power spectrum” of voltage variances as a function of frequency.
Compare V2/R to kT to see if you’ve detected anything.
Power

## Slide 7: To avoid getting swamped by these thermal fluctuations, classical computers use 100’s of electrons to turn transistors on/off. Adding/losing a couple doesn’t really screw things up.
Charge on gate:
Q = CV = (10-16 F) (0.1 V)
= 10-17 Cb
≈ 100 electrons
≈ 10-2 V
Threshold Vth to flip bit set to 10x RMS voltage of thermal noise fluctuations
This gives an extremely low bit error rate!
L. Forbes, M. Mudrow, W. Wanalertlak, Electronics Letters 2006

## Slide 8: Quantum computers store and manipulate single quanta of information. They are thus extremely susceptible to environmental disturbances
Superconducting qubit = nonlinear LC oscillator,
stores 0 or 1 quantum of electrical oscillation.
Microwave resonators can be used as quantum RAM. Stores information as single photons.
Trapped ion, neutral atom = nonlinear oscillator due to 1/R potential of electric field of the nucleus.
Stores 0 or 1 quantum of electron orbital energy.
Placing charged ion in an electromagnetic trap creates a mechanical oscillator. Mechanical QRAM stores information as single phonons of motion.

## Slide 9: As single quantum devices, qubits are extremely sensitive photon detectors. Need to operate in refrigerators with many layers of hermetic radiation shields to block thermal blackbody radiation.
Much of “classical” quantum computing R&D has focused on identifying and plugging light leaks.
Room temperature photon energy ~ 1 eV.
Cooper pair breaking energy ~ 10-3 eV.
Qubit oscillator energy ~ 10-5 eV.
Stray photons are bad since superconductors and qubits are very good single photon detectors!
Detection signature = quantum computer goes
300K
70K
4K
1K

## Slide 10: Qubits are absolutely overkill for detecting highly energetic ionizing radiation (Gamma rays fly right through the aluminum shells of the refrigerator)
Use lead or heavy copper shielding with lots of high-Z atoms to block the radiation.
Particle energy = 10 eV – 106 eV or greater
Compare:
Electron-hole band gap in silicon = 1 eV
Cooper pair breaking energy = 10-4 eV

## Slide 11: Cosmic ray events are caused by astrophysical protons and charged nuclei smashing into the earth’s atmosphere and creating a cascade of particles
Initial particle energy
~1020 eV
Creates zillions of 109 eV particles (muons) at sea level !
More bad news:

## Slide 12: Cosmic ray muon rate at sea level = “one per hand per second”
Cosmic rays are “minimum ionizing” and deposit ~ 106 eV/cm of energy in liberated charges when traversing materials. Eventually these will range out over 10’s of meters of earth.
A single cosmic ray deposits enough energy to create millions of e-h pairs in silicon (1 eV bandgap) or break billions of Cooper pairs in superconductors (10-3 eV superconducting gap)
muon
Muon has 207x electron mass

## Slide 13: Patterns of ionizing radiation hits in a silicon CCD (SENSEI DM experiment)
In silicon-based computers, Single Event Upsets (SEU) due to cosmic rays are well-known, and are believed to have given a candidate 4096 extra votes in a 2003 election in Belgium.
They can also give you super powers!
Beneficial mutations from DNA damage.

## Slide 14: Ionizing radiation produces 10-2 Hz rate of catastrophic events in superconducting QPUs (of area smaller than your hand)
Google Sycamore chip exhibits 100% chip-wide failure in response to ionizing radiation events which can be localized in both space and time
M. McEwen, et.al, Nature Physics (2022)
The ionizing radiation deposits energy primarily in the bulk substrate of the qubit chip (where most of the atoms are).
Electrons and holes recombine and the resulting phonons bounce around and break Cooper pairs in the thin film superconductors on the surface.
105 eV energy deposit
10-3 eV to break Cooper pair

## Slide 15: To reduce the rate of ionizing radiation on quantum devices, we are operating underground dilution refrigerators in Fermilab’s neutrino beamline
100m
Lead sarcophagus shields against natural radioactivity
Reduces cosmic ray rate by 1000x
Also in Gran Sasso (Italy), SNOLab (Canada)

## Slide 16: Unwanted electron-like quasiparticles from broken Cooper pairs can scramble the information stored in the qubit (ie. the Cooper pair oscillator)
A quasiparticle tunneling through the Josephson junction absorbs or transfers energy/momentum from/to the qubit oscillator. This changes the qubit’s state and scrambles the quantum information!
Throwing the ball in phase with the swinging adds energy, turns 0 into 1.
Throwing the ball out-of-phase with the swinging removes energy, turns 1 into 0.
J. Wenner, et al., PRL 110, 150502 (2013)
Potential energy
diagram

## Slide 17: Qubits are also great phonon sensors: Acoustic noise from substrate microfracture events are currently far worse than ionizing radiation!
R. Anthony-Petersen… M. Pyle, et al.,
arxiv:2208.02790
Measure spectrum using tiny, cold, low heat capacity TES sensors developed for the SuperCDMS dark matter search.
Next-generation qubit-based microcalorimeters will reduce thresholds to milli-eV, provide first look at sub-eV spectrum.
Ionizing radiation
Mechanical noise

## Slide 18: Release of mechanical stresses may explain the 20-year mystery of the non-equilibrium quasiparticle population in superconductors
E.T. Mannila, et al., Nature Physics 18 (2022)
These appear to be created in discrete, time-resolved events with much higher rate than cosmic rays.
Event rate decreases with time (over months) as the device self-anneals.

## Slide 19: What happens when QPUs become larger than your hand?
Google’s catastrophic event rate increased by 10,000x
Qubit coherence time
IBM Q
106 qubit chip needed for
universal quantum computing
10,000x collection area
NISQ hardware
102 qubits (IBM, Google)
Schoelkopf’s Law
Quantum error correction cannot help when all of the redundantly stored information has been simultaneously wiped out! Surface code, toric code, topological protection all wiped out.

## Slide 20: Even after we’ve stopped all the heat, light, sound, radiation, cosmic rays, etc we still have to worry about dark matter…
Impossible to shield from the dark matter – it interacts so weakly that it flies right through the walls.
It might still occasionally deposit energy in the qubit, enough to wipe out the quantum information.
If your quantum computer crashes, it could be due to dark matter!
… but as consolation, you’ll get a Nobel prize anyway for the discovery.
Illustration by Roni Harnik,
DOE-OHEP Basic Research Needs white paper, 2018

## Slide 21: Mystery noise in your experimental apparatus is not necessarily mundane
Penzias and Wilson, 1965:
After chasing away nesting birds with a shotgun, discovered the cosmic microwave background
– They had no idea that this was first evidence for the big bang theory
– Nobel Prize, 1978
N.B. the world was B&W before the 1970’s

## Slide 22: Known SC quantum computer pathologies
Qubit cooling: qubits have T1 lifetime < 1 ms
  There are lots of loss mechanisms so losing a quantum of excitation is nothing to get excited about.
Anomalous qubit heating: qubits are found individually to be spontaneously excited 1% of the time
  This is super annoying, and is probably due to the non-equilibrium quasiparticles transferring kinetic energy to the Cooper pair oscillation
Correlated catastrophic failures: QPUs exhibit simultaneous failure of all qubits on the chip. All information is wiped out and T1 times remain suppressed over 10 ms.
  These are the known environmental backgrounds of ionizing radiation and microfractures.
Anomalous QRAM heating: nonequilibrium photons occasionally appear in ultracold resonators. These were not put in by the quantum computational software.
  Is there still light leakage? How well do we trust our thermometers?
Could disturbances due to dark matter be hiding in any of the above backgrounds???

## Slide 23: Quantum sensors: E < 1 eV
Cartoon from Snowmass
E&M
Transmon qubits,
quantum amps, transducers, SRF cavities, SNSPDs, NMR
Current experiments:
E > 1 eV
Single phonon sensors, quantum materials
Atomic IFOs, clocks
Xe, Ar,
Si, Ge, colliders, fixed target
Aaron S. Chou, USQIS Summer School 2023

## Slide 24: Topic 2: Measuring tiny forces while soundly beating the SQL!
e.g. Measure the QRAM to see if it contains extra quanta of information that you did not put in there.

## Slide 25
Bosonic DM waves: dark photons, spin-0 particles like the QCD axion
Forces from classical dark matter waves can deliver energy/momentum in the form of single photons that mysteriously appear in your well-shielded apparatus.
Model the dark matter as a dark oscillator that is secretly coupled to your QRAM oscillator (or to your qubit oscillator).
You did not intend to put this noise source in your carefully engineered system, but too bad, you cannot get rid of it, and it is always there.

## Slide 26: Energy transfer between two coupled oscillators
Weak coupling -- takes many swings to fully transfer the wave amplitude.
In real life, the number of swings is limited by coherence time and one only gets the transfer of an occasional single quantum of energy.
QRAM Oscillator
Dark matter wave

## Slide 27: A classical sine wave is described by a rotating phasor:
The energy oscillates between potential energy and kinetic energy, as parameterized by the position X and momentum P.
For photons, “X” and “P” are the cosine and sine quadratures of the electric field oscillation.
2nd quantization: [X,P]=i even for internal field quadratures (since these can drive mechanical oscillators.)
X
P

## Slide 28: In quantum mechanics, the endpoint of each phasor is a Gaussian blob:
Time evolution of Wigner distributions in X-P “phasor” space.
Each gaussian blob of phase space area satisfies
Simulated with QuTIP
Beer o’clock topic: Heisenberg Uncertainty Principle really means that phase space is quantized in units of ½ℏ. Does this imply that our universe is a digital simulation?
X
P
or in polar coordinates:
∆N×∆𝜑 ≥ ½

## Slide 29: Oscillating force from dark matter displaces the initial cavity vacuum state to create a phasor with tiny but non-zero amplitude
(Exaggerated) displacement <10-3 of zero-point noise
x
x
p
p
𝛼=10-2
Coherent state
phase space area = ½ħ
Need millions of SQL measurements to average away the zero-point noise to resolve the tiny displacement signal.
The Gaussian blob is also effectively the probe resolution when using a linear amplifier to resolve the tiny signal sine wave. Simultaneous measurement of non-commuting observables N and 𝜑 incurs the Heisenberg uncertainty principle ∆N×∆𝜑 ≥ ½.
Force
Gaussian distribution of endpoint of phasor
Initial QRAM state is a 0-length phasor:

## Slide 30: To reduce readout noise, use photon counting to measure displacement using the Fock basis, i.e. number eigenstates
Instead, measure only displacement amplitude
no zero-point noise since we are not simultaneously measuring non-commuting observables
Measurement noise, e.g. from dark counts can be arbitrarily low
Displaced vacuum state exponentially leaks into non-zero Fock number.
Detect displacement by counting the occasional single photon.
1
2
3
Previous experiments measured both amplitude and phase, but this the dark matter phase is random and not interesting. Useless information obtained at high cost!
Blue rings give the probe resolution

## Slide 31: Transmon qubit in 6 GHz aluminum cavity
Image credit: Akash Dixit
Dark matter waves scatter on walls of cavity, depositing occasional single photon.
Measure AC Stark shift of qubit frequency.
A single quantum of information mysteriously appears in your QRAM that was not part of your quantum computation

## Slide 32: Detect single photons via the AC Stark shift of the qubit: Example: Measure qubit transition frequencies after mimicking the DM signal by weakly driving the primary cavity mode into a coherent state with <n>=1
Quantized frequency shifts occur because the electric field of the photons induces an oscillating Cooper current and drives the qubit into nonlinearity.
The measured qubit excitation spectrum exhibits a distribution of resonances which are in 1-1 correspondence with the Poisson distribution of the cavity photons.
Akash V. Dixit, et.al, Phys.Rev.Lett. 126, 141302 (2021)

## Slide 33: Ramsey measurement: compare qubit clock speed to an external stopwatch
If there is a photon, the qubit runs slower. If no photon, the qubit runs faster.
Prepare initial clock
state with 𝜋/2 pulse to give state
Evolve system to accumulate 𝜋 phase difference over Stark period
Analyze with final 𝜋/2 pulse to map: Even N 
Odd N 
Ramsey interferometry
Measure final qubit state via freq. shift of an auxiliary cavity mode.
The qubit’s “spin” flips only if a cavity photon is present.
If N = 0 or 1:

## Slide 34: Repeated Ramsey photon number parity measurements to mitigate qubit errors
=
Start / Stop the stopwatch
Quantum non-demolition measurement of photon number n which commutes with the Hamiltonian.
Data acquisition code runs half on classical CPU and half on single qubit QPU.
Notes: If we stare at the Hamiltonian for a while then we can check that it commutes with the number operator of the cavity and the qubit. It means that we can measure the same photon multiple times without actually destroying it.
This quantum non-demolition nature of the measurement allows to bring down the error rate much below an individual measurement error.

## Slide 35: Repeated QND measurements ensure high fidelity tagging of single photon events.
Data from Akash Dixit (U.Chicago)
Single photon injected, repeated successful qubit spin flips
Failed spin-flip = readout error
More successful readouts
Photon decays, qubit stuck in state
Qubit decays
Qubit spontaneously excited and then decays. Does not mimic photon event since subsequent spin-flip attempts fail.
Many failed spin-flips indicate that no photon is present.
phonon event
single photon event
Data courtesy of Akash Dixit
Signature of a single signal photon is many sequential successful qubit “spin-flips” from

## Slide 36: Metrology gain vs SQL for various single photon detectors
Superconducting nanowire single photon detectors (for IR photons):
Dark Rate R = 10-5 Hz
Bandwidth B = 1015 Hz (or smaller if narrow band filtered)
Number of modes Nmodes= Area/(wavelength)2 = 102
Effective occupation number n = (R / B) / Nmodes = 10-22
Effective noise squeezing factor = 1/sqrt(n) = 110 dB
Quantum capacitance detector (charge qubits for THz):
Dark Rate R = 1 Hz
Bandwidth B = 1 THz
Effective occupation number n = R / B = 10-12
Effective noise squeezing factor = 1/sqrt(n) = 60 dB
Transmon qubits (quantum non-demolition for GHz):
Effective occupation number n=10-3
Effective noise squeezing factor = 1/sqrt(n) = 16 dB
P. Echternach (JPL)
K. Berggren, S. Nam, et al.

## Slide 37: One can also use a huge dish antenna comprising an array of QRAMs as the dark matter scattering target
D. Horns, et.al, JCAP 1304, 016 (2013)
This is like having an array of N cavity resonators, where each cavity only gets 1 bounce.
Dark matter emits transition radiation upon impedance mismatch.
Single photon detector

## Slide 38: GQuEST: Single photon counting readout for gravitational wave interferometers
Pathway towards 50 dB below SQL?
Far, far better than the few dB of squeezing achieved so far by LIGO, limited by photon transport losses
Enables search for space-time noise from quantum gravity.
Narrowband filter cavity defines the mode linewidth
Low dark rate single photon detector
Lee McCuller, arXiv:2211.04016

## Slide 39: Topic 3: Stimulating power transfer from the weakly coupled source

## Slide 40: More stupid qubit tricks: Stimulated emission of photons from DM waves
Good!
Waiting…
Oops, wrong phase
Power =
Phase offset determines the direction of energy flow.
Start the photon wave swinging so it can more easily accept energy from the DM.

## Slide 41: However, a sinusoidally swinging oscillator actually has exactly the same resolution as an oscillator prepared in the vacuum state. Cannot evade SQL with homodyne/heterodyne detection.
Resolution is just the size of the Gaussian blob in phase space, i.e. ½ ℏ
Displacements from forces just act linearly on this phase space distribution:
It doesn’t matter whether you prepared the state at finite amplitude 𝛽 or if you started with 𝛽=0. The resolution on α is the same.
Wikipedia

## Slide 42: What happens if we initialize the probe to a Fock state instead of a Gaussian blob?
The Fock state is symmetric in phase angle
 responds equally well to pushes at any time.
It also has definite occupation number N
 no Poisson noise!
… and force × velocity still works:
N=1 Fock state
Idea from Konrad Lehnert
(JILA/U.Colorado)
A Fock state is a superposition of an oscillator in all possible phases of its sinusoidal motion: ∆N×∆𝜑 ≥ ½
= +) 

## Slide 43: Mixing between a coherent state and a Fock state
The dark matter wave is a sine wave described by a Glauber coherent state
The cavity photon mode has been prepared as a N=10 Fock state, highly sensitive to environmental disturbances
QuTiP simulation
X
P

## Slide 44: For finite coherence time << mixing time, the transfer of quanta from DM to photons is enhanced by a factor (N+1)
N=0
N=10
Displacement
Displacement
Spontaneous emission signal
Stimulated emission / absorption signals
QuTiP simulation

## Slide 45: Creating Fock states in a (non)linear system
=
“Optimal control” sequence of drives at both the qubit and cavity frequencies,
determined by “gradient ascent pulse engineering”
Slide/data from Ankur Agrawal
Notes: Fock states are quantum state of light which cannot be created in a linear system such as a cavity. However, if we rewrite the Hamiltonian again, we see that the cavity frequency is dependent on the state of the qubit. This non-linearity allows us to prepare the cavity in any quantum state.
I used an optimal control package which was developed in our lab to solve an inversion problem. Given a Hamiltonian, it uses machine learning algorithm to generate a set of qubit and cavity control drives to perform a non-trivial state transfer. I used a 3D multimode cavity coupled to a transmon as shown in the image here for the experiment.
Here is an example of such a state transfer from the ground state to n=1 Fock state. We can see the cavity’s wave function evolve from n=0 to n=1 in this movie.
Wigner function is a quasi-distribution function which represents the wavefunction of the oscillator. Parity operator is an effective experimental tool to compute the density matrix.

## Slide 46: Verifying the state preparation
Method 1: Qubit spectroscopy with a number resolved pulse
Method 2: Wigner tomography to reconstruct the density matrix
Sweep pi pulse frequency
Slide/data from Ankur Agrawal
Notes: We can use this method to verify the preparation of cavity in a Fock state.
Method 1 is a qubit spectroscopy with a number resolved pi pulse which I had described earlier. On the left, we see the qubit spectrum and a single peak in each spectrum confirms the cavity state in a definite photon number.
The other method is Wigner tomography which is slightly more involved and requires multiple measurements to reconstruct the state of the cavity.
Hence, for the rest of this talk, I am going to use a number resolved qubit pi pulse to probe the cavity state.
I would like to point out that the information that we obtain from a resolved pi pulse and the Wigner tomography is the same, as there is no phase information associated with the cavity state. Henceforth, we will just use resolved pi pulse to probe the cavity state.

## Slide 47: Stimulated emission protocol
Mock Injection
Ensures false positive probability from accidentally prepping is ,
comparable to measured cavity occupation probability
Hidden Markov model analyzes probability of observed sequence of yes’s and no’s from repeated pi pulses.
Notes: After preparing the Fock states, let me describe the stimulated emission protocol, where we have divided the sequence into two.
First part involves the state preparation and false positive reduction by conditionally pi pulsing the qubit at |n+1> peak and if and only if the answer is a series of 3 no’s do, we proceed. This is to check that the cavity didn’t accidentally start in |n+1> Fock state.
By doing so, we can suppress false positive errors below 3%.
In the next part, we inject a fake dark matter signal and then measure the cavity occupation probability being in n+1 Fock state with conditional repeated measurements using the qubit.
We then apply a Hidden Markov Model that I described in the previous section to reconstruct the state of the cavity after the coherent drive and count the number of positive events which cross a certain likelihood ratio.
I would like to point out one of the key difference in the protocol between photon counting and stimulated emission: in the photon counting we were interested in the state of the cavity before we started the first measurement where as, in this case we have to be very certain that the cavity is still in the correct Fock state before we apply the coherent displacement. And thus, it took a lot of time to come up with this sequence to balance the state preparation fidelity and the false positives.
We perform active reset of the qubit and update pulse parameters to correct for higher order terms in the Hamiltonian as they start to matter as we higher in photon numbers.

## Slide 48: Signature of enhancement
This is the first demonstration so far showing signal enhancement with = Fock state
Less than a factor of (n+1) due to measurement inefficiencies, e.g. photon decays during measurement, QND has small demolition probability, etc. HMM optimized for small background rate nbkgd<1%
Slide/data from Ankur Agrawal,
arXiv:2305.03700
Increased number of signal photons delivered … for the same applied force
Notes: Given this experimental protocol, let me describe how we characterize the detector.
After initializing the cavity in a particular Fock state, we inject a mean photon number shown on the x-axis. Y-axis is the probability of finding the cavity in (n+1) given that the cavity started in the correct Fock state.
So, let’s start with the cavity in its ground state. As we inject more photons, we measure more as expected. Now, if we initialize the cavity in n=1 Fock state then we should see higher occupation probability.
And, we do! Let’s go even higher.
As we can see, the stimulated emission does enhance the signal.
In a previous work such enhancement with n=1 was reported in an ion-trap system.
However, this is the first demonstration of enhancing weak signals using n=4 Fock state.
You may be asking why n=3 is missing. Unfortunately, we see some anomalous behaviour with n=3 and we suspect it is due to leakage to other modes in the cavity. We have identified a couple of potential transition with other modes which could explain this.

## Slide 49: Thank you for your attention! Also see related news articles:
Science, April 28, 2022
Physics Today, June 2019

## Slide 50: Backup slides

## Slide 51: Topic 4: Dark matter screwing up solid-state quantum computers

## Slide 52: Dark matter scattering deposits energy to create phonons and/or quasiparticles in the scattering target
Ping pong ball just back scatters, does not transmit much energy to heavy wall.
Pool ball stops when directly hitting an equal mass object. All kinetic energy is transferred.
Glancing hit
Direct hit
For v = galactic escape velocity 10-3 c, total kinetic energy available is 10-6 M
Slower
Faster
Train keeps moving forward when hitting a lighter obstacle

## Slide 53: If using qubit substrate as low mass DM target, use phonon modes
Y. Kahn and T. Lin, Rep. Prog. Phys. 85 (2022) 6, 066901
Optical phonons in polar materials with differently charged neighboring ions create electric dipole oscillations that couple well to photons (and dark photons).
They also have high phase velocity
v = E/p ≈ ∆/p which are better matched to the typical dark matter velocity v=10-3 c
Acoustic phonons have slow phase velocity given by the speed of sound v ≈ 10-5 c and can only couple well to the slowest dark matter in the galaxy
Higher mass DM can scatter on individual nuclei

## Slide 54: Qubits vs milli-charged dark matter Q<10-3 e
Artwork: C. Arguelles, K. Kelly, V. Munoz, 2104.13924
Due to weakly ionizing interactions, the earth scoops up millicharged particles floating around in the galaxy or created in cosmic ray air showers
Lower mass particles evaporate back into space while higher mass ones are captured and sink towards the center of the earth.
M.Pospelov, H.Ramani, Phys Rev D103, 115031 (2021)
Benchmark: 103 ambient mQ particles/cc in lab, thermalized to 300 K  108/cm2/s flying through your cryostat shields!
Upon hitting qubit substrate, kinetic energy = 0.03 eV is enough to break many Cooper pairs (0.0001 eV).

## Slide 55: Topic 5: Dark matter messing with trapped ion quantum computers

## Slide 56: Ion trap computers are sparsely populated with scattering targets, far less than Avogadro’s number. Must assume long-range forces between DM and ions.
Impulse:
Energy transfer:
(Spin-1)
(Spin-0, 2)
Low mass ions are better for spin-1 mediated long range forces

## Slide 57: Windchime concept: Larger mass accelerometers needed for detecting gravitational (spin-2) force from DM
Cubic meter array of 109 accelerometers with millimeter spacing to detect force from passing dark matter.
Probably gravitational force is too weak but can still focus on scalar or vector-mediated forces.
How to affordably read out sensor array and reconstruct track of 1000 excitations in real-time???
Probably impossible with classical computers.
  cf. LHC = 400M channels
  Heat load = 5 dedicated nuclear power plants
Diffraction of light? Quantum annealing?
If Dark matter detector = Quantum Computer
 Should provide in-situ processing of tracks
Co-located trapped ion computer seems well-suited to detect long correlation length excitations.
Phys.Rev.D 102 (2020) 7, 072003

## Slide 58: Energy budget of the universe (from various experimental probes)
We have *no* idea what is all of this other dark stuff around us.
It has so far been undetectable other than via its gravitational effects.
Prime experimental target for QUANTUM SENSING!
Things we design our shielding for

## Slide 59: Our current understanding of the dark matter landscape (APS-DPF Snowmass Study, July 2022)
A diverse variety of experimental techniques are proposed to cover every decade of possible dark matter mass.
Dark matter of some sort is probably flying through your lab.
Does it have interactions stronger than gravity???
E&M

## Slide 60: Dark matter (and visible matter) is confined to the galactic gravitational potential well
Dark matter velocity
~ escape velocity = 10-3 c
Compare to:
Sound speed = 10-5 c
Thermal gas velocity = 10-6 c
at 300 K
Terminology: “dark matter” is nonrelativistic, “dark radiation” is relativistic

## Slide 61: The smaller the DM mass, the more particles are needed to account for the inferred DM mass density. But these must fit inside the galactic box!
For mass < 70 eV, deBroglie wavelengths become large and the Pauli exclusion principle would cause dark matter clumps to swell up to be larger than the size of the smallest dwarf galaxies. (Randall, Scholtz, Unwin 2017)
 Lower mass dark matter must be coherent bosonic sine waves with macroscopic mode occupation number >>1
Higher mass dark matter acts more like billiard balls with occupation number <<1
Fermions: 1 DM particle per mode volume (1/∆p)3
∆p < pmax determined by escape velocity
Non-relativistic: wave frequency = rest mass

## Slide 62: Trigger on photons by placing threshold 𝜆 on MCMC probability ratio Prob(𝛾)/Prob(no 𝛾) for observed spin-flip sequence
Akash V. Dixit, et.al, Phys.Rev.Lett. 126, 141302 (2021)
Observed background = 10-3 photons per measurement (from leakage?)
Compare to amplifier readout which gives +/- 1 photon of zero-point variance per measurement.
Noise equivalent of 15.7 dB of squeezing!
Efficiency = 40.9%
Dark count probability =4.3×10-4
Efficiency-corrected dark count probability