## Slide 1: FPC & HOM Technology Challenges, FCC
R. Calaga, E. Montesinos, S. Zadeh
CERN
Dec 5, 2023
Ack: I. Karpov, F. Peauguer (CERN), S. Udonwgo (Rostock University)

## Slide 2
Coupling RF power into the cavity
Coupling beam power out of the cavity
FPC
HOM-C
Typically coaxial-type or waveguide-type couplers
Depending on frequency & power levels, adapted couplers are chosen
For the Future Circular Collider, up to 1 MW input and 10’s kW output is expected
narrowband
broadband

## Slide 3: FCC-ee RF Layout
90 km two ring synchroton for collisions between 100 MV – 11 GV per turn using 400 or 800 MHz SRF systems
Total beam power (x2)
Full energy booster for top up injection

## Slide 4: Basic Parameters
 | HL-LHC | Z | W | H | 
Energy [GeV] | 7000 | 45.6 | 80 | 120 | 182.5
Beam current [mA] | 1100 | 1279 | 137 | 26.7 | 4.9
RF Voltage [MV] | 12-16 | 79 | 1000 | 2080 | 2100/9380
# Cavities | 16 | 112 | 264 | 264 | 264/448
RF Power [kW] | 300 | 900 | 388 | 382 | 75/177
 | HL-LHC | Z | W | H | 
Energy [GeV] | 7000 | 45.6 | 80 | 120 | 182.5
Beam current [mA] | 1100 | 1279 | 137 | 26.7 | 4.9
RF Voltage [MV] | 12-16 | 79 | 1000 | 2080 | 2100/9380
# Cavities | 16 | 112 | 264 | 264 | 264/448
RF Power [kW] | 300 | 900 | 388 | 382 | 75/177
protons
electrons
Full energy booster not shown in the table

## Slide 5
LHC Accelerating RF - Today
8 cavities (2 CM) per beam
Cavity voltage = 2 MV (max)
Beam current = 1.1 A
Input power = 300 kW (max)
HOM power < 1 kW (max)

## Slide 6
LHC RF Input Coupler
300 kW-CW air cooled coaxial scheme
Cylindrical window for waveguide transition with matching, no door-knob
coaxial line to push multipacting to higher power levels + DC bias
Remotely controlled variable couplers to change by factor 3-5 in operation

## Slide 7: Input Power, FCC
Z
W, H
ttbar
A single RF scheme is not practical to satisfy high current and high energy – Power range of factor 5 & Coupling range () of factor 500
Present baseline  3 RF systems with fixed coupling, reasonable approach
No movable coupler is a big simplification, a movable short on air-side is being studied to adjust coupling if needed
Power vs Input Coupling

## Slide 8: Power Handling (empirical scaling)
Experience with power couplers built at CERN since 2000 used define an empirical scaling
The FCC specification in some scenarios is requiring the power levels to about factor 2 larger
Not obvious in CW mode to increment by factor 2 w/o considering novel cooling techniques, prevent multipacting damage and arcing
future
present

## Slide 9
Coupler Towards FCC
During the high gradient R&D program a MW class air-cooled coaxial-window coupler was developed for pulsed operation
This concept is used as the present baseline for the FCC. The jump to CW needs to be demonstrated, the critical point will be the RF window
An alternate disk-window outside the cryomodule is simpler option, but requires re-thinking the “clean assembly” of such a configuration
R&D on higher purity ceramic (99.5%) is ongoing

## Slide 10: Ceramic Windows Types, CERN
Disk windows
SPS, 800 MHz
150 KW CW
Cylindrical windows
LHC, 400 MHz
500 kW CW
Coaxial windows
HL-LHC Crab, 400 MHz
100 KW CW

## Slide 11
Multipacting
SEY of ceramic window very high and prone to multipacting & risk to ceramic
Improved with Ti coating on the vacuum side. Also helps to remove electrostatic discharge. Process well mastered
R&D ongoing to study low SEY ceramic. Potential simplification – pending validation & cost
DC bias (2-5 kV) is necessary to suppress multipacting – but brings additional complications. Magnetic means of suppression under study but not necessarily compatible with SRF

## Slide 12: Thermal Management
Outer-line: Stainless Steel + gold
+ copper
  Outer line: a thin Stainless Steel tube, acting as the thermal insulator to separate between the 2K and the 300K with He-gas flow or thermal intercepts
  A thin layer (~µm) of copper, to minimize RF losses, not transmitting so well the thermal losses to the cryogenic system
  With the recent HL-Crab 1.5 mm Stainless Steel tube + Gold 2 µm (flash) + Copper (or gold ) sputtering layer 10 µm being pursued as standard procedure
  Inner line: Massive OFE copper with air cooling avoid issues with freezing water at brazed joints
Peel off due to rinsing
Air-cooling

## Slide 13: Test Box & Conditioning
High power RF (pre)-conditioning of a “clean coupler” is necessary for controlled desorption of gases from the RF surface in SW & TW conditions
This process is time consuming and there is no short-cuts especially with CW power levels considered (200 kW to 1 MW)
Almost 1000 couplers to process for the main ring and ~500 couplers for the booster
Example of LHC RF conditioning system

## Slide 14: Assembly into Cavity
One of the most delicate & critical step, likely define the maximum field reach and onset of field emission. IS04 like clean room assembly makes it very cumbersome
For the HL-LHC crab cavity project, special 3D printed tooling and “semi-robotic” assembly proved to minimize the risk
Moderate gradients required for FCC, the assembly procedure needs to some re-thinking
1990’s
2017

## Slide 15
Cryomodule Integration
Cryomodules are typically conceived with cavities in mind
For very high RF power like the LHC & FCC, the power coupler and HOMC are a significant part of the “cavity assembly”. They also determine the performance reach
Present concept of installing the couplers in clean room and integration into cryomodule after may not be optimum
Can we install the couplers after the cryostating “in a clean way” ? Coupler exchange w/o de-cryostating and robotic way
Minimal distance for compact cryomodule

## Slide 16
Higher Order Mode Couplers
(HOMC)

## Slide 17
Impedance & HOMs
Three main issues to be addressed for the FCC
  Strong feedback around the fundamental mode
  Strong damping of the low frequency HOMs for CBI
  Efficient extraction of kWs of HOM power
Fundamental mode impedance
stability
opt detuning ()
-4
PRSTAB 21, 071001 (2018)

## Slide 18
LHC RF - HOM Scheme
The LHC system uses two coaxial type HOM couplers, narrow-band (low frequency) & broadband (> 700 MHz)
The large beam pipe aperture (300mm) is key for achieving very strong damping
“Narrowband”
“Broadband”
Look inside cryomodule

## Slide 19: HOM Couplers, FCC
LHC Probe-type
LHC Hook-type
DQW HOM Coupler
Example of transmission curves for 801.58 MHz
Three types of “tuned” coaxial couplers studied for strong damping targeting low frequency modes. Non-trivial geometries & tolerances
The tuning is very cavity specific, a “universal” coupler cannot be adopted as yet

## Slide 20
HOMC Design Considerations
For CW operation, the simulations and experimental experience with LHC and HL-LHC indicate
Demountable coupler with careful thermal design (gasket & feedthrough location)
Active cooling with a dedicated He-jacket
Sub-mm tolerances  cost driver
Cold RF window remains a big concern
As we approach kW level powers, we are exploring RF conditioning with a dedicated test-box
Trials with Nb-coating on Cu HOM couplers can open up a cheaper avenue, R&D started
He channel
He-Jacket
DQW coupler, HL-crabs

## Slide 21: FCC HOM Couplers, 400 MHz
Even with 1-2 cells & large aperture, stability requirements demand extremely strong damping
A cavity shape improvement from the LHC & extensive damping studies allowed to reduce to single Hook type coupler – important accomplishment!
2-Hook type couplers/cav
224
528
Notes: Review of cavity designs for FCC-ee Z, W and Higgs modes (1 cell for Z, 2 cells for W and higgs). Shape designed in a way to avoid high longitudinal impedance mode trapped in the cavity. Respective spectrums shown on the two plots. No sharp peak, especially for the single cell cavity (where current is highest). Comparison with beam stability threshold.
There are trapped modes in the transverse plane. To damp them, Shahnam has used 2 hook type coaxial couplers shown here (one for each polarisation mode). Threshold are shown with SR damping (no FB). Also added two simple rather large FPC coaxial couplers shown on next slide.

## Slide 22: FCC HOM Couplers, 800 MHz
For 5-cell cavities at 800 MHz, exhaustive studies on cavity design & HOM configuration to reach the damping requirements with a two crab cavity type coaxial coupler
Three important lessons from crab cavity program
Tight tolerances led to machining from Nb-bulk
Careful surface treatment of the Niobium surface similar to the SRF cavities (non-trivial) & active cooling
Cold-to-warm transitions to transport the wideband HOM power is a challenge
Longitudinal modes
Low freq transverse modes at the H-limit
Notes: Review of cavity designs for FCC-ee Z, W and Higgs modes (1 cell for Z, 2 cells for W and higgs). Shape designed in a way to avoid high longitudinal impedance mode trapped in the cavity. Respective spectrums shown on the two plots. No sharp peak, especially for the single cell cavity (where current is highest). Comparison with beam stability threshold.
There are trapped modes in the transverse plane. To damp them, Shahnam has used 2 hook type coaxial couplers shown here (one for each polarisation mode). Threshold are shown with SR damping (no FB). Also added two simple rather large FPC coaxial couplers shown on next slide.

## Slide 23
High Power
The very short bunches and high currents, the level of HOM power (CW) is 10’s of kW for the Z & up to 1 kW for the ttbar
The HOM power extracted with and w/o collisions can vary by several factors due to bunch length
For non-resonant excitation, the is not a strong dependence on bunch/train spacing for modes above cut-off
For resonant excitation, some filling schemes are forbidden
Safe
Dangerous
HOM
Cut-off: 765 MHz

## Slide 24: HOM Damping, Cryomodule
It was already studied since the 90’s (LHC) that the behavior of HOM damping is different in a cryomodule w.r.t a scheme optimized on a single cavity. Especially true when cavity-cavity coupling is strong due to large apertures
For FCC, inter-cavity damping and extraction of HOM power is essential. This requires accurate knowledge of power distribution in a CM and not just a single cavity

## Slide 25
Inter-Cavity Damping, 400 MHz
A 2-coax solution was found to be a simple an efficient solution for damping inter-cavity trapped modes & extraction of power above cut-off
The distribution of power (total = 40 kW) to allow for uniform output at the level of 10% look reasonable
The huge power extraction and broad-band in nature poses several technical challenges – similar to FPC and complications for CM integration

## Slide 26
Inter-Cavity Damping, 800 MHz
A single coaxial couplers for efficient damping inter-cavity trapped modes & extraction of power above cut-off. A waveguide solution was studied but more complex to implement
Similar to 400 MHz, approx. 10% of power extraction through these couplers
Some design features to capture both longitudinal and transverse modes to capture different polarizations
:
0.73 kW
0.05 kW
0.03 kW
0.06 kW
0.28 kW
0.07 kW
0.07 kW
0.31 kW
0.08 kW
0.06 kW
0.28 kW
0.07 kW
0.05 kW
0.06 kW
0.78 kW

## Slide 27: Taper or not to Taper
300 mm
Taper length
Taper small diameter
For practical reasons, it is necessary to reduce the aperture a long taper
For the FCC, the broadband part of the HOM spectrum is major contributor to HOM power
A “taper-less” cryomodule is preferable but may not be practical at 300 mm aperture
Optimum inter-cryomodule transitions with or w/o use of ferrite materials will be a challenge

## Slide 28
RF Feedthroughs for HOMs
The kW level CW power extraction through the HOM feedthrough is real challenge (much like an FPC)
With HL-LHC a substantial focus and R&D was done to develop a high-power feedthrough also taking into account transport of cryomodules ()
There is R&D necessary to master the bonding process of ceramic to Copper and manage stress to make a robust RF feedthrough that can handle high power in SRF environment
1st prototype
HL-LHC series
10cm drop test
20cm drop test

## Slide 29
RF Lines for HOMs
HOM coupler feedthrough 2K
Flexible contacts
Ceramic for thermal anchor 80 K
The kWs of power needs to be extracted from the couplers to an appropriate RF load in vacuum
A important development during the crab cavity project at CERN led to the development of semi-rigid lines to handle ~5 kW
Stainless Steel lines with 5 µm copper coating including ceramics for thermal anchor. Special RF fingers & thermal intercepts for to account for thermal cycles
Experience shows that these are not trivial & expensive. Mass production for FCC will be a major challenge

## Slide 30
Active shock logging, accelerator meters
Transport
Elaborate simulations to design supporting frame and transport restraints to minimize the stress during transport (cavities, cryomodules & components)
Logistics to apply this on large number of cryomodules is not trivial

## Slide 31
Final Thoughts
The FCC requires power couplers (0.2-1 MW level) & many HOM couplers operating at several kW’s level
Efficient power management, RF windows for high power CW operation & transport of couplers will remain the main challenges
The physics timescale proposed for the FCC-ee is very challenging (< 5yrs/working point)

## Slide 32
FPC
https://www.google.com/url?sa=t&rct=j&q=&esrc=s&source=web&cd=&cad=rja&uact=8&ved=2ahUKEwjCpNOB2fiCAxXSDOwKHZoYA1sQFnoECBIQAQ&url=https%3A%2F%2Findico.frib.msu.edu%2Fevent%2F38%2Fattachments%2F159%2F1270%2F20210624_SRF_tutorial_FPC_Eric_Montesinos.pdf&usg=AOvVaw17yghM7w82RMroy5EBoLsr&opi=89978449
HOMC
https://indico.cern.ch/event/1202105/contributions/5391663/attachments/2661531/4610909/1-cell%20and%202-cell%20400%20MHz%20cavity%20RF%20designs%20for%20FCC-ee.pdf
https://indico.cern.ch/event/1280043/
Some References

## Slide 33
Ceramic Window
Most sensitive part of an FPC & separates the beam vacuum to atmosphere through which very high-power RF has to be transmitted
Any leak on the window immediately leads into degradation of the cavity and nearby elements of the machine
It is commonly a ceramic brazed with metal (after metallization Mo-Mg deposition)
CERN specification report (Al2O3 - 97.5 %): http://cds.cern.ch/record/91419?ln=fr
R&D towards 99.5% spec is under study

## Slide 34
Elliptical cavity with radial slots and coaxial couplers for strong HOM damping
A 2-cell design at 600 MHz scenario to be use across the FCC energy regime was proposed to have a single frequency and single cavity type. It is however not beig actively pursued due to beam dynamics issues at 600 MHz for the lowest energy
A prototype at 1.3 GHz is under study for validation to understand the SRF limitations with a complex interface
The SWELL cavity, 600 MHz

## Slide 35
Use of Beam Pipe Absorbers
XFEL beam line absorber (77K)
Cornell beam line absorber (77K)
CESR beam line absorber (300K)
Beam pipe absorbers given their broadband damping nature has been exploited in various accelerators. Both 300 K and 77 K absorbers have been studied in great detail
The use for FCC is not obvious and not studied in much detail. Some R&D is required to push the usage of BLA’s in a more robust way than it is done today

## Slide 36
HOMs of the 800 MHz 5-cell cavity
7
4
7
2DQW couplers
corresponds to the power propagating through HOM couplers
correspond to radiated power through beam pipes
Some dangerous HOMs above BP cutoff weakly couple to HOM couplers  their Q-factor dominated by power propagating out through BPs
It's not enough to examine the HOMs of a single cavity  the impedance in a cavity string must be considered