## Slide 1: High Pressure Rinse Simulation Tool Applied to the SSR2 Cavity
Blake Gower SRF Process Engineer gower@frib.msu.edu
5 December 2023

## Slide 2: Overview
Why HPR for SRF?
HPR at FRIB
HPR Simulation Technique
HPR Simulation of SSR2 Cavity

## Slide 3: Why HPR for SRF?
RF fields strongest at the interior SRF cavity surface (~100s nm skin depth)
Interior surface finish dictates ultimate performance of SRF cavity
To produce high surface quality, interior cavity surface typically undergoes processes of
  Mechanical polishing
  Degreasing
  Chemical etching
    Buffered chemical polishing
    Electropolishing
  Degassing/baking
Final step is HPR with Ultra-high Purity Water
  Remove chemical residues
  Remove residual particulates

## Slide 4: Robotic HPR at FRIB
7-Axis KUKA Robot
14 L/min UPW (3.7 gpm)
69-83 bar (1000-1200 psi)
Images courtesy of L. Popielarski, E. Metzgar
Rinse booth located in ISO 5 cleanroom

## Slide 5: Simulation Method: Ray Casting and Ray-Triangle Intersection
Cavity interior as triangular mesh
Nozzle jets as rays

## Slide 6: PIP-II SSR2 Cavity Geometry
Begin with full mechanical model

## Slide 7: PIP-II SSR2 Cavity Geometry
Remove helium jacket and other exterior features

## Slide 8: PIP-II SSR2 Cavity Geometry
Isolate interior cavity surface

## Slide 9: PIP-II SSR2 Cavity Geometry
Create mesh of interior cavity surface (ANSYS Mesh)
  Element Edge Size: 0.0095 m
  Nodes: 16769
  Elements: 16674

## Slide 10: PIP-II SSR2 Cavity Geometry
Split mesh into triangles
  Element Edge Size: 0.0095 m
  Nodes: 16769
  Elements: 33162

## Slide 11: HPR Nozzle Modeling
Nozzle geometry and motion define each ray
Simulation parameters
  Nozzle geometry
    Number of jets
    Jet outlet locations
    Jet directions
  Nozzle motion
    Linear speed
    Rotational speed
    Maximum linear position
    Maximum rotation angle
    Linear step size (increment/resolution)**
    Number of passes
    Port entry coordinate
    Travel angle relative to port axis
    **Defining linear step size along with linear and rotational speeds fixes angular step size

## Slide 12: Ray Casting
Determine Ray-Triangle Intersection
Find supporting plane
Construct vectors along legs
Cross product yields plane normal vector
Sub known point into supporting plane equation

## Slide 13: Ray Casting
Determine Ray-Triangle Intersection
Find supporting plane
Construct vectors along legs
Cross product yields plane normal vector
Sub known point into supporting plane equation
Definition of a cast ray
  Origin at P in direction intersecting plane at Q
Substitute into plane equation
Find length of intersecting ray

## Slide 14: Ray Casting
Determine Ray-Triangle Intersection
Does ray-plane intersection exist?
  No intersection if ray is parallel to supporting plane
  Test if dot product of ray and plane-normal is zero (specify how close)
Does intersection occur within triangle?
  Construct vectors and use cross product to test on which side of an edge point Q is
  If on the “inside”, cross product will point the same direction as the plane normal vector (i.e. dot product will be positive)
  Check all three sides
Find supporting plane
Construct vectors along legs
Cross product yields plane normal vector
Sub known point into supporting plane equation
Definition of a cast ray
  Origin at P in direction intersecting plane at Q
Substitute into plane equation
Find length of intersecting ray

## Slide 15: Nozzle Motion and Ray-Triangle Intersection in SSR2 Cavity
Side/Rinse Port
Beam Port

## Slide 16: Result of Simple Rinsing Simulation
Side Port Rinse
Beam Port Rinse
Total Rinse
93.5% Elements Hit
Wash Accessibility
Missed Coverage
6.5% Elements Missed
100 Passes per Port
1 mm/s linear
1 deg/s rotation

## Slide 17: Improvements to Basic Rinse Routine
Change nozzle jet angles
12 Passes per Port
45°
25°
100 Passes/Port
Coverage: 93.5%
100 Passes/Port
Coverage: 95.9%

## Slide 18: Improvements to Basic Rinse Routine
On-axis motion in side/rinse ports limited by cavity spoke
Ports are large enough in diameter to allow for off-axis entry
  Greater cavity ingress
  Line-of-sight to unreached areas
[2] M. Parise et al., “PIP-II Cavities Fabrication and Processing Experience,” SRF2023 Paper TUPTB045
Rotate 20°about each non-port axis
Orient to each “quadrant”
Both side/rinse ports
8 Travel paths instead of 2

## Slide 19: Off-Axis Rinse Simulation

## Slide 20: Full Rinse Simulation Results
On-Axis Beam Port
On-Axis Rinse Port
Off-Axis Rinse Port
Total Coverage > 99.6%
Missed Coverage < 0.4%
Wash Intensity
Wash Accessibility

## Slide 21: Send Rinse Program to Robot
When wash intensity and coverage deemed satisfactory, a tabulated list of linear and angular coordinates is generated to be input to the robot control software. Shown here graphically.
Rinse Port – On-axis – 4 Passes
Beam Port – On-axis – 10 Passes

## Slide 22: Send Rinse Program to Robot
Rinse Port – Off-axis – 50 Passes
When wash intensity and coverage deemed satisfactory, a tabulated list of linear and angular coordinates is generated to be input to the robot control software. Shown here graphically.

## Slide 23: Future HPR Simulation Enhancements
Account for accumulated energy deposition
  Go beyond wash intensity by considering
    Conservation of momentum
    Impulse-momentum
    Incidence angle
    Residence time
    Jet spread, breakup
Avoid surface oxidation
  Too much HPR with UPW can leave an oxide layer on cavity surface
  Experiment to determine relationship between time, distance, incidence angle
  Put upper limit on rinse time and/or nozzle proximity in a given area based on energy deposition

## Slide 24: Summary
HPR Simulation code can be used to
Predict rinse coverage
Predict relative wash intensity
Inform nozzle design
Inform nozzle motion path

## Slide 25: References
[1] B. Gower, K. Elliot, E. Metzgar, T. Xu, “Simulation of high pressure rinse in superconducting radio frequency cavities,” in Proc. 21st Intl. Conf. on Radio-Frequency Superconductivity (SRF2023), Grand Rapids, USA, June 2023, Paper TUPTB039
[2] M. Parise, D. Passarelli, P. Berrutti, “PIP-II SSR2 Cavities fabrication and processing experience,” in Proc. 21st Intl. Conf. on Radio-Frequency Superconductivity (SRF2023), Grand Rapids, USA, June 2023, Paper TUPTB045

## Slide 26: Questions?
Thank you!

## Slide 27: Backup Slides

## Slide 28: Code Construction in MATLAB
Script
Function
Sub-Function
Triangular Cavity Mesh (Node and element connectivity matrices)
Linear speed
Rotational speed
Step size (resolution)
Port location (which port)
Number of passes
Start of linear travel path
End of linear travel path
Rotational limits (if any)
Nozzle geometry parameters
Construct nozzle geometry (jet location, direction)
Construct nozzle motion path (linear and rotational)
Loop for rays and triangles
Ray-Triangle Intersection?
Number of unique elements intersected (and which ones)
Number of intersections per unique element
Store
Next Port?
Finished?
Aggregate coverage
Missed elements/coverages
Data summary

## Slide 29: Use Case: Simulate Previously Completed HPR
Different nozzle geometries
Different travel paths
When cavity test results in failure after HPR completion due to field emission, simulate the rinse and use resulting missed coverage areas as inputs to multipacting simulation
64 particle sources, Gaussian emission with space charge effect
Image and details courtesy of J. Brown
15.6% Missed Coverage

## Slide 30: Use Case: Simulate Previously Completed HPR
Video and details courtesy of J. Brown