## Slide 1
2023-12-07
Double-Spoke Cavity Cryomodule
for CSNS-Ⅱ Project
Cong Zhang, Wenzhong Zhou, Feisi He, Rui Ge, Miaofu Xu, Tongming Huang, Qiang Ma, Zhenghui Mi, Mengxu Fan, Yun Wang, Ke Zhou, Huachang Liu，Sheng Wang, Weimin Pan
(CSNS/IHEP)

## Slide 2
OUT-
LINE
1. General Introduction To CSNS-Ⅱ
2. The Structure of DSR Cryomodule
3. The Integration of DSR Cryomodule
4. The Future Work

## Slide 3
1. General Introduction To CSNS-Ⅱ

## Slide 4
China Spallation Neutron Source II
Beam Parameters | CSNS-Ⅰ | CSNS-Ⅱ
Beam Power On Target （kW） | 100 | 500
Average Beam Current （μA） | 62.5 | 312.5
Linac Energy （MeV） | 80 | 300
Micropulse Ave Current （mA） | 15 | 40
Linac RF Frequency (MHz) | 324 | 324/648
Linac Beam Width （μS) | 400 | 600
Pulse Repetition Rate （Hz） | 25 | 25

## Slide 5
China Spallation Neutron Source II
Upgrade scheme of linear accelerator for CSNS-II
MEBT
RFQ
H-
DTL
LRBT
RCS
Elliptical cavities
Double-Spoke cavities
βg=0.62
648MHz
8cryomodules
3cav/cryomodule
β0=0.5
324MHz
10cryomodules
2 DSR/cryomodule
50keV
3MeV
80MeV
165MeV
300MeV
Х10
Double-Spoke Resonator(DSR)
324MHz
648MHz
Х8
6-Cell Elliptical Resonator

## Slide 6
2. The Structure of DSR Cryomodule

## Slide 7
DSR Cavity and Cryomodule Look
Naked DSR
DSR With Vessel
Helium Vessel
Cryomodule
Cavity：3.2mm/4.2mm RRR300 niobium sheets
Stiffening Ribs: low purity niobium
Helium Vessel: 4mm titanium sheet
Cryomodule: stainless steel
Magnetic Shielding: 1.3mm permalloy (1J79)

## Slide 8
DSR Cavity Fabrication and Test
Design Goal:
@ performance gradient Eacc=7.3 MV/m,
Q0≥3E9 without obvious FE
rinsing port added on the end covers
separate welding process
#1 cavity: Eacc~11.6 MV/m, Q0~2.2E10
#2 cavity with vessel: Eacc~11.6 MV/m,
Q0~4.6E10, Bpk~138mT, Epk~61.5MV/m

## Slide 9
DSR Cavity Cryomodule (1)
tuner
thermal partition
strut for assembly
coupler
two phase tube
liquid pulsimeter installation
target base for cavity
deformation
monitoring target
2K gas return
collimating target
beacon base
tie rod bracing
pump for insulated vacuum
collimation window
VAN gate valve
differential pressure gauge
liquid level meter, heater, T-sensor, P-sensor
Cooling Down Process:
1.helium gas filled from bottom to precool
2. 4.2K liquid helium filled from bottom
3. specifed level achieved then to 2K
4. supplement from top by throttle valve
7-channel cryogenic pipeline

## Slide 10
DSR Cavity Cryomodule (2)
tie rod support structure applied for cavity string and cold shield to decrease heat load
single layer 60K cold shield
cavity string, coupler, tuner and beam pipe integration in clean room
non-embedded installation of liquid level meter, heater and P-sensor
base support ensure fine adjustment of 6-directions
two tuner service holes on the bottom in case of parts replacement
coupler
60K cold shield
two-phase tube
tuner
tuner service hole
2K gas return
liquid level meter, heater, T-sensor, P-sensor

## Slide 11
3. The Integration of DSR Cryomodule

## Slide 12
DSR Cryomodule Assembly Procedure
cavity string in place
bottom cold shield assemby
cryogenic pipeline assemby
transducer assemby
tie rod assemby
insulating material wrapping
top cold shield assemby
aluminum fin tube welding
transducer assemby
insulating material for cold shield wrapping
installed into vacuum chamber
tie rod components assemby
cavity collimation
outside part of coupler installed
end cold shield installed
seven channel cryogenic pipeline installed
end flange installed

## Slide 13
Cavity String Assembly In Clean Room
FPC Outside Clean
Vesseled Cavity HPR
FPC Mounted To Cavity
End Cover Bellow Assembly
Cavity String Assembly Auxiliary
Cavity String Assembly
Integration:
two DSR cavities
two FPCs
two gate valves
three bellows
in class-10 clean room

## Slide 14
Mock Cavity Cryomodule R&D (1)
cavity string: mock cavity, two- phase tube, tie rod support
design pressure tolerance for mock cavity 2MPa, liquid nitrogen cold tested, positive pressure tested and vacuum tight tested, magnetic permeability <1.1
tie rod support: CFRP+316L(μ<1.05), strain test better than 0.8 TF at RT and better than 0.6 at LT
Cavity String
two-phase tube
Tie Rod Support
CFRP

## Slide 15
Mock Cavity Cryomodule R&D (2)
multi-channel cryogenic pipeline:
internal cryogenic transmission line, external vacuum line and cold shield included
316L, 304 seamless SS pipe, TU1OFC
G10 for support plate
liquid nitrogen cold shock test, positive pressure test and leakage test
ultrasonic clean before used

## Slide 16
DSR Cryomodule Assembly
Tuner Installation
Mock String Removed
C-Pipeline Welding
Bottom Shielding Installation
String Into Chamber
Completion
M-Shielding Package
Insulation Material Package
T-Sensor Installation

## Slide 17
4. The Future Work

## Slide 18
Horizontal Test Is Coming。。。
Leak Check
Water Cooling Install
Valve box pipeline installing and valve commissioning
The solid-state amplifier under commissioning
LLRF is ready

## Slide 19
Thank You For Your Attentions！