## Slide 1
DALIAN INSTITUTE OF CHEMICAL PHYSICS,
CHINESE ACADEMY OF SCIENCES
December 6,2023
Development of 1.3GHz 2-cell Superconducting Accelerator Module for DALS Injector
Quan Zhou Ph.D.
Dalian Light Source Science Laboratory,
SRF & cryogenic Tech. Research Group
Dalian YingGeShi
Dalian Advanced Light Source

## Slide 2
Report Content
Research Background
Dalian Advanced Light Source injector layout.
01
Module Design
Cavity; Coupler; Tuner; Beam line component; Cryogenic thermostat etc.
02
Research Progress
Fabrication; Process; Test; Assemble.
03

## Slide 3
Research Background
Dalian Advanced Light Source Injector
Parameter | Values | Unit
 | 100 | pC
 | 1 | MHz
Entrance | 300(DC)-750(VHF) | keV
Export | 2-4 | MeV
Normalized emittance | 0.56 | mm-mrad
 | 0.1 | mA
Longitudinal bunch length | 1(VHF)-2(DC) | mm
Parameter | Values | Unit
 | 100 | pC
 | 1 | MHz
 | 300(DC)-750(VHF) | keV
 | 2-4 | MeV
 | 0.56 | mm-mrad
 | 0.1 | mA
 | 1(VHF)-2(DC) | mm
CM00 Beam Design Parameters
DC: Direct Current gun; VHF: Very High Frequency gun;
CM00 Module
JT & Cool Down Valve
Vacuum Barrier
Post
VAT
Gate valve
Cold Plate
Magnetic Shield
Tuner
Twin
Coupler
Cavity
HTC
Manual valve
Carbon Steel Shield

## Slide 4
Module Design: Cavity
VCR
CF35
C Type Clamp
Pt
PHOM
DN 40
DN 78
Fix Limit
1.3GHz 2-cell Twin coupler TESLA Cavity
RF Parameter | Values | Unit
 | 1.3 | GHz
 | 0.23 | m
 | 219 | Ω
Geometric factor G | 273 | Ω
Operating gradient | 9 | MV/m
 | 2.03 | 
 | 4.73 | mT/(MV/m)
Field flatness | ＞95 | %
Quality factor |  | 
of field emission free | ＜16 | MV/m
RF Parameter | Values | Unit
 | 1.3 | GHz
 | 0.23 | m
 | 219 | Ω
Geometric factor G | 273 | Ω
 | 9 | MV/m
 | 2.03 | 
 | 4.73 | mT/(MV/m)
Field flatness | ＞95 | %
 | ＜16 | MV/m
Mechanical Parameter | Values | Unit
df/dp | 31 | Hz/mbar
Tunning sensitivity | 1015 | kHz/mm
Cavity stiffness | 14.4 | kN/mm
LFD coefficient | -0.67 | 
Lowest vibration fre. | 175 | Hz
Mechanical Parameter | Values | Unit
df/dp | 31 | Hz/mbar
Tunning sensitivity | 1015 | kHz/mm
Cavity stiffness | 14.4 | kN/mm
LFD coefficient | -0.67 | 
Lowest vibration fre. | 175 | Hz
Frequency(MHz) | Loss factor(V/pC) | (W)
1286 |  | 
2300-2800 | 0.256 | 
＞2800 | 2.175 | 0.217
Frequency(MHz) | Loss factor(V/pC) | 
1286 |  | 
2300-2800 | 0.256 | 
＞2800 | 2.175 | 0.217
HOM Parameters
300keV
700keV
60%
85%

## Slide 5
Module Design: Tuner
KEK Slide Type Tuner
Parameter | Design Values | Target
tunning range | 1mm/1015kHz | ≥±200kHz
Slow tunning sensitivity | 1.8Hz/Step | ≤5Hz/Step
Fast tunning range | 6μm/6.1kHz | ≥±1kHz
Fast tunning sensitivity | 0.3Hz | ≤1Hz
Tuner stiffness | 254kN/mm | ＞10×14.4kN/mm
2K Heat load | 0.52W | ＜0.5W
Parameter | Design Values | Target
 | 1mm/1015kHz | ≥±200kHz
Slow tunning sensitivity | 1.8Hz/Step | ≤5Hz/Step
Fast tunning range | 6μm/6.1kHz | ≥±1kHz
Fast tunning sensitivity | 0.3Hz | ≤1Hz
Tuner stiffness | 254kN/mm | ＞10×14.4kN/mm
2K Heat load | 0.52W | ＜0.5W
Tuner Mechanical & Heat Load Parameters
The frequency shift of 2-cell module mainly comes from :
1 Helium pressure fluctuations: 31Hz/mbar ×±0.1mbar = ±3.1Hz
2 Beam loading: = 0.1mA = ±10° Fre. shift: ±1.2Hz
3 Microphonic effect: Typical value ±10Hz
4 LFD detuning: -0.67Hz/(MV/m)^2×(9MV/m)^2=54Hz

## Slide 6
Module Design: Coupler
Modified TTF-III Coupler
Power required for cavity operation
5mm
Operating temperature map
Heat load analysis

## Slide 7
Module Design
Pipes; Thermostat; Cold plates and others
98mm
Magnetic Shield Design
2K
2K
50K
50K
DN63
DN38
Invar rod

## Slide 8
Research Progress: Cavity
Cav01
Cav01-03 with helium vessel
Cav03
Cav02
Cav02-03 helium vessel leaking
Cav03 severely compressed after transport
Cav04-05 naked cavity
Annealing after heavy EP
2K Vertical test
1296.3MHz
EP: 30μm
BCP: 15μm
EP: 30μm
BCP: 30μm
With Helium Vessel

## Slide 9
Research Progress: Tuner
Tuner01-02
Full stroke moving test in liquid nitrogen
8×10-2μm/V
7.5×10-2μm/V
Piezo01-06
Displacement curve
Creep motion

## Slide 10
Research Progress: Coupler
Coupler 01-06
Coupler RF processing clean assemble
Coupler RF processing setup
Coupler 03 warm inner conductor bellow leaking
Coupler packing
RF processing results
Coupler 01-06

## Slide 11
Research Progress
Permalloy magnetic shield
Beam tube
Manual gate valve
Thermostat demagnetization
Post alignment
RT to 2K beam tube is under fabrication
Cryogenic thermostat overall leakage check to be completed

## Slide 12
DALIAN INSTITUTE OF CHEMICAL PHYSICS,
CHINESE ACADEMY OF SCIENCES
December 6,2023
Special Thanks to
Q&A
RF Surface Technology Laboratory, Linear Accelerator Center, IMP
Superconducting module & cryogenic system team,
Institute of Advanced Science Facilities, Shenzhen
SRF Laboratory, Institute of Heavy Ion Physics, Peking University