## Slide 1: 1. Design and fabrication of a twin-FPCs 1.3GHz 9-cell cavity 2. Third Harmonic SRF Cryomodule for the SSRF Storage Ring
Hongtao Hou, SARI-CAS
Zhenyu Ma, SARI-CAS
On behalf of SRF group
7 December, 2023
TESLA Technology Collaboration Meeting, 2023, Fermilab
houht@sari.ac.cn

## Slide 2: Design and fabrication of a twin-FPCs 1.3GHz 9-cell cavity
SHINE

## Slide 3
Layout of SHINE SRF Accelerator
2
3
5
4
1
1 GUN 2 Solenoid 3 Buncher 4 Bend 5 cavity with twin FPC 6 Dump
Reduce RF kick
Suppression the influence on Emittance
2
2
4
6
6
3

## Slide 4: Influence of TESLA type cavity
Cavity with twin FPCs
Axial symmetry cavity；
Enlarged beam pipe at downstream for HOM propagation
Eliminate HOM couplers
Twin FPC located downstream
Asymmetric increase beam emittance
Perturbation from upstream HOM coupler
RF kick from FPC
Simulation shows emittance will increase from 0.25 mm mrad to 0.30 mm mrad (+24%), if using standard TESLA cavity
Beam

## Slide 5: Worldwide cavities with Twin-FPC
Cornell ERL injector
KEK cERL injector
Triumph e-linac

## Slide 6: Design of the cavity
Axial symmetry cavity；
Enlarged beam pipe at downstream for HOM propagation
Eliminate HOM couplers
Twin FPC located downstream
Using CST、Mutipac、Ansys
Beam pipe HOM absorber

## Slide 7: Simulation Results
Ql of monopole and dipole modes with different HOM absorber locations
Epeak/Eacc | Bpeak/Eacc （mT/(MV/m)） | R/Q （Ω） | G （Ω） | f（MHz） | flatness
2.0 | 4.2 | 983.4 | 273.6 | 1300.0001 | 98.3%
Report from Yan Wang, et.al, SARI-CAS

## Slide 8
Ib/mA | Pf/kW | Pb/kW | Pr/kW | Pf/KW（single FPC）
0 | 1.66 | 0 | 1.66 | 0.83
0.05 | 2.05 | 0.62 | 1.43 | 1.025
0.1 | 2.48 | 1.25 | 1.23 | 1.24
0.15 | 2.96 | 1.87 | 1.09 | 1.48
0.2 | 3.5 | 2.49 | 1.01 | 1.75
0.25 | 4.08 | 3.11 | 0.97 | 2.04
0.3 | 4.71 | 3.74 | 0.97 | 2.355
Power requirement
Eacc=12MV/m、Q0=1.5×1010，Qe=3.53×107，assuming frequency detuning by microphonics δf=10 Hz，with 15% power loss

## Slide 9: Fabrication
High purity Nb material
Deep drawing
Electron beam welding
BCP treatment
Helium vessel welding
Vertical test
Specification
Frequency：1300.2+/- 0.1 MHz @ 2.0 K， field flatness ≥ 90%（dressed cavity）
Q0> 1.5 e10 @ Eacc=12 MV/m，Eacc_max ≥ 19MV/m
Low QL of HOM modes with high r/Q： QL < 1e6
straightness ≤0.4 mm，length ≤+/- 3.0 mm，shape accuracy ≤+/- 0.5 mm
Leakrate ≤ 1e-10 mbar l/s
Pressure test of dressed cavity: 0.23 MPa

## Slide 10
Vertical test results: f=1300.146 MHz @ 2K, Q0> 1.5 e10 @ Eacc=12 MV/m，Eacc_max ~28MV/m

## Slide 11: Third Harmonic SRF Cryomodule for the SSRF Storage Ring
SSRF

## Slide 12
Motivation
  Improve beam quality and increase lifetime
    More insertion devices installed into the tunnel which reduce lifetime
  Increase single bunch beam current threshold
    Single bunch beam current >20 mA is required by Fast X-ray Imaging Beamline
Design of the system
  Passive or Active, SC or NC was compared before choosing a passive SC cryomodule
  One coupled 2-cell cavity can provide high enough harmonic voltage

## Slide 13
Main rf voltage: 4.5 ~ 5.4 MV by three 500MHz SC cryomodules
Theoretical harmonic voltage is 1.4 ~ 1.8 MV for h=3
Calculated stretching factor is larger than 2 with different filling patterns
Requirement of harmonic cavity for SSRF
Parameter | Description | Value
E | Beam energy | 3.5 GeV
C | Circumference | 432 m
Idc | DC beam current | 0.2 ~ 0.3 A
frf | RF frequency | 499.654 MHz
h | Harmonic number | 720
α | Momentum compaction | 4.2e-4
σε | Energy spread | 0.001
U0 | Radiation loss per turn | 1.4 MeV
Vrf | Main rf voltage | 4.5 ~ 5.4 MV
Qs | Nominal synchrotron tune | 0.0075
σl | Nominal rms bunch length | 3.8 mm
Vh | Harmonic rf voltage | 1.4 ~1.8 MV
Table-1: Parameters of SSRF Storage Ring

## Slide 14
Taper with ion pump
(downstream)
Gate-valve
HOM
absorber
Multi-transfer lines
Tuner
Assembly
HOM
Absorber
Gate-valve
Taper with ion pump
(upstream)
Adjustable Module base
HOM free 2-cell Nb Cavity
Sliding
Joints
Cryostat
Key component: SSRF has completed intellectual property rights.
Cryomodule=L*W*H=2338 mm*1460mm*2371mm, beam center=1300mm
  Nb cavity: HOM-free, passive, 1500MHz, two-cell cavity made of RRR>300 niobium material
  Cryostat: helium vessel, thermal shielding, magnetic shielding, sensors, safety valves and burst disc
  HOM absorber: beamline type, SiC material
  Tuner: mechanical together with piezo
  Vacuum parts: pipes, sliding joints, gate valves, tapers with synchrotron light shielding, ion pumps
  Monitor/Interlock and LLRF control: based on PLC and digital IQ techniques, interlocks
Bunch Control System at SSRF based on Passive Superconducting RF Cavity

## Slide 15
Superconducting 3HC cryomodule development
1500MHz 2-cell Nb cavity
Cavity with thermal transition
Cryostate
HOM absorber
Tuner
Cryomodule Assembly
Interlock and LLRF controller
Horizontal test
In tunnel

## Slide 16
Bunch size (Half Band Width) lengthening factor is larger than twice
  Stretching factor is 2.2 with uniform filling pattern
  Stretching factor ~ 3 with hybrid filling pattern
  Single bunch beam current reached 24.5 mA in hybrid filling pattern
  Steam camera is used to measure bunch length
3HC operation state
  Stable cavity voltage, adjusted smoothly by tuner
  Cryogenic, vacuum are stable
  No influence observed on main rf system
Commissioning with Beam
Single bunch current in Hybrid filling pattern
Uniform filling pattern
One of Hybrid filling pattern
多束团模式

## Slide 17
Thanks for your attention!