## Slide 1: Project X Proton Source
Keith Gollwitzer
Accelerator Division
Fermilab
Muon Collider Higgs Factory Mini-Workshop
November 13, 2012

## Slide 2: Outline
Summary of Project X
Upgrade of Project X to 4 MW
Possible Operational Scenarios

## Slide 3: Project X Mission Goals
Provide a neutrino beam for long baseline neutrino oscillation experiments based on a capability of targeting at least 2 MW on proton beam power at any energy between 60-120 GeV.
Provide MW-class, multi-GeV, proton beams supporting multiple kaon, muon and neutrino based precision experiments. Simultaneous operations of the rare processes and neutrino programs are required.
Provide a path toward a muon source for possible future Neutrino Factory and/or Muon Collider.
Provide Options for implementing a program of Standard Model tests with nuclei and/or nuclear energy applications.

## Slide 4: Project X Reference Design
CW Linac will support average beam current of 1 mA to 3 GeV
Pulsed Linac (3-8 GeV) will have a ~5% duty factor
Possible 8 GeV beam power of 320 kW
Programmable Chopper System (part of H- source) will provide appropriate bunch structure for the linac experiments as well as fill the appropriate part of the RF buckets in the accumulating Recycler Ring

## Slide 5: Project X Staging
Recently, DOE requested Fermilab to propose staging of Project X
  Ion Source and CW Linac to 1 GeV; inject into current Booster; possible 1 MW at 1 GeV
  CW Linac 1 to 3 GeV with 3 GeV experiment campus
  Pulsed Linac 3 to 8 GeV; inject into Recycler
  Upgrade Project X to 4 MW at 8 GeV

## Slide 6: Upgrade
Upgrade Project X to achieve 4MW at 8GeV
  Increase particles
    Doubling particles per linac bunch
    Average beam current increase to 5 mA
  Increase pulsed linac duty factor
    Increase to 10%
    Additional RF power and infrastructure
Beam Reformatting
  Accumulation Ring
  Bunch Compression

## Slide 7: Proton Driver Layout
Accumulator Ring
Compressor Ring
4MW Target

## Slide 8: Possible Operational Schemes - 1
Upgraded Project X
  Pulse at 15Hz
  Pulse for 6.67ms
  Programmable chopper allows half of beam through
Accumulation Ring
  Converts ion beam to proton beam
  RF buckets synchronized to chopper
  Results in 4 bunches

## Slide 9: Possible Operational Schemes - 2
Desired frequency to Compressor Ring
  60 Hz: Transfer single bunch at a time
  30 Hz: Transfer 2 bunches at a time
  15 Hz: Transfer all 4 bunches
Compressor Ring bunch rotates beam and extracts into 1, 2 or 4 beam lines to target
  Multiple beam lines are such that all bunches arrive simultaneously

## Slide 10: Multiple Beam Lines to Target
Extracted bunches from Compressor Ring are sent into different length beam lines

## Slide 11: Multiple Beams onto Target
Each beam line enters the target area with an angle to the solenoid axis and will have a path such that the center of the interaction region is on the solenoid’s axis

## Slide 12: Why 4 Bunches
Instability due to intense particle bunches
Believe that 1 MW per bunch is possible at 15 Hz running of Project X
If 4MW is desirable, then multiple beam lines are needed to deliver beam to target
Final Bunch Parameters
(Compressor Ring)
Initial Ring Bunch Parameters
(Accumulator Ring)
V. Lebedev: maximum power per bunch

## Slide 13: Summary
There is an upgrade path from Project X to provide 4 MW of 8 GeV proton beam to a target with the desired characteristics
Questions?