## Slide 1: High Bandwidth DAQ Systems for the Intensity Frontier
Mark Convery
January 10, 2013

## Slide 2: Introduction
  The next Intensity Frontier experiments present interesting DAQ challenges
  Rare Decay experiments (ORKA, Mu2e)
    Will have 10x-100x higher rates than predecessors from the 80’s and 90’s
    Previous trigger strategies no longer applicable
    Streaming (triggerless) DAQ presents promising solution, but requires high bandwidth
  Leveraging industry progress
  Long Baseline Neutrino Experiment
    High channel count
    High background (if at the surface)
    Streaming DAQ also desirable

## Slide 3: Moore’s Law of Bandwidth (Butter’s Law)
  Fortunately bandwidth has become extremely important commercially
  Follows its own Moore’s Law
    Butter’s Law: Bandwidth in a fiber increases by 50%/year
  Along with processing and storage improvements allows new trigger/DAQ strategies
  Leveraging this new hardware in HEP experiments may have high development costs

## Slide 4: Uses of High Bandwidth Systems

## Slide 5: Example Rare Decay: K+->p+nn
“Golden” Kaon decay mode
Extremely clean in SM
Sensitive to many forms of NP
Experimentally challenging
  Stopped K+ is the only proven technique. (In-flight decay technique being studied at NA62)
  Thought to be limited by accidentals to ~1 MHz stopped K+ rate

## Slide 6: Stopped K+ Technique
Used by BNL E787/949 (~0.7 MHz stopping K+ rate)
Proposed for FNAL ORKA (~5 MHz stopping K+ rate)
Advantages
  Well defined COM gives excellent kinematic background rejection
  Stopped pion allows 10-6 mis-ID through observation of pi->mu->e
  ~4p photon veto coverage relatively easy to achieve
Disadvantages
  Inherently “slow” technique since must wait for K, pi, mu decays -> sensitive to accidentals
  p0 photons relatively low energy

## Slide 7: Accidental Sensitivity at the Trigger Level
One example: “Delayed Coincidence” between K track in target and pi track in Range Stack to identify stopped K+
E787/949 used one target signal and one range stack signal
Need to wait for several K+ lifetimes (12 nS)
Works well if incident rate < 1MHz
Loses rejection power if rates >>1 MHz
Solution-> Higher segmentation at trigger level
Most easily done in software (triggerless system)

## Slide 8: Efficiency Loss at the Trigger Level
One example: detection of p->m decay gives excellent p ID
Needs analysis of PMT waveform to pick out m pulse
In trigger hardware, cut on height to width ratio -> loss of efficiency
In software, could do detailed pulse fit
Also significant deadtime losses mitigated by streaming trigger
Pi stop and decay
Transient digitizer data

## Slide 9: ORKA Experiment Proposal
Proposes to continue stopped K+ technique with 100x better sensitivity than E787/949
Improvements come from
  Higher K+ stopping rate (8x)
  Improved detector/trigger/analysis (11x)
High-speed (streaming) DAQ necessary for both

## Slide 10: ORKA DAQ Proposal
Propose to read full events into processor farm before any event selection
Triggerless system removes trigger deadtime
Allows higher rates without accidental losses
Reduces trigger inefficiencies due to better algorithms
Required bandwidth>400 Gbytes/sec

## Slide 11: MU2E DAQ Proposal
Mu2e also proposes streaming (triggerless) DAQ system
Plan is to run tracking code in software for event selection
Not yet clear if feasible. May need to have some rejection in FPGA
Total bandwidth: 30 Gbytes/second

## Slide 12: SLAC-Developed RCE System
A set of generic DAQ tools using modern switching and processing hardware
Reconfigurable Cluster Element (RCE) based on Xylinx Virtex-5 chip
ATCA infrastructure used
  Rear Transition Module (RTM) is a “personality” board unique to each application
Leverages industrial hardware and Detector R&D-funded hardware, firmware and software work
Currently being used in:
  ATLAS CSC, Heavy Photon Search, LSST, LCLS, etc.
Proposed for LBNE, etc.
See also, G.Haller Talk

## Slide 13: R&D For Next Generation
Current version to be used for several experiments
Goal for next phase is that for 14-slot shelve (crate)
  Provide 112 RCE’s
    112 10G Ethernet nodes capable of operating IP protocols
    Nearly 500,000 DMIPS of generic processing (Dhrystone)
    Over 100 TMACS of DSP processing
    Nearly 500 Gbytes of data buffering
  Over 700 channels of detector input
    Over 7 Tbits/s input bandwidth
  112 channels of 10G Ethernet output
    Over 1 Tbits/s data output bandwidth
  14 COB internal Ethernets
    Nearly 14 Tbits/s COB internal switching bandwidth
  One full-mesh backbone connecting network
    Over 7 Tbits/s switching network between networks
Target cost for one fully instrumented slot ~ $10k
From G. Haller’s
Talk Friday Session H

## Slide 14: Possible Application to LBNE LArTPC
Baseline DAQ assumes aggressive sparsification inside cryostat
  Reduces needed bandwidth to ~30 Mbps per APA
Use of high-bandwidth system could move sparsification to RCE’s
More flexible system with many advantages

## Slide 15: Conclusion
High-bandwidth (streaming) DAQ systems are an enabling technology for Intensity Frontier experiments
Allow to maintain (and improve) performance in the face of ever increasing rates
Fantastic industrial progress means costs are the same (or lower) than traditional system
SLAC is building and supporting a set of tools that leverage this progress and make it available with low incremental development cost
Such systems may have application even in traditionally low-rate experiments (like LBNE).