## Slide 1
PIP-II Laserwire Introduction
Vic Scarpine
PIP-II Beam Instrumentation Laser Wire Final Design Review
May 2, 2024

## Slide 2: Outline
Laserwire Basics
PIP-II Laserwire Requirements
PIP-II Laserwire Interfaces
PIP2IT Results
PIP-II Laserwire Overview
PIP-II Laser Hut
PIP-II Laserwire Team
PIP-II Laserwire Locations
PIP-II Laserwire Emittance Monitor

## Slide 3: Unique Issues with Profiling in a SC Linac
Beam profile measurements in high-intensity, superconducting H- accelerators are a challenging task.
Damage and contamination of superconducting RF cavity must be prevented at all costs.
  Invasive measurements can lead to particle contamination, degraded vacuum, beam loss leading to heating then quenching
This drives the need for non-invasive measurement of both transverse and longitudinal profiles.
Ultra-high vacuum in SC linacs make ionization profile monitors difficult.
The technique of photoionization (H- + g  H0 + e-) is preferred method for beam profiling.
PIP-II will utilize laser-based profile monitor (laserwires) for transverse and longitudinal profiling where possible.

## Slide 4: PIP-II Laserwire Choices and Challenges
Main issues for PIP-II
Small cross section  small signal
  3.5 E–17 cm^2 at 1.17 eV (l = 1064 nm)
PIP-II low beam current  small signal
Laser power limited by damage limit on optical vacuum viewports
High Peak Power Laser (free-space)
More photons per bunch – Pro
  More electrons  larger signal
  Simple Faraday cup collector
Need free-space transport – Con
Potentially larger power density on vacuum windows – Con
  Risk to damage windows  damage SRF cavities
Low Peak Power Laser (fiber)
Less photons per bunch - Con
  Less electrons  smaller signal
Laser transport through fibers – Pro/Con
  Easier transport but limited power through fibers
Lower peak power density on vacuum windows – Pro
  Less risk to SCF
Fiber-based, low-power option was tested at PIP2IT

## Slide 5: Requirements
Physics Requirements: ED0010230
  Re-released and approved. No changes to laserwire.
Laserwire Functional Requirements: ED0008303
  Re-released and approved. No changes to laserwire.
Laserwire Technical Requirements: ED0013714
  Changing requirement T-ED0013714-E004 from:
  “The free-space optics at each laserwire station shall keep the maximum average optical power density on the vacuum viewports to less than 3 W/cm2 “
  To
  “The free-space optics at each laserwire station shall keep the maximum average optical energy density on the vacuum viewports to less than 150 mJ/cm2 in 10µs and less than 3 J/cm2 in 1s“
    Note: industry standard is < 10 J/cm2 for a single laser pulse. We are requiring a 3x less energy limit. Presently we are designing to keep this limit to 50 mJ/cm2 in 10µs and less than 1 J/cm2 in 1s.

## Slide 6: Some Key PIP-II Numbers for Laserwire Design Guidance
H- Parameter | Nominal | Commissioning
Beam energy | 2.1 to 800 MeV | 2.1 to 833 MeV
Beam pulse length | 550 s | 10 ms
Bunch Intensity | 30 pC | 1.2 to 60 pC
Bunch Intensity (particles) | 1.5e8 | 6e7 to 3e8
Beam transverse size (rms) | 2 mm | 1 to 4 mm
Size of measurable region | ±15 mm | ±15 mm
Desirable typical scan time | <3 min | <5 min
Longitudinal bunch length (rms) | 200 to 4 ps | 200 to 4 ps
Need to make profile measurements with commissioning beam
With small H- beam current, we are optimizing laser pulse overlap with H- beam pulse for each beam energy (see Signal Performance talk) with following guidance:
Laser power on vacuum windows < 150mJ/cm2 per 10µs up to 20Hz
Keep laser power per pulse in linear response region (up to ~100µJ per pulse)
Select laser pulse width to maximize signal (minimize wasted photons)
Select laser pulse pattern to match chopped H- beam pattern (minimize laser power on windows)
Laser pulse rep rate ~10MHz over 10µs up to 20Hz for initial design (minimize difficult laser amplifier design)
H- Bunch Length

## Slide 7: Laser Pulse Length Studies
Amplitude of the charge profile for different jitter amplitudes, beam lengths and for laser pulse lengths from 1 ps to 1 ns
What is optimal laser pulse length for laserwire system?
May optimize laser pulse length for different H- beam energies
Laser design may allow for this. Under study

## Slide 8: Laserwire Interfaces
Interfaces identified and being managed though master interface controls document located in Teamcenter ED00010433 and Beam Instrumentation Noninvasive Beam Profile Monitor Interface Specification ED0016036.
WBS 121.03.09
Beam Instrumentation
WBS 121.03.04
LLRF
RF for laser and electronics
WBS 121.03.07
Controls
Timing, motion control and instrument control. Readout of diagnostic data.
WBS 121.04
Installation
Mechanical installation and alignment of detectors and optical transport line.
Power, rack space, cables.
WBS 121.03.06
Vacuum
Cleaning, assembly and vacuum certification of beamline components. Installation of optical transport line vacuum.
WBS 121.03.08
Safety Systems
Laser system safety interlocks
WBS 121.06
Conventional Facilities
Laser huts and laser transport line

## Slide 9: PIP2IT Prototype Laser Profile Monitor Measurements
Longitudinal beam profile with high-gain preamp
Preamp noise requires averaging
Background electrons limit dynamic range of measurement
Vertical beam profile with laser amplitude modulation detection
Potentially very sensitive technique
Sensitivity is proportional to time
Limited by cross-talk effects
Low peak power fiber-based laser with optical fiber transport
Conclusion: Low peak power fiber laser limited by amplifier noise and background  Move to higher peak power laser with free space laser transport.
PIP2IT Laser
Fiber Laser:
  162.5 MHz pulses locked to RF
  12 psec pulses at 1054 nm
  Up to 1 W at beamline
  ~6 nJ per pulse
Faraday cup for electron collection
Laser transport via LMA optical fiber

## Slide 10
PIP-II Free-Space Transport Laserwire Design

## Slide 11: PIP-II Laserwire
Free-space optical transport line above entire PIP-II WFE and Linac
Laser located outside of PIP-II tunnel in laser hut
Transport of laser light through vacuum pipe in PIP-II tunnel
Mirror boxes select which laserwire stations receive laser
  Can only select one profile measure location at a time
13 laserwire stations
~200m
Charge #2

## Slide 12: Laserwire for PIP-II
Cross sectional view of linac tunnel enclosure showing laser primary optical transport line envelope.
Transport line capable of free-space transport  low-vacuum for safety
Charge #2

## Slide 13: Laserwire Technical Progress
Progress:
Completed much of the design changes recommended from Nov 2022 mini-review of laserwire system.
Laserwire FDR May 2, 2024
  Will submit BCR to cover changes
Optical transport line design stable
Beamline design (vacuum chamber, optics box, stand, etc) moving toward final design
Short pulse laser design under development
  Lab measurements successful
Mirror Box
  Transport Line Talk
Laser System Talk
Laser Transport Optics and Alignment
Mechanical Design Talk

## Slide 14: Beamline Mechanical Design Labels
Input Optics Box
Removable Optics Breadboard
Laserwire Stand
Collection Magnets
Faraday Cup Port
Vacuum Pump
Assembly
Output Laser Dumps
Input Laser Port
Beamline Vacuum Chamber

## Slide 15: Laser Hut in Conventional Facility Drawings
RFQ
Laser hut and optical transport line light-tight and interlocked
Side View showing laser hut ceiling penetration and laser transport line
Top View

## Slide 16: Laserwire Design Team
Project manager and instrument designer
  Vic Scarpine, Scientist
Modeling and simulations, magnet design, optics design
  Randy Thurman-Keup, Scientist
  Sanjini Wijethunga, Postdoc
Laser design and development
  Jinhao Ruan, Scientist, Laser Physicist
  Parker Landon, Boston University graduate student
Beamline mechanical design (vacuum chamber, stand, optics boxes)
  Raul Campos, Mechanical engineer (Dakota Krokosz, ME)
  Tiffany Price, Mechanical engineer
Optical transport mechanical design
  Bob Steinberg, Mechanical engineer
Project CAM
  Sherese Humphrey

## Slide 17: Laserwire Locations in PIP-II SC Linac
Laser wire
HWR
SSR1
SSR2
LB650
HB650
MEBT
Emittance monitor
Most locations finalized in PIP-II accelerator physics lattice file.
  Emittance scanner laserwire location being finalized.

## Slide 18: Laserwire Locations in Accelerator Physics Lattice File
1
1
Accelerator Physics lattice file

## Slide 19: SNS Laserwire Emittance Monitor
SNS Laserwire Emittance Monitor
SNS Emittance Measurements
Laserwire Emittance Monitor Principle
Use upstream laserwire to measure X profile
  Downstream dipole steers H- but H0 goes straight
Use straight ahead detector to measure H0 which is X’ profile
How to measure H0?
H0 very small signal  PMT/EMT
H0 background from beam-beam stripping
How far apart is laserwire from H0 detector?
X
X’
PMT or EMT

## Slide 20: End of Linac Diagnostics – PIP-II Laser Emittance Monitor
End of linac beam diagnostics being finalized in accelerator physics lattice file
In the process of finalize LW for emittance location and H0 detector location
  H0 detector early in design
    Wire scanner + collection magnets + EMT
Foresee LW is possible future LW location is additional cryomodules are added
  This laserwire is not in PIP-II project scope.
LW H0 detector

## Slide 21: Evolution of H0 after Laserwire (from Abhishek)
Use these plot to determine location of downstream H0 detector
If laserwire downstream after 2nd RF separator region then H0 detector can be 10 to 15 meters downstream
A lot of flexibility in placement

## Slide 22: Summary
PIP-II Laserwire is a challenging design
PIP2IT experience was invaluable to PIP-II design
Moving to free-space laser transport gives more flexibility to laser profile monitor operation
  Allows for optimization of measurement performance
Design of beamline laserwire units, laser optical transport line and laser design meet the PIP-II requirements
Remaining talks will go into details of these designs