## Slide 1
Cable management design for Inspection Robot FERMILAB-POSTER-23-213-STUDENT
Josue Emanuel Garcia Gonzalez, Fermilab National Laboratory. Advisor: Noah Curfam
OVERVIEW
The main goal of the project is to design a cable support system connecting two electrically powered stepper motors in a gantry on an inspection robot or Remote Viewing Robot “RVR” as well as an electric-powered camera through cable carriers to prevent said cables to intertwine, bend or even rip apart.
One of the goals of the project was to secure the cable carrier in place as the actuators moves making sure both cable carriers have support where needed. This was solved by modeling parts that would allow screw holes for installing as well as back and lower support for both drag chains in the shape of aluminum plates.
horizontal brace bracket for lower support for horizontal cable carrier.
Screenshots of both vertical and horizontal drag chain supports models from 3D modeling program NX
3D model of horizontal and vertical cable carriers for Fermilab 3D modeling program NX
Screenshot taken from Fermilab 3D modeling program NX
Another objective was to allow support for the cable carriers. Both cable carriers needed support when the gantry moved achieved with two pieces of aluminum that were measured and modeled to fit the standards.
Lower right and middle bracket with 3-point screw holes for cable carrier installation
The support for the horizontal drag chain needs to be braced by the horizontal actuator through brackets which were designed and printed out of PETG filament for extra support.
INSTALLING AND SECURING CABLE CARRIERONTO RVR
DRAG CHAIN SUPPORT
RESULTS
Though PLA is more rigid, PETG has more flexibility and layer adhesion that allows the braces to hold more weight without snapping.
Successfully printed and assembled both cable carrier onto gantry allowing for easier cable management process.
Real picture of two-actuator gantry