## Slide 1
Maddie Schoell
ARR – External Validation of Updated SAD & ASE
August 15-17, 2023
Consistent Authorization Operating Limits

## Slide 2: Outline
Understanding Statement in the PEMP
Definitions for Operating Intensities
Determining Nominal Operating Intensity
Determining Maximum Operating Intensity
Determining ASE Intensity
Summary

## Slide 3: Understanding Statement in the PEMP
What is meant by “consistent authorization operating limit”
  Consistent approach for determining operating limits, and determining ASE limits
The following approach was discussed with FSO, and there were no objections that this approach would meet the intent of the PEMP statement
  Ensuring that the process for determining the Maximum Operating Limit intensity, and therefore the Credited Controls, is consistently applied for all segments/accelerators. Similarly, ensuring that the process for determining the ASE Limit intensity is consistent.
  Within the “Basis” section for each Credited Control, include statement such as “based on the Shielding Assessment performed at _____ intensity, the following Credited Control are required for operations of the _______ (applicable accelerator segment) at the maximum operating intensity limit”. (Which would be specific for each segment of the accelerator.
  Update the Beam Permit/Running Condition Credited Control section to include discussion regarding the allowance/process for operating at 5% above the Operating Limit intensity.

## Slide 4: Definitions for Operating Intensities
Nominal Operating Intensity
  The optimal hourly integrated intensity for an area. Normal fluctuations around this level are permissible. The expectation is that beam intensities for an area are generally maintained at or below the Nominal Operating Intensity.
Maximum Operating Intensity
  The maximum intensity at which an area is allowed to operate without requiring additional actions/approvals/responses. This is the area’s Nominal Operating Intensity +5%.
ASE Intensity
  The calculated intensity for an area that would produce a 500mrem accident condition, assuming a one-hour point source beam loss.

## Slide 5: Determining Nominal Operating Intensity
Nominal Operating Intensity
  Shielding Assessments developed based on operational beam intensity requirements (scientific needs) and the specific facility where it will operate
    Determines necessary controls such as shielding, fencing, and radiation monitoring
      These become Credited Controls, specified in the ASE
    Reviewed by the Shielding Assessment Review Panel (SARP) and approval recommended to the Senior Radiation Safety Officer (SRSO)
    SRSO approves final Shieling Assessment
Nominal Operating Intensity included in the accelerator or accelerator segment Beam Permit and Running Condition

## Slide 6: Determining Maximum Operating Intensity
Maximum Operating Intensity is the Nominal Operating Intensity +5%
Provides a buffer that allows for normal intensity fluctuations around the NOI
  Fluctuations caused by machine efficiency “breathing” throughout the day
Maximum Operating Intensity included in the accelerator or accelerator segment Beam Permit and Running Condition
ASE Intensity
Maximum Operating Intensity (NOI +5%)
Nominal Operating Intensity

## Slide 7: Determining ASE Intensity
ASE Intensity
  Calculation performed by ES&H Division to determine the beam intensity that could create a 500 mrem dose in one (1) hour a the “boundary” due to a 1-hour point source loss
  “Boundary” taken to be the external surface of the shielding
Beam in tunnel
500 mrem/hr
  This calculation becomes the basis for the Accelerator Operating Parameter Credited Control for the particle beam accelerators.
    This is included in ASE Section 7
    It had historically been included within a memo referenced in the ASE, moved into the ASE proper during the update.

## Slide 8: Determining ASE Intensity
ASE Intensity
  Using the 500 mrem to establish the limit:
    Allows for reasonable justification for not implementing postings or other controls at this threshold
      Using DOE-HDBK-1163-2020 risk assessment methodology, this accident scenario at ASE Intensities is Beyond Extremely Unlikely (BEU) based on the intrinsic design of the accelerator, and a Negligible (N) consequence, resulting in an acceptable Baseline Risk level IV which requires no additional controls

## Slide 9: Determining ASE Intensity
ASE Intensity
  Using the 500 mrem to establish the limit:
    Is half the DOE O 420.2D threshold for requiring DOE Program Secretarial Office approval of the ASE
    Conservative scenario, ensures Fermilab operations would never come close to this threshold
  ASE Intensity is included in the accelerator or accelerator segment Beam Permit and Running Condition

## Slide 10: Summary
A consistent approach is used to identify the Nominal Operating Intensity, which is supported by the Shielding Assessment
A consistent approach is used to determine the Maximum Operating Intensity
A consistent approach is used to calculate the ASE Intensity
Controls are established based on the Shielding Assessment
The Running Condition specifies the Nominal Operating Intensity, Maximum Operating Intensity and ASE Intensity

## Slide 11: Questions?