## Slide 1: Telecom and Security

## Slide 2: Telecom
Scope
Existing CUB
Existing incoming fiber and other connectivity infrastructure
Existing network equipment within control rooms, no dedicated telecommunications space
Existing conduits passing through the CUB
CUB Expansion Scope
All existing IT infrastructure supporting the CUB operations will be removed and replaced
Existing conduits to be adjusted/raised
Notes: Gordon

## Slide 3: Telecom
Design intent
New fiber connectivity from Cross Gallery via tunnel
New telecom room and rack to house network equipment and support CUB
New cable distribution to end devices
Adjust existing conduit route
Notes: Gordon

## Slide 4: Telecom
Existing conduit adjustment
Conduit content derives from the mac room and goes to either MI-8 or MI-60
There may also be fiber connectivity to the Kautz road substation and D0
Also services BTW and East AP buildings Along with Main Injector
Notes: https://my.matterport.com/show/?m=AJ9WPhUXFrw

## Slide 5: Telecom
Existing conduit to be adjusted
Notes: https://my.matterport.com/show/?m=AJ9WPhUXFrw

## Slide 6: Telecom
Existing conduit conditions
Eight (8) existing PVC conduits containing:
Approximately ten (10) innerduct tubes containing fiber.
Two (2) existing 100 pair phone trunk cables
Twelve (12) safety system cables
Approximately eight (8) copper hardline or heliax cables
Pull strings.
Decision required from Fermi:
Acceptable cabling splicing techniques for fiber, copper, and miscellaneous cabling

## Slide 7: Security
Design intent
Remove all existing cameras, card readers, door contacts, including miscellaneous devices / equipment
Install new devices/equipment with required cabling
New devices to connect to existing campus enterprise system
Devices connected to existing campus enterprise system via network
Install control panel to support field devices
Notes: Gordon

## Slide 8
BUILDING
SUPPORT
CURRENT
Building Parti
CHILLERS
EXPANSION
EXISTING CUB
WATER TREATMENT
HRC/HX/BOILERS
BUILDING SUPPORT