## Slide 1
APA Transport and Storage
Eric James
APA Technical Board Meeting
August 14, 2023

## Slide 2: Big Picture Issue
Current baseline plan is to fly APAs on Airbus Belugas (unpressurized cabins)
Biggest issue is on landing (rapid temperature change in potentially humid air conditions)
Aseet estimates that in high humidity conditions one could condense 35g of water within volume of APA
Not possible to “seal” APA due to pressure considerations

## Slide 3: Questions
Can an APA get wet?
  Aseet does not see a particular issue based on the current list of APA materials (assuming change to rosin-based flux)
  Probably would not want APA to sit wet for an extended period
  Would not want to get wet with “dirty” water (for example, water running down the Ross Shaft)
If the answer to the above is no (even over short time periods), it seems like there are two options
  Blow dry nitrogen through APA (requires pressurized bottles)
  Blow dry air through APA (requires power connection)

## Slide 4: Questions
If the APAs can get wet for short periods, we could blow dry air through the APAs after they arrive in the US
  At airport (within hours)?
  At storage facility (within days)?

## Slide 5: Protection Panels
Seal protection panels as well as possible with exception of four conduit holes (use these holes to blow dry air through APA)
Could cover with desiccant-filled panels at other times

## Slide 6: Transport Frame Covers
Suggest focusing on sealing the protection panels as well as possible
Could then think about eliminating the aluminum panels entirely
  Solves weight issue
  Solves issue of drilling ASF attachment points for the aluminum panels