## Slide 1: Electrostatic and Sag Considerations for Wire Tension
Aseet Mukherjee
5 Sep 2023

## Slide 2: Electrostatics
Can see from equipotential lines of TDR Figure 2.6, only X wires have significant charge
Can double-check from ΔV across planes
Expect
G to U
U to V
V to X

## Slide 3: Electrostatic Stability
https://www.cambridge.org/core/books/gaseous-radiation-detectors/multiwire-proportional-chambers/282A946D933D55B305EC0EBEFBE00465
Minimum tension for stability
Where
  𝐶: Capacitance per unit length
  𝑉: Voltage relative to neighboring plane
  𝐿: Wire length
  𝑠: Wire spacing
  𝑑 is the wire diameter.
  𝑔 is gap between layers
ε0 | 8.854E-12 | F/m
εLAr | 1.3281E-11 | F/m
s | 4.79 | mm
g | 4.75 | mm
d | 0.0152 | mm
C | 1.08041E-11 | F/m
V | 820 | V
L | 1500 | mm
TC | 0.046118824 | N

## Slide 4: Gravitational Sag
G and X layers are vertical → No sag
U and V layers are at 37.5° from vertical
Assume supports ever 150cm along vertical
Use the usual sag formula scaled for angle
  is weight per unit length
  is tension
  is length between supports
There must be other contributors to the final 0.5mm tolerance
Still… 6N seems unnecessarily high
ρ | 8.35 | g/cm3
d | 0.01524 | cm
W | 1.4942E-05 | N/cm
Lx | 150 | cm
θ | 37.5 | degrees
L | 155.120023 | cm
δ·T | 0.0273595 | cm·N
T | 6 | N
δ | 0.00455992 | cm

## Slide 5: Wire Diameter Uncertainty
Resonance mass per length
Sag gravitational acceleration
Combine
If wire sag is what sets the tension requirement wire diameter uncertainty is not an issue

## Slide 6: Other consideration?
Signal collection?
Noise? From TDR
A further complication from very low-tension wires might be an increase in noise level, introduced by wire vibrations, which can lead to vortex shedding.