## Slide 1
Preliminary results on PDE measurement of the VD-XA in Napoli
F. Di Capua, N. Canci, G. Matteucci, G. Grauso, Y. Suvorov, R. Calabrese, G. Fiorillo
Università di Napoli and INFN
A. A. Machado, E. Segreto
Campinas University
F. Terranova, C. Cattadori, C. Gotti, L. Meazza, A. Minotti
Milano Bicocca & INFN MI
G. Valdiviesso
Universidade Federal de Alfenas
D. Warner, K. Francis, Z. Rautio
Northern Illinois University
Notes: Write “many thanks to …” on corresponding slides

## Slide 2: Outline
Experimental setup for PDE Measurement
Cryostat LAr filling
Argon purity evaluation
SPE (Single PhotoElectron) measurement
Simulation
Preliminary result for PDE

## Slide 3: XA-VD measurement setup
Megacell on mechanical structure connected to dome
241Am source in Peek frame holder and connected to roto-translator
Inside the cryostat has been inserted a black shielding made by Delrin along the cryostat mantle and on the top cover
241Am source

## Slide 4: XA-VD measurement setup
Source manipulator
Megacell DB15 electrical connection
LAr level meter
Optical feedthrough
LAr filling line
Vacuum pump connection
PMT signal
PMT HV
LAr vent line

## Slide 5: Dichroic filters mounting
ZAOT filters evaporated in Campinas
Mounted in Napoli clean room
Light UV shielded during operations

## Slide 6: Electrical connection and DAQ
DMEM with two cold amplifier: preliminary tested in LN2 : both channels working
just before to close the cryostat one of two signal is not present: we changed position of one cold amplifier
After LAr filling discovered that one channel is very noisy
Output signals from second stage amplifier sent to CAEN V1725B digitizer
Cold amplifier
Warm second stage amplifier

## Slide 7: Warm amplifier
Switches to choose differential to single-ended conversion circuit
Switch towards the center of the board = With transformer
Switch towards the edge of the board = No transformer
Low/High gain mode through lateral jumpers
Our prefered conditions was low gain without transformer
with transformer
without transformer

## Slide 8: Measurement positions
Ch. 1
Ch. 2
Electronic box
PMT
Ch1: square dimples
Ch2: cylindrical dimples
PMT for purity monitoring

## Slide 9: Vacuum operations and LAr filling
Capacimeter level: the maximum correspond to 25 cm of LAr above Megacell
Evaporation rate 4 cm/24h
Pump and purge cycles before filling
Due to large amount of materials vacuum level not better than 10-4 mbar
The cryostat has been filled with LAr5.0 filtered by an in-line Trigon (Engelhard Q5-Cu0226)
During all measurement operations cryostat is in overpressure (1.2 atm) with respect to external pressure
Trigon filter

## Slide 10: LAr purity estimated with PMT
Two fitting procedures_
  3 exp. + gaussian
  Single exp (tail only)
Result of long tau component between 1.4-1.5 us
Fit executed on muon sample

## Slide 11: Monitoring of stability of LAr purity
Purity is found stable in all the measurement period
No purity correction to the measurement are required

## Slide 12: SPE response at OV=4.5V
Channels: 1,2
Filter moving average
Channel 1 very noisy → impossible to retrieve SPE
Channel 2 is ok
Charge spectrum integration 1.2 us
Vinogradov fit to photon statistics
duplication factor 0.28
fCTAP=1.28

## Slide 13: Secondary pulses estimated with Vinogradov model
From independent FBK single SiPM characterization data we have:
p=16% (PDE=45%)
Composite Poissonian to describes the joint effect of cross-talk and afterpulses
Two parameters μ e p
  p: probability to generate a secondary correlated avalanche
  μ: poissonian mean
  Kdup = p / (1-p) duplication factor
  Kdup = 0.28
  p=22%

## Slide 14: Alpha signal waveforms
Channel 1 noisy
Trigger on Channel 2

## Slide 15
4.8 us baseline
6.4 us integration windows

## Slide 16: Alpha source events
alpha selection
muons
Non-gaussian shape of the amplitude spectrum
Most likely this the effect of self-shielding of the source holder

## Slide 17: Source holder geometry
Source holder window is 23 mm diameter
Thickness of the holder edges is 6 mm: this induce a shielding of alpha particles
Due to the holder shielding the alpha spectrum becomes flat
Charge spectrum fitted with the convolution of a box function and a gaussian
Alpha yield: 50% of right tail
Alpha Spectrum has been corrected for secondary pulses (AP/CT)
6 mm

## Slide 18: Alpha spectrum: OV=4.5 V
Trigger on ch2 due to lower noise
Charge spectrum: integration
Alpha events selected via prompt light (PSD)
  Alpha distribution appears non-gaussian due to source holder shielding
  Alpha yield = fitted tail with the convolution of constant + gaussian distributions=50% of the maximum on the right tail
Measurement in six different locations for the source
Error (systematic) estimated by varying cuts
ch1
ch2

## Slide 19: Alpha spectrum: PEs vs position@ OV=4.5V

## Slide 20: Simulation (A. Machado, G. Valdiviesso)
Position | Average number of photons@ 5 cm
P2 | Under evaluation
P3 | Under evaluation
C | Under evaluation
P5 | 47000
P6 | Under evaluation
Position | Average number of photons@ 5 cm
P2 | Under evaluation
P3 | Under evaluation
C | Under evaluation
P5 | 
P6 | Under evaluation
number of photons in P5
Initial LY = 36000ph/MeV
PRELIMINARY
Implementation of source holder
Other defects solved (see Gustavo presentation)

## Slide 21: Preliminary results for PDE@OV=4.5V
Secondary pulse correcttion factor 1.28
PDE found to be in P5 about 2.2 %
 | PDE(%) @ OV=4.5V
Position | 5 cm
P2 | 
P3 | 
C | 
P5 | 2
P6 | 
 | PDE(%) @ OV=4.5V
Position | 5 cm
P2 | 
P3 | 
C | 
P5 | 
P6 | 

## Slide 22: SPE response at OV=7.0V
SPE fitted at OV=7.0V
Vinogradov fit to photon statistics
duplication factor 0.51
fCTAP=1.51

## Slide 23: Alpha spectrum: OV=7.0 V
Alpha source analysis at OV=7.0V
Spectrum includes corrections for secondary pulses (AP/CT)
ch1
ch2

## Slide 24: Alpha spectrum: PEs vs position@ OV=7.0V

## Slide 25: PDE summary
VERY PRELIMINARY
For the other positions used same scaling factor observed in simulation of P5 position before and after ne MC implementations

## Slide 26: PDE Errors
Error evaluation is very preliminary:
SPE response: 5-10%
Source PE fitting procedure: <5%
Simulation: error in initial LY not included
Systematics in source positioning to be evaluated (with simulation)
Others…..

## Slide 27: Megacell warming
At the moment the Megacell is still in the cryostat
LAr evaporated and the level is now below the X-Arapuca
Nitrogen gas flushing during warmup phase
Environment full saturated with Argon and Nitrogen gas

## Slide 28: Conclusions
A preliminary evaluation of the PDE of XA-VD system equipped with ZAOT filters and FBK SiPM has been performed
Self shielding of the source holder introduced some issue in the analysis
One channel found to be very noisy: SPE evaluated only on the good channel
Attempt to re-schedule a new measurement in October, changing the holder and collimating the source, check if there is no filter degradation