## Slide 1: Influence of Solenoid Field Quality on Electron Cooling

## Slide 2: Motivation
Magnetized electron trajectories follow magnetic field lines. -> Perturbations in velocity
Perturbations in velocity -> Reduction in electron cooling force
In Parkhomchuk model, the force depends on effective drift velocity.
A. V. Fedotov et. al., Numerical study of the magnetized cooling force, Phys. Rev. ST Accel. Beams 9, 074401, 2006.
Parkhomchuk
Derbenev and Skrinsky
Meshkov Asymptotic
N particle simulations
Longitudinal drift: Voltage jitter, space-charge voltage depression.
Transverse drift: E X B drift, electron velocity perturbations due to magnet errors.
Larmor radius: Magnetic field, electron transverse temperature
Min/Max Impact parameters: Ion velocity, plasma frequency

## Slide 3: Cooling Times: As designed
Used the Parkhomchuk model to calculate cooling times.
Requirement: Counter IBS heating times of the order of seconds at
Estimates treat cooling as a single thin-lens kick and ignore tracking through the solenoid.
We’re almost at the limit of cooling rate achievable.
The minimum moves up and to the right at higher energies.
Increasing the magnetic field boosts the maximum cooling rate marginally.
Radius (mm) | Current (mA) | Current Density (A/m2) | Cooling times (s)
18 | 80 | 78.6 | 0.79, 0.74, 0.94
14 | 1.7 | 2.76 | 12, 12, 13*
Baseline
2.5 MeV p+, Bz = 0.1 T
* Values published in IPAC’23 are incorrect.

## Slide 4: Field Errors: Simple Estimate
Assuming that the electrons follow the magnetic field lines. Ignoring the space-charge field from the electrons, the extra transverse velocity:
The temperature contribution is:
The above estimate assumes (1) No space-charge (2) We can make a practical solenoid with the above field quality.
1.1 eV @ 2 x 10-2

## Slide 5: Recap of previous work
How does solenoid field quality translate to electron velocity perturbations in the presence of static space-charge?
For realistic perturbations, the additional electron velocity arises from change in direction of the magnetic field lines. How to model the effect on cooling?
Inspired by C. Montag and J. Kewisch, in Proc. PAC'03, paper WPAE030, 2003.
Inspired by D. L. Bruhwiler et al., in Proc. PAC'05, paper TPAT087, 2005.
Plane wave
Multipole
Unrealistically small scales

## Slide 6: A 2nd look at the Parkhomchuk model
Central to the Parkhomchuk model is the effective velocity parameter.
Random: Voltage jitter
Function of position: Space-charge voltage depression, E X B drift, electron velocity perturbations due to magnet errors.
Use the voltage jitter as the sole source of effective velocity, treat position-dependent velocity changes as local frames of reference.
Treat field errors as deterministic perturbations to the electron velocity field.
p+
p+
for strong cooler
Predictions are within a factor of 2.

## Slide 7: Tracking Algorithm
Divide cooler into smaller segments.
Calculate local mean velocity of electrons at the position of the ions based on space-charge voltage depression, E X B drift, electron velocity perturbations due to magnet errors.
Calculate ion velocities w.r.t to this local rest frame.
Calculate cooling force using Parkhomchuk model and apply kick to ions.
Transport ions through a thick hard-edge ideal solenoid map in a drift-kick-drift fashion.
Transport through 1-turn 6D linear map and include an inverse map of the solenoid to cancel transverse coupling.
Other complexities: Matched distributions, eigenmode emittance calculations, fitting, fast field calculation (GPU), etc.
Solenoid body map
Thin-lens cooling kicks
Solenoid Entry and Exit Kicks
…

## Slide 8: Actual Solenoid Design
Design Requirement: (1) Max T. (2) Good field region with of length 600 mm and radius 15 mm.
Possible modifications: (1) Increase length (2) Reduce ID (3) Ferromagnetic plugs
Main coil (600 mm)
Trim coils (50 mm)
Br/Bz = 0.02
z = 300mm
r = 15 mm
R.C. Dhuley et al., JINST 16 T03009, 2021

## Slide 9: Cooling in Real Solenoid Field: Convergence
How many segments do we need to model the effect of field quality? About 10.
Parkhomchuk: for N = 10
Parkhomchuk 2: for N = 10

## Slide 10: Cooling times in real solenoid
Calculate cooling with 20000 particles, 10 steps inside solenoid, 4 turns: 720 seconds/estimate with GPU acceleration
Radius (mm) | Current (mA) | Current Density (A/m2) | Cooling times (s)
18 | 80 | 78.6 | 2.1, 1.9, 2.4
14 | 1.7 | 2.76 | 32, 31, 34
Factor of 3 degradation!

## Slide 11: Next Steps
Introduce winding errors and quantify effect on top of systematic errors.
Improve magnetic field model? (1) Increase length (2) Reduce ID (3) Ferromagnetic plugs (4) Different coil geometries?
Develop a simple way of incorporating cooling rate reduction into PyORBIT simulations.
Effect of steering toroids on field quality inside cooler and on proton beam orbit.
List plan of experiments and back-up with simulations.

## Slide 12: Appendix: Winding Errors
Design a winding error model which is consistent with experimental data.
Transverse field line deviations in CELCIUS cooler. http://cds.cern.ch/record/398603/files/p235.pdf

## Slide 13: Appendix: Cooling time with and without coupling compensation
Current (mA) | Radius (mm) | Density (A/m2) | Cooling Times (s)
1.7 | 14 | 2.76 | 370, 5.3, 8.6
80 | 18 | 78.6 | 1.5, 0.45, 0.67
Current (mA) | Radius (mm) | Density (A/m2) | Cooling Times (s)
1.7 | 14 | 2.76 | 12, 12, 13
80 | 18 | 78.6 | 0.79, 0.74, 0.94
Without
With