## Slide 1
Winding Procedures
Eric James
APA Technical Board Meeting
September 11, 2023

## Slide 2: Winding Procedures
Looked at
  8760Doc009 – Winding
  8760Doc010 – Tension Testing
  8760Doc011 – Tape, Solder, Trim
  8760Doc012 – Electrical Testing
Mentioned in Doc009
  6.5 +/- 1.0 N
  “Disposition of wires or segments falling outside the nominal 2N tolerance are evaluated after full tension measurement on both sides of layer”

## Slide 3: Winding Procedures
Mentioned in Doc009 (cont.)
  “cut five short un-tensioned wires on u- and v-layers”
  Comment that short head wires are un-tensioned
Mentioned in Doc010
  No tension measurements of segments < 5 cm
  V-layer tension measurements on 8->1146 only
  U-layer tension measurements on 9->1143 only

## Slide 4: Issues
Found no mention of re-tensioning procedures
  Suggest full replacement of wires requiring re-tensioning
  Would be advantageous for future incorporation of DWA
Found no mention of special treatment of “short” wires (with lengths < 50 cm)
Handling of very short wires (with lengths < 5cm) is not clear from procedures (at least to me)

## Slide 5: Issues (cont.)
Could not find any mention of active tension controls and procedures in case of alarm for tension values above 10N
Have not personally heard any pushback against Olga’s proposal for wire tensions (7.0 +/-1.5 N with 10% outliers outside of +/-1.5 N but within +/-2.0 N)
  Need to clarify if this up to 5% between 5.0 and 5.5 N and up to 5% between 8.5 and 9.0 N or something else