## Slide 1
Coupler for PXIE RFQ
S. Kazakov
11/29/2012

## Slide 2
Requirements:
F = 162.5
Two couplers , ~75 kW CW each
Input port ~ 3’’
Inductive coupling (loop)
5mA H-, 30 kV -> 2.1 MV
10.5 kW beam, 12% loading
Total RF power ~ 90 kW

## Slide 3
What we did after last meeting:
Bent coupler to reduce the transverse size of RFQ
Changed loop geometry to improve cooling efficiency
Simulated miltipactor in coupler region

## Slide 4
RF structure of coupler (Old)

## Slide 5
Antenna loop
Conflate flange
Ceramic window,
Standard 3-1/8’’ coaxial input
Teflon supports
Copper tubes
Capacitor
Air outlet
Air outlet
Air inlet
Arc detector
Copper tube
Mechanical design of the coupler (Old)
Rotatable flanges
Bronze bellow

## Slide 6
50 Ohm, 3-1/8’’ input
Short
to loop
Pass band (-20 dB) ~ 30 MHz
Bent geometry (new), S11

## Slide 7
Bent (new) geometry

## Slide 11
Supporting plate is removed.
Cooling efficiency of new geometry is higher ~ 17%.
Geometry of loop was changed

## Slide 12
Loop penetration and orientation
Operating angle ~ 45 dgr

## Slide 13
Angle (dgr) | RF out (kW)
0 | 101 kW
22.5 | 90 kW
45 | 59 kW
67.5 | 24 kW
90 | 3 kW

## Slide 14
R | RF out (rel. un)
R - 0.5mm | 1.0274
R | 1.0000
R + 0.5mm | 0.9348
H | RF out (rel. un)
H + 1mm | 1.0870
H | 1.0000
H- 1mm | 0.9605
Sensitivity to loop sizes

## Slide 15
Multipactor

## Slide 16
3.8 kV
7.5 kV
15 kV
Vane V

## Slide 17
30 kV
60 kV
Simulations show that
multipacor exists at 4 KV – 60 kV range of vanes voltage
(in input coaxial and cavity volume)
Vane V

## Slide 18
Vanes voltage 3.8 kV
HV bias 1.0 kV
Vanes voltage 7.5 kV
HV bias 2.0 kV
Vanes voltage 15 kV
HV bias 2.0 kV
Multipactor suppression by HV bias

## Slide 19
Vanes voltage 30 kV
HV bias 4.0 kV

## Slide 20
60 kV, -2 kV
60 kV, +2 kV

## Slide 21
60 kV, -3kV
60 kv, + 3 kV

## Slide 22
60 kV, +4 kV
60 kV, -4kV

## Slide 23
60 kV, +5 kV
60 kV, -5 kV

## Slide 24
60 kV, +6 kV
60 kV, -6 kV

## Slide 25
Conclusion:
Multipactor exists in coupler and cavity volumes.
HV bias suppresses multipactor on coupler region
Multipactor in cavity can be a problem and requires additional study.

## Slide 26
Coupler connection to RFQ body

## Slide 29
Our suggestion (following LBNL style).
LBNL should provide flange design.

## Slide 30
Future plans:
Thermal and stress analyses
Finalizing design
Design of test facilities
Drawings
Production
High power test