## Slide 1: DAPHNE Status
David Christian
FNAL
September 20, 2023

## Slide 2: DAPHNE
DAPHNE is the DUNE photodetector readout module
Developed for the horizontal drift detector
  40 channels per module (to read out PDS from 1 APA)
  Intended to operate in self-triggered mode with threshold = 1.5 PE
Developed by a Latin America/US collaboration
Inspired by the Mu2e SiPM readout module
  Uses a low cost “Analog Front End” chip made by Texas Instruments for ultrasound applications
  8 channel AFE5808A includes amplifiers, filters, 14-bit ADCs
  Digitizes analog SiPM signals and provides bias voltage for SiPMs and bias voltage for cold SiPM active ganging circuitry; can measure SiPM bias current.

## Slide 3: DAPHNE Development History (1/3)
DAPHNE_V1 (2021)
  1U enclosure
  ST microprocessor to configure AFEs, set SiPM bias voltages, configure multiplexing circuitry to measure SiPM bias currents.
  Xilinx Artix-7 FPGA to accept data from AFEs, detect signals, extract waveform snippets, and send data to FELIX on a 4.8 Gbps link (1/2 normal FELIX speed).
    High speed link can also be configured as 1 GbE; facilitates test bench use with “spy buffer” readout.
  Suffered from noise on voltages provided to the FE, difficulty communicating with the ST microprocessor as intended (100 Mbps Ethernet), noise in current and voltage monitoring,…

## Slide 4: DAPHNE Development History (2/3)
DAPHNE_V2 (2022)
  Same configuration as V1 (microprocessor + Artix 7; 1U enclosure)
  Better filtering to eliminate noise
  Modifications to enable 100 Mbps Ethernet link
  Modifications to enable 1 GbE control through FPGA concurrent with 4.8 Gbps output to FELIX; number of FELIX output links increased to 4
  Supports 2 output modes to FELIX
    Can stream data from 4 channels per FELIX link (max of 16/40 channels) – demonstrated October 2022
    Self triggered mode
      Simple threshold trigger – demonstrated Spring/summer 2023
      64 x 16 ns trigger latency allows development of more complex triggers (underway)

## Slide 5: DAPHNE Development History (3/3)
DAPHNE_V3 (2023)
  Xilinx Artix 7 & ST microprocessor replaced by Xilinx Zynq Ultrascale SOM (Kria K26)
    Artix firmware is relatively easy to implement on Zynq; K26 provides similar FPGA resources and supports much higher speed I/O.
  2U enclosure to allow space for Kria SOM (system-on-module) and better cooling.
  10 GbE output; 4 links (can stream 10 channels per link or operate in self-triggered mode)
  Control/spy buffer readout over 1 GbE
  Analog section essentially unchanged from V2 (different transformer used in differential to single-ended conversion allows more flexibility to tune digitized pulse shape)
  Redesigned power distribution; LDOs used for all analog rails
  Design completed recently and submitted for fabrication; first boards expected in early November.
  Kria test board designed and built earlier in 2023
    Allowed most control features of DAPHNE to be tested
    Allowed tests of high speed I/O
    Provided local experience with Zynq

## Slide 6: Plan for 2024
DAPHNE_V2 will be used at CERN until V3 is proven.
Development for optical interface required for FD2/NP02 will continue using V2.
  European effort, led by APC (Paris).
If NP02 runs first, expected configuration is:
  1 DAPHNE_V2 with prototype optical interface will be used to read out 8 cathode-mounted XArapucas; 16 channels of data; streaming output to FELIX (4 links)
  1 DAPHNE_V2 (unmodified) will be used to read out 4 membrane-mounted XArapucas with “FD1-style” CE; 8 channels of data; streaming output to FELIX (2 links)
  1 DAPHNE_V2 (modified to separate CE signals from power) will be used to read out 4 membrane-mounted XArapucas with “FD2-style” CE; 8 channels of data; streaming output to FELIX (2 links).
Transition to V3 will proceed ASAP
  Expect to use V3 for NP04 (1 APA with streaming output, 3 with self-triggered output)
  NP04 cold box may continue to use V2 for part of 2024