## Slide 1
Adam Watts
22 September 2023
AD Controls Department Report

## Slide 2: Resolved issues
MS3 and EAD Training Center power outages affected Meson and Neutrino CAMAC front-end availability. Systems recovered once scheduled outages (motivated by MS3 oil switch work) were finished.
Muon CAMAC link issues tracked down to apparent combination of link repeater hardware issue and failure mode where single crate saturates the link with replies. Cleared up after link repeater replacement and front-end developer assistance toggling crates on the link offline/online with diagnostic tool.
CLX40E (front-end for PLC systems) stopped responding to node poll, Ops reboot didn’t help. Front-end developer suspects related to PLCs being down during shutdown, but also identified erroneous process that was disrupting bootup. Startup process modified to not include erroneous process in the future.
Notes: We are working on another robot that used to be part of the MARV family. It is now called HERMES, short for Helpful Robotic Messenger). It is the smallest robot that we have that can be used for confined spaces and high radiation areas. A co-op engineering student designed a 3D printed chassis. Curently, under Susanna Stevenson's and Adam Watt's guidance, a senior engineering design group at Northern Illinois University is buidling a payload for autonomous photographic mapping of enclosures.

## Slide 3: Ongoing or upcoming issues
Mechanism for IRMs to sync new changes to device database stopped functioning late Wednesday. Could be related to Centra move to Alma Linux 9. Investigation and troubleshooting ongoing.
Planning for disruptive ACNET database outage next Thursdsay 9/28 to switch over to Alma Linux 9.
  0900, outage to all database connections for several minutes. This is the switch over to the standby server, already running Alma Linux 9 with a synchronized parallel database ready to go.
  Set up operational server with new OS, synchronize database.
  1400, 30-minute outage to all database connections, DB completely unavailable. Bring both servers up in high-availability failure mode, operational state.
  Lots of pre-planning, but unforeseen issues may come up after the switch. Please reach out to me so I can track and coordinate issues with the technical team.
Notes: We are working on another robot that used to be part of the MARV family. It is now called HERMES, short for Helpful Robotic Messenger). It is the smallest robot that we have that can be used for confined spaces and high radiation areas. A co-op engineering student designed a 3D printed chassis. Curently, under Susanna Stevenson's and Adam Watt's guidance, a senior engineering design group at Northern Illinois University is buidling a payload for autonomous photographic mapping of enclosures.