## Slide 1
Marco Russo
Gabriel Nathan Perdue
Final presentation
Low-latency quantum control using AI algorithms
on cryogenic microelectronic platforms

## Slide 2: Introduction
A qubit is the quantum equivalent of a bit
Instead of just 0 and 1, superposition:
Defining :
  Norm of a state is
When putting n qubits together:

## Slide 3: Introduction
Rotation along any axis can be expressed as
But how is the rotation physically achieved?
, on the Bloch sphere:

## Slide 4: Introduction
Many ways to build a quantum computer:
Neutral atoms
Photons
NMR
Trapped ions
Transmon

## Slide 5: Introduction
Superconducting circuits without and with Josephson junction
Operating temperature (for obtaining superconductivity)
Transition between |0⟩ and |1⟩ is done using EM pulses (microwaves)

## Slide 6: Quantum control with Juqbox [1]
Given a target gate , we want for any
Essential subspace of dim. , guarded subspace of dim. ()
Matrix provides a basis for the essential subspace
  So the Schrodinger’s eq. for any initial condition is given by
The optimization consists in calculating the that minimizes:

## Slide 7: Problem
This is done for one gate
  But and are arbitrary
    Off-line generation should be done over an infinity of angles
    On-line generation would take too long
      Low latency is needed (gates should take O(10 ns))
A strategy mixed with ML is needed:
  Use Juqbox to generate a finite dataset of params for
  Train an MLP neural network over the dataset
  It should be accurate over any angle

## Slide 8: Necessary steps
Dataset generation with Juqbox
Model training (simulated fidelity)
Quantization and synthesis on FPGA
Re-training on hardware (real fidelity)
Two problems:
  Hardware constraints
  How to estimate fidelity with statistical rigour?

## Slide 9: Neural networks on hardware [2]
Control electronics has limited resources
The model is adapted to the HW: quantization
  Weights are quantized from 64-bit to many fewer (16, 8, 4 bit)
The HW is adapted to the model: high-level synthesis
  HLS for optimizing an FPGA / ASIC for the model
    Pipelines for optimizing matrix mults
    The architecture of the model is taken in consideration

## Slide 10: Randomized benchmarking [3]
Given
Pauli group
  For 1 qubit,
Clifford group
  For 1 qubit,
Cayley graph for

## Slide 11: Randomized benchmarking
Group of gates
Starting from an initial pure state
  Random sequences of these gates are used
  Always possible to build a Clifford sequence
  Final state should be
  Accuracy decays exponentially with sequence length
  Fit for many lengths
Problem: are not Clifford

## Slide 12: Adapted RB for non-Clifford gates (empirical)
We want to test gates ( possible angles)
For each seq. length :
  For each seq. number :
    generate a random sequence
    each corresponds to the gate
    prepare initial state
    apply
    perform N measurements:
calculate average over the K sequences:

## Slide 13: Adapted RB for non-Clifford gates (empirical)
Set and
Fit to find using as uncertainties on the
Bounds:
is the estimated fidelity for a single gate
take cov. of the estimated parameters:
  2-tailed t-student test, with
    we get the CI radius =

## Slide 14: Simulation
Gate imperfections simulated with
M=range(2,150,10), K=500, 10 000 meas.

## Slide 15: Simulation
Gate imperfections simulated with
M=range(2,150,10), K=1000, 10 000 meas.

## Slide 16: RB on NN-generated pulses
NN trained on Juqbox (Python)
1000 angles from to (Python)
NN generates pulse params for each one (Python)
Params unitaries with Juqbox (Julia)
RB with resulting unitaries (Python)
IPC (JSON format)
IPC (JSON format)
Unitaries result from evolution with limited precision, so they are not normalized.
They are re-normalized in Python

## Slide 17: RB on NN-generated pulses
N = 10000 measurements
K = 500

## Slide 18: Next steps
How well does it perform on different physical conditions?
  NN was pre-trained with G=0
  Actual system has infinite guarded levels
  Anharmonicity hystheresis due to temperature cycles
Fine-tune the pre-trained NN
  using RB inside the loss function

## Slide 19: Testing with G guarded levels
Necessary changes:
  Initial condition must be a vector
  Unitaries coming from Juqbox have shape (2+G)x2.
  They must be padded into a (2+G)x(2+G):
} G
2 {
G {

## Slide 20: Results (NN trained on G=0)
G = 1
Anharmonicity x1 (=200 e-3)
With G=0, 0.99994…

## Slide 21: Results (NN trained on G=0)
G = 1
Anharmonicity x10 (=200 e-2)
With G=0, 4 nines
With G=0, 0.99994…

## Slide 22: Fine-tuning on G=1
NN structure:
  8 FC layers with ReLu
Total of 760 params
The loss involves numerical integration
  non (automatically) differentiable with TF

## Slide 23: Fine-tuning on G=1
Gradient Descent must be done by hand
Gradient should be calculated varying one parameter at a time
  For each epoch, 760x2 evaluations necessary
Faster method:
  SPSA

## Slide 24: Retraining
Changing at each epoch

## Slide 25: Retraining
10 fixed batches of 100 elements

## Slide 26: Conclusion
One possible path
  Many epochs are needed + early stopping
  Bigger NN for higher accuracy and faster convergence
Extreme path:
  Perform full Gradient Descent: 76 000% more computations
Alternative:
  Actually only are needed
  is «free»: obtained varying the phase
  obtainable using only : training necessary only for 2 angles!
Overall, RB is promising for adapting NN to varying phys. parameters

## Slide 27
Thank you for your attention

## Slide 28: References
[1] Petersson et al., Optimal Control of Closed Quantum Systems via B-Splines with Carrier Waves, arXiv:2106.14310
[2] Fahim et al., hls4ml: An Open-Source Codesign Workflow to Empower Scientific Low-Power Machine Learning Devices, arXiv:2103.05579
[3] Wallman et al., Randomized Benchmarking with Confidence, arXiv:1404.6025